|  | SPECTRUM ASTRO, INC. high energy Solar spectroscopic imager (hessi) PROGRAM FLIGHT software Operations Manual contract no. PPB005884 |  |
| --- | --- | --- |
| SPECTRUM ASTRO PROPRIETARY DOCUMENT |
| THIS DOCUMENT CONTAINS SPECTRUM ASTRO PROPRIETARY INFORMATION. RECIPIENT, BY ACCEPTING THIS DOCUMENT, AGREES THAT NEITHER THE DOCUMENT NOR ANY INFORMATION CONTAINED WITHIN IT SHALL BE REPRODUCED OR TRANSFERRED TO OTHER DOCUMENTS NOR USED OR DISCLOSED TO OTHERS FOR MANUFACTURING OR ANY OTHER PURPOSES EXCEPT AS SPECIFICALLY AUTHORIZED IN WRITING BY SPECTRUM ASTRO. |
| PREPARED BY: |
| SPECTRUM ASTRO, INC. |
| 1440 N. Fiesta Boulevard |
| Gilbert, Arizona 85233 |
| CAGE Code 0T9D1 |
| INITIAL RELEASE DATE |
| 14 JANUARY 2000 |

| 1110-EU-S17595 | REV - |
| --- | --- |
| 14 JANUARY 2000 |

1110-EU-S17595

|  | SPECTRUM ASTRO, INC. high energy Solar spectroscopic imager (hessi) PROGRAM FLIGHT software Operations Manual contract no. PPB005884 |  |
| --- | --- | --- |

| REVIEWED BY: |  |  |
| --- | --- | --- |
|  | CONFIGURATION/DATA CONTROL, Joe Jurhill | DATE |
| preparED BY: |  |  |
|  | engineering, Jonathan Yount | DATE |
| APPROVED BY: |  |  |
|  | QUALITY ASSURANCE, Jeff Squires | DATE |
| APPROVED BY: |  |  |
|  | sYSTEM ENGINEERING, JOHN JORDAN | DATE |
| APPROVED BY: |  |  |
|  | PROGRAM MANAGER, Mike Matranga | DATE |

| REVISION SUMMARY |  |  |  |
| --- | --- | --- | --- |
| REV | RELEASE DATE | BRIEF DESCRIPTION/REASON FOR CHANGE | EFFECTIVE PAGES |
| - | 14 January 2000 | Initial release. | All |

# TABLE OF CONTENTS

# PAGE

1.	SCOPE	0

1.1	Identification	0

1.2	System Overview	0

2.	REFERENCED DOCUMENTS	0

2.1	Referenced Documents	0

2.1.1	General	0

3.	FLIGHT SOFTWARE BOOT SEQUENCE	0

3.1	FSW Boot Overview	0

3.2	FSW Boot Configuration	0

3.3	Operating System Select	0

3.4	Flight Software Select	0

3.5	Initial Stored Sequence (Mission Mode)	0

3.6	Manually Rebooting	0

4.	IN-FLIGHT FILESYSTEM	0

4.1	EEPROM Write Protection	0

4.1.1	SMEEPROMWRITE Telecommand	0

4.1.2	EEPROM Device Level Software Data Protection Mode	0

4.1.3	Example of modifying the EEPROM1 filesystem	0

4.2	Filesystem Content Telecommand	0

5.	STORAGE MANAGEMENT SUBSYSTEM	0

5.1	Loading Tables	0

5.2	Dumping Tables	0

5.3	Aborting Table Operations	0

5.4	Loading, Copying and Dumping Memory	0

5.5	PACI Pseudo Non-Volatile Logs	0

5.6	Managing Event Messages	0

# TABLE OF CONTENTS (CONTINUED)

# PAGE

5.7	In-flight FSW Reprogramming	0

5.8	Spacecraft Clock	0

5.9	VME Interrupt Control	0

5.10	Miscellaneous Housekeeping	0

6.	STORED TELECOMMAND SEQUENCES	0

6.1	Absolute-Time Sequences	0

6.2	Relative-Time Sequences	0

6.3	Stored Sequences and the Filesystem	0

6.4	Specific Relative-Time Sequences	0

7.	PAYLOAD INTERFACE SUBSYSTEM	0

7.1	Payload Commanding	0

7.2	Payload Telemetry	0

7.3	Science Telemetry	0

7.4	Payload Telecommands	0

8.	SSR INTERFACE SUBSYSTEM	0

8.1	SSR Subsystem Initialization	0

8.2	SSR Subsystem 1 Hz Processing	0

8.3	Record and Playback Telecommands	0

8.4	SSR Passthrough Telecommand	0

8.5	SSR SOH Telemetry	0

8.6	SSR Maintenance Telecommands	0

8.7	SSR Housekeeping Telecommands	0

9.	ATTITUDE CONTROL SUBSYSTEM	0

9.1	ACS Control Telecommands	0

9.2	ACS Flight Parameters	0

9.3	ACS Telemetry	0

# TABLE OF CONTENTS (CONTINUED)

# PAGE

9.4	ACS Housekeeping Telecommands	0

10.	STATE OF HEALTH SUBSYSTEM	0

11.	UPLINK SUBSYSTEM	0

11.1	CCSDS COP-1 Protocol Control	0

11.2	Uplink Subsystem CRC Commands	0

11.3	Resetting the CIB Device FPGAs	0

11.4	Switching CIB Uplink Channel	0

11.5	Uplink Subsystem Housekeeping	0

12.	DOWNLINK SUBSYSTEM	0

12.1	Transmitter and Bypass	0

12.2	Managing Stored Telemetry	0

12.3	CIB Device Downlink Bit Rate	0

12.4	Downlinked Housekeeping	0

13.	PCB INTERFACE SYSTEM	0

13.1	Power Switches	0

13.1.1	Transmitter Switch	0

13.2	Torque Rods	0

13.3	Inertial Adjustment Device	0

13.4	Solar Array Releases	0

13.5	Mission Mode	0

13.6	PCB Miscellaneous Telecommand	0

13.7	PCB Interface Housekeeping Telecommands	0

14.	SCHEDULER SUBSYSTEM	0

15.	FAULT MANAGEMENT	0

15.1	Interrupts	0

15.2	Fault Monitors	0

# TABLE OF CONTENTS (CONTINUED)

# PAGE

15.2.1	Analog Sensors	0

15.2.2	ACS Sun Pointing Fault	0

15.2.3	Loss of Telecommanding	0

15.2.4	Clearing Fault Response Indications	0

15.3	CPU EDAC RAM Scrubbing	0

15.4	PACI EDAC RAM Scrubbing	0

15.5	CIB Watchdog Timer	0

15.6	FSW O/S Task Monitor	0

15.7	FSW Program Text Segment Corruption Monitor	0

15.8	Fault Management Housekeeping	0

16.	FLIGHT PARAMETERS	0

16.1	Changing Flight Parameters	0

17.	UTILITY APPLICATIONS	0

17.1	binToTableLoad	0

17.2	gen_itos_report	0

17.3	hessiChecksum	0

17.4	hessiLogTool	0

17.5	sendbin	0

17.6	default	0

# LIST OF TABLES

Table 4-1.  Filenames and Maximum File Length	0

Table 6-1.  Special Purpose Relative-Time Sequences	0

Table 7-1.  Spacecraft Status Segment Sources	0

Table 8-1.  SSR Subsystem Initial Vaules	44

Table 8-2.  SSR Telemetry to Monitor	52

Table 9-1.  ACS Flight Parameters	0

# LIST OF TABLES (CONTINUED)

# PAGE

Table 9-2.  ACS Telemetry	0

Table 12-1.  Stored Telemetry APIDs	0

Table 14-1.  Subsystem Wakeup Schedule	0

Table 15-1.  Interrupt Monitors	0

Table 15-2.  FSW Interrupt Telemetry Points	0

Table 15-3.  Analog Sensor Fault Monitors	0

Table 15-4.  ACS Fault Monitor	0

Table 15-5.  Loss of Telecommand Fault Response	89

Table 16-1.  Flight Parameters	0

# LIST OF ACRONYMS

| ACS | Attitude Control Subsystem |
| --- | --- |
| ADB | Auxiliary Driver Board |
| APID | Application Identifier |
| ATS | Absolute Time Sequence |
| CCB | Charge Control Board |
| CCSDS | Consultative Committee for Space Data System |
| CIB | Communication Interface Board |
| COP-1 | Command Operation Procedure, version 1 |
| CPU | Central Processing Unit |
| CRC | Critical Command |
| EDAC | RAM with single bit upset immunity |
| EEPROM | Electrically Erasible Programmable ROM |
| EFC | Engineering Flight Software |
| FARM-1 | Frame Acceptance and Reporting Mechanism, version 1 |
| FSS | Fine Sun Sensor |
| FSW | Flight Software, which is defined as the non-ACS software |
| GSFC | Goddard Space and Flight Center |
| HCD | Hardware Command Decoder |
| HESSI | High Energy Solar Spectroscopic Imager |
| IAD | Inertial Adjustment Device |
| IDPU | Instrument Data Processing Unit |
| ITOS | Integration and Test Operations System |
| MB | Mega Bytes |
| MIPS | Million Instructions Per Second |
| O/S | Operating System |

LIST OF ACRONYMS (CONTINUED)

| PACI | Payload and Attitude Control Interface |
| --- | --- |
| PCB | Power Control Board |
| PNVRAM | PACI Pseudo Non-Volatile RAM |
| RAM | Random Access Memory |
| ROM | Read-Only Memory |
| RTS | Relative Time Sequence |
| SCLK | Spacecraft Clock |
| SDP | Software Data Protection, for EEPROM |
| SMEX | Small Explorer, NASA program |
| SAS | Solar Aspect System |
| SOH | State Of Health |
| SSR | Solid State Recorder |
| SUROM | Startup ROM |
| TC | Telecommand |
| TLM | Telemetry |
| TTL | Transistor-Transistor Logic |
| VC0 | Virtual Channel 0 |
| VC1 | Virtual Channel 1 |
| VME | VersaModule Eurocard bus, a 32-bit data bus |

# SCOPE

## Identification

This document is the High Energy Solar Spectroscopic Imager (HESSI) spacecraft flight software operations manual.

## System Overview

The Flight Software(FSW) executes on a RAD6000 Flight Central Processing Unit (CPU) and supports control and access to all the spacecraft functions through sending spacecraft commands and receiving spacecraft telemetry from the Integration and Test Operations System (ITOS) ground station. The HESSI FSW interfaces with six VME hardware boards: directly access to RAD6000 CPU, Payload and Attitude Control Interface (PACI), Communications Interface Board (CIB), the Power Control Board (PCB), and the Auxiliary Driver Board (ADB), and indirect access to the Charge Control Board (CCB).

FSW communicates to the Instrument Data Processing Unit (IDPU), and Solid State Recorder (SSR) via the PACI board. The PACI board is responsible for decoding and providing all analog and digital telemetry. The PACI board is also responsible for the real-time State Of Health (SOH) telemetry frame.

The CIB board has three telemetry input paths:  VersaModule Eurocard bus, a 32-bit data bus (VME) for FSW telemetry, PACI serial for real-time SOH, and Solid State Recorder (SSR) serial for science data.

The CPU board has 128 Mega Bytes (MB) (Random Access Memory (RAM) and 3 MB Electrically Erasible Programmable ROM (EEPROM), with a CPU is running at 10 Million Instructions Per Second (MIPS).

To support in-flight reprogramming, FSW is partitioned into 24 separate files that are loaded into an EEPROM filesystem. At power up, a boot program (one file) is loaded and run.  The boot program loads and runs the Operating System (O/S) (one file). After the O/S boots, it loads flight software (22 files).

Flight software has access to two absolute-time sequence-stored telecommand sequences and sixty-four relative-time sequenced stored telecommand sequences.

# REFERENCED DOCUMENTS

## Referenced Documents

Unless otherwise specified, the following documents in their current issue form a part of this document to the extent specified herein.

### General

a.	1110-EW-T17552	HESSI Telecommand and Telemetry Database Specification

b.	1110-EW-S16620	HESSI Attitude Control Subsystem Flight Software Specification

# FLIGHT SOFTWARE BOOT SEQUENCE

## FSW Boot Overview

On power up, or as a result of a processor reset, the RAD6000 CPU starts reading instructions and starts executing out of its Start-Up ROM (SUROM).  The SUROM sets up the initial state of the processor, various hardware devices, and clears all 128 MB of EDAC RAM. The SUROM then copies a predefined region of code from EEPROM into RAM, and jumps to a predefined location.

The code that the Startup ROM(SUROM) copies is the first 4096 bytes of the bootrom.bin file from the in-flight filesystem in EEPROM. The in-flight filesystem will be described in detail in Section 4.  IN-FLIGHT FILESYSTEM starting on page 0. In brief, the are three in-flight filesystems: one read-only filesystem in EEPROM, one read-write filesystem in EEPROM, and one read-write filesystem in RAM.

The bootrom.bin is called the O/S Boot ROM program. The purpose of the O/S Boot ROM program is the allow for the flexibility of loading the Operating System (O/S) and FSW from different filesystems.  When the O/S Boot ROM program starts executing, it copies its entire contents from EEPROM into RAM, and continues execution.  The O/S Boot ROM reads various input configuration parameters, and then loads and starts executing the O/S from a filesystem.

The O/S provides access to various device resources and provides the real-time task scheduling capabilities.  After the O/S has initialized, it reads various input configuration parameters and then loads FSW from twenty-two files in the in-flight filesystem. After all files have been loaded, the boot filesystem is copied into RAM as the working filesystem. FSW is then started.

After FSW has been started, an initial stored sequence of telecommands is started.

## FSW Boot Configuration

The various files that are loaded at boot time is configurable:

a.	The O/S file load with the SMREBOOT telecommand.

b.	The FSW files loaded with the CRC22 bit or with the SMREBOOT telecommand

c.	The initial stored sequence executed with the PCBMISSNMODE telecommand

The default boot configuration on power-up or after a VME SYSRESET signal is: O/S is loaded from the EEPROM1 (read-only) filesystem, FSW is loaded from the based on FSW select Critical Command (CRC), the stored sequence selected by Mission Mode is started.

## Operating System Select

The SMREBOOT telecommand writes configuration parameters to a specific region in RAM to be read after a reboot.  One specific parameter indicates to the O/S Boot ROM the name of the O/S file in the in-flight filesystem.  The options for this parameter is either the O/S file in EEPROM1 or the O/S file RAM.

## Flight Software Select

One specific parameter that the SMREBOOT telecommand writes to a specific region in RAM indications the filesystem from which to read flight software. This filesystem can be any three of the in-flight filesystems.

If the FSW filesystem is not specified in that specific region in RAM, then the CRC22 bit is read from the CIB.  If the CRC22 bit is zero, then FSW is read from the EEPROM1 filesystem; if the bit is one, the FSW is read from the EEPROM2 filesystem.  The selected filesystem is then copied to the RAM filesystem so that ‘working’ copies are available for modification.

## Initial Stored Sequence (Mission Mode)

The initial stored sequence that is started is after boot-up is selectable with the Mission Mode indicator. The Mission Mode indicator is output as two bits from the PCB.  If either of the bits is zero, then the Mission Mode is the ‘Launch’, and the RTS00 stored sequence will be started. If both bits are one, then the Mission Mode is ‘Nominal’, and the RTS01 stored sequence will be started.

## Manually Rebooting

The SMREBOOT telecommand allows the operator to manually reboot the CPU.  The SMREBOOT telecommand has two parameters, OSBOOTDEVICE and FSBOOTDEVICE, for selecting the filesystem from which to load the O/S and FSW files. Keep in mind that the Watchdog Timer (CRC19) must be disabled when manually rebooting as otherwise it expire and send a VME SYSRESET signal to reset the CPU.

SMREBOOT Reboots the flight software from the image in EEPROM or RAM OSBOOTDEVICE (UB) Selects the device from which load 'vxWorks' O/S Range: 0 to 2 0 = OS_EEPROM1 EEPROM1 OS boot: /hessiFs/eeprom1/vxWorks 2 = OS_RAM RAM OS boot: /hessiFs/ram/vxWorks FSBOOTDEVICE (UB) Selects the device from which to load FSW Range: 0 to 2 0 = FSW_EEPROM1 EEPROM1 FSW /hessiFs/eeprom1/ 1 = FSW_EEPROM2 EEPROM2 FSW /hessiFs/eeprom2/ 2 = FSW_RAM RAM FSW /hessiFs/ram/

Telemetry: After reboot, the following telemetry points will be set appropriately: TFSWVERSION (U1234) Flight Software Version TFMBOOTDEV (UB) The current boot device (0=default boot EEPROM1, commanded 1=EEPROM1, 2=EEPROM2, 3=RAM) TFMBOOTTIMEI (TIME40) FSW Boot Time

# IN-FLIGHT FILESYSTEM

There are three in-flight filesystems:

| Filesystem Name | Filesystem Type | Filesystem Size |
| --- | --- | --- |
| /hessiFs/eeprom1/ | Read-only EEPROM | 2036 Kbytes |
| /hessiFs/eeprom2/ | Read-write EEPROM | 1024 Kbytes |
| /hessiFs/ram/ | Read-write RAM | 2048 Kbytes |

Each filesystem has a fixed size, a fixed number of 104 files, a maximum length for each file, a checksum for each file directory entry, and a checksum for the contents of each file. Table 4-1, Filenames and Maximum File Length lists the names of the files in each filesystem with their respective maximum file length.  Some files can be referenced by more than one name.  For example, the bootrom.bin file can also be referenced as ‘fsw00’. The files are organized as:

| fsw00 – fsw31 | Flight software files |
| --- | --- |
| ats00 – ats01 | Absolute-time sequenced stored telecommand sequences |
| rts00 – rts63 | Relative-time sequenced stored telecommand sequences |
| param | Flight parameters |
| file00 – file03 | General purpose files |
| directory | Filesystem information about each file |

In ITOS, files are referred to as tables. All files get loaded, and can be dumped, using the SMTBLLOAD and SMTBLDUMP telecommands described in Section 4.2, Filesystem Content Telecommand. A listing of the contents of a filesystem can be retrieved using the SMTBLDESCDMP telecommand, and displayed using the ITOS SMFSWFILES and SMSEQFILES pages.

Each file in the RAM filesystem has a corresponding telemetry point that indicates whether a file contains data. In ITOS terms, when a file contains data it is considered ‘loaded’; when a file contains no data (file length of zero), then the file is considered ‘not loaded’. These telemetry points are named TSMTBLNUM000 – TSMTBLNUM103, and are displayed on the REPROGRAMMING page.

Table 4-1.  Filenames and Maximum File Length

| Filename | Max Length |  | Filename | Max Length |  | Filename | Max Length |
| --- | --- | --- | --- | --- | --- | --- | --- |
| bootrom.bin (fsw00) | 204800 |  | rts01 | 304 |  | rts36 | 304 |
| vxWorks (fsw01) | 835584 |  | rts02 | 304 |  | rts37 | 304 |
| vxWorks.load (fsw02) | 1024 |  | rts03 | 304 |  | rts38 | 304 |
| fsw_fswLoad.o (fsw03) | 5120 |  | rts04 | 304 |  | rts39 | 304 |
| fsw_fswStart.o (fsw04) | 8192 |  | rts05 | 304 |  | rts40 | 304 |
| fsw_acs.o (fsw05) | 87040 |  | rts06 | 304 |  | rts41 | 304 |
| fsw_autocode.o (fsw06) | 41984 |  | rts07 | 304 |  | rts42 | 304 |
| fsw_commandProcessor.o (fsw07) | 95232 |  | rts08 | 304 |  | rts43 | 304 |
| fsw_devices.o (fsw08) | 37888 |  | rts09 | 304 |  | rts44 | 304 |
| fsw_downlink.o (fsw09) | 45056 |  | rts10 | 304 |  | rts45 | 304 |
| fsw_eventtask.o (fsw10) | 13312 |  | rts11 | 304 |  | rts46 | 304 |
| fsw_faultmgmt.o (fsw11) | 41984 |  | rts12 | 304 |  | rts47 | 304 |
| fsw_hessiRoot.o (fsw12) | 0 |  | rts13 | 304 |  | rts48 | 304 |
| fsw_idpuInterface.o (fsw13) | 25600 |  | rts14 | 304 |  | rts49 | 304 |
| fsw_infrastructure.o (fsw14) | 111616 |  | rts15 | 304 |  | rts50 | 304 |
| fsw_interrupts.o (fsw15) | 9216 |  | rts16 | 304 |  | rts51 | 304 |
| fsw_pcbinterface.o (fsw16) | 43008 |  | rts17 | 304 |  | rts52 | 304 |
| fsw_reprogramming.o (fsw17) | 111616 |  | rts18 | 304 |  | rts53 | 304 |
| fsw_scheduler.o (fsw18) | 17408 |  | rts19 | 304 |  | rts54 | 304 |
| fsw_simdevices.o (fsw19) | 49152 |  | rts20 | 304 |  | rts55 | 304 |
| fsw_soh.o (fsw20) | 19456 |  | rts21 | 304 |  | rts56 | 304 |
| fsw_ssrInterface.o (fsw21) | 89088 |  | rts22 | 304 |  | rts57 | 304 |
| fsw_tcmessagemap.o (fsw22) | 6144 |  | rts23 | 304 |  | rts58 | 304 |
| fsw_tcrouter.o (fsw23) | 11264 |  | rts24 | 304 |  | rts59 | 304 |
| fsw_uplink.o (fsw24) | 44032 |  | rts25 | 304 |  | rts60 | 304 |
| fsw25 | 0 |  | rts26 | 304 |  | rts61 | 304 |
| fsw26 | 0 |  | rts27 | 304 |  | rts62 | 304 |
| fsw27 | 0 |  | rts28 | 304 |  | rts63 | 304 |
| fsw28 | 0 |  | rts29 | 304 |  | params | 2048 |
| fsw29 | 0 |  | rts30 | 304 |  | file00 | 24576 |
| fsw30 | 0 |  | rts31 | 304 |  | file01 | 7168 |
| fsw31 | 0 |  | rts32 | 304 |  | file02 | 4096 |
| ats00 | 35004 |  | rts33 | 304 |  | file03 | 4096 |
| ats01 | 35004 |  | rts34 | 304 |  | . (directory) | 2496 |
| rts00 | 304 |  | rts35 | 304 |  |  |  |

## EEPROM Write Protection

The EEPROM filesystems have write protection mechanisms that need to be disabled before the user can successfully change.  The following three methods ensure that the EEPROM will not be inadvertently written to in flight:

a.	FSW Filesystem Write Enable.
On boot, FSW considers both EEPROM filesystems to be read-only. The SMEPROMWRITE telecommand allows the ground to change the filesystem write mode between read-only and read-write. When a filesystem is read-only, writes attempts return an error.

b.	Hardware EEPROM Write Enable.
The EEPROM device write-enable signal enable/disables writing to all 3MB of EEPROM. This signal is tied to CIB HCD/CRC 21. When CRC21 is clear, this signal prevents inadvertent and explicit writes from programming EEPROM.

c.	EEPROM Device Level Software Data Protection (SDP) Mode.
The first 2 MB of EEPROM, which is the first EEPROM filesystem, will be protected using the device level Software Data Protection mode of the EEPROM multi-chip modules.  The EEPROM device level write protection configuration is set during I&T and retained in the EEPROM devices during the remainder of I&T and in flight.  This feature will allows the top 1 MB portion of EEPROM to be reprogrammed in flight while protecting the lower 2MB containing the primary boot FSW image.
The device level data protection mode still allows the protected portion of EEPROM to be reprogrammed, but in order to write to the protected portion of the EEPROM a special write sequence must be followed for each data byte written.  The FSW will not contain the code that can write this special sequence, so the protected portion of EEPROM is prevented from being inadvertently reprogrammed.  To reprogramming this portion of EEPROM, additional software must be uploaded and executed.

### SMEEPROMWRITE Telecommand

The SMEPROMWRITE telecommand is used to change the filesystem write mode between read-only and read-write:

SMEPROMWRITE Enable/Disable various mechanisms to write to EEPROM ENABLESELECT (UB) Select mechanism to enable/disable writing Range: 1 to 2 1 = FSYS_EEPROM1 Enable writing to EEPROM1 filesystem. 2 = FSYS_EEPROM2 Enable writing to EEPROM2 filesystem. ENABLE (UB) 1=enable writing, 0=disable writing to EEPROM Range: 0 to 1 0 = OFF 0 = NO 0 = FALSE 1 = YES 1 = TRUE 1 = ON

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMEEP1FSWR (U12) TRUE indicates that the EEPROM1 Filesystem is enabled for writing. TSMEEP2FSWR (U12) TRUE indicates that the EEPROM2 Filesystem is enabled for writing.

### EEPROM Device Level Software Data Protection Mode

The RAD6000 EEPROM is a Hitachi HN58C1001 Series device. It is a 131072-word x 8-bit Electrically Erasable and Programmable CMOS ROM.  It has a Software Data Protection (SDP) mode that helps prevent inadvertent writes to EEPROM by forcing a specific data pattern to be written for each byte stored in the EEPROM.  The RAD6000 combines 8 chips into one 'package' to create a 1 MB EEPROM device that is 262144-word x 32-bits.  This means that there are two sets of 4 chips, each forming 32-bits. When enabling or disabling SDP mode, the special data pattern must be written to every EEPROM device in the package for the first 2 Mbytes of EEPROM.

What this means is that there are six ‘banks’ of EEPROM, each 512 Kbytes, for which SDP mode can separately enabled or disabled. Only the first four banks (2 Mbytes) have the SDP mode enabled. The software functions to enable and disable the EEPROM device level Software Data Protection (SDP) mode does not exist in the flight software. To enable or disable the EEPROM SDP, additional code must be uploaded and dynamically linked into the O/S. The object file “hessi/fsw/patches/eeprom_sdp.o’ contains three functions for use in enable, disabling and testing the SDP mode, named eepromEnableSdpMode(), eepromDisableSdpMode(), eepromTestSdpMode(size_t bankId).

eepromEnableSdpMode(int bankId) Enables the Hitachi EEPROM Software Data Protection (SDP) mode for the commanded EEPROM bank. Each bank of EEPROM is 512 Kbytes in length. The SDP mode is enabled using the following steps: 1) Read a single 32-bit value for beginning of the bank of EEPROM. 2) Write enable SDP mode pattern. 3) Write the original 32-bit value to EEPROM. Inputs: bankId - the EEPROM bank for which to enable SDP mode protection. Range is 1 to 6. Returns: 0 if successful; -1 on error.

eepromDisableSdpMode() Disables the Hitachi EEPROM Software Data Protection mode for the commanded EEPROM bank. Each bank of EEPROM is 512 Kbytes in length. Inputs: bankId – the EEPROM bank for which to disable SDP mode protection. Range is 1 to 6. Returns: 0 if successful; -1 on error

eepromTestSdpMode(int bankId) Tests to see if Software Data Protection mode is in effect by writing to a location in the commanded EEPROM bank. Each bank of EEPROM is 512 Kbytes in length. The location and original value are printed before any modifications are made. This SDP test is accomplished using the following steps: 1) Read value at specific EEPROM address. 2) Write a different value. 3) Wait 10 ms. 4) Read value. If it is the original value, then test is successful. If it is the different value, test failed. 5) If test failed, write the original value; wait 10 ms. Input: bankId – the EEPROM bank for which to test. Returns: 0 if SDP mode is in effect, and write to EEPROM failed as expected -1 if SDP mode is NOT in effect, and EEPROM was modified by write

To enable, disable or test the EEPROM SDP mode, the eeprom_sdp.o object file must first be uploaded to the HESSI spacecraft, loaded into the O/S, and then calling the various functions. Use the following steps to accomplish this:

a.	Use the binToTableLoad utility program (Section 17.1 binToTableLoad on page 0) to generate an ITOS table load file for one of the general purpose files (FILE00 – FILE03) from the eeprom_sdp.o file.

b.	Use a text editor to generate one or more script files containing the functions that need to be called.

c.	Use the binToTableLoad utility program to generate an ITOS table load file(s) from the script file(s).

d.	Uplink the load files containing the eeprom_sdp.o and script file(s) files using the ITOS LOAD command.

e.	Load the eeprom_sdp.o file into the O/S using the SMLOADMODULE telecommand.

f.	Execute the script(s) using the SMRUNSCRIPT telecommand.

### Example of modifying the EEPROM1 filesystem

The following is an example of saving a new initial stored sequence, RTS00, to the EEPROM1 filesystem.  This is a realistic example in that the RTS00 sequence is likely to be changed before launch.

a.	Build a new RTS00 load file using MPS or the ITOS leditor application.

b.	Uplink RTS00 using the ITOS LOADPKT or LOAD command to the RAM filesystem.

c.	Use the binToTableLoad utility program to generate an ITOS table load file from the eeprom_sdp.o object module:
binToTableLoad –c –t file00 –i ~/hessi/fsw/patches/eeprom_sdp.o –o ~/hessi/build/itos/loads/eeprom_sdp.atf

d.	Use a text editor to generate two script files containing the functions to be called:

File enablesdp.txt:
eepromEnableSdpMode(1)
eepromEnableSdpMode(2)
eepromEnableSdpMode(3)
eepromEnableSdpMode(4)
eepromTestSdpMode(1)
eepromTestSdpMode(2)
eepromTestSdpMode(3)
eepromTestSdpMode(4)

File disablesdp.txt:
eepromDisableSdpMode(1)
eepromDisableSdpMode(2)
eepromDisableSdpMode(3)
eepromDisableSdpMode(4)

e.	Use the binToTableLoad utility program to generate an ITOS table load files from the two script files:
binToTableLoad –t file01 –i enablesdp.txt –o ~/hessi/build/itos/loads/enablesdp.atf
binToTableLoad –t file02 –i disablesdp.txt –o ~/hessi/build/itos/loads/disablesdp.atf

f.	Uplink the load files containing the eeprom_sdp.o and script files files using the ITOS LOAD command:
LOAD eepromsdp.atf
LOAD enablesdp.atf
LOAD disablesdp.atf

g.	Load the eeprom_sdp.o file into the O/S using the SMLOADMODULE telecommand:
/SMLOADMODULE FSW_RAM, FILE00

h.	Enable writes to the EEPROM1 filesystem with the SMEPROMWRITE telecommand:
/SMEPROMWRITE FSYS_EEPROM1, ON

i.	Enable writes to the EEPROM by setting CRC21:
START CRCSET(21)

j.	Disable the EEPROM SDP mode by running the disablesdp.txt script:
/SMRUNSCRIPT FSW_RAM, FILE02

k.	Copy the RTS00 table from RAM to the EEPROM1 filesystem:
/SMTBLSELECT RTS00, SRCSRAM, DESTEEPROM1
/SMTBLCOMMIT CKDISABLE, CHECKSUM=0

l.	Enable the EEPROM SDP mode by running the enablespd.txt script:
/SMRUNSCRIPT FSW_RAM, FILE01

m.	Disable writes to EEPROM by clearing CRC21:
START CRCCLEAR(21)

n.	Disable writes to the EEPROM1 filesystem:
/SMEPROMWRITE FSYS_EEPROM1, OFF

## Filesystem Content Telecommand

The SMTBLDESCDUMP telecommand will downlink a directory listing of all files in a specific filesystem.  The

ITOS pages SMFSWFILES and SMSEQFILES display telemetry points downlinked by this telecommand.

SMTBLDESCDMP Dumps info about each table: timestamp, size, checksum, etc TABLE_DEVICE (UB) Specifies one of three table devices. Range: 1 to 3 1 = DEV_EEPROM1 Read-only EEPROM device 2 = DEV_EEPROM2 Read-write EEPROM device 3 = DEV_RAM RAM device

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results.

# STORAGE MANAGEMENT SUBSYSTEM

The Storage Management subsystem provides telecommand access to the in-flight filesystem, system memory, the VME bus, pseudo non-volatile error logs, and various housekeeping configuration functionality.

## Loading Tables

ITOS tables are stored in files in the in-flight filesystems. The HESSI FSW provides several telecommands to select, load and dump files in the in-flight filesystem.  The format and usage of these telecommands were driven by those already in use on other NASA Small Explorer (SMEX) satellites and for which there is direct ITOS support.  If the ground operator is familiar with telecommand structure of ITOS and other SMEX satellites, the HESSI table manipulation telecommand will be vary similar to those previously used.

A table is loaded, or uplinked, by “selecting” the table name to operate on, and then sending one or more “load” telecommands, followed by a “commit” telecommand indicating that the loaded table should be saved. The SMTBLSELECT telecommand is used to “select” the table.  The effect is to copy the existing file into a temporary working buffer. The SMTBLLOAD telecommand is used to “load” data into the temporary working buffer. The SMTBLCOMMIT telecommand is used to indicate that all loaded data, and unmodified previous data, in the temporary working buffer should be saved to selected file.

The following is a description of each of these telecommands.

SMTBLSELECT Select Table Operation. Copies requested file into temporary working buffer. TABLEID (U12) Identification number of table to select. Range: 0 to 103 0 = DIRECTORY Filesystem Directory 1 = FSW00 FSW Object File 0 (Boot Image) 2 = FSW01 FSW Object File 1 3 = FSW02 FSW Object File 2 . . . (see Telecommand Database document for complete listing of filenames) SOURCE_TABLE (U12) Type of source memory for the table. Range: 1 to 4 1 = SRCEEPROM1 Source is table from version in read-only EEPROM 2 = SRCSRAM Source is operational version in SRAM 3 = SRCZERO Source is zero-filled version of table 4 = SRCEEPROM2 Source is table from version in read/write EEPROM DEST_TABLE (U12) Type of destination memory for the table. Range: 1 to 4 1 = DUMPONLY Table data can not be changed 2 = DESTEEPROM2 On commit, change version in R/W EEPROM 3 = DESTSRAM On commit, change operational version in SRAM 4 = DESTEEPROM1 On commit, change version in R/O EEPROM (ground only)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMOPSTATUS (UB) Table/memory operations status will be set to discrete value SMSTNONE (0). TSMLSTOPSTAT (UB) Last table/memory operations status will be set to discrete value SMSTTBLSELCT (7). TMTBLID (UB) Table ID currently selected will be set to TABLEID in telecommand. TSMSELTBLSIZ (U1234) Size of the currently selected table. TSMSRCTYPE (UB) Table/memory operations source type, SOURCE_TABLE from telecommand. TSMDESTTYPE (UB) Table/memory operations destination type, DEST_TABLE from telecommand.

SMTBLLOAD Load data into temporary working buffer. OFFSET (U1234) Byte offset into working table to begin load. Range: 0x00000000 to 0xFFFFFFFF DUMMYARG UB Destination, which is ignored, aways 2. Range: This parameter is ignored and may contain anything. It exists only to maintain compatability with other SMEX missions. 2 = DEFAULT Default value of dummy argument NUMBYTES (UB) Number of bytes to load. Range: 1 to 200 DATA (UB) An array of <NUMBYTES> bytes of data Range: 0 to 0xFF

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMOPSTATUS (UB) Table/memory operations status will be set to discrete value SMSTNONE (0). TSMLSTOPSTAT (UB) Last table/memory operations status will be set to discrete value SMSTTBLLOAD (5). TSMSELTBLSIZ (U1234) Size of the table after the load TSMNUMBYTES (U12) Number of bytes that were loaded as specified by NUMBYTES in telecommand TSMSTARTLOC (U1234) Starting offset of load specified by OFFSET in telecommand TSMTLDRECVD (UB) # of SMTBLLOAD commands received TSMTLDREJCT (UB) # of SMTBLLOAD commands rejected

Notes: OFFSET must be less than maximum file size, and OFFSET + NUMBYTES must be no larger than maximum file size or an error will result.

SMTBLCOMMIT Commit software table data. SELECT (U12) Commit table if checksum mismatch control flag. Range: 0 to 1 0 = CKDISABLE Disables use of the CHECKSUM parameter 1 = DEFAULT Same as CKDISABLE 1 = CKENABLE Enables use of the CHECKSUM parameter 2 = UNCOMPRESS Uncompress file, then apply CHECKSUM parameter CHECKSUM (U12) The checksum to be used with the table. Range: 0x0 to 0xFFFF

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMOPSTATUS (UB) Table/memory operations status will be set to discrete value SMSTNONE (0). TSMLSTOPSTAT (UB) Last table/memory operations status will be set to discrete value SMSTTBLCOMIT (6). TMTBLID (UB) Table ID currently selected will be set to TABLEID in telecommand will be set to 0xFF (no table). TSMTCMTRECVD (UB) # of SMTBLCOMMIT commands received TSMTCMTREJCT (UB) # of SMTBLCOMMIT commands rejected TSMATSSTMPAI (TIME40) Creation Timestamp of ATS Table A set equal to first 4 bytes of file if ATSA TSMATSSTMPBI (TIME40) Creation Timestamp of ATS Table B set equal to first 4 bytes of file if ATSB TSMTBLNUM??? (U23) (where ??? is file number) Will be set to TRUE if committed table has a file size greater than zero, FALSE otherwise.

## Dumping Tables

ITOS tables are stored in files in the in-flight filesystems. The HESSI FSW provides a telecommand dump file in the in-flight filesystem, and a telecommand to abort a dump that is in process.  The format and usage of these telecommands were driven by those already in use on other NASA SMEX satellites and for which there is direct ITOS support.  If the ground operator is familiar with telecommand structure of ITOS and other SMEX satellites, the HESSI table manipulation telecommand will be very similar to those previously used.

Before a table can be dumped, it must be selected with the SMTBLSELECT telecommand.  Depending on the size of the table dumped, one or more telemetry packets will be downlinked on Virtual Channel 1, APID 7.

The following is a description of the dump and abort telecommand.

SMTBLDUMP Dump software table data. OFFSET (U1234) Byte Offset Into Table to Begin Dump. Range: 0x0 to 0xFFFFFFFF NUMBYTES (U12) Number of Bytes to Dump. Range: 1 to 65535 NUMCOPYS (U12) Number of Copies of Dump to Transmit . Range: 1 to 8

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMOPSTATUS (UB) Table/memory operations status will be set initially to discrete value SMSTTBLDUMP (4), then set to SMSTNONE (0) on table dump completion. TSMLSTOPSTAT (UB) Last table/memory operations status will be set to discrete value SMSTTBLDUMP (4) on completion. TSMSTARTLOC (U1234) Starting location of dump offset set to OFFSET from telecommand TSMNUMBYTES (U12) Number of bytes to dump set to NUMBYTES from telecommand TSMBYTESREMN (U12) Number of bytes remaining to dump decrements from NUMBYTES to 0 as dump telemetry is downlinked. TSMCOPIES (UB) - # of copies of dump to transmit set to NUMCOPYS from telecommand TSMCPYREMAIN (UB) # of remaining copies to dump decrements from NUMCOPYS to 0 as dump telemetry is downlinked.

Notes: Table dump telemetry is downlink on Virtual Channel 1, APID 7.

## Aborting Table Operations

The SMDUMPABORT is used to abort a table or memory dump operation.  If aborting a table dump, then the current table is left selected.  The SMTBLRESET telecommand is used to reset table operations.  SMTBLRESET will also abort a table load, but not a memory load.  Unlike the SMDUMPABORT telecommand, the SMTBLRESET telecommand will leave no table selected.

SMDUMPABORT Abort memory or table dump. (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMOPSTATUS (UB) Table/memory operations status will be set to discrete value SMSTNONE (0). TSMLSTOPSTAT (UB) Last table/memory operations status will be set to previous value of TSMOPSTATUS. TSMBYTESREMN (U12) Number of bytes remaining to dump set to 0. TSMCPYREMAIN (UB) # of remaining copies to dump set to 0.

Notes: This telecommand will return error if the current TSMOPSTATUS is not SMSTMEMDUMP, SMSTTBLDUMP or SMSTPNVRAM.

SMTBLRESET Reset Software Table Operations. (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMOPSTATUS (UB) Table/memory operations status will be set to discrete value SMSTNONE (0). TSMLSTOPSTAT (UB) Last table/memory operations status will be set to previous value of TSMOPSTATUS. TMTBLID (UB) Table ID currently selected will be set to 0xFF (no table). TSMSELTBLSIZ (U1234) Size of the currently selected table set to 0. TSMSRCTYPE (UB) Table/memory operations source type set to 0. TSMDESTTYPE (UB) Table/memory operations destination type set to 0. TSMSTARTLOC (U1234) Starting location of load address set to 0. TSMNUMBYTES (U12) Number of bytes to dump set to 0. TSMBYTESREMN (U12) Number of bytes remaining to dump set to 0. TSMCOPIES (UB) - # of copies of dump to transmit set to 0. TSMCPYREMAIN (UB) # of remaining copies to dump set to 0.

Notes: This telecommand will return error if the current TSMOPSTATUS is not SMSTNONE, SMSTTBLDUMP or SMSTPNVRAM.

## Loading, Copying and Dumping Memory

The HESSI FSW provides a telecommand to load and copy CPU and VME memory, and to dump memory to telemetry.  The parameter format and usage of these telecommands were driven by those already in use on other NASA SMEX satellites. If the ground operator is familiar with telecommand structure of ITOS and other SMEX satellites, the HESSI memory dump telecommand will be very similar to that previously used.

Memory dump telemetry packets will be downlinked on Virtual Channel 1, APID 7.  The SMDUMPABORT telecommand can be used to abort a memory dump in progress.  The following is a description of the memory load dump, copy and dump telecommand.

SMMEMLOAD Load C&DH Processor Memory ADDRESS (U1234) Starting address of load. Range: 0x0 to 0xFFFFFFFF DESTINATION (U12) Destination memory type and data write size. Range: 1 to 2 2 = RAM RAM memory type. 2 = DEFAULT Default value NUMBYTES (UB) Number of bytes to load. Range: 1 to 200 DATA (UB) An array of <NUMBYTES> bytes of data, Range: 0 to 0xFF

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMOPSTATUS (UB) Table/memory operations status will be set initially to discrete value SMSTNONE (0). TSMLSTOPSTAT (UB) Last table/memory operations status will be set to discrete value SMSTMEMDUMP (2). TSMSTARTLOC (U1234) Starting location of load address set to ADDRESS from telecommand TSMNUMBYTES (U12) Number of bytes to load set to NUMBYTES from telecommand TSMBYTESREMN (U12) Number of bytes remaining set to 0. TSMMLDRECVD (UB) # of SMMEMLOAD commands received will increment by one. TSMMLDREJCT (UB) # of SMMEMLOAD commands rejected will increment if a parameter is out of range.

Notes: The RAD6000 contains 128 MB of memory: CPU Addresses 0x00000000 to 0x07FFFFFE The VME A24:D16 bus starts at the CPU offset of 0xB0000000. Not all VME bus addresses are can written to. All other addresses are invalid. Reading from invalid addresses have an unpredictable behavior.

SMMEMCOPY Copy EPROM, EEPROM, SRAM or VME memory. SOURCEAD (U1234) Starting address of source memory. Range: 0x0 to 0xFFFFFFFF DESTINATION (U12) Destination memory type. Range: Only 2 2 = DESTRAM Selects RAM as destination memory type. 2 = DEFAULT Default value DESTADD (U1234) Starting address of destination memory. Range: 0x0 to 0xFFFFFFFF NUMBYTES (U12) Number of bytes to copy. Range: 1 to 65535

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMOPSTATUS (UB) Table/memory operations status will be set initially to discrete value SMSTNONE (0). TSMLSTOPSTAT (UB) Last table/memory operations status will be set to discrete value SMSTMEMCOPY (3). TSMSTARTLOC (U1234) Starting location of load address set to SOURCEAD from telecommand TSMCOPYLOC (U1234) Destination address of memory copy set to DESTADD from telecommand TSMNUMBYTES (U12) Number of bytes to load set to NUMBYTES from telecommand TSMBYTESREMN (U12) Number of bytes remaining set to 0. TSMMCPRECVD (UB) # of SMMEMCOPY commands received will increment by one. TSMMCPREJCT (UB) # of SMMEMCOPY commands rejected will increment if a parameter is out of range.

Notes: The RAD6000 contains 128 MB of memory: CPU Addresses 0x00000000 to 0x07FFFFFE Memory copies are limited to CPU memory only; copies can NOT make use of the VME Bus. All other addresses are invalid. Reading from invalid addresses have an unpredictable behavior. Overlapping memory regions will be copied correctly.

SMMEMDUMP Dump SRAM or VME memory. ADDRESS (U1234) Starting address of dump. Range: 0x0 to 0xFFFFFFFF DUMPSIZE (U12) Number of bytes to dump. Range: 1 to 65535 NUMCOPYS (U12) Number of copies of dump to transmit. Range: 1 to 8

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMOPSTATUS (UB) Table/memory operations status will be set initially to discrete value SMSTNONE (0). TSMLSTOPSTAT (UB) Last table/memory operations status will be set to discrete value SMSTMEMDUMP (1). TSMSTARTLOC (U1234) Starting location of load address set to ADDRESS from telecommand TSMNUMBYTES (U12) Number of bytes to dump set to DUMPSIZE from telecommand TSMBYTESREMN (U12) Number of bytes remaining to dump decrements from DUMPSIZE to 0 as dump telemetry is downlinked. TSMCOPIES (UB) - # of copies of dump to transmit set to NUMCOPYS from telecommand TSMCPYREMAIN (UB) # of remaining copies to dump decrements from NUMCOPYS to 0 as dump telemetry is downlinked. TSMMLDRECVD (UB) # of SMMEMLOAD commands received will increment by one. TSMMLDREJCT (UB) # of SMMEMLOAD commands rejected will increment if a parameter is out of range.

Notes: The RAD6000 contains 128 MB of memory: CPU Addresses 0x00000000 to 0x07FFFFFE The VME A24:D16 bus starts at the CPU offset of 0xB0000000. Not all VME bus addresses are written to. All other addresses are invalid. Reading from invalid addresses have an unpredictable behavior. Table dump telemetry is downlink on Virtual Channel 1, APID 8.

## PACI Pseudo Non-Volatile Logs

To help in the post-analysis of the reason for a CPU reset, FSW continually logs information to the PACI Pseudo Non-Volatile RAM (PNVRAM). The RAM is termed pseudo non-volatile because it is not a true non-volatile RAM device, it is just that the PACI hardware board is on the essential bus and is never powered off, and thus the contents of RAM are never lost. The PNVRAM memory is also made up of RAM with single bit upset immunity (EDAC) RAM to protect against single bit errors.

The PNVRAM is divided into three log areas, allowing the ground to retrieve data about the last three CPU resets that occurred.  The current log area number is downlinked in the TFMCURPNVIDX telemetry point, is determined by reading the CIB Watchdog Timer reset count, and has a range of 0, 1 and 2.

Each log area has the capacity to store:

a.	60 seconds of SOH telemetry (1 frame per second)

b.	48 most recently received telecommands

c.	100 most recently received event error or warning messages

There are three telecommands available that act upon the PNVRAM logs.  The SMDLPNVTLM telecommand is used to downlink the contents of one of the log areas. The SMCLRPNVTLM telecommand is used to clear the contents of one of the log areas. The SMREINITPNV telecommand is used to reinitialize the entire PNVRAM EDAC RAM area.

The last FSW boot time, TFMBOOTIME, and the TFMCURPNVIDX telemetry point are displayed on the ITOS FAULTMANAGEMENT page. If either of these values change unexpectedly, then the previous PNVRAM log should be downlinked for analysis.

All PNVRAM telemetry is downlinked on Virtual Channel 1.  SOH telemetry has is downlinked with APID 1, The stored telecommand log is downlinked with APID 10 for complete telecommands, and APID 12 for codeblocks. Event messages are downlinked with APID 40.

SMDLPNVTLM Downlink one of the three PACI Pseudo Non-Volatile RAM (PNVRAM) logs LOGNUMBER (UB) The PNVRAM telemetry log index Range: 0 to 2

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results.

SMCLRPNVTLM Clear one of the three PACI Pseudo Non-Volatile RAM (PNVRAM) logs LOGNUMBER (UB) The PNVRAM telemetry log index Range: 0 to 2

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results.

SMREINITPNV Reinitialize all PACI Pseudo Non-Volatile RAM (PNVRAM) Region (non parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification

## Managing Event Messages

Event message allow FSW to efficient communicate readable English messages to the ground.  Event messages are used for a variety of situations:

a.	To report error information that can not be easy communicated in normal SOH telemetry.

b.	To report why a telecommand has returned an error

c.	To provide information for diagnostic purposes

When enabled for downlink, event messages are displayed in the hessiLogTool window of the ITOS desktop.  The Downlink Subsystem will store 100 telemetry frames of event messages, which is approximately 2000 individual event messages (depending on data lengths).

Event messages report the subsystem from which the message originated, the message severity, a message number, and optional data associated with the message.  Event message severity is categorized by six levels of severity:

a.	Fatal – will cause the CPU to reboot

b.	Error – an error occurred during processing

c.	Warning – want operator of a potential problem

d.	Info_Low – a low volume informational message

e.	Info_Medium – a moderate volume informational message

f.	Info_High – a high volume informational message

The ground operator can filter out messages by severity from being downlinked or stored in the Stored Telemetry Database. Only warning and informational messages can be filtered out.  The SMEVTFILTALL telecommand will change the event filter for all subsystems.  The SMEVTFILTER telecommand will change the event filter for a specific subsystem.

SMEVTFILTER Sets the Event Message Filter for a specific task TASKNAME (UB) A task name Range: 0 to 12 0 = SCHEDULER Scheduler Task 1 = ACS ACS Task 2 = PCBINTERFACE PCB Interface Task 3 = UPLINK Uplink Task 4 = TCPUPLINK TCP Uplink Task (test only) 5 = CMDPROCESSOR Command Processor Task 6 = SOH SOH Task 7 = PLINTERFACE Payload Interface Task 8 = SSRINTERFACE SSR Interface Task 9 = FAULTMGMT Fault Management Task 10 = TCPDOWNLINK TCP Downlink Task (test only) 11 = DOWNLINK Downlink Task 12 = REPROGRAM Reprogramming Task VOLUME (UB) Volume of Event Messages desired Range: 0 to 4 0 = NONE Only Error Event Messages will be output 1 = WARNING Error, warning Event Messages will be output 2 = INFO_LOW Error, warning, low volume informational messages 3 = INFO_MEDIUM Error, warning, medium volume informational messages 4 = INFO_HIGH Error, warning, high volume informational messages

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results.

SMEVTFILTALL Set Event Message Filter for all tasks VOLUME (UB) Event Message Filter Volume Range: 0 to 4 0 = NONE Only Error Event Messages will be output 1 = WARNING Error, warning Event Messages will be output 2 = INFO_LOW Error, warning, low volume informational messages 3 = INFO_MEDIUM Error, warning, medium volume informational messages 4 = INFO_HIGH Error, warning, high volume informational messages

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results.

## In-flight FSW Reprogramming

As discussed previously in Section 3. FSW Boot Sequence, FSW is partitioned into 24 separate files stored in an in-flight filesystem. This section will discuss the details of how to reprogram the FSW while in flight.

At power up, a boot program (one file) is loaded and run.  This boot program is the first file in the filesystem. There is only one version of this file that is ever used, and it is located in the first EEPROM filesystem at “/hessiFs/eeprom1/bootrom.bin”.

The boot program loads and runs the Wind River VxWorks real-time operating system, which is one file having the name ‘vxWorks’. There are two versions of this file available for boot.  This first is the default boot O/S located in the first EEPROM filesystem at “/hessiFs/eeprom1/vxWorks”.  The second version of this file is in the RAM filesystem located at “/hessiFs/ram/vxWorks”.  The second version can only be used as a result of the SMREBOOT telecommand discussed in Section 3.6 Manually Rebooting on page 0.

After the operating system boots, it loads 22 flight software files from one of the three in-flight filesystems. By default, the O/S looks at the CRC22 bit to determine whether the FSW files should be loaded from the EEPROM1 or EEPROM2 filesystem. This can be overridden by the SMREBOOT telecommand.

Because there are 22 flight software files, it would be very hard to have one number that reflects the state of every file, and so this is not attempted. Instead, the telemetry point TFSWVERSION reflects the state of all files at the specific point in time when all 22 files where released together. The value of the flight software version number reported in TFSWVERSION is stored in the file ‘fsw_infrastructure.o”. A better indication of the version of each of the 22 FSW files would probably be the checksum of each file as these will almost certainly change between versions. The checksum for each of the FSW files can be retrieved using the SMTBLDESCDUMP telecommand.

In addition to modifying one of the 22 flight software files, another method of modifying flight software would be to load an addition software module. This can be accomplished using the SMLOADMODULE telecommand. The general purpose files FILE00 to FILE03 provide a convenient location to stored addition software modules. When the SMLOADMODULE telecommand is used, the commanded object file is loaded and linked into the currently running operating system. Afterwards, specific functions (as determined by the programmer) will automatically be executed after the file is loaded, or any loaded functions can be executed directly from a script run with the SMRUNSCRIPT telecommand.

The binToTableLoad ground utility, described in Section 17.1 on page 0, is provided to generated an ITOS load file from any file. This is used to create load files for object and script files.

To decrease the uplink time necessary, any file can be compressed on the ground, uplinked, and then uncompressed in flight. Two ground utilities provide the compress capabilities: deflate and binToTableLoad. The deflate utility, described in Section 17.6 on page 0, simply compresses an file, much like other compression utilities. The binToTableLoad has a compression option that will first compress the input file using deflate and then generate the ITOS load file; inside the load file, the SMTBLCOMMIT telecommand specifies the UNCOMPRESS parameter to indicate the file should be uncompressed when it is committed. A file can also be compressed before the binToTableLoad utility is used, and then uncompressed in flight with the SMUNCOMPRESS telecommand.

The last method of modifying flight software is to modify the current O/S and FSW image running in RAM. This can is done with the SMMEMLOAD, SMMEMDUMP and SMMEMCOPY telecommands. This method might be used to change the values of a few locations in memory.

The SMRUNSCRIPT is a very versatile telecommand in that it runs a script that can call any VxWorks O/S or FSW function currently loaded into RAM. The output of the script is redirected into telemetry on Virtual Channel 1, APID 41. The output is decoded and displayed in the ‘hessiLogTool’ window on the ITOS display.

Since the 22 FSW files are dynamically linked into the O/S at run-time, there is no static map of what FSW will look like in RAM. This means a single global variable will not be in located in the same RAM address after every reboot. To determine the location of a global variable, a VxWorks script would be written, uplinked and executed. In addition, the same script could also modify the value of the global so that a subsequence SMMEMLOAD would not be required.

The various telecommands used to reprogram FSW are discussed below.

SMLOADMODULE Load an object module from a HESSI filesystem FILESYSTEM (UB) The HESSI filesystem from which to load file Range: 0 to 2 0 = FSW_EEPROM1 EEPROM1 FSW /hessiFs/eeprom1/ 1 = FSW_EEPROM2 EEPROM2 FSW /hessiFs/eeprom2/ 2 = FSW_RAM RAM FSW /hessiFs/ram/ FILENUMBER (UB) The file number to load Range: 0 to 103 0 = DIRECTORY Filesystem Directory 1 = FSW00 FSW Object File 0 (Boot Image) 2 = FSW01 FSW Object File 1 3 = FSW02 FSW Object File 2 . . . (see Telecommand Database document for complete listing of filenames)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification. TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results.

SMRUNSCRIPT Run a VxWorks script from HESSI filesystem FILESYSTEM (UB) The HESSI filesystem from which to load script Range: 0 to 2 0 = FSW_EEPROM1 EEPROM1 FSW /hessiFs/eeprom1/ 1 = FSW_EEPROM2 EEPROM2 FSW /hessiFs/eeprom2/ 2 = FSW_RAM RAM FSW /hessiFs/ram/ FILENUMBER UB The file number of script to run Range: 0 to 103 0 = DIRECTORY Filesystem Directory 1 = FSW00 FSW Object File 0 (Boot Image) 2 = FSW01 FSW Object File 1 3 = FSW02 FSW Object File 2 . . . (see Telecommand Database document for complete listing of filenames)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results.

SMUNCOMPRESS Uncompress the selected file, which was previously compressed. (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TSMOPSTATUS (UB) Table/memory operations status will be set to discrete value SMSTNONE (0). TSMLSTOPSTAT (UB) Last table/memory operations status set to discrete value SMSTUNCOMPRESS (9). TSMSELTBLSIZ (U1234) Size of the table after the uncompress operation.

Notes: Because the size of the uncompressed file is not known, the size is calculated inferred by the uncompressed data. The algorithm used requires that the last byte in the uncompressed file can not be 0xA5. This algorithm works for all object and script files, but may not work for all stored telecommand sequence files.

## Spacecraft Clock

The spacecraft clock (SCLK) can be set to a specific time using the SMSCLKSET telecommand. The spacecraft clock can be change but a specific number of seconds using the SMSCLKDELTA telecommand. The ITOS procedure SET_SCLK_TO_WALLCLOCK is useful during integration and test, and after a reboot, to set the spacecraft SCLK to the current wall clock time.

SMSCLKSET Set the seconds of the PACI Spacecraft Clock SCLKSECONDS (U1234) Number of seconds for Spacecraft Clock Range: 0 to 0xFFFFFFFF

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: All subsequent Transfer Frame and Source Packet time stamps. TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification

SMSCLKDELTA Change the PACI Spacecraft Clock by <DELTA> seconds SCLKDELTA (I12) Delta seconds to change Spacecraft Clock. Range: -32768 to 32767

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: All subsequent Transfer Frame and Source Packet time stamps. TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification

## VME Interrupt Control

The SMINTERRUPT telecommand enables the ground to enable and disable VME interrupts from various sources.  Generally, this telecommand should not need to be used, but is provided for completeness.

SMINTERRUPT Enable or disable various VME interrupts. INTERRUPT (UB)The interrupt source Range: 1 to 7 1 = CIBCODEBLOCK CIB Codeblock received interrupt 2 = CIBBUFAVAIL CIB Telemetry Buffer Available interrupt 3 = PACIBUSTICK PACI 1 Hz Bus Tick Interrupt 4 = PACIANALOG PACI 8 Hz Analog Scan Interrupt 5 = PACIIDPUDATA PACI IDPU Data Ready Interrupt 6 = PACISSRDATA PACI SSR Data Ready Interrupt 7 = PACIEDACERR PACI EDAC Double Bit Error Interrupt ENABLE (UB) 0=disable interrupt, 1=enable interrupt. Range: 0 to 1 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results.

## Miscellaneous Housekeeping

In addition to the telecommands discussed in the previous subsections, there are a few other housekeeping telecommands. The Storage Management Subsystem is also a kind of catch-all for miscellaneous telecommand that do not have a good home elsewhere.

The SMNOOP telecommand is available to simply determine that the Storage Management Subsystem is receiving and acknowledging telecommands. The SMNOOP does nothing but increment a telecommand received counter. The SMTCRESET telecommand is used to reset the Storage Management Subsystem telecommands received, rejected and error counters. The SMRESET telecommands sets the table load and commit, memory load, and copy received and reject counters to zero.

The SMCLREVTFLAG telecommand resets a few warning indicators that the operator should not miss.

The SMPACIDIGOUT telecommand allows the ground direct control over the PACI Transistor-Transistor Logic (TTL) Digital Output bits. This telecommand is generally meant for ground testing.

The SMTCMSGDIAG telecommand allows the ground to enable or disable an Event Message diagnostic that reports timing information about the routing of telecommands.  This telecommand is generally meant for ground testing.

SMNOOP Storage management no operation telecommand. (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one.

SMTCRESET Resets Storage Mgr. APIDs TC received/rejected/error counters (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will be set to one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification will be set to 0. TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will be set to 0.

SMRESET Reset Memory Manager software statuses. (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTLDRECVD (UB) # of SMTBLLOAD commands received set to 0. TSMTLDREJCT (UB) # of SMTBLLOAD commands rejected set to 0. TSMTCMTRECVD (UB) # of SMTBLCOMMIT commands received set to 0. TSMTCMTREJCT (UB) # of SMTBLCOMMIT commands rejected set to 0. TSMMLDRECVD (UB) # of SMMEMLOAD commands received set to 0. TSMMLDREJCT (UB) # of SMMEMLOAD commands rejected set to 0. TSMMCPRECVD (UB) # of SMMEMCOPY commands received set to 0. TSMMCPREJCT (UB) # of SMMEMCOPY commands rejected set to 0.

SMCLREVTFLAG Clears a specific latched event flag EVENTFLAG (UB) Identifies the event flag to clear Range: 0 to 15 0 = EVTSSRWOVRD Indicates SSR record pointer overtook read pointer 1 = EVTNORTFRAM Indicates all real-time telemetry frames allocated

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TEVTNORTFRAM (U12) Indicates that FSW allocated all real-time telemetry frames TEVTSSRWOVRD (U12) Event Flag indicates SSR record pointer overtook read pointer

SMPACIDIGOUT Write to bits in PACI Digital Output Register BITMASK (U12) Selects the bits to which to write Range: 0 to 65535 BITVALUES (U12) Sets values of the bits selected in BITMASK Range: 0 to 65535

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results. TPACMDDIGOUT (U12) Last commanded PACI Digital Output Word

SMTCMSGDIAG Enable/disable TC message routing event message diagnostics ENABLE UB 1=enable diagnostics; 0=disable diagnostics Range: 0 to 1 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSMTCRECVD (UB) # of Storage Manager TCs received will increment by one. TSMTCREJECT (UB) # of Storage Manager TCs that failed telecommand verification TSMTCERRORS (UB) # of Storage Manager TCs that failed to execute will increment if error results.

# STORED TELECOMMAND SEQUENCES

The Stored Command Subsystem manages the starting, processing, and stopping of stored sequences of telecommands. The are two types of stored telecommand sequences: absolute time-sequenced telecommands and relative time-sequences telecommands. An Absolute Time-Sequenced (ATS) telecommand has a timestamp that indicates the precise second when the telecommand should be executed.  A Relative Time-Sequenced (RTS) telecommand indicates a precise number of seconds that should be waited before executing a telecommand.  The format of the ATS and RTS files is documented in 1110- EW-T17380 HESSI Telecommand Format Specification.

In general, only one telecommand affecting an ATS can be received in any one second; only one telecommand per RTS can be received in any one second.

## Absolute-Time Sequences

There are two ATS tables, named ATSA and ATSB, of which only one can be active at any time.  Each ATS table contains up to 35004 bytes of data.

The SCATSSTART is used to start processing ATS table. When started, the stored telecommand processor will skip all telecommands that have a timestamp less than the current time. Up to eight ATS telecommands having the same timestamp will be executed in the same second; any other telecommands with the same timestamp will be skipped.

The SCATSSTOP is used to stop a currently processing ATS file. The SCATSSWITCH telecommand is used to switch to executing the other ATS that is currently not processing.

The SCATSVERIFY telecommand is used to verify that there are no errors in the format of an ATS file.  An ATS file can be verified while it is active. To avoid confusion, invalid telecommands detected by SCATSVERIFY and those encountered during ATS execution are flagged differently in telemetry.

These telecommands have been designed to have the same general format and behavior as those used on other SMEX spacecraft.

There are a number of telemetry points that don’t get set as a result of a telecommand, but get set as an ATS is processed. The following discusses these telecommand points:

a.	TSCATSRECVD (U12) Total of all ATS stored telecommands processed

b.	TSCATSREJECT (U12) Total of all ATS stored telecommands that failed verification

c.	TSCATSERRORS (U12) Total of all ATS stored telecommands that failed to route

d.	TSCATSLICDRI (UB) ID of the ATS containing the last invalid ATS stored TC

e.	TSCATSLICDIX (U12) Index of the last invalid ATS stored telecommand

f.	TSCATSLICDST (UB) Status of the last invalid ATS stored telecommand

g.	TSCATSLICDTS (TIME40) Timestamp of the last invalid ATS stored telecommand

SCATSSTART Start Stored Command Absolute Time Sequence. BUFFER (U12) ATS buffer select. Range: 1 to 2 1 = BUFA ATS Buffer A 2 = BUFB ATS Buffer B

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCATSAVSTTS (BOOL) Activation state of the ATS will equal 1 (Active) TSCATSNTCDIX (U12) Index of the next stored telecommand to execute in the ATS TSCATSNTCDTS (TIME40) Timestamp of the next stored telecommand to execute in the ATS TSCATSPAVSSI (UB) ID of the currently active ATS set equal to BUFFER parameter of telecommand.

Notes: SCATSSTART will fail if an ATS is currently processing. SCATSSTART will fail is another ATS telecommand was received previously in the same second.

SCATSSTOP Stop Stored Command Absolute Time Sequence. (no parameters) 3

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCATSAVSTTS (BOOL) Activation state of the ATS will equal 0 (Idle)

Notes: SCATSSTOP will fail if an ATS is not currently processing. SCATSSTOP will fail is another ATS telecommand was received previously in the same second.

SCATSSWITCH Switch Absolute Time Sequence Buffers. (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCATSAVSTTS (BOOL) Activation state of the ATS will equal 1 (Active) TSCATSNTCDIX (U12) Index of the next stored telecommand to execute in the ATS TSCATSNTCDTS (TIME40) Timestamp of the next stored telecommand to execute in the ATS TSCATSPAVSSI (UB) ID of the currently active ATS set equal to BUFFER parameter of telecommand. TSCATSSWCHPG (BOOL) ATS Switch is pending state

Notes: SCATSSWITCH will fail if an ATS is not currently processing. SCATSSWITCH will fail is another ATS telecommand was received previously in the same second.

SCATSVERIFY Verifies that an ATS table has the correct format. BUFFER (UB) ATS buffer select. Range: 1 to 2 1 = BUFA ATS Buffer A 2 = BUFB ATS Buffer B

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCATSVRFYID (UB) ID of the ATS table verified, BUFFER from the telecommand TSCATSVRFYST (BOOL) State of last ATS table verification (1=pass, 0=failed)

Notes: SCATSVERIFY will fail is another ATS telecommand was received previously in the same second.

## Relative-Time Sequences

There are 64 RTS tables, named RTS00 to RTS63, of which 16 can be active or suspended at any one time.  Each RTS contains up to 304 bytes of data.

The SCRTSSTART is used to start processing RTS table. Telecommands with a timestamp of zero following a telecommand with a non-zero timestamp will be executed in the same second. A maximum of eight telecommands per RTS can be executed in any one second; subsequent zero timestamped telecommands will be skipped.

The SCRTSSTOP is used to stop a currently processing RTS file. The SCRTSSUSPEND telecommand is used suspend an active RTS, remembering the telecommand index and time count where it left off. The SCRTSRESUME telecommand is used to reactivate a previously suspended RTS; the RTS starts executing at the index and time count where it left off.

The SCRTSVERIFY telecommand is used to verify that there are no errors in the format of an RTS file.

The SCRTSDISABLE and SCRTSENABLE telecommands are used to prevent and allow the ability to start a specific RTS table.  These telecommands provide a mechanism for loading an RTS table, but making sure that it can’t be executed. On boot-up, RTS00 through RTS31 are enabled and RTS32 through RTS63 are disabled. Sending the SCRTSDISABLE telecommand for an RTS that is currently executing does not stop the RTS, but prevents it from being started again after it stops.

These telecommands have been designed to have the same general format and behavior has those used on other SMEX spacecraft.

There are a number of telemetry points that don’t get set as a result of a telecommand, but get set as the active RTS’s are processed. The following discusses these telecommand points:

a.	TSCRTSRECVD (U12) Total of all RTS stored telecommands processed.

b.	TSCRTSREJECT (U12) Total of all RTS stored telecommands that failed verification.

c.	TSCRTSERRORS (U12) Total of all RTS stored telecommands that failed to route.

d.	TSCRTSLICDRI (UB) ID of the RTS containing the last invalid RTS stored TC.

e.	TSCRTSLICDIX (UB) Index of the last invalid RTS stored telecommand.

f.	TSCRTSLICDST (UB) Status of the last invalid RTS stored telecommand.

g.	TSCRTSLICDTS (U1234) Timestamp of the last invalid RTS stored telecommand.

SCRTSSTART Start Stored Command Relative Time Sequence. RTSNUM (U12) RTS number to start. Range: 0 to 63 0 = RTS00 RTS00 1 = RTS01 RTS01 . . . 63 = RTS63 RTS63

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCRTSNRACTV (UB) Number of active-suspended RTSs TSCRTSNRACTH (UB) High-Water mark for number of active-suspended RTSs TSCRTSID?? (UB) ID of the Active or Suspended RTS set to RTSNUM, where ?? is 00 to 15. TSCRTSSTTS?? (BOOL) State of the RTS set to 1 (1=Active, 0=Suspended), where ?? is 00 to 15. TSCRTSNXTI?? (UB) Index of the next stored telecommand to execute in the RTS set to 0, where ?? is 00 to 15. TSCRTSELAP?? (U1234) Elapsed time in seconds since the RTS was started set to 0, where ?? is 00 to 15.

Notes: There are 16 ‘slots’ that track the status of the 0 to 15 active or suspended RTS’s at any one time. When the SCRTSSTART telecommand is received, the first idle slot is used to track the status of the RTS. If all 16 slots are being used, then telecommand returns in error.

SCRTSSUSPEND Suspends a stored command relative time sequence. RTSNUM (UB) The active RTS number to suspend Range: 0 to 63 0 = RTS00 RTS00 1 = RTS01 RTS01 . . . 63 = RTS63 RTS63

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCRTSSTTS?? (BOOL) State of the RTS set to 0 (1=Active, 0=Suspended), where ?? is 00 to 15

SCRTSRESUME Resumes a previously suspended RTS. RTSNUM (UB) The suspended RTS to resume. Range: 0 to 63 0 = RTS00 RTS00 1 = RTS01 RTS01 . . . 63 = RTS63 RTS63

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCRTSSTTS?? (BOOL) State of the RTS set to 1 (1=Active, 0=Suspended), where ?? is 00 to 15

SCRTSSTOP Stop Stored Command Relative Time Sequence. RTSNUM (U12) RTS number to stop. Range: 0 to 63 0 = RTS00 RTS00 1 = RTS01 RTS01 . . . 63 = RTS63 RTS63

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCRTSNRACTV (UB) Number of active-suspended RTSs TSCRTSNRACTH (UB) High-Water mark for number of active-suspended RTSs TSCRTSID?? (UB) ID of the Active or Suspended RTS set to 0xFF, where ?? is 00 to 15. TSCRTSSTTS?? (BOOL) State of the RTS set to 0 (1=Active, 0=Suspended), where ?? is 00 to 15. TSCRTSNXTI?? (UB) Index of the next stored telecommand to execute in the RTS set to 0, where ?? is 00 to 15. TSCRTSELAP?? (U1234) Elapsed time in seconds since the RTS was started set to 0, where ?? is 00 to 15.

Notes: There are 16 ‘slots’ that track the status of the 0 to 15 active or suspended RTS’s at any one time. When the SCRTSSTOP telecommand is received, the slot used to track the status of that RTS made available for the SCRTSSTART telecommand. If no slot is being used by that RTS, then telecommand returns in error.

SCRTSDISABLE Disable Stored Command Relative Time Sequence. RTSNUM (U12) RTS number to disable. Range: 0 to 63 0 = RTS00 RTS00 1 = RTS01 RTS01 . . . 63 = RTS63 RTS63

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCRTS??ENAB (BOOL) Enabled-Disabled State of RTS set to 0 (disabled), where ?? is 00 to 63 from RTSNUM

Notes: On boot-up, RTS00 through RTS31 are enabled, RTS32 through RTS63 are disabled.

SCRTSENABLE Enable Stored Command Relative Time Sequence. RTSNUM (U12) RTS number to enable. Range: 0 to 63 0 = RTS00 RTS00 1 = RTS01 RTS01 . . . 63 = RTS63 RTS63

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCRTS??ENAB (BOOL) Enabled-Disabled State of RTS set to 1 (enabled), where ?? is 00 to 63 from RTSNUM

Notes: On boot-up, RTS00 through RTS31 are enabled, RTS32 through RTS63 are disabled.

SCRTSVERIFY Verifies that an RTS table has the correct format. RTSNUM (UB) RTS number of verify. Range: 0 to 63 0 = RTS00 RTS00 1 = RTS01 RTS01 . . . 63 = RTS63 RTS63

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSCTCRECVD (UB) # of Command Processor TCs received will increment by one TSCTCREJECT (UB) # of Command Processor TCs that failed verification TSCTCERRORS (UB) # of Command Processor TCs that failed to execute TSCRTSVRFYID (UB) ID of the RTS table verified, RTSNUM from telecommand TSCRTSVRFYST (BOOL) State of RTS table verification (1=pass, 0=failed)

## Stored Sequences and the Filesystem

A SMTBLCOMMIT telecommand will return in error if the file being committed is the currently executing ATS or one of the executing RTS files.

The filesystem enforces the maximum length of a stored sequence.

## Specific Relative-Time Sequences

There are several RTS files that have a specific purpose.  By convention, RTS00 through RTS19 are reserved for special purpose relative-time sequences, and RTS20 to RTS31 are available to be started from the first 20 RTS’s. Table 6-1 lists each of the special purpose relative-time sequences.

Table 6-1.  Special Purpose Relative-Time Sequences

| RTS File | Purpose |
| --- | --- |
| RTS00 | Initial RTS started after boot when the Mission Mode is ‘Launch’. |
| RTS01 | Initial RTS started after boot when the Mission Mode is ‘Nominal’. |
| RTS10 | Fault Management RTS started when an ACS Pointing Error is detected. |
| RTS11 | Fault Management RTS started when no telecommands have been received by the CIB after a specific period of time. |
| RTS12 | Fault Management RTS started when a Battery 1 Pressure Low Error is detected. |
| RTS13 | Fault Management RTS started when a Battery 2 Pressure Low Error is detected. |
| RTS14 | Fault Management RTS started when an NEB1 Over current Condition is detected. |
| RTS15 | Fault Management RTS started when an NEB2 Over current Condition is detected. |
| RTS16 | Fault Management RTS started when an IDPU Heater Over current Condition is detected. |
| RTS17 | Fault Management RTS started when an IDPU Over current Condition is detected. |
| RTS18 | Fault Management RTS started when a CRYO Over current Condition is detected. |
| RTS19 | Fault Management RTS started when an IDPU Switched Over current Condition is detected. |

# PAYLOAD INTERFACE SUBSYSTEM

FSW communicates with the IDPU via the PACI board, which transmits data bi-directionally over a serial link. Every second, the Payload Interface Subsystem sends a command record to the IDPU, and receives a telemetry record from the IDPU. FSW will only communicate with the IDPU when the IDPU power is on as reported by telemetry point TPCBS1_IDPU.

## Payload Commanding

The Payload Interface Subsystem will be scheduled to receive wakeup messages that coincides with the 1 Hz Bus Tick.  When this message is received, a 1040 byte command record is constructed that consists of a 16 byte “Spacecraft Status Segment” and a 1024 byte “Command Segment”, as specified by HIS_SYS_001 HESSI Spacecraft to IDPU Interface Control Document.  The command record is sent to the IDPU via the PACI, with the start of transmission within 100 milliseconds of the 1 Hz Bus Tick.

The 1024 byte Command Segment consists of a concatenation of telecommands with APIDs between 0x100 and 0x1FF, with the unused portion zero filled.  Any IDPU telecommand received within a one-second period that can not fit into the remaining bytes available in the Command Segment buffer will be discarded. The TPLCMDRECVD telemetry point records the total number of telecommands received for the IDPU device.  The TPLCMDREJECT telemetry point records the total number of IDPU device telecommands rejected because the size of the Command Segment was exceeded.  The TPLCMDSENT telemetry point records the total number of IDPU device telecommands last communicated in the Command Segment.

Table 7-1 documents how each field of the Spacecraft Status Segment is populated.  The Spacecraft Status Segment is also downlinked in SOH telemetry, and the names of these telemetry points are in parenthesis beneath the field name.

Table 7-1.  Spacecraft Status Segment Sources

| Field | Sub-Field | Data Length | Source of data |
| --- | --- | --- | --- |
| Time Field (TPLCMDTIME) | N/A | 4 bytes | Current seconds from SCLK in a little-endian data format. |
| SSR Field (TPLCMDSSR) | N/A | 1 byte | TPLCMDSSR telemetry point set by the SSR Interface Subsystem.0 means empty, 255 means full. |
| Power Field (TPLCMDPOWER) | Heater Bit | 1 bit | TPCBS1_IDPUH telemetry point set by PCB Interface Subsystem |
|  | IDPU | 1 bit | TPCBS1_IDPU telemetry point set by PCB Interface Subsystem |
|  | Cryo | 1 bit | TPCBS1_CRYO telemetry point set by PCB Interface Subsystem |
|  | Switched | 1 bit | TPCBS1_IDPU28 telemetry point set by PCB Interface Subsystem |
|  | SSR Power | 1 bit | TPCBS1_SSR telemetry point set by SSR Interface Subsystem |
|  | SSR Recording | 1 bit | TSSWRTPTRVLD telemetry point set by the SSR Interface Subsystem |
| TC Status Field (TPLCMDTC) | Xmit | 1 bit | TPADINBIT20 telemetry point set by PACI Digital Input |
|  | SendSSR | 1 bit | TSSRCRDINPRG telemetry point set by the SSR Interface Subsystem |
|  | Lock | 1 bit | Bit 8 (0x0100) of the TCBHCDSTAT telemetry point set by the Uplink Subsystem |
|  | Send | 1 bit | Set if any FSW stored telemetry is enabled for downlink, or if the SSR is currently in playback mode |
| ACS Field (TPLCMDACS) | InSun | 1 bit | TPADINBIT17 telemetry point set by PACI Digital Input |

## Payload Telemetry

After the IDPU receives the 1 Hz Bus Tick, it sends a 1468 telemetry record to the PACI board, which stores the data in a memory buffer.  After all data has been received by the PACI board, a VME interrupt is generated and received by the CPU.  Upon receiving the interrupt, FSW reads the IDPU telemetry record from the PACI board. The TPLTLMRCTIME telemetry point records the S/C time when the IDPU telemetry record was received.

The IDPU telemetry record consists of three parts: a SAS segment for use by the ACS Subsystem, a SOH segment, and a diagnostic telemetry packet segment. Both the SAS segment and the SOH segment are incorporated into the FSW real-time SOH telemetry packet transmitted on VC0, APID 1. The diagnostic telemetry packet segment contains a fully populated CCSDS Source Packet sized to exactly fill one transfer frame. When the Consultative Committee for Space Data System (CCSDS) Source Packet contains a fill packet (APID 2047), it is discarded.  If the CCSDS Source Packet contains other than a fill packet, it is sent to the Downlink Subsystem for downlink or storage.

The IDPU SAS segment is available in real-time SOH at telemetry points TPLSASSEGX1 to TPLSASSEGX8, and TPLSASSEGY1 to TPLSASSEGY8. The IDPU SOH segment is available in real-time SOH at telemetry point TPLSOHSEGMNT.

## Science Telemetry

The IDPU stores science data directly to the SSR device as a complete CCSDS Source Packet sized exactly to fill one transfer frame.  For synchronization purposes, each packet is preceded by a synchronization marker.  To downlink the data, the SSR device transmits the IDPU science data directly to the CIB device.  Commanding of the SSR device to record or playback IDPU data is controlled via the SSR Interface Subsystem.

## Payload Telecommands

The PLRESET telecommand sends a reset signal to the IDPU device that is pulsed high for 100 milliseconds.

The PLNOOP telecommand acknowledges that the Payload Interface Subsystem is receiving telecommands.

The PLTCRESET telecommand resets the Payload Interface Subsystem telecommand received, rejected and error counters.

PLNOOP Verifies that the Payload Interface Subsystem is responding (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPLTCRECVD (UB) # of Payload Subsystem TCs received will increment by one

PLTCRESET Resets Payload Interface Subsystems TC received/rejected/error counters (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPLTCRECVD (UB) # of Payload Subsystem TCs received will increment by one TPLTCREJECT (UB) # of Payload Subsystem TCs that failed verification set to zero TPLTCERRORS (UB) # of Payload Subsystem TCs that failed to execute set to zero

PLRESET Resets the IDPU Device to known state (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPLTCRECVD (UB) # of Payload Subsystem TCs received will increment by one

Notes: Sends a reset signal to the IDPU device that is pulsed high for 100 milliseconds.

# SSR INTERFACE SUBSYSTEM

The SSR Interface Subsystem is responsible for commanding and receiving responses from the Solid State Recorder (SSR) device. The SSR device is solid state ‘tape recorder’ that supports sequential recording of data, and sequential playback of data.  The SSR device has a capacity of 4 Gigabytes of EDAC RAM storage. The SSR supports partitioning into the multiple logical drives, is partitioned into just one loopback drive. Although the SSR record and playback functionality is like that of a tape recorder, it differs in that all data is lost when the SSR is powered off.

FSW communicates with the SSR via the PACI board using a serial interface.  To communicate with the SSR, FSW sends a data record in accordance with a specific command format, and receives a response data record in a specific format. The User’s Manual for the HESSI SSR documents all commands, and associated responses, that can be sent to the SSR device. FSW only communicates with the SSR when it is powered, as indicated by the TPCBS1_SSR telemetry point, and the SSR Command Ready signal is low, as indicated by telemetry point TPADINBIT16. Under these conditions, the SSR SOH telemetry (termed “Normal Telemetry” in the SSR Users Manual) is queried at a 1 Hz rate when the TSSR1HZPRCEN telemetry point is TRUE, which is nominally TRUE but can be set with the SSRWORK1HZ telecommand.

## SSR Subsystem Initialization

When the SSR is powered and the SSR Command Ready signal is low, the SSR Interface Subsystem stores current stored science playback and record pointer information to the PACI PNVRAM.  This is done to ease recovery if FSW unexpectedly reboots while the SSR is record and/or playback mode.  When the SSR Subsystem is initialized, it sets the stored science playback and record pointer telemetry points to those values recorded in Table 8-1, SSR Subsystem Initial Values.  After initialization, the SSR Subsystem reads the last stored values from PNVRAM for these telemetry points. Subsequent to initialization, these telemetry points are set based on data received from the SSR device.

Table 8-1.  SSR Subsystem Initial Values

| Telemetry Point | Initial Value |
| --- | --- |
| TSSLSTWRTPTR (U1234) Last stored science record position Status | 0 |
| TSSLSTRDPTR (U1234) Last stored science playback position | 0 |
| TSSCURRDPTR (U1234) Row Offset of read pointer from when Real-Time Science Playback is in progress. | 0 |
| TSSRTMSCIPRG (BOOL) Real-time IDPU science data playback in progress | FALSE |
| TSSSTDSCIPRG (BOOL) Stored IDPU science data playback in progress | FALSE |
| TSSRCRDINPRG (BOOL) Indicates that a SSR Record is in progress | FALSE |

## SSR Subsystem 1 Hz Processing

At 1 Hz rate, the SSR Interface Subsystem retrieves the current state of the SSR device, and executes various pending telecommands. To retrieve the state of the SSR device, the SSR device commands “Send Normal Telemetry” and “Pointer Status” device commands are sent (see SSR Users Manual for details). The telemetry points in Table 8-1 are updated and stored in PACI PNVRAM. After retrieving the current state, pending telecommands are processed. The SSRPLAY, SSRPLAYRTSCI, SSRRECORD, SSRMAKEPART, and SSRPORTRESET telecommands are not executed immediately after they are received, but are scheduled for execution during 1 Hz processing.

## Record and Playback Telecommands

There are two methods of SSR data playback. The first, via the SSRPLAY telecommand, is the nominal playback of previously stored science data that has yet to be downlinked on Virtual Channel 3. The second method, using the SSRPLAYRTSCI telecommand, is what is termed ‘real-time’ science telemetry. This method downlinks a commanded number of the most recently recorded packets of stored science data on Virtual Channel 2. An SSRPLAYRTSCI telecommand can be received while a nominal playback of stored science data is in progress. In this scenario, the first playback will be suspended, the real-time science will be played, and then the original playback will be resumed from where it left off.

The SSRSTOPPLAY telecommand is used to stop a science data playback. Because the IDPU science data packets don’t fit into an increment of bytes which makes up an addressable block used by the SSR, a single duplicate science data packet may be downlinked when a playback is stopped and then resumed. The ground will be able to detect this by interrogating data contained within the science data packet. If an SSRSTOPPLAY telecommand is received while a real-time science playback is in operation, then that playback is stopped and a previously suspended nominal playback will be resumed.

The SSRRECORD telecommand is used to start recording data. This is generally done once after a reboot allowing the IDPU to store science data as needed. The SSRSTOPREC telecommand is used to stop the recording of data.

SSRPLAY Starts the playback of SSR stored science data BYPASSEDAC (UB) Indicates whether EDAC should be bypassed Range: 0 to 1 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSSTDSCIPRG (BOOL) Stored IDPU science data playback in progress set to one. TSSCRSPCMDID (UB) SSR command response telemetry command Id set to 0x26 (Random Playback) TSSCRSPRTNCD (UB) SSR command response telemetry return code set to 0 (OK) TSSCURRDPTR (U1234) Row Offset of read pointer from SSR Pointer Status will start incrementing TSSLSTRDPTR (U1234) Last stored science playback position will start incrementing TSSRDPTRVLD (BOOL) Indicates whether TSSLSTRDPTR is valid set to 1 (Valid) TSSREDACBYPS (BOOL) Indicates EDAC bypass during playback was commanded set to BYPASSEDDAC. TPLCMDSSR (UB) Indicates how full much data the SSR contains that has not been downlinked: 0 means empty, 255 means full.

Notes: SSRPLAY will fail under the following conditions: the SSR is not powered, or the SSR Command Ready signal is high 1 Hz Normal Telemetry processing has been disabled a stored science playback is currently in progress a SSRPLAY, SSRPLAYRTSCI, SSRMAKEPART or SSRPORTRESET telecommand was previously received within the last second

SSRPLAYRTSCI Playback of real-time science data NUMPACKETS (U12) Number of real-time tlm packets to playback Range: 1 to 65535 BYPASSEDAC (UB) Indicates whether EDAC should be bypassed Range: 0 to 1 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSRTMSCIPRG (BOOL) Real-time IDPU science data playback in progress set to one. TSSCRSPCMDID (UB) SSR command response telemetry command Id set to 0x26 (Random Playback) TSSCRSPRTNCD (UB) SSR command response telemetry return code set to 0 (OK) TSSCURRDPTR (U1234) Row Offset of read pointer from SSR Pointer Status will start incrementing TSSLSTRDPTR (U1234) Last stored science playback position will not increment TSSREDACBYPS (BOOL) Indicates EDAC bypass during playback was commanded set to BYPASSEDDAC.

Notes: SSRPLAYRTSCI will fail under the following conditions: the SSR is not powered, or the SSR Command Ready signal is high 1 Hz Normal Telemetry processing has been disabled a stored science playback is currently in progress a SSRPLAY, SSRPLAYRTSCI, SSRMAKEPART or SSRPORTRESET telecommand was previously received within the last second

SSRSTOPPLAY Stops the playback of IDPU science data (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSRTMSCIPRG (BOOL) Real-time IDPU science data playback in progress set to zero. TSSSTDSCIPRG (BOOL) Stored IDPU science data playback in progress set to zero if real-time playback was not in progress. TSSCRSPCMDID (UB) SSR command response telemetry command Id set to 0x37 (Stop Playback) if real-time playback was not in progress. TSSCRSPRTNCD (UB) SSR command response telemetry return code set to 0 (OK) TSSCURRDPTR (U1234) Row Offset of read pointer from SSR Pointer Status will start incrementing if real-time playback was not in progress. TSSLSTRDPTR (U1234) Last stored science playback position will not increment if real-time playback was not in progress.

Notes: SSRSTOPPLAY will fail under the following conditions: the SSR is not powered, or the SSR Command Ready signal is high

SSRRECORD Starts the recording of IDPU science data STARTOFFSET (U1234) The start offset at which to begin recording Range: to 0 to 0xffffffff

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSCRSPCMDID (UB) SSR command response telemetry command Id set to 0x27 (Random Record) TSSCRSPRTNCD (UB) SSR command response telemetry return code set to 0 (OK) TSSRCRDINPRG (BOOL) Indicates that a SSR Record is in progress set to 1 TSSWRTPTRVLD (BOOL) Indicates whether TSSLSTWRTPTR is valid set to 1 (Valid) TSSCURWRTPTR (U1234) Row Offset of write pointer from SSR Pointer Status increments when IDPU stores data TSSLSTWRTPTR (U1234) Last stored science record position Status will increment when IDPU stores data TPLCMDSSR (UB) Indicates how full much data the SSR contains that has not been downlinked: 0 means empty, 255 means full.

Notes: SSRRECORD will fail under the following conditions: the SSR is not powered, or the SSR Command Ready signal is high 1 Hz Normal Telemetry processing has been disabled a previous SSRSTOPREC telecommand is in the process of being executed a SSRRECORD, SSRMAKEPART or SSRPORTRESET telecommand was previously received within the last second the STARTOFFSET parameters is out-of-range for the capacity of the SSR device.

SSRSTOPREC Stops the recording of IDPU science data (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSCRSPCMDID (UB) SSR command response telemetry command Id set to 0x36 (Stop Record) TSSCRSPRTNCD (UB) SSR command response telemetry return code set to 0 (OK) TSSRCRDINPRG (BOOL) Indicates that a SSR Record is in progress set to 0 TSSWRTPTRVLD (BOOL) Indicates whether TSSLSTWRTPTR is valid set to 0 (Invalid) TSSCURWRTPTR (U1234) Row Offset of write pointer from SSR Pointer Status set to 0 TSSLSTWRTPTR (U1234) Last stored science record position Status set to last position written.

Notes: SSRSTOPREC will fail under the following conditions: the SSR is not powered, or the SSR Command Ready signal is high

## SSR Passthrough Telecommand

The SSR Interface Subsystem does not implement a separate telecommand for every command that the SSR device supports. Instead, the SSRPASSTHRU telecommand allows the ground to send any desired command directly to the SSR device, giving the ground full control of the SSR device. The SSR Command Response is downlinked in its entirety in VC 1, with an APID of 0x200 plus the decimal value of the command code. For example, the SSR Command Response telemetry for a Random Playback command would be downlinked on APID 0x226.

There are two classes of SSR device commands, “Privileged Commands”, and “User Commands”. The Privileged Commands must be sent twice, back to back, to the SSR device before they are acted upon. The SSR Subsystem automatically does this for the ground. The main reason that the SSR Subsystem automates this is because the 1 Hz processing, which sends status commands to the SSR device, can often occur during the gap in time between two received SSRPASSTHRU telecommands, thus invalidating the ground command. User Commands only need to be received by the SSR device once before they are acted upon.

During certain types of operations, it may be desirable to disable the SSR Subsystem 1 Hz processing.  This will ensure that no commands, other than those that the ground sends, will ever be received by the SSR device.  The SSRWORK1HZ telecommand allows the ground to enable or disable the SSR Subsystem 1 Hz processing.

SSRPASSTHRU Transmits the specified 16-byte command to the SSR. COMMANDCODE (UB) SSR Device Command Code Range: 0 to 0xFF COMMANDID (UB) SSR Device Command ID Range: 0 to 0xFF WORD1 (U12) Word 1 of SSR Device Command Parameters Range: 0 to 0xFFFF WORD2 (U12) Word 2 of SSR Device Command Parameters Range: 0 to 0xFFFF WORD3 (U12) Word 3 of SSR Device Command Parameters Range: 0 to 0xFFFF WORD4 (U12) Word 4 of SSR Device Command Parameters Range: 0 to 0xFFFF WORD5 (U12) Word 5 of SSR Device Command Parameters Range: 0 to 0xFFFF WORD6 (U12) Word 6 of SSR Device Command Parameters Range: 0 to 0xFFFF

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSCRSPCMDID (UB) SSR command response telemetry command ID set to COMMANDCODE from telecommand TSSCRSPRTNCD (UB) SSR command response telemetry return code set to response

Notes: SSR Command Response is downlinked in its entirety in VC 1, with an APID of 0x200 plus the decimal value of the command code. SSRPASSTHRU will fail under the following conditions: the SSR is not powered, or the SSR Command Ready signal is high

SSRWORK1HZ Enable/Disable SSR 1Hz Processing ENABLE (UB) 1=Enable, 0=Disable Range: 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSR1HZPRCEN (BOOL) SSR 1Hz processing is enabled set to ENABLE parameter from telecommand

## SSR SOH Telemetry

When the SSR device is powered on, SSR Command Ready signal is low, and the TSSR1HZPRCEN telemetry point is TRUE, the SSR Subsystem will read, and downlink, the SSR SOH (called Normal Telemetry in SSR documentation) telemetry at 1 Hz. The SSR SOH telemetry is downlink in the real-time telemetry frame on VC0, APID 1. The SSR SOH telemetry contains a wealth of status, error and diagnostic information about the current state of the SSR. Because FSW will not autonomously act on any error information, the ground must monitor this data to detect when errors are occurring.  Table 8-2 lists a few specific fields in the ground must monitor.

- 8-2.  SSR Telemetry to Monitor

| Field Name NOTE: Need to define telemetry points for SSR Normal Telemetry | Description |
| --- | --- |
| DRAM Mapping Status | 0=Nothing needs to be remapped 1,2,3=Reconfigure Memory required |
| Various Test Results | Words 11, 13, 14, and 16 contains various test results |
| EDAC Errors | Words 10, 20, 21, 22, and 25 contains various EDAC error report information. |
| Scrubbing Errors | Words 26 |
| Board failures and exceptions | Words 4, 6, 17 |

## SSR Maintenance Telecommands

When the SSR device is powered on, it needs to be initialized before any record or playback command will be accepted. The SSR device initialization is not done autonomously by FSW.

The SSRMAKEPART telecommand will reset the SSR device (Reset Memory command), removing any previous formatting, and then create one “loop-back” partition (Create Partition command) using all available memory. A loop-back partition allows record and playback operations to automatically wrap from the end of memory to the beginning of memory during processing.

The SSRPORTRESET telecommand will reset the SSR record and playback ports. Although this command should never need to be sent, it is useful if the ground suspects transmission errors because of the data ports. Upon receiving the SSRPORTRESET telecommand, the SSR Subsystem will stop any record or playback that is in progress, send the “Reset Data Ports” command to the SSR device, and the restart an record or playback that was previously in progress.

The SSRDLERRHIS telecommand should be periodically sent by the ground to downlink an extensive error history of the SSR device. This command returns the locations of the last 16 unfixable errors, the last 16 hard single-symbol errors, and the last 16 corrected single-symbol errors that have been found by the scrub task. The SSR device error history structure is cleared when the command completes.

SSRMAKEPART Creates a new partition in the SSR DRAM. (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSCRSPCMDID (UB) SSR command response telemetry command ID set to 0x00 (Create Partition) TSSCRSPRTNCD (UB) SSR command response telemetry return code set to 0x0 (OK)

Notes: SSRMAKEPART will fail under the following conditions: the SSR is not powered, or the SSR Command Ready signal is high a stored science or real-time science playback, record or stop record is in progress a SSRRECORD, SSRMAKEPART or SSRPORTRESET, SSRPLAY, SSRPLAYRTSCI telecommand was previously received within the last second

SSRPORTRESET Resets SSR Data Ports; restarts previous record/playback (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSCRSPCMDID (UB) SSR command response telemetry command ID set to 0x14 (Reset Data Ports) TSSCRSPRTNCD (UB) SSR command response telemetry return code set 0x0 (OK)

Notes: SSRPORTRESET will fail under the following conditions: the SSR is not powered, or the SSR Command Ready signal is high 1 Hz Normal Telemetry processing has been disabled a SSRRECORD, SSRMAKEPART or SSRPORTRESET, SSRPLAY, SSRPLAYRTSCI telecommand was previously received within the last second

SSRDLERRHIS Requests SSR Error History (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSCRSPCMDID (UB) SSR command response telemetry command ID set to 0x2F (Error History) TSSCRSPRTNCD (UB) SSR command response telemetry return code set to 0x0 (OK)

Notes: SSRDLERRHIS will fail under the following conditions: the SSR is not powered, or the SSR Command Ready signal is high

## SSR Housekeeping Telecommands

If the ground would like to replay some previously played stored science data, the SSRSETPLYPTR telecommand will set the playback pointer, telemetry point TSSLSTRDPTR, to any desired value. This will affect the calculation for the amount of data stored in the SSR which has not yet been downlinked, which is telemetry point TPLCMDSSR.

Normally, the SSR command response telemetry is only downlinked in a telemetry source packet as a result of an SSRPASSTHRU or SSRDLERRHIS telecommand.  The SSRCMDRSPTLM telecommand allows the ground to enable or disable SSR command response telemetry for all telecommands, which can be useful for diagnostic purposes.

The SSRSTATEINIT telecommand is like an SSR Subsystem reset command; it resets the state of the SSR Subsystem to that when the FSW was first booted.

The SSRNOOP telecommand acknowledges that the SSR Interface Subsystem is receiving telecommands.

The SSRTCRESET telecommand resets the SSR Interface Subsystem telecommand received, rejected and error counters.

SSRSETPLYPTR Set the SSR Playback Pointer PLAYPOINTER (U1234) The new value of the SSR play pointer Range: 0 to 0xFFFFFFFF

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSLSTRDPTR (U1234) Last stored science playback position set to PLAYPOINTER TPLCMDSSR (UB) Indicates how full much data the SSR contains that has not been downlinked: 0 means empty, 255 means full.

Notes: SSRSETPLYPTR will fail under the following conditions: the SSR is not powered, or the SSR Command Ready signal is high a stored or real-time science playback is currently in progress a SSRPLAY, SSRPLAYRTSCI, SSRPORTRESET telecommand was previously received within the last second the PLAYPOINTER parameters is out-of-range for the SSR device memory capacity.

SSRCMDRSPTLM Enables SSR command response telemetry for non-SSRPASSTHRU TCs ENABLE UB 1=Enables SSR command response telemetry; 0=Disable Range: 0 to 1 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute TSSRCMDRSPEN (BOOL) SSR Command Response telemetry enabled set to 1.

Notes: SSR Command Response is downlinked in its entirety in VC 1, with an APID of 0x200 plus the decimal value of the command code.

SSRSTATEINIT Reinitialize the state of the SSR task. (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one TSSTCREJECT (UB) # of SSR Subsystem TCs that failed verification TSSTCERRORS (UB) # of SSR Subsystem TCs that failed to execute

Notes: Resets the state of the SSR Subsystem to that when the FSW was first booted.

SSRNOOP Verifies that the SSR Subsystem is responding (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSSTCRECVD (UB) # of SSR Subsystem TCs received will increment by one

SSRTCRESET Resets SSR Subsystems TC received/rejected/error counters (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPLTCRECVD (UB) # of Payload Subsystem TCs received will increment by one TPLTCREJECT (UB) # of Payload Subsystem TCs that failed verification set to zero TPLTCERRORS (UB) # of Payload Subsystem TCs that failed to execute set to zero

# ATTITUDE CONTROL SUBSYSTEM

The Attitude Control Subsystem (ACS) has two telecommands, and many Flight Parameters, used to control operations of the ACS algorithms. See Section 16 on page 0 for a discussion of how to set the Flight Parameters. The ACS Subsystem is scheduled at 8 Hz via the receipt of a “Analog Scan Down” interrupt received from the PACI device.

## ACS Control Telecommands

The ACSSETMODE telecommand is used to for the ACS Subsystem to transition into, and stay in, a specific operating mode. Under nominal operations, the ACS operating mode is “AUTO”, which allows the ACS Subsystem to autonomously transition between modes as required by the algorithms.

The ACSSUNSENSOR telecommand directs the ACS Subsystem to use a specific sensor, either the Fine Sun Sensor (FSS) or the SAS Instrument, for pointing. Nominally, the sensor used is the FSS.

ACSSETMODE Sets the desired ACS operating mode MODE (UB) The desired ACS mode. Range: 0 to 5 0 = AUTO Allows ACS to change modes autonomously (default) 1 = ACQUISITION Establishes spin rate, damps transverse rates 2 = PRECESSION Establishes Sun-pointing orientation 3 = NORMAL Maintains Sun-pointing, nominal spin rate 4 = SPIN Establishes desired spin rate 5 = IDLE Disables control until ground intervention

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TACTCRECVD (UB) # of ACS Subsystem TCs received will increment by one TACTCREJECT (UB) # of ACS Subsystem TCs that failed verification TACTCERRORS (UB) # of ACS Subsystem TCs that failed to execute TACSCMDMODE (BOOL) Set to 0 (Autonomous Mode) if MODE parameter is AUTO, otherwise set to 1 (Commanded Mode) TACSMODE (UB) ACS current mode

ACSSUNSENSOR Selects the desired ACS Sun Sensor mode SUNSENSOR (UB) Sun Sensor Mode Range: 0 to 1 0 = FSS Fine Sun Sensor 1 = SAS SAS Instrument Telemetry Data

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TACTCRECVD (UB) # of ACS Subsystem TCs received will increment by one TACTCREJECT (UB) # of ACS Subsystem TCs that failed verification TACTCERRORS (UB) # of ACS Subsystem TCs that failed to execute TACINSUNSENS (BOOL) Sun Sensor used by ACS set to SUNSENSOR parameter.

## ACS Flight Parameters

The 1110-EW-S16620 HESSI Attitude Control Subsystem Flight Software Specification document describes the usage of each ACS Flight Parameter. Table 9-1 describes the mapping between the ACS document’s parameters name and the FSW Flight Parameter name.

Table 9-1.  ACS Flight Parameters

| ACS Document Parameter | FSW Flight Parameter | Parameter Description |
| --- | --- | --- |
| N/A | VTRQZSELECT | Selects the primary Z-axis torque rod; 1 selects redundant |
| MAG_BIAS_X | VMAGBIASX | Magnetometer bias for the X-axis |
| MAG_BIAS_Y | VMAGBIASY | Magnetometer bias for the Y-axis |
| SAS_DELAY | VSASDELAY | SAS Delay in seconds between collection time and receipt time |
| CCS_THRESH | VCSSTHRESH | ACS CCS threshold (amps). |
| FSS_BIASX | VFSS_BIASX | ACS FSS bias along x-axis |
| FSS_BIASY | VFSS_BIASY | ACS FSS bias along y-axis |
| TQR_COMP11 | VTQRCOMP11 | ACS Torque rod compensation matrix component |
| TQR_COMP12 | VTQRCOMP12 | ACS Torque rod compensation matrix component |
| TQR_COMP13 | VTQRCOMP13 | ACS Torque rod compensation matrix component |
| TQR_COMP21 | VTQRCOMP21 | ACS Torque rod compensation matrix component |
| TQR_COMP22 | VTQRCOMP22 | ACS Torque rod compensation matrix component |
| TQR_COMP23 | VTQRCOMP23 | ACS Torque rod compensation matrix component |
| TQR_COMP31 | VTQRCOMP31 | ACS Torque rod compensation matrix component |
| TQR_COMP32 | VTQRCOMP32 | ACS Torque rod compensation matrix component |
| TQR_COMP33 | VTQRCOMP33 | ACS Torque rod compensation matrix component |
| TQR_SAT_HIGH | VTQRSATHIGH | ACS Torque rod high saturation level (amp-m^2) |
| TQR_SAT_POINT_LOW | VTQRSATPNTLO | ACS Torque rod low saturation level in pointing (amp-m^2) |
| TQR_SAT_SPIN_LOW | VTQRSATSPNLO | ACS Torque rod low saturation level in spin (amp-m^2) |
| ACQ_SPIN_COM | VACQSPINCOM | ACS Commanded spin rate during acquisition (rad/sec) |
| NORM_SPIN_COM | VNORMSPINCOM | ACS Commanded spin rate during normal operations (rad/sec) |
| ACQ_GAIN | VACQGAIN | ACS Acquisition control gain (amp-m^2-sec/tesla) |
| COARSE_PREC_GAIN | VCRSPRECGAIN | ACS Coarse precession control gain (amp-m^2) |
| FINE_PREC_GAIN | VFINEPRCGAIN | ACS Fine precession control gain (N-m-sec) |
| FINE_NUT_GAIN | VFINENUTGAIN | ACS Fine nutation control gain (N-m-sec) |
| SPIN_GAIN | VSPINGAIN | ACS Spin control gain (amp-m^2-sec-tesla) |
| POINT_HIGH | VPOINTHIGH | ACS High setting for pointing hysteresis logic (rad) |
| POINT_LOW | VPOINTLOW | ACS Low setting for pointing hysteresis logic (rad) |
| POINT_CHECK | VPOINTCHECK | ACS Initial status of pointing hysteresis logic |
| DELTA_SPIN_HIGH | VDELTASPINHI | ACS High setting for pointing hysteresis logic (rad/sec) |

Table 9-1.  ACS Flight Parameters (Continued)

| DELTA_SPIN_LOW | VDELTASPINLO | ACS Low setting for pointing hysteresis logic (rad/sec) |
| --- | --- | --- |
| SPIN_CHECK | VSPINCHECK | ACS Initial state of spin hysteresis log |
| POINT_ACQ2NORM | VPTACQ2NORM | ACS Transition pointing error from Acquisition to Idle (rad) |
| POINT_PREC2NORM | VPTPREC2NORM | ACS Transition pointing error from Precession to Normal (rad) |
| POINT_NORM2IDLE | VPTNORM2IDLE | ACS Transition pointing error from Normal to Idle (rad) |
| POINT_SPIN2NORM | VPTSPIN2NORM | ACS Transition pointing error from Spin to Normal (rad) |
| RATE_ACQ2NORM | VRTACQ2NORM | ACS Transition rate from Precession to Normal (rad/sec) |
| DRATE_PREC2NORM | VDRTPREC2NRM | ACS Transition rate error from Precession to Normal (rad/sec) |
| DRATE_NORM2IDLE | VDRTNRM2IDLE | ACS Transition rate error from Normal to Idle (rad/sec) |
| DRATE_SPIN2NORM | VDRTSPIN2NRM | ACS Transition rate error from Spin to Normal |
| TIME_ACQ2NORM | VTIMACQ2NORM | ACS Transition time from Acquisition to Idle (sec) |
| TIME_ACQ2PREC | VTIMACQ2PREC | ACS Transition time from Acquisition to Precession (sec) |

## ACS Telemetry

Table 9-2 lists the SOH telemetry that is generated by the ACS Control Algorithms.

Table 9-2.  ACS Telemetry

| Mnemonic | Parameter Type | ITOS Description |
| --- | --- | --- |
| TACCSSPNTERR | DFP | ACS Coarse Sun Sensor Pointing Error (derived) |
| TACESTSPINRT | SFP | ACS estimated spin rate |
| TACFSSPNTERR | DFP | ACS Fine Sun Sensor Pointing Error (derived) |
| TACINSUNSENS | BOOL | Sun Sensor used by ACS (0 = FSS, 1 = SAS) |
| TACSASPNTERR | DFP | ACS SAS Pointing Error (derived) |
| TACSCMDMODE | BOOL | 0=autonomous mode, 1=commanded mode |
| TACSCSSSPI | BOOL | ACS CSS Sun Presence indicator |
| TACSCSSX | SFP | ACS CCS Sun vector along X-axis |
| TACSCSSY | SFP | ACS CCS Sun vector along Y-axis |
| TACSCSSZ | SFP | ACS CCS Sun vector along Z-axis |
| TACSFSSX | SFP | ACS FSS Sun vector along X-axis |

Table 9-2.  ACS Telemetry (Continued)

| TACSFSSY | SFP | ACS FSS Sun vector along Y-axis |
| --- | --- | --- |
| TACSFSSZ | SFP | ACS FSS Sun vector along Z-axis |
| TACSMAGX | SFP | ACS Magnetic field along X-axis |
| TACSMAGY | SFP | ACS Magnetic field along Y-axis |
| TACSMAGZ | SFP | ACS Magnetic field along Z-axis |
| TACSMODE | UB | ACS current mode |
| TACSSASSPI | BOOL | ACS SAS Sun Presence Indicator |
| TACSSASX | SFP | ACS SAS Sun vector along X-axis |
| TACSSASY | SFP | ACS SAS Sun vector along Y-axis |
| TACSSASZ | SFP | ACS SAS Sun vector along Z-axis |
| TACTOIDLEFLG | UB | ACS Flag describing transition to Idle Mode |
| TACTQRXCUR | SFP | ACS Commanded current to X torque rod |
| TACTQRYCUR | SFP | ACS Commanded current to Y torque rod |
| TACTQRZCUR | SFP | ACS Commanded current to Z torque rod |
| TACTRANSVRTX | SFP | ACS Transverse rate along X-axis |
| TACTRANSVRTY | SFP | ACS Transverse rate along Y-axis |

## ACS Housekeeping Telecommands

The ACSNOOP telecommand acknowledges that the Attitude Control Subsystem is receiving telecommands.

The ACSTCRESET telecommand resets the Attitude Control Subsystem telecommand received, rejected and error counters.

ACSNOOP Verifies that the Attitude Control Subsystem is responding (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TACTCRECVD (UB) # of ACS Subsystem TCs received will increment by one

ACSTCRESET Resets Attitude Control Subsystems TC received/rejected/error counters (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TACTCRECVD (UB) # of ACS Subsystem TCs received will increment by one TACTCREJECT (UB) # of ACS Subsystem TCs that failed verification set to zero TACTCERRORS (UB) # of ACS Subsystem TCs that failed to execute set to zero

# STATE OF HEALTH SUBSYSTEM

The SOH Subsystem is responsible for building the FSW SOH telemetry frames, for storing telemetry frames in the stored telemetry database, and storing telemetry frames in PACI PNVRAM.

The SOH Subsystem will read the rate for which the PACI is downlinking telemetry, as commanded by CRC17, and build the FSW SOH telemetry frame at the same rate. The FSW portion of the VC0 SOH telemetry frame is written to PACI device memory, and the PACI transmits the entire telemetry frame contents to the CIB device for downlink. VC0 APID 0 is hardware only SOH telemetry. VC1 APID 1 is hardware and FSW SOH telemetry.

After a power-up or reset, FSW will read and store in the telemetry database, the VC1 APID 1 telemetry for 10 minutes at a 1 Hz rate. A fter ten minutes, the VC1 APID 1 telemetry is read and stored at a rate specified by the VSSOHRATE flight parameter, which is specified as a period of seconds, and is by default 10 seconds.

Every second, the VC0 APID 1 telemetry will be stored in the PACI PNVRAM for retrieval in event of a CPU reset.

There are three SOH Subsystem telecommands.  The SOHNOOP telecommand acknowledges that the SOH Subsystem is receiving telecommands.  The SOHTCRESET telecommand resets the SOH Subsystem telecommand received, rejected and error counters.  The SOHFORCEBLD telecommand is useful when all O/S clock sources have been loss.  The SOHFORCEBLD telecommand forces the SOH Subsystem to build a FSW SOH frame and write it out to the PACI.

SOHNOOP Verifies that the SOH Subsystem is responding (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSOTCRECVD (UB) # of SOH Subsystem TCs received will increment by one

SOHTCRESET Resets SOH Subsystems TC received/rejected/error counters (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSOTCRECVD (UB) # of SOH Subsystem TCs received will increment by one TSOTCREJECT (UB) # of SOH Subsystem TCs that failed verification set to zero TSOTCERRORS (UB) # of SOH Subsystem TCs that failed to execute set to zero

SOHFORCEBLD Forces FSW to build FSW portion of real-time SOH telemetry (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TSOTCRECVD (UB) # of SOH Subsystem TCs received will increment by one TSOTCREJECT (UB) # of SOH Subsystem TCs that failed verification TSOTCERRORS (UB) # of SOH Subsystem TCs that failed to execute

# UPLINK SUBSYSTEM

The Uplink Subsystem is responsible for reconstructing telecommands from CCSDS Codeblocks received from the CIB board, and then routing them to the appropriate subsystem.  To ensure that an unlinked command will be received, FSW uses two methods to detect that a new codeblock has been received. At 16 Hz, the Uplink Subsystem queries the CIB registers to detect whether a codeblock has been received. In addition, the CIB will send a VME interrupt for each codeblock received.

## CCSDS COP-1 Protocol Control

The Uplink Subsystem supports the Command Operation Procedure-1 (COP-1) and Frame Acceptance and Reporting Mechanism-1 (FARM-1) protocol for telecommand acceptance and reporting as defined in the CCSDS 202.1-B-1 document.  COP-1 is a closed-loop telecommanding protocol that utilizes sequential retransmission techniques to correct telecommand frames that were rejected by the spacecraft because of error. If one or more frames are missed, retransmission is initiated either in response to a "Retransmit" Flag in the Command Link Control Word (CLCW) or a timeout on the ground.

Two COP-1 protocol control telecommands help the ground synchronize communications with the S/C.  When the S/C FARM-1 has received too many out of sequence telecommands, it enters a CCSDS “Lockout” state. The CCSDS Unlock telecommand, sent using the ITOS procedure CCSDS_UNLOCK, will move the S/C FARM-1 to an “Open” state. To reset the telecommand sequence number that the S/C FARM-1 is expecting to zero, the ground can send the CCSDS Set V(R) telecommand using the ITOS procedure CCSDS_RESET.

## Uplink Subsystem CRC Commands

The ground will generally send CRC telecommands using Virtual Channel 0 (VC0). Only Virtual Channel 1 (VC1) telecommands can be sent from an RTS or ATS. FSW supports four telecommands for setting and clearing CRC bits. The ground must enable EFC Mask bits to allow FSW telecommands to change CRC bits.  Therefore, a VC1 telecommand to change a CRC bit will only be successful if the ground has explicitly allowed that specific bit to be changed.

The UPCRCBITSET telecommand will set any one of the 24 CRC bits.  The UPCRCBITCLR telecommand will clear any one of the 24 CRC bits. The UPCRCSET telecommand can set any of the 8 bits in one CRC byte. The UPCRCCLR telecommand can clear any of the 8 bits in one CRC byte.

UPCRCBITSET Sets a specific bit on the JPL HCD/CRC ASIC BITNUM (UB) The specific CRC bit to set. Range: 0 to 23 0 = CRCRESET The HCD/CRC ASIC Reset Bit 1 = CRCCPUPOWER CPU Power 2 = CRCXMITCTRL Transmitter Control 3 = CRCANTENNA Transmit Antenna Select 4 = CRCWINGUPRI Solar Wing Release Upper Pri Release 5 = CRCWINGLPRI Solar Wing Release Lower Pri Release 6 = CRCWINGLURED Solar Wing Release Upper Red Release 7 = CRCWINGLRED Solar Wing Release Lower Red Release 8 = CRCWINGXEN Solar Wing +/- X Release Enable 9 = CRCWINGYEN Solar Wing +/- Y Release Enable 10 = CRCUVTRIPCTL Under voltage Trip Control 11 = CRCOVTRIPCTL Over voltage Trip Control 12 = CRCVTCRVSEL1 V/T Curve Select 1 of 4 13 = CRCVTCRVSEL2 V/T Curve Select 2 of 4 14 = CRCVTCRVSEL3 V/T Curve Select 3 of 4 15 = CRCVTCRVSEL4 V/T Curve Select 4 of 4 16 = CRCBATTMPSEL Battery Temp Sensor Select 17 = CRCSOHRATE SOH Packet Rate (0 = 1Hz, 1 = 8Hz) 18 = CRCDLRATE Downlink Data Rate (0 = Nominal, 1 = Low Rate) 19 = CRCWDTENABLE CIB Watchdog Timer Enable 20 = CRCEEPROM EEPROM Write Enable 21 = CRCBOOTSEL Boot Image Select (0=Primary, 1=Secondary)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TUPTCRECVD (UB) # of Uplink Subsystem TCs received will increment by one TUPTCREJECT (UB) # of Uplink Subsystem TCs that failed verification TUPTCERRORS (UB) # of Uplink Subsystem TCs that failed to execute TCBCRCBIT0 to TCBCRCBIT232 (BOOL) State of a specific CRC bit

UPCRCBITCLR Clear a specific HCD/CRC bit BITNUM (UB) The specific bit to clear Range: 0 to 23 0 = CRCRESET The HCD/CRC ASIC Reset Bit 1 = CRCCPUPOWER CPU Power 2 = CRCXMITCTRL Transmitter Control 3 = CRCANTENNA Transmit Antenna Select 4 = CRCWINGUPRI Solar Wing Release Upper Pri Release 5 = CRCWINGLPRI Solar Wing Release Lower Pri Release 6 = CRCWINGLURED Solar Wing Release Upper Red Release 7 = CRCWINGLRED Solar Wing Release Lower Red Release 8 = CRCWINGXEN Solar Wing +/- X Release Enable 9 = CRCWINGYEN Solar Wing +/- Y Release Enable 10 = CRCUVTRIPCTL Under voltage Trip Control 11 = CRCOVTRIPCTL Over voltage Trip Control 12 = CRCVTCRVSEL1 V/T Curve Select 1 of 4 13 = CRCVTCRVSEL2 V/T Curve Select 2 of 4 14 = CRCVTCRVSEL3 V/T Curve Select 3 of 4 15 = CRCVTCRVSEL4 V/T Curve Select 4 of 4 16 = CRCBATTMPSEL Battery Temp Sensor Select 17 = CRCSOHRATE SOH Packet Rate (0 = 1Hz, 1 = 8Hz) 18 = CRCDLRATE Downlink Data Rate (0 = Nominal, 1 = Low Rate) 19 = CRCWDTENABLE CIB Watchdog Timer Enable 20 = CRCEEPROM EEPROM Write Enable 21 = CRCBOOTSEL Boot Image Select (0=Primary, 1=Secondary)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TUPTCRECVD (UB) # of Uplink Subsystem TCs received will increment by one TUPTCREJECT (UB) # of Uplink Subsystem TCs that failed verification TUPTCERRORS (UB) # of Uplink Subsystem TCs that failed to execute TCBCRCBIT0 to TCBCRCBIT232 (BOOL) State of a specific CRC bit

UPCRCSET Set bits in a specific HCD/CRC byte CRCBYTE (UB) The specific CRC byte to set. Range: 0 to 2 BYTEVALUE (UB) A '1' in each bit position sets the CRC bit Range: 0 to 255

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TUPTCRECVD (UB) # of Uplink Subsystem TCs received will increment by one TUPTCREJECT (UB) # of Uplink Subsystem TCs that failed verification TUPTCERRORS (UB) # of Uplink Subsystem TCs that failed to execute TCBCRCBIT0 to TCBCRCBIT232 (BOOL) State of a specific CRC bit

UPCRCCLEAR Clear bits in a specific HCD/CRC byte. CRCBYTE (UB) The specific CRC byte to clear. Range: 0 to 2 BYTEVALUE (UB) A '1' in each bit position clears the CRC bit Range: 0 to 255

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TUPTCRECVD (UB) # of Uplink Subsystem TCs received will increment by one TUPTCREJECT (UB) # of Uplink Subsystem TCs that failed verification TUPTCERRORS (UB) # of Uplink Subsystem TCs that failed to execute TCBCRCBIT0 to TCBCRCBIT232 (BOOL) State of a specific CRC bit

## Resetting the CIB Device FPGAs

The CIB device is on the essential power bus and is never powered off. In the event of upset, UPCIBRESET telecommand allows various CIB FPGAs can be reset.  This UPCIBRESET telecommand will most likely be sent from an RTS in response to a loss of telecommanding fault response.

UPCIBRESET Reset one of three FPGAs on the CIB device CIBFPGA (UB) FPGA to reset Range: 1 to 3 1 = VMEFPGA Reset the CIB DLCTLR, SSRPACI and STSOH VME FPGAs 2 = ULCTLRFPGA Reset the CIB ULCTLR FPGA 3 = HCDASIC Reset the HCD ASIC

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TUPTCRECVD (UB) # of Uplink Subsystem TCs received will increment by one TUPTCREJECT (UB) # of Uplink Subsystem TCs that failed verification TUPTCERRORS (UB) # of Uplink Subsystem TCs that failed to execute

## Switching CIB Uplink Channel

When there is a device failure, and the CIB device no longer gets lock on one of the two uplink input channels, the UPSWITCHAB telcommand instructs the CIB device to toggle the decoded input channel. This UPCIBRESET telecommand will most likely be sent from an RTS in response to a loss of telecommanding fault response.

UPSWITCHAB Switch between CIB Uplink Channel A and B inputs (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TUPTCRECVD (UB) # of Uplink Subsystem TCs received will increment by one TUPTCREJECT (UB) # of Uplink Subsystem TCs that failed verification TUPTCERRORS (UB) # of Uplink Subsystem TCs that failed to execute TCBUPCTLUPSG (BOOL) 0 = UPL A signals for commanding; 1 = UPL B signals

## Uplink Subsystem Housekeeping

The UPNOOP telecommand acknowledges that the Uplink Subsystem is receiving telecommands.

The UPTCRESET telecommand resets the Uplink Subsystem telecommand received, rejected and error counters.

The UPCBTCRESET telecommand resets the counters for the number of codeblocks and telecommands received from the CIB device.

UPNOOP Verifies that the Uplink Subsystem is responding (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TUPTCRECVD (UB) # of Uplink Subsystem TCs received will increment by one

UPTCRESET Resets Uplink Subsystems TC received/rejected/error counters (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TUPTCRECVD (UB) # of Uplink Subsystem TCs received will increment by one TUPTCREJECT (UB) # of Uplink Subsystem TCs that failed verification set to zero TUPTCERRORS (UB) # of Uplink Subsystem TCs that failed to execute set to zero

UPCBTCRESET Resets counters for CIB codeblocks and telecommands (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TCBCBERRORS (UB) Total number of codeblocks received with errors set to zero. TCBCBRECVD (UB) Total number of codeblocks received from CIB set to zero. TCBCBREJECT (UB) Total number of codeblocks rejected from CIB set to zero. TCBTCERRORS (UB) Total number of telecommand errors received from CIB set to zero. TCBTCRECVD (UB) Total number of telecommands received from CIB set to zero. TCBTCREJECT (UB) Total number of telecommands rejected from CIB set to zero.

# DOWNLINK SUBSYSTEM

The Downlink Subsystem is responsible for communicating CCSDS Source Packet telemetry generated by FSW to the CIB board.  All FSW generated telemetry (except VC0 APID 1) is downlinked on Virtual Channel 1.

When not in contact with the ground, the Downlink Subsystem will store most types of source packets in a Stored Telemetry Database.  There are five different telemetry types that are stored in the database, as described in Table 12-1.  Each of these five telemetry types can be separately enabled or disables for downlink during a pass. The DLENABLETLM telecommand enables a telemetry type for downlink to the ground. The DLDISABLETLM telecommand disables a telemetry type from being downlinked. When enabled for downlink and all previously stored telemetry has been downlinked, new telemetry added to the database is immediately downlinked.

Table 12-1.  Stored Telemetry APIDs

| Source Packet Telemetry Type | APIDs | No. of Transfer Frames |
| --- | --- | --- |
| Stored State Of Health | 1 | 10340 |
| Telecommand Log | 10, 11, 12 | 100 |
| IDPU Diagnostic Packets | 151 through 199 | 1000 |
| Event Message Log | 40, 41 | 100 |
| SSR Response Telemetry | 0x200 – 0x2FF | 100 |

## Transmitter and Bypass

Normally, the transmitter must be powered on for stored telemetry to be enabled for downlink.  For range safety reasons, the FSW might need to be tested without powering the transmitter.  The DLBYPASSTX telecommand will allow stored telemetry to be downlinked when the transmitter is powered off. Either the transmitter must be powered, or the transmitter bypass flag must be on (telemetry point TDLTXBYPASS), to enable the downlink of stored telemetry.  When both the transmitter is power off and the transmitter bypass flag are turned off, all stored telemetry will automatically be disabled for downlink.

It should be noted that the CIB buffers up to 238 VC1 transfer frames. Therefore, even when FSW disables all stored telemetry for downlinking, the CIB will continue to transmit the previously buffered VC1 transfer frames.

DLBYPASSTX Allows downlinking stored tlm despite status of transmitter ENABLE (UB) 1=bypass transmitter status; 0=use tx status Range: 0 to 1 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TDLTCRECVD (UB) # of Downlink Subsystem TCs received will increment by one TDLTCREJECT (UB) # of Downlink Subsystem TCs that failed verification TDLTCERRORS (UB) # of Downlink Subsystem TCs that failed to execute TDLTXBYPASS (BOOL) 1=stored telemetry can be downlinked; 0=downlinked based on transmitter status

## Managing Stored Telemetry

The DLENABLETLM telecommand enables downlinking one or more sources of stored telemetry. The transmitter must be powered on, or the transmitter bypass flag must be on, to enable stored telemetry to be downlinked.

When more than one source of telemetry is enabled for downlink, one telemetry frame is retrieved in an round-robin fashion from each enabled source and downlinked until each enabled source has no more telemetry frames in the database. The DLSETWEIGHT telecommand allows the ground to slow the retrieval of telemetry frames from specific sources, thereby increasing the rate at which the other telemetry types are downlinked. The higher the weight, the slower a telemetry source is downlinked. A weight of zero is the nominal value. A weight of N means that N requests for a telemetry frame will be skipped before a frame is downlinked. For example, if the SOH downlink weight is 0, and the TC Log downlink weight is 10, then 11 SOH frames will be downlinked for every 1 TC Log frame.

It is important to note that the DLSETWEIGHT telecommand does not change the CIB device downlink frame, just the percentage of one stored telemetry source versus another source.

The DLDISABLETLM telecommand disables the downlinking of one or more sources of stored telemetry.

The DLDELETETLM deletes all stored telemetry for one more telemetry type.

DLENABLETLM Enables downlinking of one or more stored telemetry types TLMTYPE1 UB 1st stored telemetry type Range: 0 to 1 0 = DEFAULT 1 = SSOH Stored State of Health TLMTYPE2 UB 2nd stored telemetry type Range: 0 or 2 0 = DEFAULT 2 = TCLOG Telecommand Log TLMTYPE3 UB 3rd stored telemetry type Range: 0 or 3 0 = DEFAULT 3 = IDPUDIAG IDPU Diagnostics TLMTYPE4 UB 4th stored telemetry type Range: 0 or 4 0 = DEFAULT 4 = EVENTLOG Event Message Log TLMTYPE5 UB 5th stored telemetry type Range: 0 or 5 0 = DEFAULT 5 = SSR SSR Telemetry

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TDLTCRECVD (UB) # of Downlink Subsystem TCs received will increment by one TDLTCREJECT (UB) # of Downlink Subsystem TCs that failed verification TDLTCERRORS (UB) # of Downlink Subsystem TCs that failed to execute TDLENBLEVENT (BOOL) Indicates that stored event messages are enabled for downlink TDLENBLIDIAG (BOOL) Indicates that stored IDPU Diagnostics are enable for downlink TDLENBLSOH (BOOL) Indicates that Stored SOH is enabled to be downlinked TDLENBLSSR (BOOL) Indicates that stored SSR telemetry is enabled for downlink TDLENBLTCLOG (BOOL) Indicates that stored telecommand log is enabled for downlink

DLDISABLETLM Disables downlinking of one or more stored telemetry types TLMTYPE1 UB 1st stored telemetry type Range: 0 to 1 0 = DEFAULT 1 = SSOH Stored State of Health TLMTYPE2 UB 2nd stored telemetry type Range: 0 or 2 0 = DEFAULT 2 = TCLOG Telecommand Log TLMTYPE3 UB 3rd stored telemetry type Range: 0 or 3 0 = DEFAULT 3 = IDPUDIAG IDPU Diagnostics TLMTYPE4 UB 4th stored telemetry type Range: 0 or 4 0 = DEFAULT 4 = EVENTLOG Event Message Log TLMTYPE5 UB 5th stored telemetry type Range: 0 or 5 0 = DEFAULT 5 = SSR SSR Telemetry

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TDLTCRECVD (UB) # of Downlink Subsystem TCs received will increment by one TDLTCREJECT (UB) # of Downlink Subsystem TCs that failed verification TDLTCERRORS (UB) # of Downlink Subsystem TCs that failed to execute TDLENBLEVENT (BOOL) Indicates that stored event messages are enabled for downlink TDLENBLIDIAG (BOOL) Indicates that stored IDPU Diagnostics are enable for downlink TDLENBLSOH (BOOL) Indicates that Stored SOH is enabled to be downlinked TDLENBLSSR (BOOL) Indicates that stored SSR telemetry is enabled for downlink TDLENBLTCLOG (BOOL) Indicates that stored telecommand log is enabled for downlink

DLSETWEIGHT Sets the transmission weight of a stored telemetry type. TLMTYPE (U12) The stored telemetry type Range: 1 to 5 1 = SSOH Stored State of Health 2 = TCLOG Telecommand Log 3 = IDPUDIAG Stored IDPU Diagnostics 4 = EVENTLOG Event Message Log 5 = SSR Stored SSR Telemetry WEIGHT (UB) The new transmission weight Range: 0 to 255

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TDLTCRECVD (UB) # of Downlink Subsystem TCs received will increment by one TDLTCREJECT (UB) # of Downlink Subsystem TCs that failed verification TDLTCERRORS (UB) # of Downlink Subsystem TCs that failed to execute TDLTXWTEVENT (UB) Transmission weight for Message Event TDLTXWTIDIAG (UB) Transmission weight for IDPU Diagnostic TDLTXWTSOH (UB) Transmission weight for SOH TDLTXWTSSR (UB) Transmission weight for SSR TDLTXWTTCLOG (UB) Transmission weight for Telecommand Log

DLDELETETLM Deletes all stored telemetry of one or more types TLMTYPE1 UB 1st stored telemetry type Range: 0 to 1 0 = DEFAULT 1 = SSOH Stored State of Health TLMTYPE2 UB 2nd stored telemetry type Range: 0 or 2 0 = DEFAULT 2 = TCLOG Telecommand Log TLMTYPE3 UB 3rd stored telemetry type Range: 0 or 3 0 = DEFAULT 3 = IDPUDIAG IDPU Diagnostics TLMTYPE4 UB 4th stored telemetry type Range: 0 or 4 0 = DEFAULT 4 = EVENTLOG Event Message Log TLMTYPE5 UB 5th stored telemetry type Range: 0 or 5 0 = DEFAULT 5 = SSR SSR Telemetry

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TDLTCRECVD (UB) # of Downlink Subsystem TCs received will increment by one TDLTCREJECT (UB) # of Downlink Subsystem TCs that failed verification TDLTCERRORS (UB) # of Downlink Subsystem TCs that failed to execute TDLNUMEVENT (UB) # of Message Event stored tlm frames TDLNUMIDIAG (U12) # of IDPU Diagnostic stored tlm frames TDLNUMRT (UB) Number of real-time telemetry frames queued for downlink TDLNUMRTHIGH (UB) High watermark for queued real-time telemetry frames TDLNUMSOH (U12) # of SOH stored tlm frames TDLNUMSSR (UB) # of SSR stored tlm frames

## CIB Device Downlink Bit Rate

The CRC18 bit selects between the CIB low and high rate.  The low rate is always 125 kbps. The high rate is nominally 4 Mbps, but can be changed with the DLSETRATE telecommand.

DLSETRATE Sets the CIB Board's nominal downlink bit rate BITRATE (UB) The nominal downlink bit rate. Range: 0 to 5 0 = RATE4MBPS 4 Mbps 1 = RATE2MBPS 2 Mbps 2 = RATE1MBPS 1 Mbps 3 = RATE500KBPS 500 kbps 4 = RATE250KBPS 250 kbps 5 = RATE125KBPS 125 kbps

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TDLTCRECVD (UB) # of Downlink Subsystem TCs received will increment by one TDLTCREJECT (UB) # of Downlink Subsystem TCs that failed verification set to zero TDLTCERRORS (UB) # of Downlink Subsystem TCs that failed to execute set to zero TCBDLCTLHIRT (U12) High Rate Downlink Rate

## Downlinked Housekeeping

The DLNOOP telecommand acknowledges that the Downlink Subsystem is receiving telecommands.

The DLTCRESET telecommand resets the Downlink Subsystem telecommand received, rejected and error counters.

Multiple CCSDS Source Packets that are smaller than one transfer frame (TC log, Event Messages, SSR telemetry) can be concatenated to fit into one transfer frame. The DLRTMULTIPKT telecommand, normally only used in testing, controls this concatenation. Enabling multiple source packets per transfer frame is the nominal state.

DLNOOP Verifies that the Downlink Subsystem is responding (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TDLTCRECVD (UB) # of Downlink Subsystem TCs received will increment by one

DLTCRESET Resets Downlink Subsystems TC received/rejected/error counters (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TDLTCRECVD (UB) # of Downlink Subsystem TCs received will increment by one TDLTCREJECT (UB) # of Downlink Subsystem TCs that failed verification set to zero TDLTCERRORS (UB) # of Downlink Subsystem TCs that failed to execute set to zero

DLRTMULTIPKT Selects downlink multiple source packets per frame mode APPENDSEL (UB) 1 = selects multi-packet, 0 = single packet Range: 0 to 1 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TDLTCRECVD (UB) # of Downlink Subsystem TCs received will increment by one TDLTCREJECT (UB) # of Downlink Subsystem TCs that failed verification TDLTCERRORS (UB) # of Downlink Subsystem TCs that failed to execute

# PCB INTERFACE SYSTEM

The Power Controller Board (PCB) Interface Subsystem is responsible for communications between the FSW and the hardware power subsystem. There are four major interfaces in the power subsystem: power switches, torque rods, inertial adjustment device, and the solar array releases.

## Power Switches

The PCBSETSWITCH telecommand is used to turn a power switch on or off.

PCBSETSWITCH Set a specific power switch on the Power Converter Board PCBSWITCH (UB) The ID of the switch to set. Range: 0 to 24 0 = PCBNEB1 Primary Bus - Non-essential bus #1 1 = PCBIDPUH Primary Bus - IDPU heater bus 2 = PCBNEB2 Primary Bus - Non-essential bus #2 3 = PCBCRYO Primary Bus - Cryocooler bus 4 = PCBIDPU Primary Bus - IDPU bus 5 = PCBIDPU28 Primary Bus - +28V bus 6 = PCBSSR Primary Bus - Solid State Recorder bus 7 = PCBRF Primary Bus - RF Antenna (on=forward, off=aft) 8 = PCBFSSHTR Secondary Bus - Fine Sun Sensor heater 9 = PCBSADHTR Secondary Bus - Solar Array Damper Heater 10 = PCBTQHTR Secondary Bus - Torque Rod heater 11 = PCBXPHTR Secondary Bus - Transponder heater 12 = PCBSSRHTR Secondary Bus - Solid State Recorder heater 13 = PCBSPARE1 Secondary Bus - Spare secondary switch #1 14 = PCBSEMHTR Secondary Bus - SEM heater 15 = PCBBATHTR Secondary Bus - Battery heater 16 = PCBXZTQ Secondary Bus - Torque Rod XZ 17 = PCBYZTQ Secondary Bus - Torque Rod YZ 18 = PCBSPARE2 Secondary Bus - Spare secondary switch #2 19 = PCBIAD1 Secondary Bus - Inertia Adjustment Device #1 20 = PCBIAD2 Secondary Bus - Inertia Adjustment Device #2 21 = PCBBATHTR2 Secondary Bus - Battery heater #2 22 = PCBFSS Secondary Bus - Fine Sun Sensor 23 = PCBXMIT Secondary Bus – Transmitter 24 = PCBMAG Secondary Bus – Magnetometer SWITCH_VALUE (UB) The desired switch value. Range: 0 to 1 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one TPCTCREJECT (UB) # of PCB Interface Subsystem TCs that failed verification TPCTCERRORS (UB) # of PCB Interface Subsystem TCs that failed to execute

### Transmitter Switch

For Range Safety purposes, the transmitter power switch has a FSW protection to help prevent inadvertent powering of the transmitter.  The PCBENABLTXSW telecommand enables the transmitter to be powered on if the PCBSWITCH telecommand to power the transmitter (PCBSETSWTICH PCBXMIT, ON) is received within 10 seconds.  After 10 seconds, the enable expires, and the PCBSWITCH telecommand to power the transmitter will have no effect.  In addition, a transmitter switch off telecommand will cause the enable to expire.

PCBENABLTXSW Enable the transmitter power switch to be turned on ENABLE (UB) 1=enableTx switch to be turned on; 0 = disable Range: 0 to 1 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one TPCTCREJECT (UB) # of PCB Interface Subsystem TCs that failed verification TPCTCERRORS (UB) # of PCB Interface Subsystem TCs that failed to execute TPCTXSWENBL (BOOL) The Transmitter Power Switch Enable is set to ENABLE from telecommand.

Notes: When ENABLE is ON, the TPCTXSWENBL telemetry point will have a value of one until: the following telecommand is received: PCBSETSWITCH PCBXMIT, ON the following telecommand is received: PCBSETSWITCH PCBXMIT, OFF the following telecommand is received: PCBENABLETX OFF ten seconds after PCBENABLETXSW telecommand was received

## Torque Rods

The PCBCMDTORQUE telecommand is used to manually drive each of the torque rods with a specific current for 2.5 seconds, which is when the PCB device automatically shuts off the current.

PCBCMDTORQUE Command the torque rods XTORQUEROD (SFP) Desired X torque rod current in amps Range: -0.25 to 0.25 YTORQUEROD (SFP) Desired Y torque rod current in amps Range: -0.25 to 0.25 Z1TORQUEROD (SFP) Desired Z torque rod #1 current in amps Range: -0.25 to 0.25 Z2TORQUEROD (SFP) Desired Z torque rod #2 current in amps Range: -0.25 to 0.25

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one TPCTCREJECT (UB) # of PCB Interface Subsystem TCs that failed verification TPCTCERRORS (UB) # of PCB Interface Subsystem TCs that failed to execute TPCBTRQCMDX (U12) Last commanded Torque Rod X count TPCBTRQCMDY (U12) Last commanded Torque Rod Y count TPCBTRQCMDZ1 (U12) Last commanded primary Torque Rod Z count TPCBTRQCMDZ2 (U12) Last commanded redundant Torque Rod Z count

## Inertial Adjustment Device

The PCBDRIVEIAD telecommand allows the ground to drive the Inertial Adjustment Device.  This will generally be one at the beginning of the mission.

PCBDRIVEIAD Drive the Inertial Adjustment Device DRIVE_NUMBER (UB) Range: 1 to 2 1 = IAD1 Inertial Adjustment Device 1 2 = IAD2 Inertial Adjustment Device 2 STEPS (U12) Number of IAD motor steps. Range: 0 to 1023 IADDIRECTION (UB) Direction of motor movement. Range: 0 to 1 0 = CLOCKWISE Drive IAD motor clockwise (+Z Wingtip Travel) 1 = COUNTERCLOCK Drive IAD motor counter-clockwise (-Z Wingtip)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one TPCTCREJECT (UB) # of PCB Interface Subsystem TCs that failed verification TPCTCERRORS (UB) # of PCB Interface Subsystem TCs that failed to execute TADBIADSEL (BOOL) Which IAD device is selected; 0 = IAD#1, 1 = IAD#2 TADBIADXPHA (BOOL) Current command for the IADX Phase A TADBIADXPHB (BOOL) Current command for the IADX Phase B TADBIADYPHA (BOOL) Current command for the IADY Phase A TADBIADYPHB (BOOL) Current command for the IADY Phase B TADBPULSECNT (BOOL) The IAD Pulse Count TADBSTEPCNT (BOOL) The IAD step count TADBUPCNT (BOOL) IAD rotation direction; 0 = counter clockwise, 1 = clockwise

## Solar Array Releases

The PCBSAENABLE telecommand enables a solar array release mechanism.  The PCBSADISABLE telecommand disables a solar array release mechanism.  These two telecommands are useful in test and for anomaly conditions.

PCBSAENABLE Enable a Solar Array Release RELEASE_P (UB) Primary Solar Array Release Mechanism Range: 0 or 255 0 = PRIMARY Primary Solar Array Release 255 = DEFAULT RELEASE_S (UB) Secondary Solar Array Release Mechanism Range: 1 or 255 1 = SECONDARY Secondary Solar Array Release 255 = DEFAULT RELEASE_XU (UB) X-Axis Upper Solar Array Release Mechanism Range: 2 or 255 2 = XUPPER ADB X-Axis Upper Solar Array Release Mechanism 255 = DEFAULT RELEASE_YU (UB) Y-Axis Upper Solar Array Release Mechanism Range: 3 or 255 3 = YUPPER ADB Y-Axis Upper Solar Array Release Mechanism 255 = DEFAULT RELEASE_XL (UB) X-Axis Lower Solar Array Release Mechanism Range: 4 or 255 4 = XLOWER ADB X-Axis Lower Solar Array Release Mechanism 255 = DEFAULT RELEASE_YL (UB) Y-Axis Lower Solar Array Release Mechanism Range: 5 or 255 5 = YLOWER ADB Y-Axis Lower Solar Array Release Mechanism 255 = DEFAULT

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one TPCTCREJECT (UB) # of PCB Interface Subsystem TCs that failed verification TPCTCERRORS (UB) # of PCB Interface Subsystem TCs that failed to execute TADBSAPRI (BOOL) Solar array release primary bus command monitor TADBSASEC (BOOL) Solar array release secondary bus command monitor TADBSAXLOW (BOOL) Solar array release X-axis lower command monitor TADBSAXUP (BOOL) Solar array release X-axis upper command monitor TADBSAYLOW (BOOL) Solar array release Y-axis lower command monitor TADBSAYUP (BOOL) Solar array release Y-axis upper command monitor TADBSEPCOUNT (BOOL) The current automated array release count TADBXLPRI (BOOL) Status of X-axis lower primary array release TADBXLSEC (BOOL) Status of X-axis lower secondary array release TADBXUPRI (BOOL) Status of X-axis upper primary array release TADBXUSEC (BOOL) Status of X-axis upper secondary array release TADBYLPRI (BOOL) Status of Y-axis lower primary array release TADBYLSEC (BOOL) Status of Y-axis lower secondary array release TADBYUPRI (BOOL) Status of Y-axis upper primary array release TADBYUSEC (BOOL) Status of Y-axis upper secondary array release

## Mission Mode

The FSW Mission Mode determines which initial stored sequence is started after the Mission Mode indicator is selectable via two bits in the PCB.  If either of the bits is zero, then the Mission Mode is the ‘Launch’, and the RTS00 stored sequence will be started.  If both bits are one, then the Mission Mode is ‘Nominal’, and the RTS01 stored sequence will be started. The PCBMISSNMODE telecommand will set these two bits.

PCBMISSNMODE Sets mission mode which determines the boot-up sequence. MODEPARAM (UB) Mission mode is either launch or nominal. Range: 0 to 1 0 = LAUNCH Use launch boot-up sequence 1 = NOMINAL Use post-launch, or nominal boot-up sequence

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one TPCTCREJECT (UB) # of PCB Interface Subsystem TCs that failed verification TPCTCERRORS (UB) # of PCB Interface Subsystem TCs that failed to execute TPADINBIT05 (BOOL) CCB MISSION MODE STATUS 1 set to MODEPARAM in telecommand TPADINBIT06 (BOOL) CCB MISSION MODE STATUS 2 set to MODEPARAM in telecommand

## PCB Miscellaneous Telecommand

The PCBCLRLATCH telecommand clears the PCB device latched outputs OC, LUV1, LUV2 and LUV3.

The PCBFPGARESET telecommand resets the PCB FPGA logic devices. This telecommand does not affect the state of the switches.

The PCBSETUVLEVL sets or clears the degrade bit for each of the under voltage trip levels.

PCBCLRLATCH Clears the PCB latched outputs OC, LUV1, LUV2, and LUV3 (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one TPCTCREJECT (UB) # of PCB Interface Subsystem TCs that failed verification TPCTCERRORS (UB) # of PCB Interface Subsystem TCs that failed to execute

PCBFPGARESET Resets the PCB FPGA Logic. Does not affect switch states. (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one TPCTCREJECT (UB) # of PCB Interface Subsystem TCs that failed verification TPCTCERRORS (UB) # of PCB Interface Subsystem TCs that failed to execute

PCBSETUVLEVL Sets/clears the degrade bit for under voltage trip levels UVTRIPSELECT (UB) Selects the UV trip level to operate upon Range: 1 to 3 1 = UV1 Under Voltage trip level 1 2 = UV2 Under Voltage trip level 2 3 = UV3 Under Voltage trip level 3 BITSTATE (UB) When set, degrades UV trip level. Clear=nominal Range: 0 to 1 0 = OFF Off 0 = NO No 0 = FALSE False 1 = YES Yes 1 = TRUE True 1 = ON On

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one TPCTCREJECT (UB) # of PCB Interface Subsystem TCs that failed verification TPCTCERRORS (UB) # of PCB Interface Subsystem TCs that failed to execute

## PCB Interface Housekeeping Telecommands

The PCBNOOP telecommand acknowledges that the PCB Interface Subsystem is receiving telecommands.

The PCBTCRESET telecommand resets the PCB Interface Subsystem telecommand received, rejected and error counters.

PCBNOOP Verifies that the PCB Interface Subsystem is responding (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one

PCBTCRESET Resets PCB Interface Subsystems TC received/rejected/error counters (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TPCTCRECVD (UB) # of PCB Interface Subsystem TCs received will increment by one TPCTCREJECT (UB) # of PCB Interface Subsystem TCs that failed verification set to zero TPCTCERRORS (UB) # of PCB Interface Subsystem TCs that failed to execute set to zero

# SCHEDULER SUBSYSTEM

The Scheduler Subsystem is responsible for synchronizing the 64 Hz CPU clock with the 1 Hz Bus Tick received from the PACI, and for sending “wakeup” messages to each of the Subsystems at a specific rate.  Table 14-1 lists the rates at which each of the Subsystems are scheduled.

Table 14-1.  Subsystem Wakeup Schedule

| Subsystem | Ticks Received |
| --- | --- |
| ACS | none |
| Downlink Subsystem | 8th |
| Fault Management Subsystem | 16th, 48th |
| Payload Interface Subsystem | 0th |
| PCB Interface Subsystem | 8th |
| SOH Subsystem | 8th tick, and 8 Hz starting from 3rd tick |
| SSR Interface Subsystem | 0th |
| Storage Management Subsystem | none |
| Stored Command Processor | 0th |
| Uplink Subsystem | 16 Hz starting from 0th tick |

The Scheduler Subsystem receives a 64 Hz interrupt from the CPU clock, a 1 Hz Bus Tick interrupt from the PACI device, and an 8 Hz Analog Scan Done interrupt from the PACI device.  The Scheduler task uses these three interrupts to ensure that it will always be able to schedule the various tasks.  By default, all scheduling uses the CPU 64 Hz clock. If the 64 Hz clock is lost, the 8 Hz PACI interrupt is used for scheduling.  If the 8 Hz PACI interrupt is lost, then the 1 Hz PACI interrupt is used for scheduling.  It should be noted that at 1 Hz, the Fault Management Subsystem can’t feed the CIB Watchdog Timer quick enough, so the Timer must be disabled by the ground.  In addition, if scheduling is based on the 1 Hz PACI interrupt, then all tasks in Table 4-1 only be run at a 1 Hz rate.

# FAULT MANAGEMENT

The Fault Management Subsystem monitors the system looking for anomalous conditions, and if found, makes a predefined response.  In addition, the Fault Management Subsystem is responsible for feeding the CIB Watchdog Timer, and for scrubbing the CPU EDAC RAM.

## Interrupts

The Fault Management Subsystem monitors interrupts received, and alerts the ground when an interrupt source is lost. In addition, spurious interruptS that may occur from the PACI and CIB devices are tracked.  There are seven interrupt sources that are monitored, for which the monitoring can individually be enabled or disabled.  Table 15-1 contains a list of all interrupt monitors, the flight parameter for enabling/disabling the monitor, and the telemetry point used for reporting. Table 15-2 contains a list of telemetry points that report the current interrupt state.

Table 15-1.  Interrupt Monitors

| Interrupt Description | FM Monitor Enable Flight Parameter | Interrupt Active Telemetry Point | No. Times Loss Telemetry Point |
| --- | --- | --- | --- |
| 64 Hz CPU clock interrupt | VFMEN64HTICK | TFMRCVCPUINT | TFMLS64HZTCK |
| 1 Hz PACI Bus Tick interrupt | VFMEN1HZINTR | TFMRCV1HZINT | TFMLSBUSTCK |
| 8 Hz PACI Analog Scan Done interrupt | VFMEN8HZINTR | TFMRCV8HZINT | TFMLSACSINT |
| PACI IDPU data received interrupt | VFMENPLINTR | TFMRCVPLINT | TFMLSIDPUINT |
| PACI SSR data received interrupt | VFMENSSRINTR | TFMRCVSSRINT | TFMLSSSRINT |
| CIB codeblock received interrupt | VFMENCBINTR | TFMRCVCBINT | TFMLSCBINT |
| CIB downlink buffer empty interrupt | VFMENDLINTR | TFMRCVTLMINT | TFMLSDLINT |

Table 15-2.  FSW Interrupt Telemetry Points

TFMLS64HZTCK (UB) Number of times the 64 Hz Bus Tick was lost. TFMLSACSINT (UB) Counts PACI Analog Scan interrupt losses TFMLSBUSTCK (UB) Number of times the 1 Hz Bus Tick was lost. TFMLSCBINT (UB) Counts CIB codeblock interrupt losses TFMLSDLINT (UB) Counts CIB downlink buffer empty interrupt losses TFMLSIDPUINT (UB) Counts PACI IDPU data receive interrupt losses TFMLSSSRINT (UB) Counts PACI SSR data receive interrupt losses TFMRCV1HZINT (BOOL) Currently receiving PACI 1 Hz Bus Tick interrupt TFMRCV8HZINT (BOOL) Currently receiving PACI 8 Hz Analog Scan interrupt TFMRCVCBINT (BOOL) Currently receiving CIB Codeblock Received interrupt TFMRCVCPUINT (BOOL) Currently receiving CPU 64Hz Interrupt. TFMRCVPLINT (BOOL) Currently receiving PACI IDPU Data Ready interrupt TFMRCVSSRINT (BOOL) Currently receiving PACI SSR Data Ready interrupt TFMRCVTLMINT (BOOL) Currently receiving CIB Telemetry Buffer Available interrupt TFMSPCIBINT (BOOL) Spurious CIB interrupts occurred; CIB interrupts disabled TFMSPPACIINT (BOOL) Spurious PACI interrupts occurred; PACI interrupts disabled TFMUNKNINTR (UB) Counts number of unknown interrupts that occur

## Fault Monitors

The Fault Management Subsystem monitor eight different analog channels, ACS Sun Pointing and loss of the ability of the S/C to received telecommands. When a fault is detected, a specific RTS is started. The name of each RTS associated with a fault response is listed in Table 6-1, Special Purpose Relative-Time Sequences.  Except for the Loss of Telecommanding fault response, a fault response will only be triggered once until the fault response indicator telemetry point has been cleared using the FMCLEAR telecommand (see Section 15.2.4 Clearing Fault Response Indications on page 0).

### Analog Sensors

The Fault Management Subsystem monitors eight different analog channels for sensor reading that are out of the “safe” range as determined by Systems Engineering. Table 15-3 lists the following in each column:

a.	Name of a analog channel fault monitor test

b.	RTS that is started when a fault condition is met

c.	Flight parameter name for the variable that enables the fault monitor test. By default, this test is disable when booting the primary FSW image.

d.	The flight parameter names for the range of values that will trigger a fault response

e.	The analog telemetry point that is checked and the telemetry point that is set when a fault response is triggered.

A specific analog fault monitor test can be enabled or disabled by setting the ‘enabling’ flight parameter to TRUE or FALSE accordingly.  Flight parameters can be changed during flight using the procedures outlined in Section 16. FLIGHT PARAMETERS starting on page 0.

Table 15-3.  Analog Sensor Fault Monitors

| Fault Description | RTS Started | Enabling Flight Parameter | Fault Range Flight Parameters | Telemetry Points |
| --- | --- | --- | --- | --- |
| Battery 1 Pressure Low Fault | RTS12 | VFMENLOWBAT | VFMLMTLOBATL VFMLMTLOBATH | TPAGPACH03 TFMHITLOBAT1 |
| Battery 2 Pressure Low Fault | RTS13 | VFMENLOWBAT | VFMLMTLOBATL VFMLMTLOBATH | TPAGPACH04 TFMHITLOBAT2 |
| NEB1 Over Current Fault | RTS14 | VFMENNEB1 | VFMLMTNEB1L VFMLMTNEB1H | TPAGPACH31 TFMHITNEB1 |
| NEB2 Over Current Fault | RTS15 | VFMENNEB2 | VFMLMTNEB2L VFMLMTNEB2H | TPAGPACH33 TFMHITNEB2 |
| IDPU Heater Over Current Fault | RTS16 | VFMENIDPUH | VFMLMTIDPUHL VFMLMTIDPUHH | TPAGPACH32 TFMHITIDPUH |
| IDPU Over Current Fault | RTS17 | VFMENIDPU | VFMLMTIDPUL VFMLMTIDPUH | TPAGPACH34 TFMHITIDPU |
| Cryocooler Over Current Fault | RTS18 | VFMENCRYO | VFMLMTCRYOL VFMLMTCRYOH | TPAGPACH35 TFMHITCRYO |
| IDPU Switched Over Current Fault | RTS19 | VFMENIDPUSW | VFMLMTIDPUSL VFMLMTIDPUSH | TPAGPACH36 TFMHITIDPUSW |

### ACS Sun Pointing Fault

The ACS Subsystem transitions to the ‘Idle’ mode when its pointing error is outside of an acceptable range.  FSW duplicates this check to protect against the event that the ACS Subsystem fails and continues to command the spacecraft to point outside the acceptable range.  Table 15-4 lists the following in each column:

a.	Name of fault monitor test

b.	RTS that is started when a fault condition is met

c.	Flight parameter name for the variable that enables the fault monitor test. By default, this test is disable when booting the primary FSW image.

d.	The flight parameter names for the range of values that pointing error must fall between to avert a fault response. FSW converts the Gray Code received in the telemetry point to a decimal value, then compares then to flight parameter values.

e.	The analog telemetry points that are checked and the telemetry point that is set when a fault response is triggered.

The ACS Sun Pointing fault monitor test can be enabled or disabled by setting the ‘enabling’ flight parameter to TRUE or FALSE accordingly.  Flight parameters can be changed during flight using the procedures outlined in Section 16. FLIGHT PARAMETERS starting on page 0.

Table 15-4.  ACS Fault Monitor

| Fault Description | RTS Started | Enabling Flight Parameter | Valid Range Flight Parameters | Telemetry Points |
| --- | --- | --- | --- | --- |
| ACS Sun Pointing Fault | RTS10 | VFMENSUNPT | VFMLMTSUNPTL VFMLMTSUNPTH | TPAFSSSIN1 TPAFSSSIN2 TFMHITSUNPT |

### Loss of Telecommanding

The CIB device is on the Essential Bus, and never gets powered off, and nominally never gets reset.  In the event that the CIB device has a failure that results in no telecommands being received by FSW after a certain amount of time, an RTS will be started that will attempt to reset the CIB device.  After the fault response is triggered, the seconds since the last telecommand was received will be reset to zero. The fault response can then be triggered again after no telecommands have been received by FSW after the set period of time.  This is the only fault monitor response that will continue to be triggered after the faults have been previously triggered.

Table 15-5 lists the following in each column:

a.	Name of fault monitor test.

b.	RTS that is started when a fault condition is met.

c.	Flight parameter name for the variable that enables the fault monitor test.

d.	The flight parameter names for the value to be exceeded before the fault response is triggered.

e.	The telemetry point reporting the number of seconds since the last FSW telecommand was received, and the telemetry point that is set when a fault response is triggered.

The Loss of Telecommanding fault monitor test can be enable or disabled by setting the ‘enabling’ flight parameter to TRUE or FALSE accordingly. Flight parameters can be changed during flight using the procedures outlined in Section 16. FLIGHT PARAMETERS starting on page 0.

Table 15-5.  Loss of Telecommand Fault Response

| Fault Description | RTS Started | Enabling Flight Parameter | Loss Threshold Parameters | Telemetry Points |
| --- | --- | --- | --- | --- |
| Loss of Telecommanding | RTS11 | VFMENTCLOSS | VFMLMTTCLOSS | TFMSECLASTTC TFMHITTCLOSS |

### Clearing Fault Response Indications

Each of the telemetry points that indicate that a fault response had previously been trigger can be reset using the FMCLEAR telecommand.  Except for the TFMHITTCLOSS telemetry point, all other telemetry points being set will prevent the fault response from being triggered in the future. So, not only does using this command let the Operations acknowledge to FSW that it has recognized that the fault had occurred, but it allows FSW to trigger the fault again in the future.

FMCLEAR Clear the Fault Management telemetry counters and flags FAULTID (UB) ID of fault response to clear. Range: 1 to 11 1 = HITNEB1 Clear NEB1 fault response indicator 2 = HITNEB2 Clear NEB2 fault response indicator 3 = HITLOBAT1 Clear Low Battery 1 fault response indicator 4 = HITLOBAT2 Clear Low Battery 2 fault response indicator 5 = HITCRYO Clear CRYO fault response indicator 6 = HITIDPU Clear IDPU fault response indicator 7 = HITIDPUH Clear IDPU Heater fault response indicator 8 = HITSUNPT Clear ACS Sun Pointing fault response indicator 9 = HITTCLOSS Clear telecommand loss fault response indicator 10 = INTERRUPTCNT Clear all interrupt loss counters 11 = HITIDPUSW Clear IDPU Switched fault response indicator

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TFMTCRECVD (UB) # of Fault Management Subsystem TCs received will increment by one TFMTCREJECT (UB) # of Fault Management Subsystem TCs that failed verification TFMTCERRORS (UB) # of Fault Management Subsystem TCs that failed to execute TFMHITLOBAT1 (BOOL) Low BAT1 State of Charge fault response occurred TFMHITLOBAT2 (BOOL) Low BAT2 State of Charge fault response occurred TFMHITNEB1 (BOOL) Hit NEB1 over current condition TFMHITNEB2 (BOOL) Hit NEB2 over current condition TFMHITIDPUH (BOOL) Hit IDPU Heater over current condition TFMHITIDPU (BOOL) Hit IDPU over current condition TFMHITCRYO (BOOL) Hit CRYO over current condition TFMHITIDPUSW (BOOL) Hit IDPU Switched over current condition TFMHITSUNPT (BOOL) Sun Pointer Error fault response occurred TFMHITTCLOSS (BOOL) Telecommand loss fault response occurred

## CPU EDAC RAM Scrubbing

The Fault Management Subsystem completely scrubs all 128 MB of CPU EDAC RAM every 18.2 hours. During the scrub process, the CPU records any single-bit errors that were fixed, allow with the CPU RAM address where the error occurred. CPU EDAC RAM scrubbing can be disabled be setting the flight parameter VFMENEDACSCB to FALSE.

TFMSBEDACADR( U1234) CPU Address of last RAD6000 CPU EDAC Single Bit Error TFMSBEDACNUM (UB) Number of RAD6000 CPU EDAC Single Bit Errors

## PACI EDAC RAM Scrubbing

The PACI device continually scrubs it own 256 Kbytes of EDAC RAM. PACI EDAC RAM scrubbing can not be disabled. When a double-bit error is encountered, a VME interrupt is issued. FSW acknowledges the interrupt and increments a counter, and telemeters this information to the ground. The TFMEDACERRCT telemetry point indicates the number of PACI EDAC double-bit error interrupts received (counts at most 255 interrupts). The TFMHITEDAC telemetry point simply alerts the ground that at least one PACI EDAC double-bit error interrupt was received.

TFMEDACERRCT (UB) Count of the number of EDAC error interrupts from PACI TFMHITEDAC (BOOL) At least one PACI EDAC memory error occurred.

## CIB Watchdog Timer

On power up, or reset, the CIB Watchdog Timer does not expire until 60 seconds, and is not feed until all FSW has been loaded and the Fault Management Subsystem has been started. After the Fault Management Subsystem had been started, it feeds the watchdog timer at a rate of 2 Hz.

The CIB device counts the number of times that the watchdog timer has expired, which is reported in the telemetry point TCBSYSRSTCNT and has a range of 0 to 2. After the 1st and 2nd watchdog timer time-out, the CIB sends a VME SYSRESET signal, resetting the CPU, PACI, PCB, and ADB boards. When the watchdog timer time-out count is 2, and another time-out occurs, the CIB sends a signal to the CCB board to power cycle the CPU. After the CPU has been power cycled, the TCBSYSRSTCNT telemetry point will read 0.

The ground can reset the CIB watchdog timer time-out count with the FMCLRWDTCNT telecommand.

The CIB Watchdog Timer can only be disabled with a VC0 HCD/CRC telecommand.

FMTCRESET Resets Fault Management Subsystems TC received/rejected/error counters (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TFMTCRECVD (UB) # of Fault Management Subsystem TCs received will increment by one TFMTCREJECT (UB) # of Fault Management Subsystem TCs that failed verification TFMTCERRORS (UB) # of Fault Management Subsystem TCs that failed to execute TCBSYSRSTCNT (U12) CIB VME SYSRESET count (range is 0 to 2)

## FSW O/S Task Monitor

The Fault Management Subsystem monitors all FSW tasks running under the VxWorks O/S to ensure that none have died or have suspended. If any task has died or is suspended, then the Fault Management Subsystem will withhold feeding the CIB Watchdog Timer, and let the CPU be reset. This task monitor can be enabled or disable with the VFMENTASKCHK flight parameter. By default, it is enabled when booting the primary FSW image.

## FSW Program Text Segment Corruption Monitor

At 1 Hz, the Fault Management Subsystem calculates a checksum on all of the FSW that has been loaded into RAM. If any loaded FSW has become corrupted, the Fault Management Subsystem will withhold feeding the CIB Watchdog Timer, and let the CPU be reset. This task monitor can be enabled or disable with the VFMENMODCHSM flight parameter. Before any RAM patch is made to FSW, this flight parameter must be set to FALSE or FSW will reboot. By default, the flight parameter is enabled when booting the primary FSW image.

## Fault Management Housekeeping

The FMNOOP telecommand acknowledges that the Fault Management Subsystem is receiving telecommands.

The FMTCRESET telecommand resets the Fault Management Subsystem telecommand received, rejected and error counters.

FMNOOP Verifies that the Fault Management Subsystem is responding (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TFMTCRECVD (UB) # of Fault Management Subsystem TCs received will increment by one

FMTCRESET Resets Fault Management Subsystems TC received/rejected/error counters (no parameters)

Telemetry: After execution of the telecommand, the following telemetry points will be set appropriately: TFMTCRECVD (UB) # of Fault Management Subsystem TCs received will increment by one TFMTCREJECT (UB) # of Fault Management Subsystem TCs that failed verification set to zero TFMTCERRORS (UB) # of Fault Management Subsystem TCs that failed to execute set to zero

# FLIGHT PARAMETERS

Flight parameters allow the ground to modify and customize the behavior of FSW. Flight parameters change the value of data variables used by FSW. Some flight parameters enable or disable certain FSW tests. Other variables are used to modify data used in the Attitude Control Subsystem algorithms. Table 16-1 contains a complete list of all of the FSW flight parameters.

Flight parameters are stored in binary form in the file named ‘params’ in the in-flight filesystem. When FSW is booted, the flight parameters table is copied from the boot filesystem to the RAM filesystem, and then read. The RAM filesystem is considered to contain the working copy of the flight parameters file. To update the flight parameters used during flight, the ground uplinks a flight parameters file to the RAM filesystem. When the flight parameters table is committed, FSW will start using the new parameter values. See Section 5.1 Loading Tables on page 0 for the telecommands that support unlinking a file in flight.

During boot, if the flight parameters file is empty or has been corrupted (file checksum is incorrect), then the default values given in Table 16-1 are used for each variable. When a new flight parameter file is uplinked, it must be of the correct size or the SMTBLCOMMIT telecommands will return in error.

Table 16-1.  Flight Parameters

| Mnemonic | Data Type | Default Value | Range Low | Range High | ITOS Description |
| --- | --- | --- | --- | --- | --- |
| SPAREBYTE01 | unsigned char | 0 | 0 | 0 | Spare Byte 01 |
| SPAREBYTE02 | unsigned char | 0 | 0 | 0 | Spare Byte 02 |
| SPAREBYTE03 | unsigned char | 0 | 0 | 0 | Spare Byte 03 |
| SPAREBYTE04 | unsigned char | 0 | 0 | 0 | Spare Byte 04 |
| VFMENLOWBAT | unsigned char | 0 | 0 | 1 | Value of true enables Low Battery State Of Charge FM response |
| SPAREBYTE05 | unsigned char | 0 | 0 | 0 | Spare Byte 05 |
| SPAREBYTE06 | unsigned char | 0 | 0 | 0 | Spare Byte 06 |
| VFMENSUNPT | unsigned char | 0 | 0 | 1 | Value of true enables Sun Pointing Error FM response |
| VFMENTCLOSS | unsigned char | 1 | 0 | 1 | Value of true enables the Uplink Telecommand Low FM response |
| VSSOHRATE | unsigned char | 10 | 1 | 255 | Period of seconds between each Stored SOH collection. |
| VTRQZSELECT | unsigned char | 0 | 0 | 1 | 0 selects the primary Z-axis torque rod; 1 selects redundant |
| VFMEN1HZINTR | unsigned char | 1 | 0 | 1 | True enables the PACI 1 Hz interrupt check |
| VFMEN8HZINTR | unsigned char | 1 | 0 | 1 | True enables the PACI 8 Hz interrupt check |
| VFMEN64HTICK | unsigned char | 1 | 0 | 1 | True enables the CPU 64 Hz clock check |
| SPAREBYTE07 | unsigned char | 1 | 0 | 1 | Spare Byte 07 |
| VFMENCBINTR | unsigned char | 1 | 0 | 1 | True enables CIB codeblock received interrupt check |

Table 16-1.  Flight Parameters (Continued)

| VFMENDLINTR | unsigned char | 1 | 0 | 1 | True enables CIB downlink buffer empty interrupt check |
| --- | --- | --- | --- | --- | --- |
| VFMENPLINTR | unsigned char | 1 | 0 | 1 | True enables PACI IDPU Data Ready interrupt check |
| VFMENSSRINTR | unsigned char | 1 | 0 | 1 | True enables PACI SSR Data Ready interrupt check |
| VFMENEDACSCB | unsigned char | 1 | 0 | 1 | True enables EDAC RAM scrubbing |
| VFMLMTLOBATL | unsigned short | 2595 | 0 | 4095 | Low Battery State of Charge low bad range |
| VFMLMTLOBATH | unsigned short | 3100 | 0 | 4095 | Low Battery State of Charge high bad range |
| VFMLMTNEB1L | unsigned short | 2459 | 0 | 4095 | NEB1 overcurrent condition low bad range |
| VFMLMTNEB1H | unsigned short | 4095 | 0 | 4095 | NEB1 overcurrent condition high bad range |
| VFMLMTNEB2L | unsigned short | 2569 | 0 | 4095 | NEB2 overcurrent condition low bad range |
| VFMLMTNEB2H | unsigned short | 4095 | 0 | 4095 | NEB2 overcurrent condition high bad range |
| VFMLMTIDPUHL | unsigned short | 2451 | 0 | 4095 | IDPU Heater overcurrent condition low bad range |
| VFMLMTIDPUHH | unsigned short | 4095 | 0 | 4095 | IDPU Heater overcurrent condition high bad range |
| VFMLMTIDPUL | unsigned short | 2384 | 0 | 4095 | IDPU overcurrent condition low bad range |
| VFMLMTIDPUH | unsigned short | 4095 | 0 | 4095 | IDPU overcurrent condition high bad range |
| VFMLMTCRYOL | unsigned short | 2712 | 0 | 4095 | CRYO overcurrent condition low bad range |
| VFMLMTCRYOH | unsigned short | 4095 | 0 | 4095 | CRYO overcurrent condition high bad range |
| VFMLMTIDPUSL | unsigned short | 2382 | 0 | 4095 | IDPU Switched overcurrent condition low bad range |
| VFMLMTIDPUSH | unsigned short | 4095 | 0 | 4095 | IDPU Switched overcurrent condition high bad range |
| SPAREWORD11 | unsigned short | 0 | 0 | 0 |  |
| SPAREWORD12 | unsigned short | 0 | 0 | 0 |  |
| Table 16-1. Flight Parameters (Continued) |
| VFMLMTTCLOSS | unsigned long | 345600 | 86400 | 2592000 | Uplink Telecommand Loss limit in seconds to be exceeded |
| VMAGBIASX | float | 0 | -0.00002 | 0.00002 | Magnetometer bias for the X-axis |
| VMAGBIASY | float | 0 | -0.00002 | 0.00002 | Magnetometer bias for the Y-axis |
| VSASDELAY | float | 2.5 | 0 | 3.5 | SAS Delay in seconds between collection time and receipt time |
| VCSSTHRESH | float | 0.0005 | 0 | 0.001 | ACS CCS threshold (amps). |
| VFSS_BIASX | float | 0 | -1 | 1 | ACS FSS bias along x-axis |
| VFSS_BIASY | float | 0 | -1 | 1 | ACS FSS bias along y-axis |
| VTQRCOMP11 | float | 0 | -20 | 20 | ACS Torque rod compensation maxtrix component |
| VTQRCOMP12 | float | 0 | -20 | 20 | ACS Torque rod compensation maxtrix component |
| VTQRCOMP13 | float | 0 | -20 | 20 | ACS Torque rod compensation maxtrix component |
| VTQRCOMP21 | float | 0 | -20 | 20 | ACS Torque rod compensation maxtrix component |
| VTQRCOMP22 | float | 0 | -20 | 20 | ACS Torque rod compensation maxtrix component |
| VTQRCOMP23 | float | 0 | -20 | 20 | ACS Torque rod compensation maxtrix component |
| VTQRCOMP31 | float | 0 | -20 | 20 | ACS Torque rod compensation maxtrix component |
| VTQRCOMP32 | float | 0 | -20 | 20 | ACS Torque rod compensation maxtrix component |
| VTQRCOMP33 | float | 0 | -20 | 20 | ACS Torque rod compensation maxtrix component |
| VTQRSATHIGH | float | 60 | 0 | 100 | ACS Torque rod high saturation level (amp-m^2) |
| VTQRSATPNTLO | float | 30 | 0 | 100 | ACS Torque rod low saturation level in pointing (amp-m^2) |
| VTQRSATSPNLO | float | 10 | 0 | 100 | ACS Torque rod low saturation level in spin (amp-m^2) |
| VACQSPINCOM | float | 0.035 | 0 | 0.1 | ACS Commanded spin rate durning acquisition (rad/sec) |
| VNORMSPINCOM | float | 1.57 | 0 | 2 | ACS Commanded spin rate during normal operations (rad/sec) |
| VACQGAIN | double | 1E+11 | 0 | 1E+11 | ACS Acquisition control gain (amp-m^2-sec/tesla) |
| Table 16-1. Flight Parameters (Continued) |
| VCRSPRECGAIN | float | 10000 | 0 | 1000000 | ACS Coarse precession control gain (amp-m^2) |
| VFINEPRCGAIN | float | 1.5 | 0 | 5 | ACS Fine precssion control gain (N-m-sec) |
| VFINENUTGAIN | float | 4.5 | 0 | 20 | ACS Fine nutation control gain (N-m-sec) |
| VSPINGAIN | float | 1 | 0 | 10 | ACS Spin control gain (amp-m^2-sec-tesla) |
| VPOINTHIGH | float | 0.001745 | 0 | 0.004 | ACS High setting for pointing hysteresis logic (rad) |
| VPOINTLOW | float | 0.0008725 | 0 | 0.002 | ACS Low setting for pointing hysteresis logic (rad) |
| VPOINTCHECK | unsigned long | 1 | 0 | 1 | ACS Initial status of pointing hysteresis logic |
| VDELTASPINHI | float | 0.1 | 0 | 0.4 | ACS High setting for pointing hysteresis logic (rad/sec) |
| VDELTASPINLO | float | 0.05 | 0 | 0.2 | ACS Low setting for pointing hysteresis logic (rad/sec) |
| VSPINCHECK | unsigned long | 1 | 0 | 1 | ACS Initial state of spin hysteresis log |
| VPTACQ2NORM | float | 0.0873 | 0 | 0.2 | ACS Transition pointing error from Acquisition to Idle (rad) |
| VPTPREC2NORM | float | 0.0035 | 0 | 0.01 | ACS Transistion pointing error from Precession to Normal (rad) |
| VPTNORM2IDLE | float | 0.0088 | 0 | 0.01 | ACS Transition pointing error from Normal to Idle (rad) |
| VPTSPIN2NORM | float | 0.0035 | 0 | 0.01 | ACS Transition pointing error from Spin to Normal (rad) |
| VRTACQ2NORM | float | 0.0126 | 0 | 0.1 | ACS Transition rate from Precession to Normal (rad/sec) |
| VDRTPREC2NRM | float | 0.05 | 0 | 0.5 | ACS Transition rate error from Precession to Nomal (rad/sec) |
| VDRTNRM2IDLE | float | 0.15 | 0 | 0.5 | ACS Transition rate error from Normal to Idle (rad/sec) |
| VDRTSPIN2NRM | float | 0.05 | 0 | 0.5 | ACS Transition rate error from Spin to Normal |

| Table 16-1. Flight Parameters (Continued) |
| --- |
| VTIMACQ2NORM | float | 600 | 0 | 1800 | ACS Transition time from Acquisition to Idle (sec) |
| VTIMACQ2PREC | float | 9000 | 0 | 11000 | ACS Transition time from Acquition to Precession (sec) |
| VFMENTASKCHK | unsigned char | 1 | 0 | 1 | Enable the Fault Management Tasks Alive check |
| VFMENMODCHSM | unsigned char | 1 | 0 | 1 | Enable the Fault Management O/S Module not corrupt check |
| VFMLMTSUNPTL | unsigned char | 30 | 0 | 63 | Sun Pointing Error low good range |
| VFMLMTSUNPTH | unsigned char | 34 | 0 | 63 | Sun Pointing Error high good range |
| VFMENNEB1 | unsigned char | 0 | 0 | 1 | Value of true enables the NEB1 Overcurrent check |
| VFMENNEB2 | unsigned char | 0 | 0 | 1 | Value of true enables the NEB2 Overcurrent check |
| VFMENIDPUH | unsigned char | 0 | 0 | 1 | Value of true enables the IDPU Heater Overcurrent check |
| VFMENIDPU | unsigned char | 0 | 0 | 1 | Value of true enables the IDPU Overcurrent check |
| VFMENCRYO | unsigned char | 0 | 0 | 1 | Value of true enables the CYRO Overcurrent check |
| VFMENIDPUSW | unsigned char | 0 | 0 | 1 | Value of true enables the IDPU Switched Overcurrent check |

## Changing Flight Parameters

The FSW distribution contains the ITOS file ‘hessi/build/itos/loads/tablefields.data’ that defines the flight parameter table with the mnemonics, types, default values and ranges as defined in Table 16-1. The ITOS ‘leditor’ application is used for changing parameter values and generating table loads.  After a table load file is created, the flight parameter table can be uplinked using the ITOS ‘LOAD’ command.

# UTILITY APPLICATIONS

The FSW distribution contains the directory ‘hessi/bin’ that contains a number of utility applications that may be of use to the Operations and for FSW maintenance.

## binToTableLoad

The binToTableLoad application is used to generate an ITOS formatted image load file. The ITOS LOAD command can be used to uplinked the file to the spacecraft.

binToTableLoad [-c] -t tableName -i inputFile -o outputFile Parameters: -c compress file for uplink -t tableName is the table identifier from the SMTBLSELECT TABLEID parameter -i inputFile is the name of the file from which to generate a formatted image load file. -o outputFile is the name of the generated formatted image load file. Should probably be a file name with a complete path to the ITOS loads directory

## gen_itos_report

The gen_itos_report application is used during FSW testing to generate a report using an ITOS log file as input.

gen_itos_report < filename where filename is an ITOS log file.

## hessiChecksum

The hessiChecksum application is used to calculate the checksum of a file on the ground.  The checksum is calculated using the same method as used in FSW.

hessiChecksum filename where filename is the file for which to calculate a checksum.

## hessiLogTool

The hessiLogTool application is used to decode Event Message (APID 40, 41) and Telecommand Log (APID 10, 11, 12) telemetry into human readable ASCII output.  The hessiLogTool is automatically started when ITOS is started via the ‘forward_fswevents.proc’ STOL script.

hessiLogTool -e eventFile -t tcFile [-p portnum] Parameters: -e eventFile is the hessi/include/auto_events.h header file -t tcFile is the hessi/build/itos/dbx/itos-tc-query.txt telecommand database extract file -p portnum is an optional port number for the socket (default=20342) used for input communications

## sendbin

The sendbin application is used for initial programming of the RAD6000. It will never be used by Operations, but might be used by the Spectrum Astro staff if FSW need to be loaded onto the RAD6000 CPU from scratch.

## default

The default application is used to compress a file on the ground that can later be uncompressed in flight.  This utility is used by the binToTableLoad application when the ‘-c’ option is selected.

deflate < inputFile > outputFile where inputFile is the file to be compressed, and outputFile is the resulting compress file.