|  | SPECTRUM ASTRO, INC. High Energy Solar Spectroscopic Imager (HESSI) PRODUCT FUNCTION SPECIFICATION for the IDPU BACKPLANE contract no. PP005884 |  |
| --- | --- | --- |
| SPECTRUM ASTRO PROPRIETARY DOCUMENT |
| THIS DOCUMENT CONTAINS SPECTRUM ASTRO PROPRIETARY INFORMATION. RECIPIENT, BY ACCEPTING THIS DOCUMENT, AGREES THAT NEITHER THE DOCUMENT NOR ANY INFORMATION CONTAINED WITHIN IT SHALL BE REPRODUCED OR TRANSFERRED TO OTHER DOCUMENTS NOR USED OR DISCLOSED TO OTHERS FOR MANUFACTURING OR ANY OTHER PURPOSES EXCEPT AS SPECIFICALLY AUTHORIZED IN WRITING BY SPECTRUM ASTRO. |
| PREPARED BY: |
| SPECTRUM ASTRO, INC. |
| 1440 N. Fiesta Boulevard |
| Gilbert, Arizona 85233 |
| CAGE Code 0T9D1 |
| INITIAL RELEASE DATE |
| 4 SEPTEMBER 1998 |

| 1110-ew-e11231 | REV A |
| --- | --- |
| 4 SEPTEMBER 1998 |

1110-ew-e11231A

|  | SPECTRUM ASTRO, INC. High Energy Solar Spectroscopic Imager (HESSI) PRODUCT FUNCTION SPECIFICATION for the IDPU BACKPLANE contract no. PP005884 |  |
| --- | --- | --- |

| reviewed BY: |  |  |
| --- | --- | --- |
|  | CONFIGURATION/DATA CONTROL, dAVE mAIDEN | DATE |
| APPROVED BY: |  |  |
|  | QUALITY ASSURANCE, JEFF SQUIRES | DATE |
| prepared BY: |  |  |
|  | ENGINEERING, mike matranga | DATE |
| approved BY: |  |  |
|  | sYSTEM ENGINEERING, JOHN JORDAN | DATE |
| APPROVED BY: |  |  |
|  | pROGRAM mANAGEMENT, JEFF PREBLE | DATE |

| REVISION SUMMARY |  |  |  |
| --- | --- | --- | --- |
| REV | RELEASE DATE | BRIEF DESCRIPTION/REASON FOR CHANGE | EFFECTIVE PAGES |
| - | 26 August 1998 | Initial release. | All |
| A | 4 September 1998 | Complete rewrite. | All |

TABLE OF CONTENTS

PAGE

1.  INTRODUCTION	1

1.1 Purpose	1

1.2 Applicable Documents	1

2.  REQUIREMENTS	1

2.1 Mechanical	1

2.1 Board Thickness	1

2.2 Design	1

2.2.1 Standards	1

2.2.2 Trace Thickness	1

2.2.3 Power Traces	1

2.2.4 Trace Spacing	2

2.2.5 Thermal Relief	2

2.2.6 Layers	2

2.2.7 Ground Plane	2

2.2.8 Ground Plane Jumpers	3

2.2.9 Special Routing Requirements	3

2.2.10 Packaging	3

2.2.11 Chassis Connections	4

LIST OF FIGURES

Figure 2-1.  DGND/AGND Layout	3

LIST OF TABLES

Table 2-1.  Power Traces	2

Table 2-2.  Layer Stack-up	2

Table 2-3.  Special Routing Instructions	3

Table 2-4.  IDPU Backplane Packages	3

LIST OF ACRONYMS

| PFS | Product Function Specification |
| --- | --- |
| HESSI | High Energy Solar Spectroscopic Imager |
| CVS | Component Verification Specification |
| VME | Versa Module Eurocard |
| TBR | To Be Revised |
| IDPU | Integrated Data Processing Unit |
| PWB | Printed Wiring Board |

# 1.  INTRODUCTION

## 1.1 Purpose

This specification establishes the performance, design, development and test requirements for a space flight suitable Integrated Data Processing Unit (IDPU) Backplane to be used on the High Energy Solar Spectroscopic Imager (HESSI) program.

## 1.2 Applicable Documents

The following documents of the exact issue shown form a part of this specification to the extent specified herein. In the event of conflict between the documents referenced herein and the contents of this specification, the contents of this specification shall be considered a superseding requirement.

a.	CID, IDPU Backplane	CID-209864, Rev –

b.	Design Standard for Rigid Printed Boards and Rigid Printed 	IPC-D-275

Board Assemblies

# 2.  REQUIREMENTS

## 2.1 Mechanical

The mechanical configuration of the IDPU backplane shall be per CID-209864.

## 2.1 Board Thickness

The IDPU Backplane Printed Wiring Board (PWB) thickness shall be 0.070 + 0.000 – 0.012 in.

## 2.2 Design

### 2.2.1 Standards

The IDPU backplane shall be designed in accordance with IPC-D-275.

### 2.2.2 Trace Thickness

Unless otherwise specified, all signal traces shall be 8 mils thick.

### 2.2.3 Power Traces

The following nets are used for conducting power in the IDPU Backplane and shall be at least 100 mil. thick.

The net names, descriptions, trace width and spacing requirements are as follows.  Refer to Table 2-1.

- 2-1.  Power Traces

| Signal Name | Description | Thickness | Spacing |
| --- | --- | --- | --- |
| VP5D | +5V Digital | 0.100 | 0.025 |
| VP5 | +5V Analog | 0.100 | 0.025 |
| VM5 | -5V Analog | 0.100 | 0.025 |
| VP12 | +12V Analog | 0.100 | 0.025 |
| VM12 | -12V Analog | 0.100 | 0.025 |
| VP15 | +15V Analog | 0.100 | 0.025 |
| VHTR | +28V Heater Power | 0.100 | 0.025 |
| VHTRRET | +28V Heater Return | 0.100 | 0.025 |

### 2.2.4 Trace Spacing

Unless otherwise specified, all traces shall be spaced at least 10 mils apart.

### 2.2.5 Thermal Relief

All connections to power planes or power nets shall have thermal relief.

### 2.2.6 Layers

The IDPU Backplane shall consist of eight (8) layers.  The layer stack-up shall be as shown in Table 2-2.

- 2-2.  Layer Stack-up

| Layer Number | Definition | Copper |
| --- | --- | --- |
| 1 | Signal | 2 oz |
| 2 | Chassis | 2 oz |
| 3 | Signal | 2 oz |
| 4 | AGND/DGND | 2 oz |
| 5 | Signal | 2 oz |
| 6 | Signal | 2 oz |
| 7 | Chassis | 2 oz |
| 8 | Signal | 2 oz |

### 2.2.7 Ground Plane

The IDPU Backplane contains one (1) power plane, and two (2) thermal planes.  The power plane shall be split into two halves.  One half shall be the DGND plane, and the other half shall be the AGND plane.  The board shall be split at the 24th  row as shown in Figure 2-1.  The two planes shall be at least 100 mils apart.

- 2-1.  DGND/AGND Layout

### 2.2.8 Ground Plane Jumpers

E27 through E40 shall be used to jumper the AGND/DGND planes together (if necessary).  The e-points shall be evenly distributed throughout the board such that there is at least one jumper pair for every other connector.  The e-points shall be placed such that if a jumper is installed, it shall be as short as possible.

### 2.2.9 Special Routing Requirements

The net routing requirements shall be as shown in Table 2-3.

- 2-3.  Special Routing Instructions

| Net Name | Requirement |
| --- | --- |
| AHKP | AHKP shall be routed away from all signals except AGND to avoid crosstalk. |

### 2.2.10 Packaging

There are five unique components used on the IDPU Backplane.  The component reference designators along with their associated package are shown in Table 2-4.

- 2-4.  IDPU Backplane Packages

| REF DES | Package |
| --- | --- |
| J1, J2, J3, J4, J5, J6, J7, J8, J9, J10, J11, and J12 | 96-PIN DIN CONNECTOR |
| R1, R2, R3, R4, R5, R6, R7, R8, R9, R10, R11, R12, R13, R14, R15, R16, R17, R18, R19, R20, R21, R22, R23, and R24 | RWR81 RESISTOR |
| C1, C2, C3, C4, C5, C6, C7, C8, C17, C18, C19, C20, C21, C22, C23, C24, C33, C34, C35, C36, C37, C38, C39, and C40 | CDR05 CAPACITOR |
| C9, C10, C11, C12, C13, C14, C15, C16, C41, C42, C43, and C44 | CWR06 CAPACITOR, CASE D |
| C25, C26, C27, C28, C29, C30, C31, C32, C45, C46, C47, and C48 | CWR06 CAPACITOR, CASE H |

### 2.2.11 Chassis Connections

E-points 1 thru 26 (E1 to E26) shall be connected to the internal chassis planes.  Both the top and bottom sides of the board shall have thermal mounting strips along the edges of the board , as shown in CID-209864, which connect the mounting hardware and external frame to the internal chassis planes.

# Text boxes

Row 24