|  | SPECTRUM ASTRO, INC. HIGH ENERGY SOLAR SPECTROSCOPIC IMAGER (HESSI) PRODUCT FUNCTIONAL SPECIFICATION (PFS) FOR THE POWER CONTROL BOARD (PCB) CONTRACT NO. PPB005884 |  |
| --- | --- | --- |
| SPECTRUM ASTRO PROPRIETARY DOCUMENT |
| THIS DOCUMENT CONTAINS SPECTRUM ASTRO PROPRIETARY INFORMATION. RECIPIENT, BY ACCEPTING THIS DOCUMENT, AGREES THAT NEITHER THE DOCUMENT NOR ANY INFORMATION CONTAINED WITHIN IT SHALL BE REPRODUCED OR TRANSFERRED TO OTHER DOCUMENTS NOR USED OR DISCLOSED TO OTHERS FOR MANUFACTURING OR ANY OTHER PURPOSES EXCEPT AS SPECIFICALLY AUTHORIZED IN WRITING BY SPECTRUM ASTRO. |
| PREPARED BY: |
| SPECTRUM ASTRO, INC. |
| 1440 N. Fiesta Boulevard |
| Gilbert, Arizona 85233 |
| CAGE Code 0T9D1 |
| INITIAL RELEASE DATE |
| 13 November 1998 |
| 1110-EW-E11304 | REV B |
| 14 JUNE 1999 |

1110-EW-E11304B

|  | SPECTRUM ASTRO, INC. HIGH ENERGY SOLAR SPECTROSCOPIC IMAGER (HESSI) PRODUCT FUNCTIONAL SPECIFICATION (PFS) FOR THE POWER CONTROL BOARD (PCB) CONTRACT NO. PPB005884 |  |
| --- | --- | --- |

| REVIEWED BY: |  |  |
| --- | --- | --- |
|  | , CONFIGURATION/DATA CONTROL, dave maiden | DATE |
| APPROVED BY: |  |  |
|  | engineering, john michalek | DATE |
| APPROVED BY: |  |  |
|  | , QUALITY ASSURANCE, jeff squires | DATE |
| APPROVED BY: |  |  |
|  | , engineering, eli kawam | DATE |
| APPROVED BY: |  |  |
|  | , systems engineer, john jordan | DATE |
| APPROVED BY: |  |  |
|  | , PROGRAM MANAGER, jeff preble | DATE |

| REVISION SUMMARY |  |  |  |
| --- | --- | --- | --- |
| REV | RELEASE DATE | BRIEF DESCRIPTION/REASON FOR CHANGE | EFFECTIVE PAGES |
| - | 13 November 1998 | Initial release. | All |
| A | 14 March 1999 | Re-write after division of PCB to PCB + ADB | All |
| B | 14 June 1999 | Changed Name of Spare 2 switch to Mission Mode Relays | 4, 6 |
|  |  | Changed Name of Spare 1 Switch to Battery Strain Gauge Power | 4,6 |
|  |  | Changed timing for slow over current trip level to 30 ms for all switches containing over current protection | 5,6 |
|  |  | Changed slow overcurrent trip point on IDPU bus to 5.0A | 5 |
|  |  | Changed ±5% to ±0.215V | 7 |
|  |  | Added that a switch shall remain off after an overcurrent trip until the OC flag is cleared | 8 |
|  |  | Added that the CPU shall turn off if essential bus +15V is removed | 8 |
|  |  | Added a +/-20 sec tolerance to 15 min timer of transmitter | 9 |
|  |  | Changed logic governing control of RF switch | 9 |
|  |  | Corrected front panel connector pin assignments | 16, 17 |

TABLE OF CONTENTS

PAGE

1.  INTRODUCTION	0

1.1 Purpose	0

1.2 Scope	0

2.  APPLICABLE DOCUMENTS	0

2.1 Spectrum Astro, Inc. Documents	0

3.  REQUIREMENTS	0

3.1 Functional Requirements	0

3.2 General	0

3.2.1 Grounding	0

3.3 Detailed Requirements	0

3.3.1 Power Distribution Requirements	0

3.3.2 Undervoltage Trip	0

3.3.2.1 UV Trip Adjustments	0

3.3.2.2. UV Trip Flag	0

3.3.2.3 UV Trip Enable/Disable	0

3.3.3 Overcurrent Trip	0

3.3.3.1 Overcurrent Trip Flag	0

3.3.3.2 Overcurrent Trip Enable/Disable	0

3.3.4 CPU On/Off Control	0

3.3.5 Separation Detection	0

3.3.6 Transmitter On/Off Control	0

3.3.6.1 RF Switch Control	0

3.3.7 IDPU Safemode Signal	0

3.3.8 Current Monitors	0

4.  VME INTERFACE	0

4.1 Data Interfacing Requirements	0

4.2 HCD Map	0

TABLE OF CONTENTS (Continued)

PAGE

4.3 VME Address Map	0

4.4 VME Interface Requirements	0

4.4.7 VME System Reset	0

4.4.8 Triple Modular Redundancy	0

4.5 FPGA Register Assignments	0

4.5.1 Primary and Secondary Switches	0

4.5.2 Switch On/Off Control	0

4.5.3 Undervoltage Reset	0

4.5.4 PCB Status 1 Register	0

4.5.5 PCB Status 2 Register	0

4.5.6 PCB Reset Register	0

4.5.7 PCB Control Register	0

5.  Electrical Interfaces	0

5.1 Connector Pinouts	0

5.2 Physical Characteristics	0

6.  Power	0

6.1 Operating Voltage	0

6.1.2 Survival Voltage	0

6.1.3 Power Interrupt	0

6.1.4 Thermal Characteristics	0

6.2 Bonding	0

7.  Environmental Conditions	0

7.1 Temperature	0

7.1.1 Operating	0

7.1.2 Non Operating	0

7.1.3 Storage	0

7.1.4 Pressure Decay/Venting	0

TABLE OF CONTENTS (Continued)

PAGE

7.1.5 Random Vibration	0

7.1.6 Acceleration	0

7.1.7 Pyrotechnic Shock	0

LIST OF FIGURES

Figure	3-1.  PCB Function Diagram	0

Figure	3-2.  SEM Grounding Scheme	0

Figure	3-3.  Power Distribution	0

Figure	3-4.  Instrument Power Circuit Breaker Characteristics (Dual Trip)	0

LIST OF TABLES

Table	3-1.  Power Output Requirements	0

Table	3-2.  UV Trip Set Points	0

Table	4-1.  HCD Map	0

Table	4-2.  VME Address Map	0

Table	5-1.  Electrical Connector Types and Pinouts	0

Table	6-1.  Bus Voltage Acceptable Limits	0

LIST OF ACRONYMS

| ACS | Attitude Control System |
| --- | --- |
| CCB | Charge Control Board |
| CIB | Communications Interface Board |
| CID | Component Interface Drawing |
| CPU | Central Processing Unit |
| CVS | Component Verification Specification |
| EEE | Electrical, Electronic, and Electromechanical |
| EPS | Electrical Power Subsystem |
| ESB | Essential Bus |
| ESD | Electrostatic Discharge |
| fpga | Field Programmable Gate Array |
| fss | Fine Sun Sensor |
| GSE | Ground Support Equipment |
| hcd | Hardware Command Decode |
| hessi | High Energy Solar Spectroscopic Imager |
| iad | Inertia Adjustment Device |
| IDPU | Instrument Data Processing Unit |
| IEEE | Institute for Electrical and Electronic Engineers |
| IF | Intermediate Frequency |
| NEB1 | Non-Essential Bus #1 |
| neb2 | Non-Essential Bus #2 |
| PCB | Power Control Board |
| PFS | Product Function Specification |
| POR | Power On Reset |
| pwa | Printed Wiring Assembly |
| PWB | Printed Wiring Board |
| RF | Radio Frequency |
| SEM | Spacecraft Electronics Module |
| SPG | Single Point Ground |
| SSR | Solid State Recorder |
| ttl | Transistor-Transistor Logic |
| UV | Undervoltage |
| vme | Versa Module Eurocard |
| XMTR | Transmitter |

# 1.  INTRODUCTION

## 1.1 Purpose

The purpose of this document is to describe the technical requirements for the Power Control Board (PCB) for the HESSI Program.

## 1.2 Scope

This document captures all requirements, with the exception of environmental and quality assurance, which are covered by the Component Verification Specification (CVS).  This document specifies the minimum performance required of the PCB.  Included are functional requirements, electrical interfaces, and mechanical interfaces.  The document also provides the necessary information, including references to other documents required, to mechanically and electrically interface to this PCB board.

# 2.  APPLICABLE DOCUMENTS

## 2.1 Spectrum Astro, Inc. Documents

Document	Description

a.	1110-EW-Y09781	HESSI Component Verification Specification (CVS)

b.	CID-209810	Spectrum Astro, Inc. Drawing, Component Interface Definition, PCB

# 3.  REQUIREMENTS

## 3.1 Functional Requirements

The primary function of the Power Control Board (PCB) is to distribute unregulated power to all of the components on the HESSI spacecraft.  The PCB shall receive the power via the Spacecraft Bus from the Charge Control Board (CCB) and distribute it into six (6) output buses, two (2) servicing avionics, and four (4) servicing the science payload.  The PCB shall further distribute the avionics busses into individual outputs, some of which shall also be independently switched.

Other major functions of the PCB include space vehicle separation detection and startup, data interface to the avionics via VME bus interface, battery undervoltage detection and mitigation, and various state-of-health instrumentation.

Refer to Figure 3-1 for an overall function diagram of the PCB.

- 3-1.  PCB Function Diagram

## 3.2 General

### 3.2.1 Grounding

The Single Point Ground (SPG) for the HESSI spacecraft is considered to be located on the PCB.  SPG connections shall be made available for spacecraft interfaces such as structure, chassis, etc.  A grounding diagram for the Spacecraft Electronics Module (SEM) is shown in Figure 3-2.

## 3.3 Detailed Requirements

### 3.3.1 Power Distribution Requirements

The PCB shall distribute power from the CCB (Charge Control Board) to the entire spacecraft.  Primary and Secondary switches shall be provided as required.  The design requirements for each output are detailed in Table 3-1.  The general block diagram of the power distribution is found in Figure 3-3.

- 3-2.  SEM Grounding Scheme

- 3-3.  Power Distribution

| 3-1. Power Output Requirements |
| --- |
| Output Name | ESB (BUS) | Transponder | ESB DC/DC Converter | CPU Converter | Solar Array Releases | IDPU BUS | Cryocooler +28 BUS | IDPU Switched +28 BUS | IDPU Heater BUS | NEB1 BUS | TRD X & Zp | TRD Y & Zr | IAD “X” | IAD “Y” |
| Feed Channel | S/C Bus (CCB) | ESB | ESB | CPU | S/C Bus (CCB) | S/C Bus (CCB) | S/C Bus (CCB) | S/C Bus (CCB) | NEB2 | S/C Bus (CCB) | NEB1 | NEB1 | NEB1 | NEB1 |
| Loads Supplied | Transponder, Avionics DC/DC’s | Transmitter/ Receiver | ESB DC/DC Converters (+5, +/-15 V) | CPU DC/DC Converter (+5V) | Array Release Switch Matrix | IDPU | Cryocooler +28 | IDPU Switched +28 | IDPU Heaters | IAD’s, SSR, FSS, RF Sw. Driver | Torque Rod Drivers “X” & “Z primary” | Torque Rod Drivers “Y” & “Z redundant” | Onboard Driver Circuit | Onboard Driver Circuit |
| Switching Command Source Command Signal Type Command Decoding | None | Transmitter VME BiLevel 0X2E = off 0X6E = on | None | State VME BiLevel 1 = On 0 = Off | None | Latching VME 0x08 = Off 0x48 = On | Latching VME 0x06 = Off 0x46 = On | Latching VME 0x0A = Off 0x4A = On | Latching VME 0x02 = Off 0x42 = On | Latching VME 0x00 = Off 0x40 = On | State VME 0x20=Off 0x60=On | State VME 0x22=Off 0x62=On | State VME 0x26=Off 0x66=On | State VME 0x28=Off 0x68=On |
| Overcurrent Protection Trip Point/Tolerance Reset Mechanism | None | None | None | None | None | Yes 20A +/- 1A <15us & 5.0 ± 0.5 A > 30 ms Reassert “ON” | Yes 20A +/-1A < 15us & 10.5 ± 0.5 A > 30ms Reassert “ON” | Yes 20A +/-1A <15us & 5 ± 0.5 A > 30ms Reassert “ON” | Yes 20A +/-1A < 15us & 7.5 ± 0.5 A > 30ms Reassert “ON” | Yes 20A +/-1A <15us & 6 ± 0.3 A > 30ms Reassert “ON” | None | None | None | None |
| Channel Rating | 20Adc | 5A | 5A | 5A | 20Adc | 20 A/10mS, 6.5 Adc | 20A/10ms, 10.5Adc | 20 A/10ms, 5.5Adc | 7.5Adc | 7.5Adc | 1.2A | 1.2A | 1.2 A | 1.2 A |
| Load Characteristics Maximum Current Load Inrush Peak Transient Constant I/P/R Input L/C Back EMF/Blocking Required | ( ( ( ( ( ( | 1.54 A 5 A 65A P=4.8/37 W See Inrush No | 2.5 A Not Switched N/A P= 19W N/A No | 2.5A N/A 15W N/A No | 8.5A N/A N/A Resistive N/A No | 4A 10A/lms ±2V/lms P=0 to 54W See inrush Yes | 7 A 10A/lms ±2V/lms P=0 to 120W See inrush Yes | 3.91 10A/lms ±2V/lms P=0 to 62.5W See inrush Yes | 5 A N/A N/A Resistive N/A No | ( ( ( ( ( ( | 1.2 A 3.2A 3.2A Current 1F No | 1.2 A 3.2A 3.2A Current 1F No | 0.650 A See Cap. N/A N/A 1F No | 0.650 A See Cap. N/A N/A 1F No |
| Status Feedback | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |
| Current Sense Input Range Accuracy Transfer Function Frequency Response | Yes 6.5A ±5% Full Scale V TLM=1/2 ISense 159 KHZ | None | None | None | None | Yes 0-4A ±5% Full Scale V TLM=1/2 I Sense 159KHZ | Yes 0-9A ±5% Full Scale V TLM=1/2 I peak 159KHZ | Yes 0-4A ±5% Full Scale V TLM=1/2 I Sense 159KHZ | Yes 0-5A ±5% Full Scale V TLM=1/2 I Sense 159KHZ | Yes 0-4A ±5% Full Scale V TLM=1/2 I Sense 159KHZ | None | None | None | None |

| Table 3-1. Power Output Requirements (Continued) |
| --- |
| Output Name | Solid State Recorder | Fine Sun Sensor | Software Mode Relays | NEB2 (BUS) | FSS Heater | S/A Damper Heaters | Torque Rod Heaters | Transponder Heater | SSR Heater | SEM Heater | Battery Heater 1 | Battery Heater 2 | Battery Strain Gauge | Magnetometer +/-15 V (Tandem Switches) |
| Feed Channel | NEB1 | NEB1 | NEB1 | S/C Bus (CCB) | NEB2 | NEB2 | NEB2 | NEB2 | NEB2 | NEB2 | NEB2 | NEB2 | NEB2 | Onboard +/-15V |
| Loads Supplied | Solid State Recorder | Fine Sun Sensor | Mode Staus Relays | Various Heaters | FSS Heater | S/A Damper Heaters | Torque Rod Heaters | Transponder Heater | SSR Heater | SEM Heater | Battery Heater | Battery Heater | Batt. Strain Gauge | Magnetometer |
| Switching Command Source Command Decoding | Latching VME 0x0C = Off 0x4C = On | State VME 0x2C = Off 0x6C = On | State VME 0x24 = Off 0x64 = On | Latching VME 0x04 = Off 0x44 = On | State VME 0x10 = Off 0x50 = On | State VME 0x12 = Off 0x52 = On | State VME 0x14 = Off 0x54 = On | State VME 0x16 = Off 0x56 = On | State VME 0x18 = Off 0x58 = On | State VME 0x1C = Off 0x5C = On | State VME 0x1E = Off 0x5E = On | State VME 0x2A = Off 0x6A = On | State VME 0x1A = Off 0x5A = On | State VME 0x30 = Off 0x70 = On |
| Voltage Regulation Setting/Tolerance | None | None | None | None | None | None | None | None | None | None | None | None | None | None |
| Current Regulation Setting/Tolerance | None | None | None | None | None | None | None | None | None | None | None | None | None | None |
| Overcurrent Protection Trip Point/Tolerance Reset Mechanism | None | None | None | Yes 20A±1A <15us & 10 ± 1 A>30ms Reassert “ON” | None | None | None | None | None | None | None | None | None | None |
| Channel Rating | 6A/40ms, 1.2 Adc | 3A/10ms, 1.2 Adc | 1.2 A | 20A/10ms,11Adc | 1.2A | 1.2A | 1.2A | 1.2A | 1.2A | 1.2A | 1.2 Adc | 1.2 Adc | 1.2 A | 2A, 40ms, 1.2 Adc |
| Load Characteristics Maximum Current Load Inrush Peak Transient Constant I/P/R Input L/C Back EMF/Blocking Required | 0.60 A 3.187 3.187 P Input Filter No | 0.1 A 1.5A/20ms 1.5A/20ms P C=22uF No | 0.12 A 3.2A 3.2A R N/A No | ( ( ( ( ( ( | 0.35 A N/A N/A Resistive N/A No | 0.26 A N/A N/A Resistive N/A No | 0.39 A N/A N/A Resistive N/A No | 0.434 A N/A N/A Resistive N/A No | 0.520 A N/A N/A Resistive N/A No | 0.65 A N/A N/A Resistive N/A No | 0.911 A N/A N/A Resistive N/A No | 0.911 A N/A N/A Resistive N/A No | 0.12 A 3.2A 3.2A R N/A No | 45mA 1A,40ms 1A,40ms P 4.7uF No |
| Status Feedback | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |
| Current Sense Input Range Accuracy Transfer Function Frequency Response | None | None | None | Yes 0-10A ±5% Full Scale V TLM = ½ I sense 159 KHZ | None | None | None | None | None | None | None | None | None | None |

- 3-4.  Instrument Power Circuit Breaker Characteristics (Dual Trip)

### 3.3.2 Undervoltage Trip

The PCB shall provide battery undervoltage mitigation.  At battery voltages specified in Table 3-2, with tolerance ± 0.215V, the specified switches shall be commanded off.  Once tripped, the switches shall remain off until commanded on again.

### 3.3.2.1 UV Trip Adjustments

The undervoltage trip levels shall be made adjustable via set resistors.  The alternate UV trip levels (UV1, UV2, UV3) shall be commandable during the mission.  These alternate trip levels shall also have a tolerance of ± 0.215V.  Refer to Table 3-2 for these alternate trip levels.

### 3.3.2.2. UV Trip Flag

The PCB shall apply a +5V signal to pin P2-A31 to indicate that an undervoltage condition has occurred.  This signal shall be cleared by the CPU, via a VME command.

### 3.3.2.3 UV Trip Enable/Disable

Undervoltage trip operation shall be enabled/disabled by HCD command to the PCB.

- 3-2.  UV Trip Set Points

| UV Trip Designation | Battery Trip Voltage | Battery Alternate Trip Voltage | Action |
| --- | --- | --- | --- |
| UV1 | < 26.85V | < 24.86V | Activate “IDPU Safemode” signal |
| UV2 | < 26.33 V | < 24.15V | Turn-off NEB1, and Magnetometer Inhibit CPU Power Converter |
| UV3 | < 25.70 V | < 23.54V | Turn-off NEB2, IDPU, IDPU Switched, Cryocooler, IDPU Heater Bus |

### 3.3.3 Overcurrent Trip

The PCB shall disable the switched buses in the event of an overcurrent condition.  These levels are specified in Table 3-1, with the respective bus switches.  The IDPU Bus, Cryocooler 28V Bus, IDPU Heater Bus, NEB1, NEB2 and IDPU SW +28 Bus shall exhibit performance as depicted in Figure 3-4.  Once a switch is disabled by an overcurrent condition it shall remain off until the trip flag is cleared. Actual settings are specified in Table 3-1.

### 3.3.3.1 Overcurrent Trip Flag

The PCB shall apply a +5V signal to pin P2-A32 on the VME backplane, to indicate that an overcurrent condition has occurred.  This signal shall be cleared by the CPU, via a VME command.

### 3.3.3.2 Overcurrent Trip Enable/Disable

Overcurrent trip operation shall be enabled/disabled by HCD command to the PCB.

### 3.3.4 CPU On/Off Control

The PCB shall have the ability to turn the CPU power converter on or off.  This can be commanded via HCD command.  The CPU converter shall be turned on after the separation detection circuitry intially detects separation.  Upon receipt of the watchdog signal from the CIB, the CPU power will be disabled and then enabled again after a 60ms ±10 ms time delay.  This signal is communicated from the CIB via the P2 connector on the VME backplane and is active high.  The separation detection circuitry shall have the ability to turn on the CPU converter regardless of the state of the HCD command. The default condition for the CPU is off.  If the essential bus +5V, +/-15V power should turn off, the CPU Power shall also be turned off.  When a command is received to turn off the CPU, the PCB shall first turn off the four switches that power torque rod XZp, torque rod Yzr, IAD X, and IAD Y.  After turning off these switches, the PCB shall wait 1.5sec +/-0.6sec before executing the off command to the CPU converter.  In addition, any attempts to turn on these four switches while the CPU converter is off, shall not be executed until the CPU converter has been commanded to turn on.

### 3.3.5 Separation Detection

Three separation lines shall be biased to +5V through pull-up resistors, sensed, and voted by the PCB to determine launch vehicle separation.  Once the PCB has determined valid separation has occurred, NEB1, NEB2, and the CPU power converter shall be turned ON autonomously by the PCB.  Launch separation is determined by a low to a high signal transition on two of three of the separation signals.

### 3.3.6 Transmitter On/Off Control

The PCB shall issue a bilevel discrete TTL enable signal to the transmitter portion of the transponder.  This shall occur in response to a command to the PCB.  This command will be received as either an HCD level command or a VME command.  The HCD and VME commands shall be utilized such that either command can turn the transmitter on.  A high signal on the HCD command will indicate the transmitter to turn on.  The PCB shall timeout the transmitter enable at fifteen (15) minutes +/-20seconds, if not commanded to disable the transmitter in less than 15 minutes.

### 3.3.6.1 RF Switch Control

The PCB shall control the RF ( Radio Frequency) transfer switch.  Activation of this switch will be commanded by an HCD level or VME command.  The RF switch commands shall be interlocked with transmitter power status.  The RF switch shall switch between forward and aft antennae.  A low-level signal on the HCD command will indicate that the switch shall be changed to the aft antenna.  A rising or falling edge shall indicate a change of the switch position is required.  The logic governing control of the RF switch shall be as follows:

a.	Receive RF switch command

b.	Wait for transmitter disable command if transmitter is on.

c.	Power forward or aft antenna, position coil for 50 ms, depending on HCD level or VME command.

### 3.3.7 IDPU Safemode Signal

An IDPU safemode flag shall be generated by the PCB when a UV1 Trip event occurs.  The TTL signal is active HI.  This flag shall be cleared by VME command.

### 3.3.8 Current Monitors

The PCB shall incorporate current sensing circuitry as listed in Table 3-1.  The output of these current sensors shall be discrete analog voltage signals 0-10V.  Transfer functions shall be as listed in Table 3-1.

# 4.  VME INTERFACE

## 4.1 Data Interfacing Requirements

The commands and status of the switched buses shall be transmitted via the P1 connector, using the VME data bus and other dedicated lines on the backplane, accessed via P2.  When the PCB receives a command from the VME bus, the FPGA shall provide VME readback of the information received.

## 4.2 HCD Map

The HCD commands that are to be used by the PCB are listed in Table 4-1.  Their number assignments and logic states are also indicated.  HCD commands are level states and are communicated from the CIB via dedicated lines on the P2 connector of the VME backplane.

- 4-1.  HCD Map

| No. | Component | Function | Low | High |
| --- | --- | --- | --- | --- |
| 1 | PCB | CPU Power Control | Off | On |
| 2 | PCB | Transmitter Control | Off | On |
| 3 | PCB | Transmit Antenna Select | Forward | Aft |
| 10 | PCB | Undervoltage Trip Control | Disable | Enable |
| 11 | PCB | Overcurrent Trip Control | Disable | Enable |

## 4.3 VME Address Map

Commands to the PCB for board control that are VME accessible each have a VME address.  Table 4.2 indicates the address for each of these.

- 4-2.  VME Address Map

| Acronym | Address Offset | Register Description |
| --- | --- | --- |
| NEB1_OFF | 0 | Primary Bus – Non-essential bus #1 off. |
| IDPUH_OFF | 2 | Primary Bus – Instrument Data Processing Unit heater bus off. |
| NEB2_OFF | 4 | Primary Bus – Non-essential bus #2 off. |
| CRYO_OFF | 6 | Primary Bus – Cryocooler bus off |
| IDPU_OFF | 8 | Primary Bus – Instrument Data Processing Unit bus off. |
| IDPU28_OFF | A | Primary Bus – Instrument Data Processing Unit +28V bus off. |
| SSR_OFF | C | Secondary Bus – Solid State Recorder bus off. |
| RF_FWD | E | Primary - RF Antenna facing forward is enabled, aft is disabled. |
| FSSHTR_OFF | 10 | Secondary Bus – Fine Sun Sensor heater off. |
| SADHTR_OFF | 12 | Secondary Bus – Solar Array Damper heater off. |
| TQHTR_OFF | 14 | Secondary Bus – Torque Rod heater off. |
| XPHTR_OFF | 16 | Secondary Bus – Transponder heater off. |
| SSRHTR_OFF | 18 | Secondary Bus – Solid State Recorder heater off. |
| SPARE1_OFF | 1A | Secondary Bus – Spare secondary switch #1 off. |
| SEM_HTR_OFF | 1C | Secondary Bus – SEM heater off. |
| BAT_HTR1_OFF | 1E | Secondary Bus – Battery heater #1 off. |
| XZTQ_OFF | 20 | Secondary Bus – Torque Rod XZ off. |
| YZTQ_OFF | 22 | Secondary Bus – Torque Rod YZ off. |
| SPARE2_OFF | 24 | Secondary Bus – Spare secondary switch #2 off. |
| IAD1_OFF | 26 | Secondary Bus – Inertia Adjustment Device #1 off. |
| IAD2_OFF | 28 | Secondary Bus – Inertia Adjustment Device #2 off. |
| BAT_HTR2_OFF | 2A | Secondary Bus – Battery heater #2 off. |
| FSS_OFF | 2C | Secondary Bus – Fine Sun Sensor off. |
| XMIT_OFF | 2E | Secondary Bus – Transmitter off. |
| MAG_OFF | 30 | Secondary Bus – Magnetometer off. |
| NEB1_ON | 40 | Primary Bus – Non-essential bus #1 on. |
| IDPUH_ON | 42 | Primary Bus – Instrument Data Processing Unit heater bus on. |
| NEB2_ON | 44 | Primary Bus – Non-essential bus #2 on. |
| CRYO_ON | 46 | Primary Bus – Cryocooler bus on. |
| IDPU_ON | 48 | Primary Bus – Instrument Data Processing Unit bus on. |
| IDPU28_ON | 4A | Primary Bus – Instrument Data Processing Unit +28V bus on. |
| SSR_ON | 4C | Secondary Bus – Solid State Recorder bus on. |
| RF_AFT | 4E | Primary - RF Antenna facing aft is enabled, forward is disabled. |
| FSSHTR_ON | 50 | Secondary Bus – Fine Sun Sensor heater on. |
| SADHTR_ON | 52 | Secondary Bus – Solar Array Damper heater on. |
| TQHTR_ON | 54 | Secondary Bus – Torque Rod heater on. |
| XPHTR_ON | 56 | Secondary Bus – Transponder heater on. |
| SSRHTR_ON | 58 | Secondary Bus – Solid State Recorder heater on. |
| Table 4-2. VME Address Map (Continued) |
| SPARE1_ON | 5A | Secondary Bus – Spare secondary switch #1 on. |
| SEM_HTR_ON | 5C | Secondary Bus – SEM heater on. |
| BAT_HTR1_ON | 5E | Secondary Bus – Battery heater #1 on. |
| XZTQ_ON | 60 | Secondary Bus – Torque Rod XZ on. |
| YZTQ_ON | 62 | Secondary Bus – Torque Rod YZ on. |
| SPARE2_ON | 64 | Secondary Bus – Spare secondary switch #2 on. |
| IAD1_ON | 66 | Secondary Bus – Inertia Adjustment Device #1 on. |
| IAD2_ON | 68 | Secondary Bus – Inertia Adjustment Device #2 on. |
| BAT_HTR2_ON | 6A | Secondary Bus – Battery heater #2 on. |
| FSS_ON | 6C | Secondary Bus – Fine Sun Sensor on. |
| XMIT_ON | 6E | Secondary Bus – Transmitter on. |
| MAG_ON | 70 | Secondary Bus – Magnetometer on. |
| UVRST | 80 | Under Voltage Trip Reset |
| PCBSTA1 | 82 | Primary power status (Read Only) |
| PCBSTA2 | 84 | Secondary power status (Read Only) |
| PCBRST | 86 | PCB FPGA software logic reset. |
| PCBCNTL | 88 | General control/status |

## 4.4 VME Interface Requirements

4.4.1 VME Slave

The PCB shall act as an A24/D16 slave on the VME bus.

4.4.2 VME Access Time

The PCB shall have an access time of < 800ns (worst case) for all D16 sustained data transfers on the VME bus.

4.4.3 VME Address

The most significant nibble (A23 to A20) of the PCB VME board address shall be jumper selectable.

4.4.4 VME Address Modifiers

The PCB shall support the following set of address modifiers: 0x3E, 0x3D, 0x3A, and 0x39.

4.4.5 VME Data Transfers

The PCB shall support D16 transfers only.

4.4.6 VME Isolation

The PCB shall be fully isolated from the VME bus such that when the VME bus master is powered off, the PCB shall not source more than 500 A back into the bus.  The PCB shall monitor the CPU+5V power input on the VME backplane and shall use this signal to enable/disable its VME buffers.

### 4.4.7 VME System Reset

The PCB shall reset its VME logic in response to the VME system reset signal being asserted low (0).

### 4.4.8 Triple Modular Redundancy

The PCB FPGA shall be designed using triple modular redundant logic.

## 4.5 FPGA Register Assignments

The following information details the VME bit assignments for commands and status to and from the PCB FPGA.

### 4.5.1 Primary and Secondary Switches

The following is the base address and most significant bit to least significant bit configuration used for VME control of the primary and secondary switches.

| PRIMARY AND SECONDARY SWITCHES | 15 (MSB) – 0(LSB) |
| --- | --- |
| base + 0x00 to 0x70 | N/A |
| Reset | 0 |

### 4.5.2 Switch On/Off Control

When any switch register is accessed (either a read or write) the respective power bus will be turned “On” or “Off” as defined by the address.  There must be a minimum of 80ms between any access of the primary switch registers (Offset addresses 0x00 through 0x0E and offset addresses 0x40 through 0x4E).  The status is obtained from the PCBSTA1 and PCBSTA2 registers.  The primary switches retain their previous “On” or “Off” state upon power-up.  The secondary switches will all be set to an “Off” state on power-up.

### 4.5.3 Undervoltage Reset

Any access to this register will reset the undervoltage logic.  The VME address and most significant bit to least significant bit configuration is as follows:

| UVRST | 15 (MSB) – 0 (LSB) |
| --- | --- |
| base + 0x80 | N/A |
| Reset | 0 |

### 4.5.4 PCB Status 1 Register

This register is a “read only” register.  It gives the status of all the pulsed primary switches.  When the bit is set, that particular bus is “On”.  When the bit is cleared, that particular bus is “Off”.

| PCBSTA1 | 15 (MSB) - 8 |
| --- | --- |
| base + 0x82 | N/A |
| Reset | 0 |

|  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | N/A | SSR_ST | IDPU28_ST | IDPU_ST | CRYO_ST | NEB2_ST | IDPUH_ST | NEB1_ST |
|  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

Bits 15 - 7. N/A

These bits are not implemented.

Bit 6. SSR_ST

This bit reads the status of the Solid State Recorder (SSR) power bus.

Bit 5. IDPU28_ST

This bit reads the status of the Instrument Data Processing Unit (IDPU) switched 28V power bus.

Bit 4. IDPU_ST

This bit reads the status of the Instrument Data Processing Unit (IDPU) power bus.

Bit 3. CRYO_ST

This bit reads the status of the cryocooler power bus.

Bit 2. NEB2_ST

This bit reads the status of the Non-Essential Bus #2 power bus.

Bit 1. IDPUH_ST

This bit reads the status of  the Instrument Data Processing Unit (IDPU) heater bus.

Bit 0. NEB1_ST

This bit reads the status of the Non-Essential Bus #1 power bus.

### 4.5.5 PCB Status 2 Register

This register is a “read only” register.  It gives the status of some secondary switches.  When the bit is set, that particular bus is “On”.  When the bit is cleared, that particular bus is “Off”.

| PCBSTA2 | 15 (MSB) | 14 | 13 | 12 | 11 | 10 | 9 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Base + 0x84 | XMIT_ST | FSS_ST | BATHTR2 | IAD2_ST | IAD1_ST | SPARE2 | YTQ_ST | XTQ_ST |
| Reset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

|  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | BATHTR1 | SEMHTR_ST | SPARE1 | SSRHTR_ST | XPHTR_ST | TQHTR_ST | SADHTR_ST | FSSHTR_ST |
|  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

Bit 15. XMIT_ST

This bit reads the status of the Transmitter power bus.

Bit 14. FSS_ST

This bit reads the status of the Fine Sun Sensor (FSS) Electronics power bus.

Bit 13. BATHTR2

This bit reads the status of the Battery Heater power bus.

Bit 12. IAD2_ST

This bit reads the status of the Inertial Adjustment Device 2 (IAD2) power bus.

Bit 11. IAD1_ST

This bit reads the status of the Inertial Adjustment Device 1 (IAD1) power bus.

Bit 10. SPARE2

This bit reads the status of the Spare #2 power bus.

Bit 9. YTQ_ST

This bit reads the status of the Y-axis toque rod.

Bit 8. XTQ_ST

This bit reads the status of the X-axis toque rod power.

Bit 7. BATHTR1

This bit reads the status of the Battery Heater #1 power bus.

Bit 6. SEMHTR_ST

This bit reads the status of the Spacecraft Electronics Module (SEM) Heater bus.

Bit 5. SPARE1

This bit reads the status of the Spare #1 power bus.

Bit 4. SSRHTR_ST

This bit reads the status of the Solid State Recorder (SSR) Heater power bus.

Bit 3. XPHTR_ST

This bit reads the status of the Transponder Heater power bus.

Bit 2. TQHTR_ST

This bit reads the status of the Torque Rod Heater power bus.

Bit 1. SADHTR_ST

This bit reads the status of the Inertia Adjustment Device (IAD) Heater power bus.

Bit 0. FSSHTR_ST

This bit reads the status of the Fine Sun Sensor (FSS) Heater power bus.

### 4.5.6 PCB Reset Register

Any access to this register will issue a local reset to the PCB FPGA logic.  This reset will not affect the states of the Primary or Secondary switches.

| PCBRST | 15 (MSB) – 0 (LSB) |
| --- | --- |
| Base + 0x86 | N/A |
| Reset | 0 |

### 4.5.7 PCB Control Register

Access to the PCB Control Register will give the status that an overcurrent or undervoltage condition has occurred.  In addition, it can be written to change the UV trip level or clear a flag set by one of these conditions.  The description of each bit is detailed below.

| PCBCNTL | 15 (MSB) | 14 | 13 | 12 | 11 | 10 | 9 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x88 | UV3_SEL | UV2_SEL | UV1_SEL | IDPU28_OFF | IDPU_OFF | CRYO_OFF | NEB2_OFF | IDPUH_OFF |
| Reset |  |  |  |  |  |  |  | 0 |

|  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | NEB1_OFF | UV3 | UV2 | UV1 | LUV3 | LUV2 | LUV1 | UVEN |
|  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | HCD |

Bit 15. UV3_SEL

When set, this bit degrades the UV3 trip level.  When clear, the UV3 trip level is nominal.

Bit 14. UV2_SEL

When set, this bit degrades the UV2 trip level.  When clear, the UV2 trip level is nominal.

Bit 13. UV1_SEL

When set, this bit degrades the UV1 trip level.  When clear, the UV1 trip level is nominal.

Bit 12. IDPU28_OFF

When set, this bit indicates that a IDPU28 Over Current (OC) event or a LUV2 event (same as bit #2) has occurred .  This bit is read only.

Bit 11. IDPU_OFF

When set, this bit indicates that a IDPU Over Current (OC) event or a LUV2 event (same as bit #2) has occurred .  This bit is read only.

Bit 10. CRYO_OFF

When set, this bit indicates that a CRYO Over Current (OC) event or a LUV2 event (same as bit #2) has occurred .  This bit is read only.

Bit 9. NEB2_OFF

When set, this bit indicates that a NEB2 Over Current (OC) event or a LUV2 event (same as bit #2) has occurred .  This bit is read only.

Bit 8. IDPUH_OFF

When set, this bit indicates that a IDPUH Over Current (OC) event or a LUV2 event (same as bit #2) has occurred.  This bit is read only.

Bit 7. NEB1_OFF

When set, this bit indicates that a NEB1 Over Current (OC) event or a LUV2 event (same as bit #2) has occurred.  This bit is read only.

Bit 6. UV3

This bit is the raw Under Voltage #3 (UV3) input.  This bit is read only.

Bit 5. UV2

This bit is the raw Under Voltage #2 (UV2) input.  This bit is read only.

Bit 4. UV1

This bit is the raw Under Voltage #1 (UV1) input.  This bit is read only.

Bit 3. LUV3

This bit is the latched Under Voltage #3 (UV3) output.  This bit will be set when the UVEN is set and a rising edge occurs on the UV3 input.  This bit is cleared by writing a “1” to the UVEN bit.  This bit is read only.

Bit 2. LUV2

This bit is the latched Under Voltage #2 (UV2) output.  This bit will be set when the UVEN is set and a rising edge occurs on the UV2 input. .  This bit is cleared by writing a “1” to the UVEN bit. This bit is read only.

Bit 1. LUV1

This bit is the latched Under Voltage #1 (UV1) output.  This bit will be set when the UVEN is set and a rising edge occurs on the UV1 input. .  This bit is cleared by writing a “1” to the UVEN bit. This bit is read only.

Bit 0. UVEN

This bit has two different modes depending if it is written or read.  When read this bit is the raw Under Voltage Enable input as driven by the CIB’s HCD command (When “1” the UV inputs are enabled, when “0” these inputs are disabled).  When a “1” is written to this register all the latched outputs (OC, LUV1, LUV2 and LUV3) will be cleared.

# 5.  Electrical Interfaces

## 5.1 Connector Pinouts

Electrical connector types and pinouts shall be as defined in Table 5-1.

- 5-1.  Electrical Connector Types and Pinouts

| J1 SND37M5R70T2G 2.072" X 0.494" |
| --- |
| Pin Number | Signal Name |  | Pin Number | Signal Name |
| 1 | PCB BUS |  | 26 | Cryocooler +28V Power RTN |
| 2 | PCB BUS |  | 27 | Cryocooler +28V Power |
| 3 | PCB BUS |  | 28 | Cryocooler +28V Power |
| 4 | PCB BUS |  | 29 | IDPU Power RTN |
| 5 | PCB BUS |  | 30 | IDPU Power |
| 6 | Cryocooler +28V Power RTN |  | 31 | IDPU Switched +28V Power RTN |
| 7 | Cryocooler +28V Power RTN |  | 32 | IDPU Switched +28V Power |
| 8 | Cryocooler +28V Power |  | 33 | PCB BUS RTN |
| 9 | Cryocooler +28V Power |  | 34 | PCB BUS RTN |
| 10 | IDPU Power RTN |  | 35 | PCB BUS RTN |
| 11 | IDPU Power |  | 36 | PCB BUS RTN |
| 12 | IDPU Power |  | 37 | PCB BUS RTN |
| 13 | IDPU Switched +28V Power RTN |  |  |  |
| 14 | IDPU Switched +28V Power |  |  |  |
| 15 | PCB BUS RTN |  |  |  |
| 16 | PCB BUS RTN |  |  |  |
| 17 | PCB BUS RTN |  |  |  |
| 18 | PCB BUS RTN |  |  |  |
| 19 | PCB BUS RTN |  |  |  |
| 20 | PCB BUS |  |  |  |
| 21 | PCB BUS |  |  |  |
| 22 | PCB BUS |  |  |  |
| 23 | PCB BUS |  |  |  |
| 24 | PCB BUS |  |  |  |
| 25 | Cryocooler +28V Power RTN |  |  |  |

Table 5-1.  Electrical Connector Types and Pinouts (Continued)

| J2 SDD62F4R70T2G 2.088" X 0.494" |
| --- |
| Pin Number | Signal Name |  | Pin Number | Signal Name |
| 1 | Spacecraft Essential Bus |  | 32 | IAD2_PWR_RTN |
| 2 | Spacecraft Essential Bus |  | 33 | IAD2_PWR_RTN |
| 3 | Spacecraft Essential Bus |  | 34 | Battery Heater 2 RTN |
| 4 | Spacecraft Essential Bus |  | 35 | Battery Heater 2 RTN |
| 5 | Spacecraft Essential Bus |  | 36 | Spare_1_PWR_RTN |
| 6 | Spacecraft Essential Bus |  | 37 | Spare_1_PWR_RTN |
| 7 | Battery Strain Gauge Power |  | 38 | Spare_2_PWR_RTN |
| 8 | Battery Strain Gauge Power |  | 39 | Spare_2_PWR_RTN |
| 9 | IAD1_PWR |  | 40 | ADB +28 Power |
| 10 | IAD1_PWR |  | 41 | TR_XZ_PWR |
| 11 | IAD2_PWR |  | 42 | TR_XZ_PWR |
| 12 | IAD2_PWR |  | 43 | TR_XZ_PWR_RTN |
| 13 | Batter Heater_2 |  | 44 | TR_XZ_PWR_RTN |
| 14 | Battery Heater_2 |  | 45 | TR_YZ_PWR |
| 15 | Spare_1_PWR |  | 46 | TR_YZ_PWR |
| 16 | Spare_1_PWR |  | 47 | TR_YZ_PWR_RTN |
| 17 | Spare_2_PWR |  | 48 | TR_YZ_PWR_RTN |
| 18 | Spare_2_PWR |  | 49 | ADB +28 Power Return |
| 19 | ADB +28 Power |  | 50 | ADB +28 Power Return |
| 20 | ADB +28 Power |  | 51 | ADB +28 Power Return |
| 21 | ADB +28 Power |  | 52 | ADB +28 Power Return |
| 22 | Spacecraft Essential Bus RTN |  | 53 | Spare |
| 23 | Spacecraft Essential Bus RTN |  | 54 | Spare |
| 24 | Spacecraft Essential Bus RTN |  | 55 | SPG |
| 25 | Spacecraft Essential Bus RTN |  | 56 | SPG |
| 26 | Spacecraft Essential Bus RTN |  | 57 | SPG |
| 27 | Spacecraft Essential Bus RTN |  | 58 | SPG |
| 28 | Battery Strain Gauge Power RTN |  | 59 | SPG |
| 29 | Battery Strain Gauge Power RTN |  | 60 | Spare |
| 30 | IAD1_PWR_RTN |  | 61 | Spare |
| 31 | IAD1_PWR_RTN |  | 62 | Spare |

Table 5-1.  Electrical Connector Types and Pinouts (Continued)

| J3 SDD78F4R70T2G 2.088"X0.494" |
| --- |
| Pin Number | Signal Name | Pin Number | Signal Name |
| 1 | Solid State Recorder Power | 40 | SEM Heater Power |
| 2 | Solid State Recorder Power | 41 | SEM Heater Power |
| 3 | Fine Sun Sensor Electronics Power | 42 | Battery Heater_1 |
| 4 | Fine Sun Sensor Electronics Power | 43 | Battery Heater_1 |
| 5 | Transmitter Switch (Forward) | 44 | IDPU Heater Power |
| 6 | Transmitter Switch (Aft) | 45 | IDPU Heater Power |
| 7 | Transponder Heater Power | 46 | +15V Regulated VME Power |
| 8 | Transponder Heater Power | 47 | +15V Regulated VME Power |
| 9 | Solid State Recorder Heater Power | 48 | -15V Regulated VME Power |
| 10 | Solid State Recorder Heater Power | 49 | -15V Regulated VME Power |
| 11 | IDPU_OFF | 50 | IDPU Safemode Signal |
| 12 | NEB1 RTN (RF Switch) | 51 | Separation Sense 1 PWR |
| 13 | Fine Sun Sensor Electronics Heater Power | 52 | CPU_Inhibit |
| 14 | Fine Sun Sensor Electronics Heater Power | 53 | XPD_On_Off |
| 15 | XPD_PWR | 54 | XPD_On_Off_RTN |
| 16 | XPD_PWR | 55 | Spare |
| 17 | S/A Damper Heater Power | 56 | TAC_CPU_ON_CMD |
| 18 | S/A Damper Heater Power | 57 | TAC_CPU_ON_CMD_RTN |
| 19 | Torque Rod Heater Power | 58 | TAC_CPU_RELAY_STATUS |
| 20 | Torque Rod Heater Power | 59 | Torque Rod Heater Power RTN |
| 21 | Solid State Recorder Power RTN | 60 | SEM Heater Power RTN |
| 22 | Solid State Recorder Power RTN | 61 | SEM Heater Power RTN |
| 23 | Fine Sun Sensor Electronics Power RTN | 62 | Battery Heater_1 RTN |
| 24 | Fine Sun Sensor Electronics Power RTN | 63 | Battery Heater_1 RTN |
| 25 | CPU Inhibit RTN | 64 | IDPU Heater Power RTN |
| 26 | CPU Inhibit RTN | 65 | IDPU Heater Power RTN |
| 27 | Transponder Heater Power RTN | 66 | +15V Regulated VME Power RTN |
| 28 | Transponder Heater Power RTN | 67 | +15V Regulated VME Power RTN |
| 29 | Solid State Recorder Heater Power RTN | 68 | -15V Regulated VME Power RTN |
| 30 | Solid State Recorder Heater Power RTN | 69 | -15V Regulated VME Power RTN |
| 31 | NEB1 RTN (RF Switch) | 70 | Separation Sense 2 PWR |
| 32 | CPU Inhibit | 71 | Separation Sense 3 PWR |
| 33 | Fine Sun Sensor Electronics Heater Power RTN | 72 | TAC_CPU_RELAY_STATUS_RTN |
| 34 | Fine Sun Sensor Electronics Heater Power RTN | 73 | Torque Rod Heater Power |
| 35 | XPD_PWR_RTN | 74 | Torque Rod Heater Power RTN |
| 36 | XPD_PWR_RTN | 75 | TSTAT_Mon_Rtn |
| 37 | Inertia Adjustment Device Heater Power RTN | 76 | Separation Sense 1 RTN |
| 38 | Inertia Adjustment Device Heater Power RTN | 77 | Separation Sense 2 RTN |
| 39 | Torque Rod Heater Power RTN | 78 | Separation Sense 3 RTN |

| Table 5-1. Electrical Connector Types and Pinouts (Continued) |
| --- |
| P1 – VME Connector Assignments |
| A1 | D0 | B1 | NC | C1 | D8 |
| A2 | D1 | B2 | NC | C2 | D9 |
| A3 | D2 | B3 | NC | C3 | D10 |
| A4 | D3 | B4 | NC | C4 | D11 |
| A5 | D4 | B5 | NC | C5 | D12 |
| A6 | D5 | B6 | NC | C6 | D13 |
| A7 | D6 | B7 | NC | C7 | D14 |
| A8 | D7 | B8 | NC | C8 | D15 |
| A9 | GND | B9 | NC | C9 | GND |
| A10 | NC | B10 | NC | C10 | NC |
| A11 | GND | B11 | NC | C11 | BERR* |
| A12 | DS1* | B12 | NC | C12 | SYSRESET* |
| A13 | DS0* | B13 | NC | C13 | LWORD* |
| A14 | WRITE* | B14 | NC | C14 | AM5 |
| A15 | GND | B15 | NC | C15 | A23 |
| A16 | DTACK* | B16 | AM0 | C16 | A22 |
| A17 | GND | B17 | AM1 | C17 | A21 |
| A18 | AS* | B18 | AM2 | C18 | A20 |
| A19 | GND | B19 | AM3 | C19 | A19 |
| A20 | IACK* | B20 | GND | C20 | A18 |
| A21 | A22 | B21 | NC | C21 | A17 |
| A22 | A21 | B22 | NC | C22 | A16 |
| A23 | AM4 | B23 | GND | C23 | A15 |
| A24 | A7 | B24 | NC | C24 | A14 |
| A25 | A6 | B25 | NC | C25 | A13 |
| A26 | A5 | B26 | NC | C26 | A12 |
| A27 | A4 | B27 | NC | C27 | A11 |
| A28 | A3 | B28 | NC | C28 | A10 |
| A29 | A2 | B29 | NC | C29 | A9 |
| A30 | A1 | B30 | NC | C30 | A8 |
| A31 | -15VDC | B31 | NC | C31 | +15VDC |
| A32 | VCC | B32 | VCC | C32 | VCC |

| Table 5-1. Electrical Connector Types and Pinouts (Continued) |
| --- |
| P2 – VME Connector Assignments |
| A1 | GND | B1 | VCC | C1 | GND |
| A2 | NC | B2 | GND | C2 | NEB1_Bus_Current |
| A3 | NC | B3 | NC | C3 | IDPU_HTR_Bus_Current |
| A4 | NC | B4 | NC | C4 | NEB2_Bus_Current |
| A5 | NC | B5 | NC | C5 | IDPU_Current |
| A6 | NC | B6 | NC | C6 | Cryocooler_Current |
| A7 | NC | B7 | NC | C7 | IDPU_SW+28_Current |
| A8 | NC | B8 | NC | C8 | NC |
| A9 | NC | B9 | NC | C9 | NC |
| A10 | ESB_CURRENT | B10 | NC | C10 | NC |
| A11 | NC | B11 | NC | C11 | NC |
| A12 | GND | B12 | GND | C12 | GND |
| A13 | HCD01 | B13 | VCC | C13 | CPU_+5V |
| A14 | HCD02 | B14 | NC | C14 | NC |
| A15 | HCD03 | B15 | NC | C15 | NC |
| A16 | NC | B16 | NC | C16 | NC |
| A17 | NC | B17 | NC | C17 | NC |
| A18 | NC | B18 | NC | C18 | NC |
| A19 | NC | B19 | NC | C19 | NC |
| A20 | NC | B20 | NC | C20 | NC |
| A21 | NC | B21 | NC | C21 | NC |
| A22 | HCD10 | B22 | GND | C22 | NC |
| A23 | HCD11 | B23 | NC | C23 | NC |
| A24 | NC | B24 | NC | C24 | NC |
| A25 | 1 HZ | B25 | NC | C25 | WDOG |
| A26 | GND | B26 | NC | C26 | GND |
| A27 | NC | B27 | NC | C27 | NC |
| A28 | NC | B28 | NC | C28 | GND |
| A29 | NC | B29 | NC | C29 | STAT_IDPU_Bus |
| A30 | CPU_PWR_STATUS | B30 | NC | C30 | NC |
| A31 | Undervoltage_Trip_Status | B31 | GND | C31 | NC |
| A32 | Overcurrent_Trip_Status | B32 | VCC | C32 | NC |

## 5.2 Physical Characteristics

Envelope and mass, shall be as shown on Spectrum Astro Inc. Drawing CID-209810, Component Definition, PCB.

# 6.  Power

## 6.1 Operating Voltage

The PCB shall operate nominally with the voltage inputs given in Table 6-1:

- 6-1.  Bus Voltage Acceptable Limits

| Voltage Bus | Min | Max | Predicted Nominal Current Draw | Maximum Allowed Current Draw (Excluding Outputs) |
| --- | --- | --- | --- | --- |
| 28V | 24.0V | 34.0V | .234A | .3 A |
| +5V | 4.75V | 5.25V | .384 | .5A |
| +15V | 13.8V | 16.2V | .026 | .1A |
| -15V | -16.2V | -13.8V | .0129 | .10A |

### 6.1.2 Survival Voltage

The PCB shall survive voltage inputs of 16V - 40V on the 28V input, with no degradation in performance.

### 6.1.3 Power Interrupt

The PCB board shall be able to operate with power interruptions less than 10 msec in duration.  Should the +5V or ± 15V supplies drop out of specification for less than 10 msec, PCB operation, including switch states, shall be unaltered.

### 6.1.4 Thermal Characteristics

The PCB shall not dissipate more than 15 W.

## 6.2 Bonding

Mechanical mounting interfaces shall be electrically isolated from all PCB board signals by a resistance of at least 1 M(.

# 7.  Environmental Conditions

## 7.1 Temperature

### 7.1.1 Operating

The PCB Board shall be cooled by conduction through the wedge lock clamps at the short edges of the PCB board.  The temperature of the HESSI VME rack at the wedge lock interface will be –24 °C to +61°C.

### 7.1.2 Non Operating

The PCB board shall be designed to withstand a non-operating temperature range from -34(C to + 71(C.

### 7.1.3 Storage

The PCB board shall be designed to withstand a storage temperature range from -34(C to + 71(C.

### 7.1.4 Pressure Decay/Venting

Not applicable.

### 7.1.5 Random Vibration

The PCB board is designed to withstand the qualification random vibration levels as described in Section 7.6 and listed in Figure 7-3 and Table 7-2 of the Component Verification Specification.

### 7.1.6 Acceleration

The PCB board is designed to withstand acceleration levels described in Section 7.2 of the Component Verification Specification.

### 7.1.7 Pyrotechnic Shock

The PCB board is designed to withstand the pyrotechnic shock levels given in Section 7.8, Table 7-4, and Figure 7-5 of the Component Verification Specification.

# Comments

Recheck all these numbers.  The changes were extensive.