|  | SPECTRUM ASTRO, INC. high energy solar spectroscopic imager (hessi) PROGRAM PRODUCT FUNCTION SPECIFICATION DIGITAL SUN SENSOR contract no. ppb005884 |  |
| --- | --- | --- |
| SPECTRUM ASTRO PROPRIETARY DOCUMENT |
| THIS DOCUMENT CONTAINS SPECTRUM ASTRO PROPRIETARY INFORMATION. RECIPIENT, BY ACCEPTING THIS DOCUMENT, AGREES THAT NEITHER THE DOCUMENT NOR ANY INFORMATION CONTAINED WITHIN IT SHALL BE REPRODUCED OR TRANSFERRED TO OTHER DOCUMENTS NOR USED OR DISCLOSED TO OTHERS FOR MANUFACTURING OR ANY OTHER PURPOSES EXCEPT AS SPECIFICALLY AUTHORIZED IN WRITING BY SPECTRUM ASTRO. |
| PREPARED BY: |
| SPECTRUM ASTRO, INC. |
| 1440 N. Fiesta Boulevard |
| Gilbert, Arizona 85233 |
| CAGE Code 0T9D1 |
| initial release date |
| 11 SEPTEMBER 1998 |
| 1110-EW-T10163 | rev - |
| 11 SEPTEMBER 1998 |

1110-EW-T10163

|  | SPECTRUM ASTRO, INC. high energy solar spectroscopic imager (hessi) Program PRODUCT FUNCTION SPECIFICATION DIGITAL SUN SENSOR contract no. ppb005884 |  |
| --- | --- | --- |

| APPROVED BY: |  |  |
| --- | --- | --- |
|  |  | DATE |
| reviewED BY: |  |  |
|  | configURATION/data control, dave maiden | DATE |
| APPROVED BY: |  |  |
|  | SUBCONTRACT MGT., donna greenwood | DATE |
| APPROVED BY: |  |  |
|  | QUALITY ASSURANCE, JEFF SQUIRes | DATE |
| APPROVED BY: |  |  |
|  | ENGINEERING, glenn creamer | DATE |
| APPROVED BY: |  |  |
|  | SYSTEM ENGINEERING, JOhn JORDAN | DATE |
| APPROVED BY: |  |  |
|  | PROGRAM MANAGER, jEFF PREble | DATE |

| REVISION SUMMARY |  |  |  |
| --- | --- | --- | --- |
| REV | RELEASE DATE | BRIEF DESCRIPTION/REASON FOR CHANGE | EFFECTIVE PAGES |
| - | 11 September 1998 | Initial release | All |

TABLE OF CONTENTS

PAGE

1.  SCOPE	1

1.1 Scope	1

1.2 Classification	1

2.  APPLICABLE DOCUMENTS	1

2.1 Documents	1

2.2 Precedence	1

3.0  REQUIREMENTS	2

3.1 Item Definition	2

3.1.1 Physical Description	2

3.1.2 References	2

3.1.2.1 Coordinate System	2

3.1.2.2 Optical Reference	3

3.1.3 Interfaces	3

3.1.3.1 Physical Interfaces	3

3.1.3.1.1 Envelope and Mounting Configuration	3

3.1.3.1.2 Stray Light Keep-out Zone	3

3.1.3.1.3 Thermal Interface	3

3.1.3.2 Connectors and Pin Assignments	3

3.1.3.3 Electrical Interfaces	6

3.1.3.3.1 Electrical Power Interface	6

3.1.3.3.1.1 Power Source Definition	6

3.1.3.3.1.1.1 Source Impedance	6

3.1.3.3.1.1.2 Main Bus Ripple	7

3.1.3.3.1.1.3 Main Bus Transient Response	7

3.1.3.3.1.1.4 Power Control	7

3.1.3.3.1.1.5 Voltage Definition	7

TABLE OF CONTENTS (CONTINUED)

PAGE

3.1.3.3.1.1.6 Electrical Ground Interface	7

3.1.3.3.1.2 Load Description	7

3.1.3.3.1.2.1 Power Consumption	7

3.1.3.3.1.2.2 Inrush Current	7

3.1.3.3.1.2.3 Power Interruption	7

3.1.3.3.1.2.4 Reverse Polarity	7

3.1.3.3.1.2.5 Warm-up Time	7

3.1.3.3.1.2.6 Load Power Quality	8

3.1.3.3.1.2.6.1 Ripple Voltage	8

3.1.3.3.1.2.6.2 Over and Under Voltage	8

3.1.3.3.2 Command and Data Interface	8

3.1.3.3.2.1 Command Interface	8

3.1.3.3.2.2 Data Interface	8

3.1.3.3.2.2.1 Sensor	8

3.1.3.3.2.2.1.1 Solar Aspect Data	8

3.1.3.3.2.2.2 Electronics	9

3.1.3.3.2.2.2.1 Input Signals	9

3.1.3.3.2.2.2.2 Sun Presence Output	9

3.1.3.3.2.2.2.3 Angle Data Read-Out	10

3.1.3.3.2.2.2.4 DSS State-of-Health Data	11

3.2  Characteristics	11

3.2.1 Performance Characteristics	11

3.2.1.1 Field-of-View	11

3.2.1.2 Resolution	11

3.2.1.3 Accuracy	11

3.2.2 Physical Characteristics	12

TABLE OF CONTENTS (CONTINUED)

PAGE

3.2.2.1 Mass Properties	12

3.2.2.2 Physical Dimensions	12

3.2.3 Reliability	12

3.2.4 Environmental Conditions	12

3.2.5 Transportability	12

3.3 Design and Construction	12

3.3.1 Electromagnetic Radiation	12

3.3.2 Safety	12

3.3.3 Life Requirements	12

4.0  QUALITY ASSURANCE PROVISIONS	12

5.  PREPARATION FOR DELIVERY	13

5.1 Packaging, Preservation, and Shipping	13

5.2 Special Handling	13

5.3 Marking for Shipment	13

LIST OF FIGURES

Figure 3-1.  Sensor Coordinate System	2

Figure 3-2.  Clock and Enable Input Circuit	9

Figure 3-3.  Sun Presence and Serial Data Output Circuit	10

Figure 3-4.  Serial Data Readout Timing	10

Figure 3-5.  Analog Data Output Circuit	11

LIST OF TABLES

Table	3-1.  Connector Identification	3

Table	3-2.  Sensor Head Pin Functions	3

Table	3-3.  Sensor Electronics Pin Functions (J1)	4

Table	3-4.  Sensor Electronics Pin Functions (J2)	5

LIST OF ACRONYMS

| AU | Astronomical Unit |
| --- | --- |
| ARO | After Receipt of Order |
| CSS | Coarse Sun Sensor |
| CVS | Component Verification Specification |
| DSS | Digital Sun Sensor |
| EEE | Electrical, Electronic qnd Electromechanical |
| HESSI | High Energy Solar Spectroscopic Imager |
| ICD | Interface Control Document |
| PFS | Product Function Specification |
| QA | Quality Assurance |
| SDRL | Subcontractor Data Requirements List |
| SOW | Statement Of Work |
| TIM | Technical Interchange Meeting |

# 1.  SCOPE

## 1.1 Scope

This specification establishes the design, manufacturing, test, and performance requirements for a Two-Axis Digital Sun Sensor, consisting of a single sensor head and an electronics assembly, for use on the High Energy Solar Spectroscopic Imager Program (HESSI).  Hereinafter, the Two-Axis Digital Sun Sensor shall be referred to as the DSS or unit.

This unit will be used as the primary solar aspect sensor in the HESSI Attitude Determination and Control System.  The HESSI instrument also includes a Solar Aspect Sensor which will be used to establish the initial boresight co-alignment with the DSS, and will subsequently be used as a contingency sensor.

This specification is designed to be used in conjunction with a lower level specification, the Component Verification Specification.  The specification is proprietary to Spectrum Astro, Inc.

## 1.2 Classification

This document is UNCLASSIFIED.

# 2.  APPLICABLE DOCUMENTS

## 2.1 Documents

The following documents, of the current issue in effect, form a part of this specification to the extent specified herein.  In the event of conflict between the documents listed below and the contents of this specification, the contents of this specification shall be a superseding requirement.  The version of the documents applies unless otherwise specified.

a	1110-EW-Y09781	Component Verification Specification

b.	1110-EZ-R10161 	Statement of Work – Digital Sun Sensor and Coarse Sun Sensors

## 2.2 Precedence

The order of precedence for documentation under this contract shall be as follows:

a. 	Statement of Work (SOW)

b.	Product Function Specification (PFS)

c.	Configuration Interface Definition Drawing (CID), if included

d. 	Component Verification Specification (CVS)

e.	Other referenced standards or specifications

f.	Reference guidance documents

g. 	Best commercial practice

In case of inconsistencies within this specification, please notify Spectrum Astro, Inc prior to taking action.

# 3.0  REQUIREMENTS

## 3.1 Item Definition

The DSS will be used as the primary solar aspect sensor in the HESSI Attitude Determination and Control System.  The HESSI instrument also carries a Solar Aspect Sensor which will be used to establish the initial boresight co-alignment with the DSS, and will subsequently be used as a contingency sensor.

The DSS, consisting of a single sensor head and the associated electronics, is used to measure direct sun pointing error for the HESSI solar inertial, magnetic control system.  The sensor and associated electronics shall provide conditioned data from which the sun pointing error can be deduced.  The sensor shall be capable of generating two-axis sun pointing error data, in the prescribed format, over the field-of-view, and with data accuracy as prescribed in paragraphs herein.  The sensor shall also generate a bi-level signal to indicate sun presence in the field-of-view.

### 3.1.1 Physical Description

The DSS shall consist of a single sensor head and the associated electronics box to provide solar aspect data for space vehicle sun pointing error determination.

### 3.1.2 References

### 3.1.2.1 Coordinate System

The coordinate system used for the sensor head shall be a right-hand orthogonal system, as illustrated in Figure  3-1.

Figure 3-1.  Sensor Coordinate System

### 3.1.2.2 Optical Reference

The sensor coordinate system shall be related to the spacecraft reference system through the use of an optical reference surface which shall be installed on the sensor head.  The angular errors between the sensor frame and the optical reference surfaces shall be known to < 0.03 degrees per axis.

### 3.1.3 Interfaces

### 3.1.3.1 Physical Interfaces

### 3.1.3.1.1 Envelope and Mounting Configuration

The mounting interfaces of the sensor and electronics shall be planar surfaces.  The normal to the planar mounting surface of the sensor shall be used as one of the mechanical coordinate frame axes.

### 3.1.3.1.2 Stray Light Keep-out Zone

The stray light field-of-view, or the region beyond which the stray light cannot degrade sensor performance, shall be no greater than +/-85 degrees relative to the sensor boresight, in each of the two measurement axes.  Usable field of view shall be per Section 3.2.1.1.  Stray light baffles are not required for the sensor head.

### 3.1.3.1.3 Thermal Interface

The HESSI spacecraft will operate in a 600 km, 38 degree inclined orbit, and will experience up to 35-minute eclipses on every orbit for the duration of the mission.  Both the sun sensor and the electronics will be mounted on the sun facing side of the HESSI spacecraft with the electronics covered by thermal blankets.  Therefore, heat generated internal to the sensor electronics shall be conducted directly through the baseplate.

### 3.1.3.2 Connectors and Pin Assignments

The unit’s sensor head connector and sensor electronics connectors shall be as identified in Table 3-1.  The pin assignments are listed in Tables 3-2 through 3-4 for the sensor head connector and the sensor electronics connectors.

The Seller shall supply one set of mating connectors, plus one set of spares, to facilitate rapid wire harness fabrication.  The Seller shall identify any constraints on the sensor-to-electronics cable length, or preferences on the wire type.

Table 3-1.  Connector Identification

| CONNECTOR LOCATION | CONNECTOR DESIGNATOR |
| --- | --- |
| On Sensor Head | MS27499E14F35P |
| On Sensor Electronics (J1) | DBMAM-25P-NMB-A106 |
| On Sensor Electronics (J2) | DCMAM-37P-NMB-A106 |

- 3-2.  Sensor Head Pin Functions

| Pin No. | Function |
| --- | --- |
| 1 | Bit 7CB |
| 2 | Bit 6CB |
| 3 | Bit 4CB |
| 4 | Bit 1FB |
| 5 | Bit 2FB |
| 6 | Bit 4FB |
| 7 | ATA-B |
| 8 | Bit 4FA |
| 9 | Bit 2FA |
| 10 | Bit 4CA |
| 11 | Bit 6CA |
| 12 | Bit 7CA |
| 13 | Bit 8CA |
| 14 | Bit 9CA |
| 15 | Signal Return |
| 16 | Spare |
| 17 | Chassis Gnd |
| 18 | Bit 8CB |
| 19 | Spare |
| 20 | Bit 5CB |
| 21 | Spare |
| 22 | Bit 3FB |
| 23 | Spare |
| 24 | Bit 3FA |
| 25 | Bit 5CA |
| 26 | Spare |
| 27 | Spare |
| 28 | ATA-A |
| 29 | Spare |
| 30 | Spare |
| 31 | Spare |
| 32 | Spare |
| 33 | Spare |
| 34 | Spare |
| 35 | Bit 9CB |
| 36 | Spare |
| 37 | Bit 1FA |

- 3-3.  Sensor Electronics Pin Functions (J1)

| Pin No. | Function |
| --- | --- |
| 1 | Bus Voltage |
| 2 | Spare |
| 3 | Bus Voltage Return |
| 4 | Signal Return |
| 5 | Signal Return |
| 6 | Clock |
| 7 | Spare |
| 8 | Enable Gate |
| 9 | Spare |
| 10 | Spare |
| 11 | Spare |
| 12 | Voltage Monitor |
| 13 | Serial Output |
| 14 | Spare |
| 15 | Spare |
| 16 | Spare |
| 17 | Sun Presence Output |
| 18 | Spare |
| 19 | Spare |
| 20 | Spare |
| 21 | Spare |
| 22 | Sensitivity Control |
| 23 | Sin |
| 24 | Cos |
| 25 | Chassis |

- 3-4.  Sensor Electronics Pin Functions (J2)

| Pin No. | Function |
| --- | --- |
| 1 | Chassis |
| 2 | ATA-A |
| 3 | Bit 1FA |
| 4 | Bit 2FA |
| 5 | Bit 3FA |
| 6 | Bit 4FA |
| 7 | Bit 4CA |
| Table 3-4. Sensor Electronics Pin Functions (J2) (Continued) |
| Pin No. | Function |
| 8 | Bit 5CA |
| 9 | Bit 6CA |
| 10 | Bit 7CA |
| 11 | Bit 8CA |
| 12 | Bit 9CA |
| 13 | ATA-B |
| 14 | Spare |
| 15 | Spare |
| 16 | Spare |
| 17 | Spare |
| 18 | Spare |
| 19 | Chassis |
| 20 | Signal Return |
| 21 | Signal Return |
| 22 | Bit 1FB |
| 23 | Bit 2FB |
| 24 | Bit 3FB |
| 25 | Bit 4FB |
| 26 | Bit 4CB |
| 27 | Bit 5CB |
| 28 | Bit 6CB |
| 29 | Bit 7CB |
| 30 | Bit 8CB |
| 31 | Bit 9CB |
| 32 | Spare |
| 33 | ??? |
| 34 | Spare |
| 35 | Spare |
| 36 | Spare |
| 37 | Chassis |

### 3.1.3.3 Electrical Interfaces

### 3.1.3.3.1 Electrical Power Interface

### 3.1.3.3.1.1 Power Source Definition

### 3.1.3.3.1.1.1 Source Impedance

The source impedance of the spacecraft power bus shall be 500 ± 250 m.

### 3.1.3.3.1.1.2 Main Bus Ripple

The unit shall be capable of operating in the presence of narrowband ripple on the input power lines as specified in the CS01 and CS02 requirements of MIL-STD-461C, Part 3, for class A2a equipment.

### 3.1.3.3.1.1.3 Main Bus Transient Response

The unit shall be capable of operating in the presence of broadband spikes on the input power lines as specified in the CS05 & CS06 requirement of MIL-STD-461C, Part 3, for class A2a equipment.

### 3.1.3.3.1.1.4 Power Control

N/A

### 3.1.3.3.1.1.5 Voltage Definition

The unit shall have the capability to meet the performance requirements of this specification when operating from a nominal 28 Volt Direct Current (VDC) power source.  Under steady state conditions, the voltage shall range from 22 VDC to 34 VDC.

### 3.1.3.3.1.1.6 Electrical Ground Interface

The unit shall be compatible with a single-point system ground power distribution concept.  Power returns shall be provided through the connectors and shall be isolated from the chassis of the unit by a minimum of 1 M.

### 3.1.3.3.1.2 Load Description

The unit electronics shall operate in a voltage range of 28 ± 6 V.  The unit electronics power shall be directly switchable by the user.

### 3.1.3.3.1.2.1 Power Consumption

The steady-state power consumption shall not exceed 2.8 W over the operating voltage range specified in Section 3.1.3.3.1.1.5.

### 3.1.3.3.1.2.2 Inrush Current

Inrush current at 28 VDC shall not exceed 1.5 amps for 5 microseconds and shall be at its steady state value within 20 milliseconds.

### 3.1.3.3.1.2.3 Power Interruption

The unit shall continue to operate after a power interruption of up to 8 milliseconds.  Power interruptions longer than 8 milliseconds shall not damage the unit.

### 3.1.3.3.1.2.4 Reverse Polarity

The unit shall not be damaged by a reversal of input voltage on the primary power and return lines.

### 3.1.3.3.1.2.5 Warm-up Time

The Sun Sensor Electronics shall be fully operational within 2 seconds after power has been applied.

### 3.1.3.3.1.2.6 Load Power Quality

### 3.1.3.3.1.2.6.1 Ripple Voltage

The ripple induced on the main power bus due to operation of the unit shall conform to the CE01 and CE03 requirements of MIL-STD-461C, Part 3, for class A2a equipment.

### 3.1.3.3.1.2.6.2 Over and Under Voltage

The unit shall not be damaged by input voltages below 22 VDC on the primary power line.  The unit shall not be required to perform to the requirements of this specification during the undervoltage condition.  The unit shall not be damaged by the continuous application of 35 VDC.

### 3.1.3.3.2 Command and Data Interface

### 3.1.3.3.2.1 Command Interface

The unit shall become operational upon application of power.  No commands shall be required.

### 3.1.3.3.2.2 Data Interface

### 3.1.3.3.2.2.1 Sensor

### 3.1.3.3.2.2.1.1 Solar Aspect Data

When the sun is in the sensor field of view, the DSS shall generate two-axis of solar aspect data from which the sun pointing errors in the spinning sensor reference frame can be deduced.  The solar aspect data for each axis shall be provided through a combination of a 6-bit Gray coded coarse angle plus axis ID bit on the digital interface and a simultaneous analog signal pair for the same axis on the A/D interface.  Transfer functions for combining the 10 bit digital output word and the fine angle analog signals for each axis into an overall sun angle shall be as follows (see Figure 3-1 for sensor axis definitions):

 - o =  tan-1 [1.4553 X / [0.202644 - 1.17898(X2-Y2)] 1/2]

 - o =  tan-1 [1.4553 Y / [0.202644 - 1.17898(X2-Y2)] 1/2]

where:

X = 0.011 NX - 0.176,

Y = 0.011 NY - 0.176

NX and NY are derived from the Gray coded angle, NG, and analog data, Vsin and Vcos,  from the respective axis according to:

N = NC + NF 			    0  < N < 32

where:

NF = (1/2) tan-1 [Vsin / Vcos],	    0 < NF < 1

NC  = ½ [ NG + 1 ]		    if   NF < 0.25

= ½ [ NG - 1 ] 		    if   NF > 0.75

= ½ NG			    elsewhere

NG = Base 10 equivalent of the 6 bit Gray code output

### 3.1.3.3.2.2.2 Electronics

### 3.1.3.3.2.2.2.1 Input Signals

The DSS electronics shall accept a burst of 10 cycles at 9600 Hz +10% clock and an enable gate signal from the C&DH processor to initiate the transmittal of digital data for each axis, per Figure 3-2.  The digital data shall be clocked out by the enable gate and 10 clock cycles while the fine angle analog data at the A/D interface shall be valid for the duration of the enable gate.  The analog data axis provided during a particular gate signal shall be identified in the first bit of the digital data.  Separation between sequential enable gates shall be at least 10 ms in length, but this value shall be minimized and fixed to reduce unknown spin coupling between data axes.  The baseline 10 ms separation between axes corresponds to a 0.9 degree coupling of data at the 15 RPM spin rate.

Figure 3-2.  Clock and Enable Input Circuit

### 3.1.3.3.2.2.2.2 Sun Presence Output

The electronics shall generate a logic high indicator of sun presence, which will have a value of 1 when the sun is in the sensor FOV identified in Section 3.2.1.1.   The sun presence indication shall represent the "data good" range of the sensor.  Sun presence and digital data output circuit shall be as shown in Figure 3-3.

Figure 3-3.  Sun Presence and Serial Data Output Circuit

### 3.1.3.3.2.2.2.3 Angle Data Read-Out

When the sun presence output signal is true, the 10-bit digital data word per axis, representing Gray coded  coarse angle data, and the two analog signals per axis, representing fine angle data, shall be available to be read.  As the solar aspect angle changes with spacecraft attitude, each Gray code bit undergoing a binary transition shall be immediately updated in the electronics unit, from which the electronics shall immediately construct the coarse and fine angle data.

The 10-bit digital data word for each axis shall include an axis identification as bit one, zero in bits two through four, and a 6-bit Gray coded coarse angle measurement in bits five through ten - shifted out LSB first.  Data bits shall be shifted out on the falling edge of the clock, per Figure 3-4.  The first data bit shall be stable within 10 sec of the leading edge of the enable gate and the subsequent bits shall be stable within 10 sec of the falling edge of the clock.  The two 10-bit digital data words shall alternate between the  and  sensor axes, with the  axis identified by logic one in the first data bit.

Figure 3-4.  Serial Data Readout Timing

The two fine angle analog signals per axis shall alternate between the  and  sensor axes, along with the digital data words, switching between axes on the falling edge of the enable gate.  During nominal operation of the HESSI mission, the control system will operate mainly from the analog data, within the LSB of the coarse data.  Fine angle data and DSS state of health data analog output circuit shall be as shown in Figure 3-5.

Figure 3-5.  Analog Data Output Circuit

All solar aspect data, including fine analog data, coarse digital data, and the sun presence indicator, shall be read by the flight processor at a baseline rate of 10 Hz.  Based on a minimum of 10 ms between consecutive enable gates and two alternating sensor axes, the DSS electronics can support data readout at up to 50 Hz.

### 3.1.3.3.2.2.2.4 DSS State-of-Health Data

In addition to the sun aspect data, the unit shall output an analog voltage monitor to convey the state of health of the DSS electronics’ internal secondary converter.  This signal shall have a nominal value of 3.5 V and an output impedance of 10k.

## 3.2  Characteristics

### 3.2.1 Performance Characteristics

### 3.2.1.1 Field-of-View

The sensor head shall have a minimum of ±32 x ±32 field of view with respect to the sensor boresight.  The sun-presence field of view, or that region over which the sun presence signal is true (indicated by logic “1”), shall be ±31.50.5 per axis.

### 3.2.1.2 Resolution

The sensor resolution shall be determined by the fine angle analog output data to be better than 0.005° throughout the ±10° field of view.  This resolution is for an assumed 8 bit A/D converter in the data acquisition electronics, and will improve with the resolution of the A/D.  The analog output shall have a ±5 V output range, and an output resistance of less than 1.1 K (see Figure 3-5).

### 3.2.1.3 Accuracy

The sensor head shall have an accuracy of  0.05 in each axis for the region of ±10° per axis relative to the boresight and  0.1 for the remainder of the field of view.

### 3.2.2 Physical Characteristics

### 3.2.2.1 Mass Properties

The weight of the sensor head shall not exceed 0.32 kg.  The weight of the electronics shall not exceed 1.04 kg.

### 3.2.2.2 Physical Dimensions

The maximum dimensions of the unit and mechanical interface shall be 3.8” x 3.8” x 1.4” and 5.5” x 3.6” x 2.5” for the sun sensor and the electronics, respectively.

### 3.2.3 Reliability

Three year reliability prediction of the DSS unit shall be prepared and provided, along with any unique operating recommendations which would improve reliability.  The DSS is critical to the success of the HESSI mission.

### 3.2.4 Environmental Conditions

The unit shall be designed and constructed to meet the requirements of the CVS.  DSS will be utilized in a 600 km circular, 38 degree inclined orbit throughout the 3 year mission life.  The sun sensor will be continuously sun pointed and will experience up to a 35 minute eclipses during each orbit, continuously.

### 3.2.5 Transportability

Protective packing and packaging shall be provided to withstand environmental conditions associated with shipping, storage, and handling.

### 3.3 Design and Construction

The design and construction of the unit shall be in accordance with this specification, the unit envelope drawing and all drawings assembled thereunder, and the CVS.

### 3.3.1 Electromagnetic Radiation

The design of the unit shall conform to MIL-STD-461C, Part 3, for class A2a equipment, Methods CE01, CE03, CE06, CE07, CS01, CS02, CS03, CS04, CS05, CS06, RE01, RE02, RS02, and RS03 when tested in accordance with MIL-STD-462.

### 3.3.2 Safety

The unit shall be so designed that when stored, transported, or operated in accordance with applicable procedures, it will not cause damage to itself or to other equipment or cause injury to personnel.

### 3.3.3 Life Requirements

The unit shall be capable of the specified performance under continuous operation for a three year minimum flight duration.

# 4.0  QUALITY ASSURANCE PROVISIONS

The requirements of Section 3 shall be verified by a combination of analysis, inspection, demonstration, and tests in accordance with the provisions of the CVS.

# 5.  PREPARATION FOR DELIVERY

## 5.1 Packaging, Preservation, and Shipping

Preservation, packaging, and container design shall be accomplished in a manner which will protect the unit against damage during shipment.

## 5.2 Special Handling

If any component requires special attention during receiving inspection, installation and operation, or if non-obvious characteristics require a component to be given special handling, written notification shall be provided at delivery and a removable instruction tag attached if necessary.  Components shall be hand carried by Adcole to  to Spectrum Astro, Inc.’s facility.

## 5.3 Marking for Shipment

The following data shall be identifiable on the packing container used for shipment:

a.	Item Nomenclature

b.	Spectrum Astro, Inc. Part Number

c.	Contract Number

d.	Supplier Name

e.	Supplier Part Number and Serial Number

f.	Fragile - Handle with Care - Flight Hardware

g.	ESD Sensitive Item

- Special Handling Requirements