|  | SPECTRUM ASTRO, INC. high energy Solar spectroscopic imager (hessi) PROGRAM COMPONENT VERIFICATION SPECIFICATION (cvs) contract no. TBD |  |
| --- | --- | --- |
| SPECTRUM ASTRO PROPRIETARY DOCUMENT |
| THIS DOCUMENT CONTAINS SPECTRUM ASTRO PROPRIETARY INFORMATION. RECIPIENT, BY ACCEPTING THIS DOCUMENT, AGREES THAT NEITHER THE DOCUMENT NOR ANY INFORMATION CONTAINED WITHIN IT SHALL BE REPRODUCED OR TRANSFERRED TO OTHER DOCUMENTS NOR USED OR DISCLOSED TO OTHERS FOR MANUFACTURING OR ANY OTHER PURPOSES EXCEPT AS SPECIFICALLY AUTHORIZED IN WRITING BY SPECTRUM ASTRO. |
| PREPARED BY: |
| SPECTRUM ASTRO, INC. |
| 1440 N. Fiesta Boulevard |
| Gilbert, Arizona 85233 |
| CAGE Code 0T9D1 |
| INITIAL RELEASE DATE |
| 29 APRIL 1998 |

| 1110-EW-Y09781 | REV - |
| --- | --- |
| 29 APRIL 1998 |

1110-EW-Y09781

|  | SPECTRUM ASTRO, INC. high energy Solar spectroscopic imager (hessi) PROGRAM COMPONENT VERIFICATION SPECIFICATION contract no. TBD |  |
| --- | --- | --- |

| reviewed BY: |  |  |
| --- | --- | --- |
|  | CONFIGURATION/DATA CONTROL, dAVE mAIDEN | DATE |
| APPROVED BY: |  |  |
|  | SUBCONTRACT mgT, donna greenwood | DATE |
| APPROVED BY: |  |  |
|  | QUALITY ASSURANCE, dON hENRIQUES | DATE |
| prepared BY: |  |  |
|  | sYSTEM ENGINEERING, JOHN JORDAN | DATE |
| APPROVED BY: |  |  |
|  | pROGRAM mANAGEMENT, JEFF PREBLE | DATE |

| REVISION SUMMARY |  |  |  |
| --- | --- | --- | --- |
| REV | RELEASE DATE | BRIEF DESCRIPTION/REASON FOR CHANGE | EFFECTIVE PAGES |
| - | 29 April 1998 | Initial release. | All |

TABLE OF CONTENTS

PAGE

1.  INTRODUCTION

1.1 Scope

1.2 Definitions

2.  APPLICABLE DOCUMENTS

2.1 General

2.2 Specifications, Standards and Handbooks

3.  PARTS, MATERIALS, AND PROCESSES

3.1 General

3.1.1 Parts, Materials, and Processes List.

3.1.2 Limited Shelf Life Materials

3.1.3 Raw Materials

3.1.4 Printed Wiring Boards

3.1.5 Traceability

3.1.6 Venting and Outgassing

3.2 Mechanical Parts Selection

3.2.1 Prohibited Materials

3.3 Electronic Parts Control

3.3.1 EEE Parts Selection

3.3.1.1 Commercial Parts

4.  RELIABILITY

4.1 General

4.2 Mean Time Between Failure

4.3 Power Supply Transient Measurement

4.4 Stress Analysis

4.5 Single Event Effects

4.6 Parts Radiation Requirements

TABLE OF CONTENTS (CONTINUED)

PAGE

4.7 Government-Industry Data Exchange Program Alerts

4.8 Failure Reporting, Failure Analysis and Corrective Action

4.8.1 Parts Failure Analysis

4.9 Control of Static Sensitive Parts, Assemblies and Components

5.  QUALITY ASSURANCE

5.1 General

5.2 Government/Customer Surveillance

5.3 Control of Procurement Sources

5.4 Identification, Handling and Storage

5.5 Configuration Control

5.5.1 Drawing and Change Control

5.6 Inspections and Tests

5.6.1 Retest

5.7 Indication of Inspection Status

5.8 Process Control

5.9 Nonconforming Material Control and Corrective Action

5.10 Workmanship and Soldering

5.11 Preservation, Packaging, Packing and Shipping

5.12 Acceptance Data Package

6.  SAFETY

6.1 General

6.2 Hazard Identification

6.3 Hazardous Materials

7.  TEST REQUIREMENTS

7.1 General

7.2 Test Procedures and Levels

TABLE OF CONTENTS (CONTINUED)

PAGE

7.2.1 Protoflight Qualification Testing

7.2.2 Acceptance Testing

7.3 Test Application

7.4 Functional Test

7.5 Safety Margins

7.6 Random Vibration

7.7 Acoustic Test

7.8 Shock Test

7.9 Pressure Decay/Venting

7.10 Pressure Test

7.11 Leak Detection Test.

7.12 Burn-in

7.13 Thermal Tests

7.13.1 Thermal Cycling

7.13.2 Thermal Vacuum

7.14 Electromagnetic Compatibility Testing

7.14.1 Electromagnetic Compatibility

7.14.2 RF Radiated Emissions

7.14.3 RF Radiated Susceptibility

7.14.4 Conducted Emissions

7.14.5 Conducted Susceptibility

7.14.6 Electrostatic Discharge

7.14.7 Bonding

8.  SOFTWARE ASSURANCE

8.1 General

8.2 Development

TABLE OF CONTENTS (CONTINUED)

PAGE

8.3 Configuration and Change Control

8.4 Problem/Failure Reporting and Analysis

9.  GROUND SUPPORT EQUIPMENT

9.1 General

9.2 Software

9.2.1 GSE Acceptance Data Package

LIST OF FIGURES

Figure 7-1.  Suggested Test Sequence

Figure 7-2.  Mass Acceleration Curve (Single Axis, Worst Case Direction)

Figure 7-3.  Random Vibration Profile

Figure 7-4.  Acoustic Spectrum Profile

Figure 7-5.  Shock Environment Profile

Figure 7-6.  Ascent Pressure Profile

Figure 7-7.  Thermal Cycling and Thermal Vacuum Profile

LIST OF TABLES

Table 4-1.  Total Ionizing Radiation Dose vs. Aluminum Shield Thickness

Table 7-1.  Test Requirements Matrix

Table 7-2.  Random Vibration Levels

Table 7-3.  Acoustic Spectrum Levels

Table 7-4.  Shock Response Levels

Table 7-5.  Pressure Decay Profile

Table 7-6.  Thermal Cycling And Thermal Vacuum Test Temperatures

Table 7-7.  HESSI RF Transmit And Receive Frequencies

LIST OF ACRONYMS

| ADP | Acceptance Data Package |
| --- | --- |
| C of C | Certificate of Conformance |
| CVS | Component Verification Specification |
| EEE | Electrical, Electronic, and Electromechanical |
| EMC | Electromagnetic Compatibility |
| EMI | Electromagnetic Interference |
| ESD | Electrostatic Discharge |
| GIDEP | Government-Industry Data Exchange Program |
| GSE | Ground Support Equipment |
| HESSI | High Energy Solar Spectroscopic Imager |
| MSDS | Material Safety Data Sheet |
| MTBF | Mean Time Between Failure |
| NASA | National Aeronautics and Space Administration |
| PFR | Problem Failure Report |
| PFS | Product Function Specification |
| PWB | Printed Wiring Board |
| QA | Quality Assurance |
| RDE | Responsible Design Engineer |
| RF | Radio Frequency |
| SDP | Software Development Plan |
| SEE | Single Event Effects |
| SOW | Statement of Work |
| VDD | Version Description Document |

# 1.  INTRODUCTION

## 1.1 Scope

This specification establishes the requirements applicable to the design, construction, reliability, quality assurance, safety and environmental test provisions for flight spacecraft components to be used on the High Energy Solar Spectroscopic Imager (HESSI) mission.  This specification is intended for use with a Statement of Work (SOW) and/or a Product Function Specification (PFS) which identifies the detailed requirements for the product. Changes to this document shall be controlled by Spectrum Astro, Inc. The supplier should provide any cost effective approaches which are consistent with the minimum standards imposed by this specification.  It is recommended that the supplier use existing documentation whenever possible.

## 1.2 Definitions

a.	Abbreviated Functional Test:  A shortened version of the baseline functional test.  It is a series of test operations that exercise the critical functional performance parameters of the component under test.  This test is designed to verify that a component is operating in accordance with established performance parameters.  The abbreviated functional test will be described specifically in the functional test procedure for each component.

b.	Component:  Generally, a component is a functional subdivision of a subsystem and a self-contained deliverable item.  A component may be a subassembly (circuit card), unit (i.e., a "black box") or subsystem, depending on complexity.

c.	Functional Test:  Functional test is a series of test operations that exercise the critical functional performance parameters of the test item.

d.	Product Function Specification:  A specification that describes the functional and physical requirements for component or subassembly.  The PFS is a statement of functional requirements for performance, design, configuration, and test requirements.  The PFS provides the basis for technical and engineering management control.

e.	Temperature Stabilization:  The condition that exists when the rate of change of temperatures has decreased to the point where the test item may be expected to remain within the specified test tolerance for the necessary duration or where further change is considered acceptable.

f.	Test Failure:  A departure from specification that is discovered during protoflight or acceptance testing.

# 2.  APPLICABLE DOCUMENTS

## 2.1 General

Unless otherwise specified, the following documents form a part of this specification to the extent specified herein.  Documents that are not specified in this document shall be used as guidance documents.  If a specific issue of a document is not called out, then the latest issue at the date of contract shall apply.  In the event of a conflict between this specification and other referenced documents, the following order of precedence shall apply:

a.	Statement of Work

b.	Product Function Specification

c.	Component Verification Specification

## 2.2 Specifications, Standards and Handbooks

a.	MIL-STD-275	Printed Wiring for Electronic Equipment

b.	MIL-STD-461D	Electromagnetic Emission and Susceptibility Requirements for the Control of Electromagnetic Interference

c.	MIL-STD-462D	Measurement of Electromagnetic Interference Characteristics

d.	MIL-STD-975	NASA Standard Electrical, Electronic and Electromechanical Parts

e.	MIL-STD-1522	Standard General Requirements for Safe Design and Operation of Pressurized Missile and Space Systems

f.	MIL-STD-1541	Electromagnetic Compatibility Requirements for Space Systems

g.	MIL-STD-1686A	Electrostatic Discharge Control Program

h.	MIL-STD-2000	Standard Requirements for Soldered Electrical and Electronic Assemblies

i.	MIL-HDBK-217	Reliability and Stress and Failure Rate Data for Electronic Equipment

j.	MIL-PRF-38534	Hybrid Microcircuits

k.	MIL-PRF-38535	General Specification for Integrated Circuits Manufacturing

l.	MIL-P-55110E	General Specifications for Printed Wiring

m.	MIL-S-19500	General Specification for Semiconductor Devices

n.	NHB5300.4 (3A-2)	Requirements for Soldered Electrical Connections

o.	EWR 127-1	East and West Range Safety Requirements

# 3.  PARTS, MATERIALS, AND PROCESSES

## 3.1 General

Parts and materials shall be chosen from experience on previous space hardware, whenever possible.  Selection of parts and materials shall emphasize proven performance, minimum contamination potential and suitability for 2 year storage and 3 year lifetime.  Materials will be procured from qualified suppliers and shall be inspected to assure that they meet the applicable specifications in this document.  Parts and materials used in space flight hardware should be qualified for flight use whenever possible.

### 3.1.1 Parts, Materials, and Processes List.

The supplier shall prepare and maintain an "As-Built" parts list for all assemblies and components.  This parts list shall include all parts and materials, by generic part number and manufacturer, used in space flight hardware.  The "As-Built" parts list shall be maintained for all deliverable flight hardware.  The "As-Built" lists shall be maintained on file by the supplier and delivered as part of the Acceptance Data Package.

### 3.1.2 Limited Shelf Life Materials

The supplier shall mark all limited life materials that degrade with age to indicate the date critical life was initiated and when it will be expended.  Expired material shall not be used.

### 3.1.3 Raw Materials

Purchased raw materials used in deliverable hardware shall be tested to verify conformance to applicable specifications.  Manufacturer's test reports are acceptable.  Test reports shall be traceable to the material tested.  The supplier shall maintain the reports on file for Spectrum Astro, Inc. review upon request.

### 3.1.4 Printed Wiring Boards

Printed Wiring Boards (PWBs) used in the manufacture of deliverable hardware shall be designed to the requirements of MIL-STD-275 and fabricated to MIL-P-55110.

### 3.1.5 Traceability

All parts and materials shall be identified and shall be traceable to a specific manufacturer lot number or lot date code.  Certification of conformance from the manufacturer is required for all procured parts.  Lot date code limitations for electrical, electronic and electromechanical parts will be 5 years.

### 3.1.6 Venting and Outgassing

Parts, materials, devices and components shall be capable of operating in a vacuum for the lifetime of the program, and adequately accommodate pressure differentials and/or venting rates generated during the launch and ascent to orbit.  Materials selected shall have a total mass loss of less than 1% and a collected volatile condensable of less than 0.1% when heated in a vacuum to 105C and collected at 23C.  Materials not meeting this requirement may be baked out in a thermal vacuum chamber to achieve the desired limits upon approval by Spectrum Astro, Inc.

## 3.2 Mechanical Parts Selection

Mechanical parts shall be based on similar applications on prior space flight programs whenever possible.  Selection shall emphasize proven performance, minimum contamination potential and suitability for the expected life of each component as stated in the Product Function Specification.  Major factors such as outgassing, flammability, aging, stability, corrosion, and electrical properties of materials shall be considered.  New design mechanical parts shall be analyzed and/or tested to ensure adequate performance.

### 3.2.1 Prohibited Materials

The following materials shall not be used:

a.	Cadmium, magnesium, zinc or selenium, except internal to hermetically sealed devices.

b.	Unalloyed tin.

c.	Corrosive solder fluxes, unless detailed cleaning procedures are specified, along with appropriate verification methods to insure removal of residual contaminants.

d.	Mercury and compounds of mercury.

e.	Materials that exhibit or are known to exhibit natural radioactivity such as uranium, potassium, radium, thorium, and/or any alloys thereof.

f.	Dissimilar metals shall not to be used in conjunction with each other.

## 3.3 Electronic Parts Control

Control of Electrical, Electronic and Electromechanical (EEE) parts used on deliverable flight hardware shall be governed by the requirements of this document and the applicable supplier's procedures.  The supplier's procedures shall be available for Spectrum Astro, Inc. review.  Suppliers are encouraged to use the highest level of parts that are available (i.e., that will not significantly increase cost or schedule).

### 3.3.1 EEE Parts Selection

EEE parts shall be selected from MIL-S-19500, QPL JANTXV for discretes, or MIL-PRF-38535, Class Q for microcircuits, as a minimum.  Passive parts shall be selected from MIL-STD-975 with a failure rate level of R or S.  Custom microcircuits shall meet the requirements of MIL-PRF-38534 and MIL-PRF-38535, QML (as applicable).  EEE parts meeting the requirements of MIL-S-19500, QPL JANTXV, MIL-PRF-38534 and MIL-PRF-38535, QML (as applicable), and/or MIL-STD-975 are considered qualified.

### 3.3.1.1 Commercial Parts

Commercial parts shall be up screened to meet the applicable military specification as necessary to ensure mission success.  In the event that the parts selected do not meet the requirements of Section 3.3.1, the supplier shall obtain Spectrum Astro, Inc. approval prior to installation of the parts.  The approval request shall include a complete description of the part, the reason for the request, the part application, the technical justification for use and the criteria that is used to ensure that the commercial part is acceptable for flight use.  The approval request shall be reviewed and approved by a Spectrum Astro, Inc. Quality Assurance Representative.

# 4.  RELIABILITY

## 4.1 General

Reliability shall be considered during all phases of design, development and fabrication of the flight component. Some of the areas of concern for reliability are: simplicity of design and construction; the use of screened/burned-in parts to the maximum extent feasible; the conservative application of parts within their ratings and within their capabilities; and the use of heat sinks and conductive paths to minimize hot spot temperatures.  Components shall be designed to meet the expected life as stated in Section 3.1.

## 4.2 Mean Time Between Failure

A Mean Time Between Failure (MTBF) calculation of the flight component shall be established using MIL-HDBK-217.  MIL-HDBK-217 may be tailored by the supplier and presented to Spectrum Astro, Inc. for approval.

## 4.3 Power Supply Transient Measurement

Measurements shall be made of all power transient conditions presented to the spacecraft power bus, including ON/OFF transients, in-rush current, component state changes, etc.  These measurements shall be made over the specified voltage range of the component power inputs.  The measurements shall be delivered to Spectrum Astro, Inc. as part of the Acceptance Data Package.

## 4.4 Stress Analysis

Stress analyses shall be performed to verify that the applied stress on each component does not exceed the specified rating for the application.  EEE parts shall be derated in accordance with MIL-STD-975.  The seller shall take appropriate steps to correct any over stressed condition unless specifically approved by Spectrum Astro, Inc.  A summary of each stress analysis performed shall be provided to Spectrum Astro, Inc. prior to acceptance testing.  The supplier shall maintain the stress analyses on file and copies of the stress analyses shall be available to Spectrum Astro, Inc. upon request.

## 4.5 Single Event Effects

Semiconductors susceptible to Single Event Effects (SEE) with an LET level less than 10 MeV/mg-cm2 shall be avoided whenever possible.  Microcircuits shall be single event latchup immune and single event upset tolerant.  Power bipolar transistors shall be evaluated for single event burnout.  Power HEXFET's shall be evaluated for single event gate rupture.  Circuit designs containing SEE sensitive electronic parts shall be analyzed to minimize the effect of SEE and to assure compliance with component level requirements.  Single event upsets shall not cause unrecoverable failure or performance degradation of the flight component. Parts susceptible to single event burnout and gate rupture shall not be used.

## 4.6 Parts Radiation Requirements

Electronic parts shall tolerate twice the expected total dose ionizing radiation environment (RDM = 2).  The expected total dose ionizing radiation environment is 15 krads (Si) for the mission.  Consequently, electronic parts shall tolerate a minimum of 30 krads (Si) when protected with a 30 mil aluminum wall.  Table 4-1 lists the total dose as a function of total equivalent aluminum shielding thickness.  Parts which are spot shielded shall use environmental transport assumptions commensurate with the degree to which the coverage provided by their spot shields is complete.

| Table 4-1. Total Ionizing Radiation Dose vs. Aluminum Shield Thickness |
| --- |
| Effective Shield Thickness (mil Al) | Total Ionizing Dose for 3 Year Mission (krad) | Total Ionizing Dose Design Requirement (krad) |
| 1 | 2224 | 4448 |
| 5 | 726 | 1452 |
| 10 | 268 | 536 |
| 20 | 45 | 90 |
| 30 | 15 | 30 |
| 40 | 9 | 18 |
| 50 | 5 | 10 |
| 60 | 4 | 8 |
| 70 | 3 | 6 |
| 80 | 3 | 6 |
| 90 | 3 | 6 |
| 100 | 2 | 4 |
| 250 | 1 | 2 |

## 4.7 Government-Industry Data Exchange Program Alerts

Government-Industry Data Exchange Program (GIDEP) alerts are issued by Government contractors to document potential part, material or design problems discovered with Government qualified parts or materials.  GIDEP alerts submitted by Spectrum Astro, Inc. shall be reviewed by the seller for potential impact or non applicability to their product.  Any alert determined to have potential impact on their product shall be addressed in a formal response to Spectrum Astro, Inc. indicating impact and recommended resolution.  The seller shall respond to all GIDEP inquiries from Spectrum Astro, Inc.

## 4.8 Failure Reporting, Failure Analysis and Corrective Action

The seller shall have a formal closed-loop problem/failure reporting system.  Failures occurring during qualification, protoflight and acceptance testing shall be reported to Spectrum Astro, Inc. within 48 hours of occurrence, including the type of failure, the suspected cause and the proposed failure analysis.  The seller shall document each functional failure encountered during acceptance and qualification testing (including returned items) on a Problem Failure Report (PFR).  Upon completion, the PFR shall be submitted to Spectrum Astro, Inc. for review.  The PFR shall describe (as a minimum):

a.	The type or nature of the failure, including identification of the failed item.

b.	Type of test and environmental conditions at the time of the failure.

c.	The symptoms and cause, including potential impact on other hardware/software.

d.	Analysis and verification approach, and the results.

e.	Any rework or retest performed.

f.	Final disposition and corrective action.

### 4.8.1 Parts Failure Analysis

Part failures that occur during or after protoflight or acceptance testing shall be subjected to failure analysis to determine the cause of the failure.

## 4.9 Control of Static Sensitive Parts, Assemblies and Components

All electronic parts and assemblies containing parts that are susceptible to damage or degradation from application of static electricity shall be identified, protected and handled to protect them from Electrostatic Discharge (ESD).  ESD sensitive electronic parts, subassemblies and assemblies shall be identified with an applicable ESD symbol as shown in MIL-STD-1686 or equivalent.  Size of the symbol shall be commensurate with space restraints but shall be noticeable to unaided visual inspection.  Marking shall be done in a contrasting color.  ESD sensitive items shall be wrapped for shipment in an anti-static material.  The package and shipping container shall be plainly marked with standard ESD symbols, and a caution note such as "Electrostatic Sensitive Items."

# 5.  QUALITY ASSURANCE

## 5.1 General

The seller shall maintain a documented Quality Assurance (QA) inspection program to ensure compliance to contract requirements.  The seller's QA program shall be planned and organized to ensure that defects or other unsatisfactory conditions are discovered and corrected at the earliest practical point.  The QA system shall provide recorded evidence of quality in the form of inspection and test results.  QA shall participate in design activities to ensure that designs permit and facilitate producibility, repeatability, inspectability and that related quality requirements are included.

## 5.2 Government/Customer Surveillance

The QA system of the seller shall be subject to surveillance by Spectrum Astro, Inc. and the Government. Spectrum Astro, Inc.'s QA representative shall notify the seller's QA representative of such visits and determine mutually agreed upon dates of each visit.  Actions by Spectrum Astro, Inc. or the Government may determine whether the requirements of this document are met and that the contract articles are of satisfactory quality and meet the intended design or use.  In the event of a visit, the seller will be notified in writing of any unacceptable areas and will be given an appropriate period of time to correct them.  Spectrum Astro, Inc. reserves the right to witness any or all tests performed as part of the terms and conditions of the contract.  The seller shall notify Spectrum Astro, Inc. at least 5 business days in advance of the start of environmental and final functional testing.

## 5.3 Control of Procurement Sources

The seller shall be responsible for adequate and effective control over procurement sources to ensure that materials, supplies, hardware, software and services purchased meet all quality and reliability requirements specified herein.  Adequate records of inspections and tests performed by the seller at the subtiers facility shall be maintained by the seller.  The responsibility for supplying quality hardware rests with the seller and includes those materials, parts and assemblies and components procured from subtier vendors.  The requirements of this specification shall be imposed on subtier vendors as necessary to ensure the quality and reliability of their products.

## 5.4 Identification, Handling and Storage

Adequate methods and facilities shall be established for controlling the identification, handling, and storage of deliverable articles.  These controls shall prevent damage, deterioration, loss and substitution.  The parts, materials and articles shall be controlled from the time of receipt until use or delivery.  The seller shall identify deliverable items by a specific part number and a unique serial number.  Part number and serial number traceability shall be maintained to the next lower assembly.  All deliverable components shall be properly marked or labeled to identify the manufacturer’s CAGE number, component part number, approved nomenclature, and serial number.  Each external electrical or Radio Frequency (RF) interface connection of the assembly or component shall be clearly labeled with a unique reference designation such as J1, J2, etc., as applicable.

## 5.5 Configuration Control

A configuration control program shall be established to control the configuration of components.  Technical documentation, such as drawings, specifications and procedures used to manufacture deliverable hardware and software, shall be released and under change control.  Drawings used to manufacture space flight hardware shall be assigned a specific part number and shall be released prior to manufacture.  Test procedures shall be released prior to use with space flight hardware.  Deliverable items shall be fabricated, inspected, and tested to the latest applicable drawing, specification or procedure.

### 5.5.1 Drawing and Change Control

The seller shall ensure that deliverable items are fabricated, inspected and tested to the latest applicable drawing or specification.  These drawings and procedures shall be under change control procedures.  All approved changes shall be incorporated into each deliverable component prior to delivery and so evidenced on inspection records.  Engineering changes shall be classified as Class I or Class II.  Class I changes shall be submitted to Spectrum Astro, Inc. for review.  Class I and Class II changes are defined as:

a.	Class I:	A change that affects the contractually specified form, fit or function of the deliverable item.

b.	Class II:	A change that is not classified as Class I.

## 5.6 Inspections and Tests

Sufficient inspections and tests shall be performed to ensure that all hardware and software conform to applicable drawings and specifications with respect to all details such as workmanship, finish, construction, functional performance, weight, interchange ability, identification and marking.  Written travelers and procedures shall make clear the details of the operations, inspections and tests to be performed.  Criteria for determining quality acceptance or rejection of items shall be established.  QA shall verify that tests are conducted to approved test procedures.  Suitable inspection, measuring and test equipment of the range, accuracy and type necessary to ensure conformance of items to contract requirements shall be used.  Tools, gages, jigs or fixtures that measure dimensions, contours or locations affecting quality characteristics shall be inspected for accuracy prior to use.  Inspection and test equipment shall be calibrated in accordance with MIL-STD, ANSI, or ISO calibration requirements.  QA shall ensure recorded test results are accurate and complete.  When tests and inspections so require, the actual measurements and observations obtained shall be indicated, including any instrument multiplier factors.  Adequate records of all operations, inspections and tests performed shall be maintained and kept on file for a period of 5 years.  Records shall be made available upon request.

### 5.6.1 Retest

Whenever the design of the hardware is changed, the hardware involved shall be retested to verify the design change and to show that no new problems have been introduced.  Retesting may be necessary if a test discrepancy occurs during testing.  If it is determined that a discrepancy has negated prior testing, the item shall be reinspected and retested.

## 5.7 Indication of Inspection Status

The seller shall maintain a system for indicating the inspection status of articles.  This shall be accomplished by means of initials, stamps, seals or decals.  The method of their application on individual articles, tags, routing cards, move tickets or other normal control devices attached to the articles or their containers shall also be defined.  Indications shall not be applied in any way which may damage or compromise the function or quality of the articles.

## 5.8 Process Control

The seller shall establish those inspections and controls over processes as necessary to ensure compliance with quality requirements.  These processes include plating, anodizing, heat treating, welding, soldering and other critical processes which affect the physical characteristics of the deliverable items.  Processes or procedures used to fabricate and test hardware, including processes generated for rework or retrofit, shall be documented.  The system of documentation shall establish process requirements, essential procedures, and critical controls necessary to ensure process reproducibility, product integrity, and reliability.  Operators and inspectors shall be trained and certified to special processes procedures and specifications.  Recertification will be at appropriate intervals.  The applicable military specification will be used when training for special process certification.  However, the training may be tailored for specific applications.  Contamination shall be controlled to eliminate possible particulate matter that could be detrimental to a part or component.  Contamination shall be controlled to meet a Class 100 K clean environment (in accordance with federal clean room standards), as a minimum.  Flight components shall be visibly clean of all contamination when inspected under 4X magnification.

## 5.9 Nonconforming Material Control and Corrective Action

The seller shall control nonconforming items to prevent their use as articles offered for delivery.  Nonconforming items shall be identified and separated from normal work operations.  When the seller believes that a nonconformance will affect form, fit or function of the end item and wishes to offer the nonconforming item for delivery, the seller shall notify Spectrum Astro, Inc. for disposition of the nonconformance.  The seller shall maintain records of any waivers or approvals of nonconforming items and shall identify the items so involved.  Nonconformance documentation shall indicate the cause of the nonconformance, the disposition of the nonconformance, and corrective action.  The seller shall take prompt action to correct conditions which have resulted or might result in substandard or defective materials, parts, components or services.  This action shall include preventive measures as well as correction of conditions that have occurred.  Inspection and test results and detailed examination of deficient or failed articles shall be used to determine the nature and basic causes of deficiencies or failures.  The seller shall document the efforts to correct existing deficiencies and minimize their future occurrence.

## 5.10 Workmanship and Soldering

Workmanship shall be of the highest standards in accordance with written procedures.  Particular attention shall be accorded of the quality of workmanship of soldering, welding, wiring, marking of parts and assemblies, plating and painting.  Soldering shall meet the requirements of MIL-STD-2000 or NHB5300.4(3A-2), as a minimum.  MIL-STD-2000 or NHB5300.4(3A-2) requirements may be tailored by the seller and submitted to Spectrum Astro, Inc. for approval.

## 5.11 Preservation, Packaging, Packing and Shipping

The seller shall maintain adequate control of packaging, packing and shipping to ensure that the quality of the fabricated items is maintained and that damage, deterioration, loss and substitution are prevented.  Packaging shall comply with the ESD controls as defined in this document.  The seller shall ensure that all requirements of the contract have been met and the deliverable items are complete prior to packaging for shipping.  The seller shall ensure that all shipments of deliverable items are marked or labeled in accordance with the requirements of the contract.

## 5.12 Acceptance Data Package

An Acceptance Data Package (ADP) shall be prepared and delivered for each end item delivered to Spectrum Astro, Inc., as applicable.  The ADP shall contain the following items, as a minimum:

a.	A cover sheet indicating the name, part number and serial number of the end item.

b.	A sign-off page with signatures of the responsible design engineer (RDE) and quality assurance (QA) indicating acceptance of the data package.

c.	As-built configuration record for the end item.

d.	The "as-built" drawing and parts list, including part and software version number, as applicable.

e.	Mechanical and electrical interfaces of the end item.

f.	End item acceptance (or qualification) test data, including environmental test results.

g.	Engineering summary, including operating time, mass and power levels of the end item.

h.	Copy of all nonconformance documentation applicable to the end item.

i.	Inspection and test records showing completion and acceptance of the end item.

# 6.  SAFETY

## 6.1 General

The seller shall maintain a safe and healthy work environment and have a safety program that establishes internal procedures and reporting systems for hazard identification, investigation and disposition of mishaps and safety incidents.  The seller shall ensure, to the extent practical, the inherent safety of program personnel through the use of appropriate design features, parts, materials, and operations.  Component designs shall meet the requirements of EWR 127-1 safety requirements.  Safety issues will be addressed prior to acceptance testing.

## 6.2 Hazard Identification

The seller shall provide a systematic approach to identify, eliminate and control hazards associated with the design in order to protect the life, health and physical well being of personnel.  Hazardous operations shall be assessed to determine the risk to program personnel and use the assessment to establish guidelines, procedures for resolution of the hazards, and safe conduct of operations.  The seller will consider alternate approaches to minimize or reduce risk from hazards that cannot be eliminated.  Safety warning devices or warning and caution notes shall be provided in the operating instructions and distinctive markings should be on hazardous components to ensure protection of personnel.  Mishaps shall be investigated to determine the cause and corrective action to prevent recurrence.  Hazard analysis shall be performed at the interface level for all items determined to be hazardous.  The analysis shall consider the following (as a minimum):

a.	Nature and causes of the hazard.

b.	The methods of controlling the hazard and applicable safety requirements.

c.	Actions taken to eliminate hazards or reduce their risk to an acceptable level.

d.	Risk acceptance rationale and approval by management.

Identified hazards that could cause the death of program personnel shall be reported to Spectrum Astro, Inc.  The seller shall maintain records of hazard assessments and analyses performed, and mishap reports on file and available to review by Spectrum Astro, Inc. upon request.

## 6.3 Hazardous Materials

Personnel handling hazardous materials shall be instructed as to the hazard associated with their use and in the proper use of the materials.  Hazardous materials delivered to Spectrum Astro, Inc. shall be accompanied by a Material Safety Data Sheet (MSDS).

# 7.  TEST REQUIREMENTS

## 7.1 General

Components shall demonstrate acceptable performance during protoflight qualification or acceptance tests prior to delivery.  Components passing the required series of protoflight and acceptance tests are acceptable for use.  End item acceptance or qualification test data including environmental test data shall be delivered with each component.  Components shall be tested as stated herein unless amended by the SOW and/or the PFS.  Inspections shall be performed prior to the start of protoflight qualification and acceptance tests to ensure that the unit is acceptable to start testing. Connector savers shall be used during testing of flight hardware. Test connectors that mate with flight hardware shall be flight connectors.

## 7.2 Test Procedures and Levels

Tests shall be conducted using documented test procedures prepared for performing all of the required tests in accordance with the test objectives.  A test procedure shall be developed for each component.  The test procedure shall clearly state the test objectives, pass/fail criteria, test setup description and should incorporate provisions for QA verification ("stamp-off") of test setups and data.  The test procedures shall cover all operations in enough detail so that there is no doubt as to the execution of any step.  The "as-run" test data shall be traceable to the component under test.

### 7.2.1 Protoflight Qualification Testing

Protoflight qualification (or protoflight) testing is required for all new designs in order to demonstrate that adequate margins exist in the final product to assure that the specification and operational requirements are met.  The objective of protoflight testing is to test the hardware to verify that there are no deficiencies in the design and methods of manufacture without stressing the hardware beyond the limits of the design and operational capabilities. Components shall be protoflight qualified to the performance and environmental levels as specified herein.  Protoflight hardware is intended to be used as flight hardware.

### 7.2.2 Acceptance Testing

Acceptance tests are the required formal tests that are conducted to demonstrate acceptability of an item for delivery.  Acceptance tests shall measure performance parameters and should reveal inadequacies in manufacturing process such as workmanship or material.  Acceptance tests shall demonstrate acceptable performance over the specified range of mission requirements. Acceptance testing is not required for a component that has been subjected to protoflight qualification tests.

## 7.3 Test Application

Unless otherwise specified, all components shall successfully complete the required tests shown in Table 7-1.  Any additional or "Special Tests" shall be performed as specified in the SOW or the PFS.  Selection of protoflight qualification or acceptance tests shall be made based on the individual component qualification status, using the guidelines described in this specification.  The suggested test sequence is shown in Figure 7-1.

- Table 7-1.  Test Requirements Matrix

| COMPONENT | Func. Test | Acoustic | Random Vibration | Shock | Thermal Cycle | Thermal Vacuum | Proof Pressure | Leak Detect | EMC | Burn-in |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| STRUCTURE & MECHANISMS |  |  |  |  |  |  |  |  |  |  |
| Passive Nutation Damper (PND) | X |  | X |  | X |  |  |  |  | X |
| Linear Mass Driver (LMD) | X |  | X |  | X |  |  |  |  | X |
| TELECOMMUNICATIONS |  |  |  |  |  |  |  |  |  |  |
| Transponder (XPD) | X |  | X |  |  | X |  |  | X | X |
| Combiner/Divider | X |  | X |  |  | X |  |  |  |  |
| Antenna | X |  | X |  |  | X |  |  |  |  |
| ELECTRICAL POWER |  |  |  |  |  |  |  |  |  |  |
| Solar Panels (incl. Solar Cells and Laydown) | X |  |  |  | X |  |  |  |  |  |
| Solar Array Wing Assembly (SWA) | X | X |  |  |  |  |  |  |  |  |
| NiH2 Common Pressure Vessels (CPV) | X |  | X |  | X |  | X | X |  |  |
| Nickel Hydrogen Battery Assembly (BAT) | X |  | X |  |  | X |  |  |  |  |
| Charge Control Board (CCB) | X |  | * | * | X | * |  |  | * | X |
| Power Control Board (PCB) | X |  | * | * | X | * |  |  | * | X |
| Wire Harness | X |  |  |  |  |  |  |  |  |  |
| COMMAND & DATA HANDLING |  |  |  |  |  |  |  |  |  |  |
| Central Processor Unit (CPU) | X |  | X | * | X | * |  |  | * | X |
| Communications Interface Board (CIB) | X |  | * | * | X | * |  |  | * | X |
| Payload & Attitude Control Interface (PACI) | X |  | * | * | X | * |  |  | * | X |
| VME Backplane | X |  | * | * | X | * |  |  | * | X |
| Solid State Recorder (SSR) | X |  | X |  | X |  |  |  |  | X |
| Spacecraft Electronics Module (SEM)** | X |  | X | X |  | X |  |  | *** | X |
| ATTITUDE CONTROL |  |  |  |  |  |  |  |  |  |  |
| Fine Sun Sensor Electronics (FSE) | X |  | X |  | X |  |  |  |  | X |
| Fine Sun Sensor Head (FSH) | X |  | X |  | X |  |  |  |  | X |
| Coarse Sun Sensor (CSS) | X |  | X |  | X |  |  |  |  | X |
| Three-Axis Magnetometer (MAG) | X |  | X |  | X |  |  |  |  | X |
| Electromagnetic Torque Rod (TQR) | X |  | X |  | X |  |  |  |  | X |

X - Component Level Test Required

* - Component Level Test Performed with Integrated EPS and C&DH Subsystem Elements

** - Spacecraft Electronics Module (SEM) consists of VME card cage with integrated EPS and C&DH components

*** - Conducted susceptibility and emissions EMI/EMC tests only, no radiated tests

- Figure 7-1.  Suggested Test Sequence

## 7.4 Functional Test

Functional test is a series of test operations that verify the functional performance parameters of the component under test.  The functional test parameters and limits will be described specifically in the functional test procedure for each component.  The functional test verifies that mechanical and electrical performance of the test item meets the SOW and PFS requirements.  A baseline functional test shall be performed at the beginning of protoflight and acceptance tests.  Abbreviated functional tests shall be performed to the extent necessary between the different environmental tests to ensure that testing has not caused a degradation in performance.  A final functional test will be performed after the completion of all other protoflight and acceptance tests.  The baseline functional test data shall be compared with the final functional test data to look for trends or degradation that might affect the life of the mission.

## 7.5 Safety Margins

Components shall have positive structural safety margins demonstrated by analysis, test or a combination of analysis and test.  The limit load factors are defined in the mass acceleration curve shown in Figure 7-2.  The component will be designed to be subjected to structural testing at 1.25 times the limit load (1.4 times for qualification) or show positive margins of safety by analysis at 2.6 times the limit load for ultimate failure modes such as material fracture or buckling.

- Figure 7-2.  Mass Acceleration Curve (Single Axis, Worst Case Direction)

## 7.6 Random Vibration

Components shall operate in accordance with its PFS after application of the loads specified in Figure 7-3 and Table 7-2.  The components shall be mounted rigidly to the vibration exciter.  Vibrations shall be applied at the base of the adapter or fixture in each of three orthogonal directions (X, Y and Z).  All mechanical and electrical items shall be in their launch configuration and monitored for failures and intermittent operations to the maximum extent possible.  An abbreviated functional test shall be performed before and after the test to verify operation.  A calibrated control accelerometer shall be used and the output signal shall be recorded continuously during the test.  Power spectral density plots of the random vibration will be made and included in the qualification/acceptance test reports delivered with the test item.

7-3.  Random Vibration Profile

- Table 7-2.  Random Vibration Levels

| CONDITIONS FOR ALL AXIS | FREQUENCY RANGE (Hz) | PSD LEVEL (g2/Hz) | Acceleration (g) | DURATION (sec/axis) |
| --- | --- | --- | --- | --- |
| ACCEPTANCE | 20 20 - 50 50 - 800 800 - 2000 2000 | 0.013 +6 dB/oct 0.08 -6 dB/oct 0.013 | 10.0 Grms | 60 sec |
| PROTOFLIGHT | 20 20 - 50 50 - 800 800 - 2000 2000 | 0.026 +6 dB/oct 0.16 -6 dB/oct 0.026 | 14.1 Grms | 60 sec |

## 7.7 Acoustic Test

Components that have a large surface area to mass ratio (such as solar arrays) shall be subject to acoustic testing to determine survival during the launch/ascent phase acoustic environment.  Components shall be in the launch/ascent mechanical and electrical configuration and shall be subjected to a uniform omni-directional acoustic field with load and durations as specified per Table 7-3 and Figure 7-4.  The component shall be installed in a reverberate acoustic cell capable of generating the required sound pressure levels with uniform sound energy density throughout the chamber.  A functional test shall be performed before and after the test to verify operational conformance with the PFS.  The acoustic test sound pressure level will be controlled to within 1/3 an Octave Band at 3.0 dB, and overall 1.5 dB.

- Figure 7-4.  Acoustic Spectrum Profile

- Table 7-3.  Acoustic Spectrum Levels

| 1/3 Octave Center Frequency (Hz) | Acceptance (dB) | Protoflight Qualification (dB) | 1/3 Octave Center Frequency (Hz) | Acceptance (dB) | Protoflight Qualification (dB) |
| --- | --- | --- | --- | --- | --- |
| 20 | 123.5 | 126.5 | 500 | 129.6 | 132.6 |
| 25 | 123.5 | 126.5 | 630 | 129.6 | 132.6 |
| 31.5 | 123.5 | 126.5 | 800 | 128.4 | 131.4 |
| 40 | 123.5 | 126.5 | 1000 | 127.2 | 130.2 |
| 50 | 123.5 | 126.5 | 1250 | 126.0 | 129.0 |
| 63 | 123.5 | 126.5 | 1600 | 124.7 | 127.7 |
| 80 | 123.5 | 126.5 | 2000 | 123.5 | 126.5 |
| 100 | 123.5 | 126.5 | 2500 | 122.4 | 125.4 |
| 125 | 123.5 | 126.5 | 3150 | 121.2 | 124.2 |
| 160 | 123.5 | 126.5 | 4000 | 119.9 | 122.9 |
| 200 | 126.6 | 129.6 | 5000 | 115.9 | 118.9 |
| 250 | 129.6 | 132.6 | 6000 | 111.7 | 114.7 |
| 315 | 129.6 | 132.6 | 8000 | 107.3 | 110.3 |
| 400 | 129.6 | 132.6 | 10000 | 103.3 | 106.3 |

## 7.8 Shock Test

Components shall be tested to the shock input spectrum provided in Table 7-4 and Figure 7-5.  The shock input shall be applied to the base of the test item.  The input shock pulse time history shall be oscillatory in nature and shall decay to less than 10% of its peak value within 50 milliseconds.  The spectrum shape shall be controlled to within +6/-3 dB, and shall be applied in each of three (3) orthogonal axes.  At least 30% of spectrum amplitudes shall exceed the nominal test specification.  Components that are powered-on during spacecraft separation shall be shock tested in the powered-on state.

- Figure 7-5.  Shock Environment Profile

- Table 7-4.  Shock Response Levels

| FREQUENCY (Hz) | ACCEPTANCE (g Peak) | PROTOFLIGHT (g Peak) |
| --- | --- | --- |
| 100 | 100 | 150 |
| 100-800 | - | - |
| 800-10,000 | 1,750 | 2,625 |

## 7.9 Pressure Decay/Venting

Components shall be designed to withstand the maximum pressure decay time history shown in Table 7-5 and Figure 7-6.  Verification of this requirement may be performed by analysis.

- Table 7-5.  Pressure Decay Profile

| TIME (sec) | COMPARTMENT PRESSURE (psi) |
| --- | --- |
| 0 | 14.70 |
| 10 | 13.47 |
| 20 | 10.52 |
| 40 | 4.13 |
| 60 | 0.85 |
| 80 | 0.20 |
| 100 | 0.04 |

- Figure 7-6.  Ascent Pressure Profile

## 7.10 Pressure Test

Pressure vessels and pressurized components shall be designed and tested in accordance with MIL-STD-1522.

## 7.11 Leak Detection Test

A leak detection test is required for components such as seals, pressure vessels, and leak-proof valves.  Components which operate as hermetically sealed units, or which have hermetically sealed subassemblies attached will be subject to a leak detection test.  For purposes of this test, a hermetically sealed unit shall be defined as a sealed unit which contains a gaseous atmosphere, as opposed to potted units.  Leak test should be performed at the end of environmental testing.  Measurement shall be made per the manufacturer’s standard procedures.

## 7.12 Burn-in

At the component level, a minimum of 100 hours of operation is required for burn-in testing.  The last 24 hours is intended to cover final functional testing.  The last 50 hours of burn-in at the component level shall be free of failures.  A systems on-time log shall be maintained to record all hours logged on the component.  Functional testing performed as a part of protoflight or acceptance testing of the end item, including during dynamic and thermal testing, counts toward total burn-in time.  Valves, fluid equipment, thrusters, and other items whose life is better measured by cycles of operation, shall be operated for 5% of the total expected service life cycles.  Devices that have extremely limited life cycles shall be tested in accordance with requirements established by the PFS.

## 7.13 Thermal Tests

Components shall be subjected to the thermal environment specified in Table 7-6 to discover workmanship defects and to verify the design. Components shall be powered and critical parameters monitored for proper operation during the total test except for the "turn-on" tests.  Components shall be turned off during the high and low dwells until the temperature stabilizes, for at least 30 minutes, and then turned back on.  Components shall exhibit normal turn-on characteristics.  Components shall be functionally tested during at least one high and one low temperature extreme after temperature stabilization in the thermal test.  Components shall be exposed to survival temperatures one time during the thermal test.  Components shall be turned off during survival temperature extremes and then turned back on when temperature reaches normal operating range.  The temperature shall be measured at a representative location such as component mounting feet on the base plate.  The master temperature sensor shall be controllable to within 5C.  The data measurement and recording equipment will be calibrated to an accuracy of ±2C.

- Table 7-6.  Thermal Cycling And Thermal Vacuum Test Temperatures

|  | Acceptance |  | Qualification/Protoflight |  | Survival |  |
| --- | --- | --- | --- | --- | --- | --- |
| Component | Min. | Max | Min. | Max | Min. | Max |
| Telecommunications |  |  |  |  |  |  |
| Transponder | -24°C | 61°C | -20°C | 65°C | -34°C | 71°C |
| Combiner/Divider | -24°C | 61°C | -34°C | 71°C | -34°C | 71°C |
| Antenna | -24°C | 61°C | -34°C | 71°C | -34°C | 71°C |
| Electrical Power |  |  |  |  |  |  |
| Solar Panels (incl. Cells and Laydown) | TBD | TBD | TBD | TBD | TBD | TBD |
| Solar Array Wing Assembly | TBD | TBD | TBD | TBD | TBD | TBD |
| NiH2 Common Pressure Vessels | -10°C | 30°C | -10°C | 30°C |  |  |
| Nickel Hydrogen Battery Assembly | -10°C | 30°C | -10°C | 30°C |  |  |
| Charge Control Board | -24°C | 61°C | -34°C | 71°C | -34°C | 71°C |
| Power Control Board | -24°C | 61°C | -34°C | 71°C | -34°C | 71°C |
| Wire Harness | -24°C | 61°C | -34°C | 71°C | -34°C | 71°C |
| Command and Data Handling |  |  |  |  |  |  |
| Central Processor Unit | -24°C | 61°C | -34°C | 71°C |  |  |
| Communications Interface Board | -24°C | 61°C | -34°C | 71°C |  |  |
| PACI Board | -24°C | 61°C | -34°C | 71°C |  |  |
| VME Backplane | -24°C | 61°C | -34°C | 71°C |  |  |
| Spacecraft Electronics Module | -24°C | 61°C | -34°C | 71°C |  |  |
| Solid State Recorder | -24°C | 61°C | -34°C | 71°C |  |  |
| Attitude Control |  |  |  |  |  |  |
| Fine Sun Sensor Electronics | -20°C | 60°C | -25°C | 65°C |  |  |
| Fine Sun Sensor Head | -20°C | 60°C | -40°C | 105°C |  |  |
| Coarse Sun Sensor | -24°C | 61°C | -34°C | 71°C |  |  |
| Passive Nutation Damper | -24°C | 61°C | -34°C | 71°C |  |  |
| Linear Mass Driver | -24°C | 61°C | -34°C | 71°C |  |  |
| Magnetometer | -24°C | 61°C | -34°C | 71°C |  |  |
| Magnetic Torque Rod | -24°C | 61°C | -34°C | 71°C |  |  |

### 7.13.1 Thermal Cycling

Components shall operate as specified in the PFS during exposure to the appropriate thermal environment defined in Table 7-6 and Figure 7-7.  Transitions between temperature extremes shall be at an average rate of 3C per minute (air temperature), with the temperature rate maintained at all times during the transition between 2°C per minute and 4°C per minute.

- Figure 7-7.  Thermal Cycling and Thermal Vacuum Profile

### 7.13.2 Thermal Vacuum

Components shall operate as specified in the PFS during exposure to the thermal vacuum environment defined in Table 7-6 and Figure 7-7.  Testing shall be performed at 10-5 Torr. and shall have an adequate conduction path to ensure proper cycling.  During pump down, it shall be demonstrated that components generate no corona which degrades their performance below specified limits while operating in the launch mode at vacuum.  Transitions between temperature extremes shall be at an average rate between 1C per minute and 3C per minute.  Care will be taken when returning the chamber to ambient to ensure that no condensation forms on the test items.  The master temperature sensor shall be controllable to within ±5C.  The data measurement and recording equipment will be calibrated to an accuracy of ±2C.

## 7.14 Electromagnetic Compatibility Testing

### 7.14.1 Electromagnetic Compatibility

Electromagnetic Compatibility (EMC) test procedures, conditions and limits shall comply with MIL-STD-461 and MIL-STD-462 for conducted and radiated emissions.  Waivers to a full testing program may be granted by Spectrum Astro, Inc. if a clear exception is shown.  The general requirements for electromagnetic compatibility are as follows:

### 7.14.2 RF Radiated Emissions

The test item shall not emit RF radiated emissions as measured at 1 meter from the test item, in excess of the following:

a.	MIL-STD-461C, Part 3, Class A2a.  Transmitted and received frequencies for the HESSI S/C are shown in Table 7-7.

### 7.14.3 RF Radiated Susceptibility

The test item shall operate within specification when exposed to RF fields per MIL-STD-461, Part 3, Class A2a.  Transmitted and received frequencies for the HESSI S/C are shown in Table 7-7.

- Table 7-7.  HESSI RF Transmit And Receive Frequencies

| MODE | FREQUENCY |
| --- | --- |
| TRANSMIT | 2210 MHz |
| RECEIVE | 2040 MHz |

### 7.14.4 Conducted Emissions

The test item shall operate within specification when exposed to conducted emissions per MIL-STD-461, Part 3, Class A2a.

### 7.14.5 Conducted Susceptibility

The test item shall operate within specification when exposed to conducted susceptibility per MIL-STD-461, Part 3, Class A2a.

### 7.14.6 Electrostatic Discharge

All components shall operate within specification when the ESD transient is applied per MIL-STD-1541 requirements.

### 7.14.7 Bonding

All components shall be bonded to the structure of the spacecraft by less than 0.0025 ohms.

# 8.  SOFTWARE ASSURANCE

## 8.1 General

Deliverable software, firmware, software contained in deliverable hardware and software used to test flight hardware shall be controlled to provide traceability.  The software shall be identified by a part number and version number.

## 8.2 Development

Development of software shall be documented and controlled as necessary to provide evidence that the software is adequately designed and that requirements are met.  It is recommended that the seller generate a Software Development Plan (SDP).  The plan should be used to document hardware interface requirements as well as software development methods.  Software QA should be brought into the software development process as an active team member at the earliest possible point in the development process.  Engineering peer reviews should be held at key points in the development process to find any shortcomings in the development process.  Flight software shall be released, validated and verified prior to use with flight hardware.  A Version Description Document (VDD) shall be generated for software.  The VDD shall indicate the software part number, the version number and the associated hardware part numbers.  The VDD shall provide a summary of the functions performed by the software.  An altered item drawing shall be generated for firmware to indicate the generic part number of the altered item, the software part number and version number.

## 8.3 Configuration and Change Control

A streamlined configuration system should be developed to satisfy the needs of the developer and the needs of the user.  Deliverable software shall be assigned a part number and a version number to provide configuration control.  Changes to software will be indicated by a unique version number.  Changes may be informal up to the time of delivery or that the software will interface with flight hardware.  Prior to integration with flight hardware, software will be released and placed under configuration control.  A copy of all software after release (i.e., the master copy) shall be provided to configuration control for safekeeping.  Changes to software after integration into flight hardware shall be formally controlled.

## 8.4 Problem/Failure Reporting and Analysis

The seller shall have a formal closed-loop problem/failure reporting system for software problems and failures.  Problem/failure reporting may be informal up to the time of integration with flight hardware.  After flight software/hardware integration, problem/failure reporting will be similar to that described in Section 4.8 of this document.

# 9.  GROUND SUPPORT EQUIPMENT

## 9.1 General

Deliverable Ground Support Equipment (GSE) shall be assigned a part number and shall be controlled to provide traceability to the assembled hardware and software.  GSE shall be manufactured and assembled in accordance with workmanship specifications and documentation sufficient to provide evidence that the hardware and software is suitable for the application.  GSE that will interface with flight hardware shall be functionally tested to the extent necessary to verify that it is suitable for use with flight hardware.  Custom electrical GSE shall be analyzed to verify that no failure in the GSE will propagate to the flight hardware.  Software used in GSE shall comply with the requirements of Section 8.1 of this document.

## 9.2 Software

GSE Software shall meet the requirements of Section 8 of this document.

### 9.2.1 GSE Acceptance Data Package

A GSE ADP shall be prepared and delivered for each end item delivered to Spectrum Astro, Inc., as applicable.  The ADP shall contain the following items, as a minimum:

a.	A cover sheet indicating the name, part number and serial number of the end item.

b.	The as-built drawing and parts list for the end item.

c.	End item acceptance test data, including verification and validation of acceptance for use.

d.	Inspection and test records showing completion and acceptance of assembly and test of the end item.

e.	Copy of all nonconformance documentation, waivers, deviations and acceptance test failure documentation applicable to the end item.

f.	Operating manuals for the end item and off-the-shelf items contained within the end item.

g.	Certificate of Compliance (C of C) certifying that the end item meets all requirements specified in the contract or purchase order.  The C of C shall reference all approved waivers and deviations.