|  | SPECTRUM ASTRO, INC. High Energy Solar Spectroscopic Imager (HESSI) PRODUCT FUNCTION SPECIFICATION (PFS) for the payload and attitude control interface (PACi) Board contract no. PP005884 |  |
| --- | --- | --- |
| SPECTRUM ASTRO PROPRIETARY DOCUMENT |
| THIS DOCUMENT CONTAINS SPECTRUM ASTRO PROPRIETARY INFORMATION. RECIPIENT, BY ACCEPTING THIS DOCUMENT, AGREES THAT NEITHER THE DOCUMENT NOR ANY INFORMATION CONTAINED WITHIN IT SHALL BE REPRODUCED OR TRANSFERRED TO OTHER DOCUMENTS NOR USED OR DISCLOSED TO OTHERS FOR MANUFACTURING OR ANY OTHER PURPOSES EXCEPT AS SPECIFICALLY AUTHORIZED IN WRITING BY SPECTRUM ASTRO. |
| PREPARED BY: |
| SPECTRUM ASTRO, INC. |
| 1440 N. Fiesta Boulevard |
| Gilbert, Arizona 85233 |
| CAGE Code 0T9D1 |
| INITIAL RELEASE DATE |
| 11 SEPTEMBER 1998 |

| 1110-EW-E11465 | REV A |
| --- | --- |
| 17 SEPTEMBER 1998 |

1110-EW-E11465A

|  | SPECTRUM ASTRO, INC. High Energy Solar Spectroscopic Imager (HESSI) PRODUCT FUNCTION SPECIFICATION (PFS) for the payload and attitude control interface (PACi) Board contract no. PP005884 |  |
| --- | --- | --- |

| reviewed BY: |  |  |
| --- | --- | --- |
|  | CONFIGURATION/DATA CONTROL, dAVE mAIDEN | DATE |
| APPROVED BY: |  |  |
|  | QUALITY ASSURANCE, JEFF SQUIRES | DATE |
| prepared BY: |  |  |
|  | ENGINEERING, mike matranga | DATE |
| approved BY: |  |  |
|  | sYSTEM ENGINEERING, JOHN JORDAN | DATE |
| APPROVED BY: |  |  |
|  | pROGRAM mANAGEMENT, JEFF PREBLE | DATE |

| REVISION SUMMARY |  |  |  |
| --- | --- | --- | --- |
| REV | RELEASE DATE | BRIEF DESCRIPTION/REASON FOR CHANGE | EFFECTIVE PAGES |
| - | 11 September 1998 | Initial release. | All |
| A | 17 September 1998 | Added reference to CVS | 1 |
|  |  | Added 1 MHz clock phasing | 4 |
|  |  | Added PACI to CIB SOH data interface requirements | 9-10 |
|  |  | Added programmable AP ID register | 16-17 |
|  |  | Modified SOH data acquisition rate to 8 Hz | 16 |
|  |  | Added VME interrupt at end of SOH data acquisition | 16 |
|  |  | Modified J1, J3, and P2 pinouts | A-1, 3 ,4 |
|  |  | Increased SOH packet size to accommodate Fine Sun Sensor | 19 |

TABLE OF CONTENTS

PAGE

1.  INTRODUCTION	1

1.1 Purpose	1

1.2 Applicable Documents	1

2.  INTERFACE REQUIREMENTS	2

2.1 Input Power Requirements	3

2.1.1 Input Voltage Range	3

2.1.2 Input Power	3

2.1.3 Inrush Current	3

2.2 Versa Module Eurocard (VME) Interface Requirements	3

2.2.1 VME Slave	3

2.2.2 VME Access Time	3

2.2.3 VME Address	3

2.2.4 VME Address Modifiers	3

2.2.5 VME Data Transfers	3

2.2.6 VME Interrupts	3

2.2.7 VME Isolation	3

2.3 Precision Clock Requirements	3

2.3.1 Clock Input	3

2.3.2 Spacecraft Time	4

2.3.2.1 MHz Clock Output	4

2.3.2.2 1 Hz Clock Output	4

2.3.3 External Clock Outputs	4

2.4 Serial Interface Requirements	4

2.4.1 SSR Serial Interface	5

2.4.1.1 SSR Command Interface	5

2.4.1.2 SSR Command Clock	5

TABLE OF CONTENTS (CONTINUED)

PAGE

2.4.1.3 SSR Command Data	5

2.4.1.4 SSR Command Valid	6

2.4.1.5 SSR Command Control	6

2.4.1.6 SSR Telemetry Interface	7

2.4.1.7 SSR Telemetry Clock	7

2.4.1.8 SSR Telemetry Data	7

2.4.1.9 SSR Telemetry Valid	7

2.4.1.10 SSR Telemetry Control	8

2.4.2 IDPU Serial Interface	9

2.4.2.1 IDPU Communications	9

2.4.2.2 IDPU Data Rate	9

2.4.2.3 IDPU Serial Data Format	9

2.4.2.4 IDPU Series Termination	10

2.4.2.5 IDPU Transmit and Receive Buffers	10

2.4.2.6 IDPU Transmit Data Control	10

2.4.2.7 IDPU Receive Data Control	10

2.4.3 Fine Sun Sensor Serial Interface	10

2.4.3.1 Input Signals	10

2.4.3.2 Angle Data Read-Out	11

2.4.4 Communications Interface Board (CIB) Serial Interface	12

2.4.4.1 PACI SOH Interface Timing	13

2.4.4.2 PACI High Speed SOH Data	14

2.4.5 Launch Vehicle SOH Data Serial Interface	14

2.5 Digital Interface Requirements	14

2.5.1 Digital Inputs	14

2.5.1.1 Digital Inputs Over/Under Voltage Protection	14

TABLE OF CONTENTS (CONTINUED)

PAGE

2.5.1.2 Digital Inputs Logic Levels	14

2.5.2 Digital Outputs	14

2.5.2.1 Digital Output Current Limit	14

2.5.2.2 Digital Out Logic Levels	14

2.6 Analog Channel Requirements	15

2.6.1 Coarse Sun Sensor (CSS) Interface Requirements	15

2.6.1.1 CSS Input	15

2.6.1.2 CSS Input Current Range	15

2.6.1.3 CSS Output Voltage Range	15

2.6.1.4 CSS Cutoff Frequency	15

2.6.1.5 Number of CSS Inputs	15

2.6.2 AD590 Temperature Sensor Requirements	15

2.6.2.1 AD590 Temperature Sensor Input	15

2.6.2.2 AD590 Input Current Range	15

2.6.2.3 AD590 Output Voltage Range	15

2.6.2.4 AD590 Cutoff Frequency	15

2.6.2.5 Number of AD590 Sensors	15

2.6.3 PRT Temperature Sensor Requirements	16

2.6.3.1 PRT Temperature Sensor Input	16

2.6.3.2 PRT Excitation	16

2.6.3.3 PRT Output Voltage Range	16

2.6.3.4 PRT Cutoff Frequency	16

2.6.3.5 Number of PRT Sensors	16

2.6.4 General Purpose Analog Sensor Requirements	16

2.6.4.1 Number of Channels	16

2.6.4.2 Input Voltage Range	16

TABLE OF CONTENTS (CONTINUED)

PAGE

2.6.4.3 Over/Under Voltage Protection	16

2.6.4.4 Input Impedance	16

2.6.5 Analog to Digital (A/D) Interface Requirements	16

2.6.5.1 A/D Input Voltage Range	16

2.6.5.2 A/D Conversion Resolution	16

2.6.5.3 A/D Conversion Accuracy	17

2.6.5.4A/D Conversion Linearity	17

2.7 Memory Requirements	17

2.7.1 PACI Memory	17

2.7.2 CPU Memory	17

2.7.3 SRAM EDAC	17

2.7.3.1 EDAC Scrub Rate	17

3.  Functional REQUIREMENTS	18

3.1 SEU Mitigation	18

3.1.1 Triple Modular Redundancy	18

3.1.2 Invalid States	18

3.1.3 External Reset	18

3.2 State of Health Data Acquisition	18

3.2.1 State of Health Data Packet Generation	18

3.2.2 SOH Packet Size	18

3.2.3 SOH Packet Format	18

3.2.4 Programmable AP ID Register	21

3.2.4 SOH Packet Transmission	21

3.2.5 SOH Packet Transmission to Launch Vehicle	22

4.  MEchanical REQUIREMENTS	22

4.1 Size and Configuration	22

TABLE OF CONTENTS (CONTINUED)

PAGE

4.2 Compatibility	22

4.3 Ejector Holes	22

4.4 Mass	22

4.5 Grounding / Isolation	22

LIST OF FIGURES

Figure	2-1.  PACI Block Diagram	2

Figure	2-2.  1MHz Timing Diagram	4

Figure	2-3.  PACI to SSR Command Interface	5

Figure	2-4.  SSR Command Timing	6

Figure	2-5.  PACI to SSR Telemetry Interface	7

Figure	2-6.  SSR Telemetry Timing	8

Figure	2-7.  IDPU Serial Interface	9

Figure	2-8.  IDPU Serial Data Format	9

Figure	2-9.  Clock and Enable Input Circuit	11

Figure	2-10.  Sun Presence and Serial Data Output Circuit	11

Figure	2-11.  Serial Data Readout Timing	12

Figure	2-12.  Analog Data Output Circuit	12

Figure	2-13.  PACI to CIB Interface	13

Figure	2-14.  PACI to CIB Timing Diagram	13

LIST OF TABLES

Table	2-1.  1 MHz Timing Data	4

Table	2-2.  SSR Command Format	5

Table	2-3.  SSR Command Timing Data	6

Table	2-4.  SSR Telemetry Format	7

Table	2-5.  SSR Telemetry Timing Data	8

Table	2-6.  PACI to CIB Timing Data	13

Table	3-1.  PACI SOH Data Packet Format	18

LIST OF TABLES (CONTINUED)

PAGE

Table	A-1.  PACI VME P1 Pin Assignments	2

Table	A-2.  PACI VME P2 Pin Assignments	3

Table	A-3.  PACI J1 Pin Assignments	4

Table	A-4.  PACI J2 Pin Assignments	5

Table	A-5.  PACI J3 Pin Assignments	6

APPENDICES CONTENTS

APPENDIX	A Pinouts	A-1

LIST OF ACRONYMS

| CCSDS | Consultative Committee for Space Data Systems |
| --- | --- |
| CIB | Communications Interface Board |
| CPU | Central Processing Unit |
| CSS | Coarse Sun Sensor |
| CVS | Component Verification Specification |
| EDAC | Error Detection and Correction |
| FSS | Fine Sun Sensor |
| HESSI | High Energy Solar Spectroscopic Imager |
| IAD | Inertial Adjustment Device |
| IDPU | Integrated Data Processing Unit |
| IEEE | Institute of Electrical and Electronics Engineers |
| IRQ | Interrupt Request |
| LSW | Least Significant Word |
| Mbps | Mega Bit/Sec |
| MSB | Most Significant Bit |
| PACI | Payload & Attitude Control Interface |
| PFS | Product Function Specification |
| PRT | Precision Resistance Thermometer |
| SIT | Select In Test |
| SOH | State of Health |
| SRAM | Static Random Access Memory |
| SSR | Solid State Recorder |
| TBD | To Be Determined |
| TBR | To Be Revised |
| VME | Versa Module Eurocard |

# 1.  INTRODUCTION

## 1.1 Purpose

This specification establishes the performance, design, development and test requirements for a space flight suitable Payload and Attitude Control Interface card to be used on the HESSI program.  Hereinafter the Payload and Attitude Control Interface is referred to as the PACI card.

## 1.2 Applicable Documents

The following documents of the exact issue shown form a part of this specification to the extent specified herein. In the event of conflict between the documents referenced herein and the contents of this specification, the contents of this specification shall be considered a superseding requirement.

a.	HESSI Component Verification Specification (CVS)	1110-EW-E09781

b.  	IEEE Standard for a Versatile Backplane Bus: VME bus	IEEE STD 1014-1987

c.	Standard for Mechanical Core Specification for 	IEEE STD 1101.2-1992

Conduction Cooled Eurocards

# 2.  INTERFACE REQUIREMENTS

The PACI interfaces are shown in Figure 2-1.

Figure 2-1.  PACI Block Diagram

## 2.1 Input Power Requirements

### 2.1.1 Input Voltage Range

The PACI shall receive +5V and ±15V essential bus power from the VME backplane.  The PACI shall meet all of its performance requirements over its full operating temperature range for input voltages in the range of 5.00 ± 0.25 Vdc, and 15.0 ± 0.5 Vdc.

### 2.1.2 Input Power

The power consumption of the PACI shall not exceed 7W for both the 5V and 15V supplies combined.

### 2.1.3 Inrush Current

The power-on inrush current of the PACI shall not exceed 2.5A and shall be within 60% of its steady state value within 100 milliseconds.

## 2.2 Versa Module Eurocard (VME) Interface Requirements

### 2.2.1 VME Slave

The PACI shall act as an A24/D16 slave on the VME bus.

### 2.2.2 VME Access Time

The PACI shall have an access time of < 800ns (average) for all D16 sustained data transfers on the VME bus.

### 2.2.3 VME Address

The most significant nibble (A23 to A20) of the PACI VME board address shall be jumper selectable using select-in-test (SIT) resistors.

### 2.2.4 VME Address Modifiers

The PACI shall support the following set of address modifiers: 0x3E, 0x3D, 0x3A, and 0x39.

### 2.2.5 VME Data Transfers

The PACI shall support D16 transfers only.

### 2.2.6 VME Interrupts

The PACI shall be capable of asserting one VME interrupt request, IRQ1*.  IRQ1* shall be used for the 1 Hz timer tick interrupt and all other PACI interrupt sources.  The PACI shall be the only source for IRQ1*.

### 2.2.7 VME Isolation

The PACI shall be fully isolated from the VME bus such that when the VME bus master is powered off, the PACI shall not source more than 500 A back into the bus.  The PACI shall receive a +5V active high signal which indicates the state of the VME bus power and shall use this signal to enable/disable its VME buffers.

## 2.3 Precision Clock Requirements

### 2.3.1 Clock Input

The PACI shall receive as an input the 222 (4194304.0) Hz precision clock from the VME backplane.

### 2.3.2 Spacecraft Time

The PACI shall maintain the spacecraft time by providing a 32-bit (unsegmented) counter representing the spacecraft time (in seconds).  The PACI shall also maintain a 16-bit (unsegmented) counter representing the spacecraft time (in sub-seconds).  The sub-second counter shall be incremented at a 216 (65536.0) Hz rate.  The PACI shall make both counters accessible through the VME interface.  The 32-bit seconds counter shall have read/write access, and the 16-bit sub-second counter shall have read only access.

### 2.3.2.1 MHz Clock Output

The PACI shall divide the 222 (4194304.0) Hz precision clock by four (4) to generate a 1 MHz (220, 1048576.0 Hz) which shall be distributed to the Instrument Data Processing Unit (IDPU) and the Communications Interface Board (CIB).  The PACI shall not introduce more than 50 ns of phase lag into the output.  The timing diagram and data are shown below.

- 2-2.  1MHz Timing Diagram

- 2-1.  1 MHz Timing Data

|  | Characteristic | Min | Max | Comments |
| --- | --- | --- | --- | --- |
| 1 | Time delay from 1 MHz falling edge to 1 Hz rising edge | 0 ns | 50 ns | TBR |
| 2 | 1 Hz rising edge to 1 Mhz rising edge (setup time) | 450 ns | 500 ns | TBR |
| 3 | Time from 1 Mhz rising edge to 1 Hz falling edge (hold time) | 500 ns | 550 ns | TBR |

### 2.3.2.2 1 Hz Clock Output

The PACI shall divide the 16-bit sub-second clock by 65536 to generate a 1 Hz timing signal which shall be used to increment the 32-bit seconds counter and to generate a 1 Hz VME interrupt.  The PACI shall provide a VME accessible bit for enabling/disabling the 1 Hz interrupt.

### 2.3.3 External Clock Outputs

The PACI shall buffer both the 220 Hz and the 1 Hz clock outputs and make them available on one of its external connectors and the VME P2 connector.  Both outputs shall be short circuit protected.

## 2.4 Serial Interface Requirements

The PACI shall provide serial differential interfaces for communicating with the Solid State Recorder (SSR), the Integrated Data Processing Unit (IDPU), and the Launch Vehicle SOH Telemetry Interface.  The PACI shall provide single-ended serial interfaces for communicating with the Fine Sun Sensor (FSS) and the CIB.  The requirements for each interface are detailed in the following sections.

### 2.4.1 SSR Serial Interface

### 2.4.1.1 SSR Command Interface

The PACI shall send commands to the SSR via a 3-wire serial differential interface consisting of a command clock, command data, and command valid signal.  Refer to Figure 2-3.

Figure 2-3.  PACI to SSR Command Interface

### 2.4.1.2 SSR Command Clock

The command clock to the SSR shall be a 50% ± 5% duty cycle clock continuously operating at 1.0 MHz.  The PACI shall provide 49.9 ( series termination resistors on the inverting and non-inverting differential clock outputs.

### 2.4.1.3 SSR Command Data

The PACI shall provide 49.9 ( series termination resistors on the inverting and non-inverting differential data outputs to the SSR.  The PACI shall provide at least an 8 word (16-bit) buffer for storing SSR commands prior to transmission. The command buffer shall be made accessible via the VME interface.  The PACI shall transmit the most significant bit (MSB) of the least significant word (LSW) of the serial command buffer first.

- 2-2.  SSR Command Format

| Bit | 15 | 8 | 7 | 0 |
| --- | --- | --- | --- | --- |
| Word 0 | Command Code | Command ID |
| Word 1 | Parameter One | Parameter Two |
| Word 2 | Parameter Three |
| Word 3 | Parameter Four (MSH of 32 bit Parameter) |
| Word 4 | Parameter Five (LSH of 32 bit Parameter) |
| Word 5 | Parameter Five | Parameter Six |
| Word 6 | Parameter Seven |
| Word 7 | Checksum |

### 2.4.1.4 SSR Command Valid

The PACI shall provide a command valid signal to the SSR indicating the presence of command data.  The command valid signal shall go low (logic “0”) on the start of the serial command string and go high (logic “1”) at the end of the serial command string.  The PACI shall provide 49.9 ( series termination resistors on the differential data valid outputs to the SSR.   Refer to Figure 2-4 and Table 2-3.

- 2-4.  SSR Command Timing

(NOTE: Bit 0 in this diagram is the MSB, and Bit 15 is the LSB)

- 2-3.  SSR Command Timing Data

### 2.4.1.5 SSR Command Control

The PACI shall provide a 16-bit VME accessible location containing the number of 16-bit words to transfer, herein referred to as the SSR command transmission count register.  The PACI shall begin transmission of command data upon having this register written to.  The PACI shall provide status information indicating the busy status of serial command status and it shall be made accessible via the VME interface.  The PACI shall be limited to transferring a maximum of 255 words on this interface.  Furthermore, a command transmission count of “0” shall cause no data transfer to occur.

### 2.4.1.6 SSR Telemetry Interface

The PACI shall receive telemetry from the SSR via a 3-wire serial differential interface consisting of a telemetry clock, telemetry data, and telemetry valid signal.  The PACI shall provide the serial clock and in response, the SSR shall provide the telemetry data and telemetry valid signals.  Refer to Figure 2-5.

- 2-5.  PACI to SSR Telemetry Interface

### 2.4.1.7 SSR Telemetry Clock

The telemetry clock to the SSR shall be a 50% ± 5% duty cycle clock continuously operating at 1.0 MHz.  The PACI shall provide 49.9 ( series termination resistors on the inverting and non-inverting differential clock outputs.

### 2.4.1.8 SSR Telemetry Data

The PACI shall provide at least a 512 word (16-bit) buffer for storing SSR telemetry.  The telemetry buffer shall be made accessible via the VME interface.  The PACI shall receive the most significant bit (MSB) of the least significant word (LSW) of the serial telemetry buffer first.  The number of telemetry words is variable and depends upon the command sent.  Refer to Table 2-4.

- 2-4.  SSR Telemetry Format

| Bit | 15 | 8 | 7 | 0 |
| --- | --- | --- | --- | --- |
| Word 0 | Command Code | Command ID |
| Word 1 | Parameter One | Parameter Two |
| ….. | Data |
| Word N | Checksum |

### 2.4.1.9 SSR Telemetry Valid

The PACI shall begin storing SSR telemetry data on the falling edge of the telemetry valid signal and shall continue storing data until the telemetry valid signal goes high.  Refer to Figure 2-6 and Table 2-5.

- 2-6.  SSR Telemetry Timing

(NOTE: Bit 0 in this diagram is the MSB, and Bit 15 is the LSB)

- 2-5.  SSR Telemetry Timing Data

### 2.4.1.10 SSR Telemetry Control

The PACI shall provide a 16-bit VME accessible location containing the number of 16-bit words received.  The PACI shall provide status information indicating the busy status and overflow status of the serial telemetry data received and it shall be made accessible via the VME interface.  The PACI shall be capable of generating an interrupt signifying the end of receiving the SSR telemetry data.  In addition, the PACI shall be capable of enabling/disabling this interrupt via the VME interface.

### 2.4.2 IDPU Serial Interface

### 2.4.2.1 IDPU Communications

The PACI shall communicate with the IDPU via asynchronous serial differential interfaces.  This communication shall include IDPU command data from the PACI to the IDPU and telemetry data from the IDPU to the PACI.  Refer to Figure 2-7.

- 2-7.  IDPU Serial Interface

### 2.4.2.2 IDPU Data Rate

The PACI shall transmit and receive data at 38,400 baud ± 2%.

### 2.4.2.3 IDPU Serial Data Format

The PACI serial data shall consist of one (1) start bit, eight (8) data bits, one (1) even parity bit, and one (1) stop bit.  Data shall be transmitted and received least significant bit first and least significant byte first.  Refer to Figure 2-8.

| Start | Bit 0 | Bit 1 | Bit 2 | Bit 3 | Bit 4 | Bit 5 | Bit 6 | Bit 7 | Parity | Stop |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Stop Bit |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Parity Bit (Even) |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Data Bit 7 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Data Bit 6 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Data Bit 5 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Data Bit 4 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Data Bit 3 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Data Bit 2 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Data Bit 1 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Data Bit 0 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Start Bit |

- 2-8.  IDPU Serial Data Format

### 2.4.2.4 IDPU Series Termination

The PACI shall provide 49.9 ( series termination on the transmit data outputs going to the IDPU.

### 2.4.2.5 IDPU Transmit and Receive Buffers

The PACI shall provide 2Kbytes of transmit data storage and 2Kbytes of receive data storage.  Both the transmit and receive data buffers shall be accessible via the VME interface.

### 2.4.2.6 IDPU Transmit Data Control

The PACI shall provide a transmit data count register containing the number of bytes to transfer.  The PACI shall begin transmission of the serial data stored in the transmit data buffer upon having the transmit data count register written to.  The PACI shall provide transmit status information which shall be VME accessible. In addition, the PACI shall be capable of generating an interrupt upon completion of transmitting the command number of data bytes.  The PACI shall be capable of enabling/disabling the transmit complete interrupt.  The PACI shall make all status and control bits accessible via the VME interface.

### 2.4.2.7 IDPU Receive Data Control

The PACI shall provide a “receive” data start register.  Once written to, the PACI shall begin storing the serial data received into the “receive” data buffer.  The PACI shall terminate receiving serial data when the data line goes idle (high) for more than 2.0 ms ± 0.2ms.  The PACI shall wait for the first byte to be received before starting to check for the serial receive line going idle for more than 2.0 ms.  The PACI shall be capable of generating an interrupt upon completion of receiving the serial data (after the 2.0 ms timeout).  The PACI shall be capable of enabling/disabling the receive data complete interrupt.  The PACI shall provide a register containing the number of serial data bytes received and stored.  The PACI shall make all status and control bits shall be accessible via the VME interface.

### 2.4.3 Fine Sun Sensor Serial Interface

### 2.4.3.1 Input Signals

The PACI shall provide a burst of 10 clock cycles at 9600 Hz ±10% and an enable gate signal to initiate the transmittal of digital data for each axis, per Figure 2-9.  The digital data shall be clocked out by the enable gate and 10 clock cycles while the fine angle analog data at the A/D interface shall be valid for the duration of the enable gate.  The analog data axis provided during a particular gate signal shall be identified in the first bit of the digital data.  Separation between sequential enable gates shall be at least 10 ms in length.

# Figure 2-9.  Clock and Enable Input Circuit

# Figure 2-10.  Sun Presence and Serial Data Output Circuit

### 2.4.3.2 Angle Data Read-Out

When the sun presence output signal is true, the 10-bit digital data word per axis, representing Gray coded  coarse angle data, and the two analog signals per axis, representing fine angle data, shall be read by the PACI.  The 10-bit digital data word for each axis shall include an axis identification as bit one, zero in bits two through four, and a 6-bit Gray coded coarse angle measurement in bits five through ten - shifted out LSB first.  Data bits shall be shifted out on the falling edge of the clock, per Figure 2-11.  The first data bit shall be stable within 10 sec of the leading edge of the enable gate and the subsequent bits shall be stable within 10 sec of the falling edge of the clock.  The two 10-bit digital data words shall alternate between the  and  sensor axes, with the  axis identified by logic one in the first data bit.

# Figure 2-11.  Serial Data Readout Timing

The two fine angle analog signals per axis shall alternate between the  and  sensor axes, along with the digital data words, switching between axes on the falling edge of the enable gate.

# Figure 2-12.  Analog Data Output Circuit

All solar aspect data, including fine analog data, coarse digital data, and the sun presence indicator, shall be read by the PACI as part of its nominal SOH data acquisition cycle.

### 2.4.4 Communications Interface Board (CIB) Serial Interface

The PACI interfaces to the Communications Interface Board (CIB) by sending real time State of Health (SOH) data.  The interface shall be a 3-wire interface consisting of clock, data, and an enable signal.  The PACI shall provide series current limiting resistors for protection.  All signals shall be routed through the VME P2 backplane connector.  Refer to Figure 2-13 below.

- 2-13.  PACI to CIB Interface

### 2.4.4.1 PACI SOH Interface Timing

The PACI shall begin transmission of the SOH data to the CIB by raising the ENA signal high.  Data shall be shifted out of the PACI on the rising edge of CLK, and shall be latched into the CIB on the falling edge of CLK.  The PACI shall transmit the Least Significant Bit (LSb) of the Least Significant Byte (LSB) first.  The PACI shall transmit 1098 bytes of SOH data in each transmission.   Nominally, the PACI shall transmit one full frame (1098 bytes) per second. Refer to Figure 2-14 below.  The timing data is shown in Table 2-6 below.

- 2-14.  PACI to CIB Timing Diagram

- 2-6.  PACI to CIB Timing Data

|  | Characteristic | Min | Max | Comments |
| --- | --- | --- | --- | --- |
| 1 | Time delay from ENA to first CLK | 0 ns | TBD ns |  |
| 2 | Clock Period | 1.0 us | - | 50% ( 5% duty cycle |
| 3 | Time from rising edge of CLK to data valid | 0 ns | TBD ns |  |

### 2.4.4.2 PACI High Speed SOH Data

The PACI shall be capable of transmitting every SOH data packet acquired to the CIB.  The PACI shall provide a VME accessible bit for selecting between low speed (once a second), and high speed (every packet) transmission to the CIB.  The PACI default shall be for low speed (once per second) packet transmission.

### 2.4.5 Launch Vehicle SOH Data Serial Interface

TBD

## 2.5 Digital Interface Requirements

The PACI shall provide digital bi-level interfaces for communicating with the Integrated Data Processing Unit (IDPU), the HESSI transponder, and the Power Control Board (CIB).  The requirements for each interface are detailed in the following sections.

### 2.5.1 Digital Inputs

The PACI shall have 32 bits of digital input status.  All digital inputs shall be accessible via the VME interface.  The PACI shall reserve 16 of the 32 digital input channels for external connections and shall be made accessible through an external front panel connector.  The PACI shall reserve 16 of the 32 digital input channels for internal connections and shall be made accessible through the VME backplane.  All bi-level digital inputs shall be pulled up to +5.0 Vdc through a 10K ( resistor.

### 2.5.1.1 Digital Inputs Over/Under Voltage Protection

The PACI shall have over voltage and under voltage protection on all digital input lines.  The PACI shall not be damaged by a 10.0 Vdc over/under voltage condition.  The PACI shall provide input protection diodes and pull-up resistors on all digital inputs.

### 2.5.1.2 Digital Inputs Logic Levels

All digital inputs shall be TTL compatible input logic levels.

### 2.5.2 Digital Outputs

The PACI shall have 16 bits of digital output.  The PACI shall allow the level of any of the digital output to be read or written via the VME BUS at any time.  All of the PACI digital outputs shall be for external connections and shall be made available through a front panel connector.

### 2.5.2.1 Digital Output Current Limit

The PACI shall have current limiting series resistors on all of its digital outputs.  Each output shall be short-circuit protected and shall be current limited to 15.0 mA (330 ().

### 2.5.2.2 Digital Out Logic Levels

All digital outputs shall be TTL compatible logic levels.

## 2.6 Analog Channel Requirements

### 2.6.1 Coarse Sun Sensor (CSS) Interface Requirements

### 2.6.1.1 CSS Input

For each Coarse Sun Sensor input channel, the PACI shall provide a current to voltage conversion amplifier. All of the CSS inputs shall be external to the PACI and shall be made accessible through an external front panel connector.

### 2.6.1.2 CSS Input Current Range

The PACI shall support an input Coarse Sun Sensor current in the range from 0 to 1300 A.

### 2.6.1.3 CSS Output Voltage Range

The PACI CSS signal conditioning circuit shall provide a linear output voltage from –10.0 to +10.0 Vdc, corresponding to the input current range of 0 to 1300 A.

### 2.6.1.4 CSS Cutoff Frequency

The PACI shall provide a 10.0 KHz (TBR) cutoff frequency for all Coarse Sun Sensor channels.

### 2.6.1.5 Number of CSS Inputs

The PACI shall provide 8 Coarse Sun Sensor circuits.

### 2.6.2 AD590 Temperature Sensor Requirements

### 2.6.2.1 AD590 Temperature Sensor Input

For AD590 input channel, the PACI shall provide a current to voltage conversion amplifier.  The PACI shall also provide appropriate gain and offset scaling.  All of the AD590 inputs shall be external to the PACI and shall be accessible through an external front panel connector.

### 2.6.2.2 AD590 Input Current Range

The PACI shall support an input current in the range from 0 to 425.0 A.  From 0uA to 223uA the output shall be saturated at –10Vdc.

### 2.6.2.3 AD590 Output Voltage Range

The PACI AD590 signal conditioning circuit shall provide a linear output voltage from –10.0 to +10.0 Vdc, corresponding to the input current range of 223.0 to 423.0 A.

### 2.6.2.4 AD590 Cutoff Frequency

The PACI shall provide a 10.0 KHz (TBR) cutoff frequency for all AD590 temperature sensor channels.

### 2.6.2.5 Number of AD590 Sensors

The PACI shall provide 24 channels of AD590 sensor circuits.

### 2.6.3 PRT Temperature Sensor Requirements

### 2.6.3.1 PRT Temperature Sensor Input

For each Precision Resistance Thermometer (PRT) input channel, the PACI shall provide a resistance to voltage conversion amplifier.  The PACI shall also provide appropriate gain and offset scaling.  All of the PRT inputs shall be external to the PACI and shall be accessible through an external front panel connector

### 2.6.3.2 PRT Excitation

The PACI shall provide a 1.0 mA ± 1% constant current excitation for all PRT input channels

### 2.6.3.3 PRT Output Voltage Range

The PACI PRT signal conditioning circuit shall provide a linear output voltage from –10.0 to +10.0 Vdc, corresponding to an input resistance in the range of 1.0 k( to 3.0 k(.

### 2.6.3.4 PRT Cutoff Frequency

The PACI shall provide a 10.0 KHz (TBR) cutoff frequency for all PRT temperature sensor channels.

### 2.6.3.5 Number of PRT Sensors

The PACI shall provide 8 channels of PRT conversion circuits.

### 2.6.4 General Purpose Analog Sensor Requirements

### 2.6.4.1 Number of Channels

The PACI shall provide 40 channels of single ended, analog inputs.  The PACI shall reserve 20 of the 40 analog input channels for external connections and shall be made accessible through an external front panel connector.  The PACI shall reserve 20 of the 40 analog input channels for internal connections and shall be made accessible through the VME P2 backplane.

### 2.6.4.2 Input Voltage Range

The PACI shall be capable of converting voltages in the range of –10.0 to +10.0 Vdc.

### 2.6.4.3 Over/Under Voltage Protection

The PACI shall provide over/under voltage protection circuitry and shall not be damaged by analog inputs as high as +35.0 Vdc, and as low as –35.0 Vdc.

### 2.6.4.4 Input Impedance

The PACI shall provide at least 100 k( of input impedance on all of its general purpose analog inputs.

### 2.6.5 Analog to Digital (A/D) Interface Requirements

### 2.6.5.1 A/D Input Voltage Range

The PACI shall be capable of converting voltages in the range of –10.0 to +10.0 Vdc.

### 2.6.5.2 A/D Conversion Resolution

The PACI shall provide 12-bit A/D conversion resolution.

### 2.6.5.3 A/D Conversion Accuracy

The PACI shall provide ± 5 bits of A/D conversion accuracy.

### 2.6.5.4A/D Conversion Linearity

The PACI shall provide an A/D conversion linearity of <= ± 3 bits over the full scale output.

## 2.7 Memory Requirements

### 2.7.1 PACI Memory

The PACI shall provide 256K bytes of Static Random Access Memory (SRAM).  The memory shall be shared by all PACI functions requiring RAM data storage.

### 2.7.2 CPU Memory

The PACI shall provide 256K bytes of Static Random Access Memory (SRAM).  The memory shall be reserved for the spacecraft computer only, and shall not be used by any other PACI function.  The PACI shall make the memory VME read/write accessible.

### 2.7.3 SRAM EDAC

The PACI shall provide an additional 128K bytes of SRAM Error Detection and Correction (EDAC).  The EDAC shall be flow-through, and consist of a 6-bit Hamming Code.  The PACI shall detect and correct all single-bit errors, and detect all double-bit errors.  The PACI shall report a double-bit SRAM error via a VME interrupt.  The interrupt shall be maskable via the VME interface.

### 2.7.3.1 EDAC Scrub Rate

The PACI shall autonomously scrub the SRAM EDAC without processor intervention.  The scrub rate shall be programmable.  The PACI shall provide a VME accessible register for setting the scrub rate interval.

# 3.  Functional REQUIREMENTS

## 3.1 SEU Mitigation

The PACI shall be designed to mitigate the effects of Single Event Upset (SEU) conditions.

### 3.1.1 Triple Modular Redundancy

All critical timing state machines shall employ the use of triple modular redundancy voting schemes.

### 3.1.2 Invalid States

All logic state machines shall have an “idle” state.  All logic state machines shall be designed such that entry into an invalid state shall cause the state machine to transition into the “idle” state.

### 3.1.3 External Reset

The PACI shall provide a VME accessible location such that, when accessed, it shall perform a global reset to the PACI board.

## 3.2 State of Health Data Acquisition

The PACI shall autonomously scan through and convert all of its analog channel inputs, and store the data in memory local to the PACI board.  The PACI shall also read and store all of its digital input, and store the data in the same memory.  This memory shall be read/write accessible through the VME interface.  The PACI shall perform this process 8 times per second (8 Hz).  At the end of each SOH data packet collection, the PACI shall generate a VME interrupt.  The interrupt shall be maskable.

### 3.2.1 State of Health Data Packet Generation

The PACI shall generate a CCSDS compatible data packet containing all of the acquired State of Health (SOH) data.  The packet shall consist of a CCSDS header, a time stamp indicating the time the data was acquired, the hardware SOH data (collected by the PACI), and software SOH data.

### 3.2.2 SOH Packet Size

The SOH packet shall be 1098 bytes in length.

### 3.2.3 SOH Packet Format

The format for the PACI SOH data packet is as follows:

- 3-1.  PACI SOH Data Packet Format

| Byte Offset | Bit Offset | Length (bits) | Definition |
| --- | --- | --- | --- |
| 0 | 0 | 16 | Packet ID |
| 0 | 0 | 3 | Version Number. Always set to “000” |
| 0 | 3 | 1 | Packet Type. Always set to “0” |
| 0 | 4 | 1 | Secondary Header Flag. Always set to “1” |
| 0 | 5 | 11 | Application ID. See Below |
| 2 | 0 | 16 | Packet Sequence Control |
| 2 | 0 | 2 | Group Flag. Always set to “11” |

| Table 3-1. PACI SOH Data Packet Format (Continued) |
| --- |
| Byte Offset | Bit Offset | Length (bits) | Definition |
| 2 | 2 | 14 | Sequence Count. Shall continuously increment. |
| 4 | 0 | 16 | Packet Length. Always set to “0x0443” (1091 dec). |
| 6 | 0 | 16 | MS Word of 32-bit S/C Seconds packet time stamp |
| 8 | 0 | 16 | LS Word of 32-bit S/C Seconds packet time stamp |
| 10 | 0 | 16 | 16-bit S/C Sub-Seconds packet time stamp |
| 12 | 0 | 16 | Digital Input Channels 0 to 15 (external) |
| 14 | 0 | 16 | Digital Input Channels 16 to 31 (internal) |
| 16 | 0 | 16 | General Purpose Analog Channel 1 |
| 18 | 0 | 16 | General Purpose Analog Channel 2 |
| 20 | 0 | 16 | General Purpose Analog Channel 3 |
| 22 | 0 | 16 | General Purpose Analog Channel 4 |
| 24 | 0 | 16 | General Purpose Analog Channel 5 |
| 26 | 0 | 16 | General Purpose Analog Channel 6 |
| 28 | 0 | 16 | General Purpose Analog Channel 7 |
| 30 | 0 | 16 | General Purpose Analog Channel 8 |
| 32 | 0 | 16 | General Purpose Analog Channel 9 |
| 34 | 0 | 16 | General Purpose Analog Channel 10 |
| 36 | 0 | 16 | General Purpose Analog Channel 11 |
| 38 | 0 | 16 | General Purpose Analog Channel 12 |
| 40 | 0 | 16 | General Purpose Analog Channel 13 |
| 42 | 0 | 16 | General Purpose Analog Channel 14 |
| 44 | 0 | 16 | General Purpose Analog Channel 15 |
| 46 | 0 | 16 | General Purpose Analog Channel 16 |
| 48 | 0 | 16 | General Purpose Analog Channel 17 |
| 50 | 0 | 16 | General Purpose Analog Channel 18 |
| 52 | 0 | 16 | General Purpose Analog Channel 19 |
| 54 | 0 | 16 | General Purpose Analog Channel 20 |
| 56 | 0 | 16 | General Purpose Analog Channel 21 |
| 58 | 0 | 16 | General Purpose Analog Channel 22 |
| 60 | 0 | 16 | General Purpose Analog Channel 23 |
| 62 | 0 | 16 | General Purpose Analog Channel 24 |
| 64 | 0 | 16 | General Purpose Analog Channel 25 |
| 66 | 0 | 16 | General Purpose Analog Channel 26 |
| 68 | 0 | 16 | General Purpose Analog Channel 27 |
| 70 | 0 | 16 | General Purpose Analog Channel 28 |
| 72 | 0 | 16 | General Purpose Analog Channel 29 |
| 74 | 0 | 16 | General Purpose Analog Channel 30 |
| 76 | 0 | 16 | General Purpose Analog Channel 31 |
| 78 | 0 | 16 | General Purpose Analog Channel 32 |
| 80 | 0 | 16 | General Purpose Analog Channel 33 |
| 82 | 0 | 16 | General Purpose Analog Channel 34 |
| 84 | 0 | 16 | General Purpose Analog Channel 35 |
| 86 | 0 | 16 | General Purpose Analog Channel 36 |
| 88 | 0 | 16 | General Purpose Analog Channel 37 |
| 90 | 0 | 16 | General Purpose Analog Channel 38 |
| 92 | 0 | 16 | General Purpose Analog Channel 39 |
| 94 | 0 | 16 | General Purpose Analog Channel 40 |
| 96 | 0 | 16 | Coarse Sun Sensor Channel 1 |
| 98 | 0 | 16 | Coarse Sun Sensor Channel 2 |
| 100 | 0 | 16 | Coarse Sun Sensor Channel 3 |
| 102 | 0 | 16 | Coarse Sun Sensor Channel 4 |
| 104 | 0 | 16 | Coarse Sun Sensor Channel 5 |
| 106 | 0 | 16 | Coarse Sun Sensor Channel 6 |
| 108 | 0 | 16 | Coarse Sun Sensor Channel 7 |
| 110 | 0 | 16 | Coarse Sun Sensor Channel 8 |
| 112 | 0 | 16 | AD590 Channel 1 |
| 114 | 0 | 16 | AD590 Channel 2 |
| 116 | 0 | 16 | AD590 Channel 3 |
| 118 | 0 | 16 | AD590 Channel 4 |
| 120 | 0 | 16 | AD590 Channel 5 |
| 122 | 0 | 16 | AD590 Channel 6 |
| 124 | 0 | 16 | AD590 Channel 7 |
| 126 | 0 | 16 | AD590 Channel 8 |
| 128 | 0 | 16 | AD590 Channel 9 |
| 130 | 0 | 16 | AD590 Channel 10 |
| 132 | 0 | 16 | AD590 Channel 11 |
| 134 | 0 | 16 | AD590 Channel 12 |
| 136 | 0 | 16 | AD590 Channel 13 |
| 138 | 0 | 16 | AD590 Channel 14 |
| 140 | 0 | 16 | AD590 Channel 15 |
| 142 | 0 | 16 | AD590 Channel 16 |
| 144 | 0 | 16 | AD590 Channel 17 |
| 146 | 0 | 16 | AD590 Channel 18 |
| 148 | 0 | 16 | AD590 Channel 19 |
| 150 | 0 | 16 | AD590 Channel 20 |
| 152 | 0 | 16 | AD590 Channel 21 |
| 154 | 0 | 16 | AD590 Channel 22 |
| 156 | 0 | 16 | AD590 Channel 23 |
| 158 | 0 | 16 | AD590 Channel 24 |
| 160 | 0 | 16 | PRT Channel 1 |
| 162 | 0 | 16 | PRT Channel 2 |
| 164 | 0 | 16 | PRT Channel 3 |
| 166 | 0 | 16 | PRT Channel 4 |
| 168 | 0 | 16 | PRT Channel 5 |
| 170 | 0 | 16 | PRT Channel 6 |
| 172 | 0 | 16 | PRT Channel 7 |
| 174 | 0 | 16 | PRT Channel 8 |
| 176 | 0 | 16 | Fine Sun Sensor Sine 1 |
| 178 | 0 | 16 | Fine Sun Sensor Cosine 1 |
| 180 | 0 | 16 | Fine Sun Sensor Sine 2 |
| 182 | 0 | 16 | Fine Sun Sensor Cosine 2 |
| 184 | 0 | 16 | Fine Sun Sensor Digital 1 |
| 186 | 0 | 16 | Fine Sun Sensor Digital 2 |
| 188 | 0 | 7280 | Reserved for software SOH data |

### 3.2.4 Programmable AP ID Register

The PACI shall provide a VME accessible register for the CPU to write the Application ID (AP ID).  If the CPU writes the AP ID register, the PACI shall use the value written by the CPU.  If the CPU does not write to the AP ID register, the PACI shall set the AP ID value to 0.

### 3.2.4 SOH Packet Transmission

The PACI shall transmit the SOH data packet to the HESSI Communications Interface Board (CIB) via the CIB serial interface at a 1 Hz rate.

### 3.2.5 SOH Packet Transmission to Launch Vehicle

The PACI shall provide the ability to transmit the SOH data packet via the launch vehicle serial interface during captive carry.  The PACI shall use the separation switch to enable/disable this interface.

# 4.  MEchanical REQUIREMENTS

## 4.1 Size and Configuration

The PACI shall be a conduction cooled VME-6U form factor board per IEE Std 1101.2-1992.  The PACI shall occupy a single card slot in the VME chassis and shall have a maximum pitch of 0.8 in.

## 4.2 Compatibility

The PACI shall be designed and built such that it is compatible with a commercial VME chassis as well as a VME conduction cooled chassis.

## 4.3 Ejector Holes

The PACI shall provide ejector holes to allow the use of tools to mate/demate the card assembly.  The PACI shall follow the VME guidelines for the location of the ejector holes.

## 4.4 Mass

The PACI mass shall not exceed 0.55 kg.

## 4.5 Grounding / Isolation

The PACI shall provide a 1 Meg Ohm isolation impedance between its analog/digital grounds and the PACI chassis.  The PACI shall use the chassis ground for thermal conduction.

- A
Pinouts

- A-1.  PACI VME P1 Pin Assignments

| VME Pin Number | Assignment | VME Pin Number | Assignment | VME Pin Number | Assignment |
| --- | --- | --- | --- | --- | --- |
| A1 | D0 | B1 |  | C1 | D8 |
| A2 | D1 | B2 |  | C2 | D9 |
| A3 | D2 | B3 |  | C3 | D10 |
| A4 | D3 | B4 |  | C4 | D11 |
| A5 | D4 | B5 |  | C5 | D12 |
| A6 | D5 | B6 |  | C6 | D13 |
| A7 | D6 | B7 |  | C7 | D14 |
| A8 | D7 | B8 |  | C8 | D15 |
| A9 | GND | B9 |  | C9 | D16 |
| A10 | SYSCLK | B10 |  | C10 |  |
| A11 | GND | B11 |  | C11 | BERR* |
| A12 | DS1* | B12 |  | C12 | SYSRESET* |
| A13 | DS0* | B13 |  | C13 | LWORD* |
| A14 | WRITE* | B14 |  | C14 | AM5 |
| A15 | GND | B15 |  | C15 | A23 |
| A16 | DTACK* | B16 | AM0 | C16 | A22 |
| A17 | GND | B17 | AM1 | C17 | A21 |
| A18 | AS* | B18 | AM2 | C18 | A20 |
| A19 | GND | B19 | AM3 | C19 | A19 |
| A20 | IACK* | B20 | GND | C20 | A18 |
| A21 | IACK IN | B21 |  | C21 | A17 |
| A22 | IACK OUT | B22 |  | C22 | A16 |
| A23 | AM4 | B23 | GND | C23 | A15 |
| A24 | A7 | B24 |  | C24 | A14 |
| A25 | A6 | B25 |  | C25 | A13 |
| A26 | A5 | B26 |  | C26 | A12 |
| A27 | A4 | B27 |  | C27 | A11 |
| A28 | A3 | B28 |  | C28 | A10 |
| A29 | A2 | B29 |  | C29 | A9 |
| A30 | A1 | B30 | IRQ1* | C30 | A8 |
| A31 | -15 VDC | B31 | +5 VDC | C31 | +15 VDC |
| A32 | +5 VDC | B32 | +5 VDC | C32 | +5 VDC |

- A-2.  PACI VME P2 Pin Assignments

| VME Pin Number | Assignment | VME Pin Number | Assignment | VME Pin Number | Assignment |
| --- | --- | --- | --- | --- | --- |
| A1 | AGND | B1 | +5 VDC | C1 | AGND |
| A2 | Analog Input 1 | B2 | DGND | C2 | Analog Input 11 |
| A3 | Analog Input 2 | B3 | RESERVED | C3 | Analog Input 12 |
| A4 | Analog Input 3 | B4 | Digital Input 5 | C4 | Analog Input 13 |
| A5 | Analog Input 4 | B5 | Digital Input 6 | C5 | Analog Input 14 |
| A6 | Analog Input 5 | B6 | Digital Input 7 | C6 | Analog Input 15 |
| A7 | Analog Input 6 | B7 | Digital Input 8 | C7 | Analog Input 16 |
| A8 | Analog Input 7 | B8 | Digital Input 9 | C8 | Analog Input 17 |
| A9 | Analog Input 8 | B9 | Digital Input 10 | C9 | Analog Input 18 |
| A10 | Analog Input 9 | B10 | Digital Input 11 | C10 | Analog Input 19 |
| A11 | Analog Input 10 | B11 | Digital Input 12 | C11 | Analog Input 20 |
| A12 | AGND | B12 | DGND | C12 | AGND |
| A13 | HCD Output 1 | B13 | +5 VDC | C13 | USER |
| A14 | HCD Output 2 | B14 | CIBCLK | C14 | HCD Output 13 |
| A15 | HCD Output 3 | B15 | CIBDAT | C15 | HCD Output 14 |
| A16 | HCD Output 4 | B16 | CIBENA | C16 | HCD Output 15 |
| A17 | HCD Output 5 | B17 | Spare | C17 | HCD Output 16 |
| A18 | HCD Output 6 | B18 | WDOG | C18 | HCD Output 17 |
| A19 | HCD Output 7 | B19 | WDOGRET | C19 | HCD Output 18 |
| A20 | HCD Output 8 | B20 | SPARE | C20 | HCD Output 19 |
| A21 | HCD Output 9 | B21 | SPARE | C21 | HCD Output 20 |
| A22 | HCD Output 10 | B22 | GND | C22 | HCD Output 21 |
| A23 | HCD Output 11 | B23 | CPU+5V | C23 | HCD Output 22 |
| A24 | HCD Output 12 | B24 | SPARE | C24 | HCD Output 23 |
| A25 | 1 Hz Clock | B25 | SPARE | C25 | HCD Output 24 |
| A26 | DGND | B26 | SPARE | C26 | DGND |
| A27 | 1 MHz Clock | B27 | SPARE | C27 | 4 MHz Clock |
| A28 | DGND | B28 | SPARE | C28 | DGND |
| A29 | Digital Input 1 | B29 | SPARE | C29 | Digital Input 13 |
| A30 | Digital Input 2 | B30 | SPARE | C30 | Digital Input 14 |
| A31 | Digital Input 3 | B31 | GND | C31 | Digital Input 15 |
| A32 | Digital Input 4 | B32 | +5 VDC | C32 | Digital Input 16 |

- A-3.  PACI J1 Pin Assignments

| Pin Number | Assignment | Pin Number | Assignment | Pin Number | Assignment | Pin Number | Assignment |
| --- | --- | --- | --- | --- | --- | --- | --- |
| J1-1 | DGND | J1-26 | DIG_DOUT4 | J1-51 | (USER) | J1-76 | SCH1-RX422_LO |
| J1-2 | DIG_DIN0 | J1-27 | DIG_DOUT5 | J1-52 | (USER) | J1-77 | SSSR-TXCMDCLK_HI |
| J1-3 | DIG_DIN1 | J1-28 | DGND | J1-53 | DGND | J1-78 | SSSR-TXCMDCLK_LO |
| J1-4 | DGND | J1-29 | DIG_DOUT6 | J1-54 | DGND | J1-79 | SCH2-RX422_HI |
| J1-5 | DIG_DIN2 | J1-30 | DIG_DOUT7 | J1-55 | ACH1-TX422_HI | J1-80 | SCH2-RX422_LO |
| J1-6 | DIG_DIN3 | J1-31 | DIG_DOUT8 | J1-56 | ACH1-TX422_LO | J1-81 | DGND |
| J1-7 | DIG_DIN4 | J1-32 | DIG_DOUT9 | J1-57 | ACH2-TX422_HI | J1-82 | DGND |
| J1-8 | DIG_DIN5 | J1-33 | DIG_DOUT10 | J1-58 | ACH2-TX422_LO | J1-83 | SSSR-TXCMDVAL_HI |
| J1-9 | DIG_DIN6 | J1-34 | DIG_DOUT11 | J1-59 | ACH3-TX422_HI | J1-84 | SSSR-TXCMDVAL_LO |
| J1-10 | DGND | J1-35 | DIG_DOUT12 | J1-60 | ACH3-TX422_LO | J1-85 | SCH3-RX422_HI |
| J1-11 | DIG_DIN7 | J1-36 | DIG_DOUT13 | J1-61 | ACH4-TX422_HI | J1-86 | SCH3-RX422_LO |
| J1-12 | DIG_DIN8 | J1-37 | DGND | J1-62 | ACH4-TX422_LO | J1-87 | SSSR-TXCMDDATA_HI |
| J1-13 | DIG_DIN9 | J1-38 | DIG_DOUT14 | J1-63 | DGND | J1-88 | SSSR-TXCMDDATA_LO |
| J1-14 | DIG_DIN10 | J1-39 | DIG_DOUT15 | J1-64 | DGND | J1-89 | SCH4-RX422_HI |
| J1-15 | DIG_DIN11 | J1-40 | (USER) | J1-65 | ACH1-RX422_HI | J1-90 | SCH4-RX422_LO |
| J1-16 | DIG_DIN12 | J1-41 | (USER) | J1-66 | ACH1-RX422_LO | J1-91 | DGND |
| J1-17 | DIG_DIN13 | J1-42 | (USER) | J1-67 | ACH2-RX422_HI | J1-92 | SSSR-TXTLMCLK_HI |
| J1-18 | DIG_DIN14 | J1-43 | (USER) | J1-68 | ACH2-RX422_LO | J1-93 | SSSR- TXTLMCLK _LO |
| J1-19 | DIG_DIN15 | J1-44 | (USER) | J1-69 | ACH3-RX422_HI | J1-94 | (USER) |
| J1-20 | DGND | J1-45 | (USER) | J1-70 | ACH3-RX422_LO | J1-95 | (USER) |
| J1-21 | DIG_DOUT0 | J1-46 | (USER) | J1-71 | ACH4-RX422_HI | J1-96 | (USER) |
| J1-22 | DIG_DOUT1 | J1-47 | (USER) | J1-72 | ACH4-RX422_LO | J1-97 | (USER) |
| J1-23 | DGND | J1-48 | (USER) | J1-73 | DGND | J1-98 | (USER) |
| J1-24 | DIG_DOUT2 | J1-49 | (USER) | J1-74 | DGND | J1-99 | KEY FILLED |
| J1-25 | DIG_DOUT3 | J1-50 | (USER) | J1-75 | SCH1-RX422_HI | J1-100 | DGND |

- A-4.  PACI J2 Pin Assignments

| Pin Number | Assignment | Pin Number | Assignment | Pin Number | Assignment | Pin Number | Assignment |
| --- | --- | --- | --- | --- | --- | --- | --- |
| J2-1 | DGND | J2-26 | AD590_IN23 | J2-51 | AD590_EXC23 | J2-76 | ASUNSEN_RTN2 |
| J2-2 | AGND | J2-27 | AD590_IN24 | J2-52 | AD590_EXC24 | J2-77 | ASUNSEN_IN3 |
| J2-3 | AD590_IN1 | J2-28 | AGND | J2-53 | AGND | J2-78 | ASUNSEN_RTN3 |
| J2-4 | AD590_IN2 | J2-29 | AD590_EXC1 | J2-54 | GP_ANALOG_CH1 | J2-79 | ASUNSEN_IN4 |
| J2-5 | AD590_IN3 | J2-30 | AD590_EXC2 | J2-55 | GP_ANALOG_CH2 | J2-80 | ASUNSEN_RTN4 |
| J2-6 | AD590_IN4 | J2-31 | AD590_EXC3 | J2-56 | GP_ANALOG_CH3 | J2-81 | AGND |
| J2-7 | AD590_IN5 | J2-32 | AD590_EXC4 | J2-57 | GP_ANALOG_CH4 | J2-82 | AGND |
| J2-8 | AD590_IN6 | J2-33 | AD590_EXC5 | J2-58 | GP_ANALOG_CH5 | J2-83 | ASUNSEN_IN5 |
| J2-9 | AD590_IN7 | J2-34 | AD590_EXC6 | J2-59 | GP_ANALOG_CH6 | J2-84 | ASUNSEN_RTN5 |
| J2-10 | AD590_IN8 | J2-35 | AD590_EXC7 | J2-60 | GP_ANALOG_CH7 | J2-85 | ASUNSEN_IN6 |
| J2-11 | AD590_IN9 | J2-36 | AD590_EXC8 | J2-61 | GP_ANALOG_CH8 | J2-86 | ASUNSEN_RTN6 |
| J2-12 | AD590_IN10 | J2-37 | AD590_EXC9 | J2-62 | GP_ANALOG_CH9 | J2-87 | ASUNSEN_IN7 |
| J2-13 | AD590_IN11 | J2-38 | AD590_EXC10 | J2-63 | GP_ANALOG_CH10 | J2-88 | ASUNSEN_RTN7 |
| J2-14 | AD590_IN12 | J2-39 | AD590_EXC11 | J2-64 | AGND | J2-89 | ASUNSEN_IN8 |
| J2-15 | AD590_IN13 | J2-40 | AD590_EXC12 | J2-65 | GP_ANALOG_CH11 | J2-90 | ASUNSEN_RTN8 |
| J2-16 | AD590_IN14 | J2-41 | AD590_EXC13 | J2-66 | GP_ANALOG_CH12 | J2-91 | KEY FILLED |
| J2-17 | AD590_IN15 | J2-42 | AD590_EXC14 | J2-67 | GP_ANALOG_CH13 | J2-92 | AGND |
| J2-18 | AD590_IN16 | J2-43 | AD590_EXC15 | J2-68 | GP_ANALOG_CH14 | J2-93 | AGND |
| J2-19 | AD590_IN17 | J2-44 | AD590_EXC16 | J2-69 | GP_ANALOG_CH15 | J2-94 | GP_ANALOG_CH17 |
| J2-20 | AD590_IN18 | J2-45 | AD590_EXC17 | J2-70 | GP_ANALOG_CH16 | J2-95 | GP_ANALOG_CH18 |
| J2-21 | AD590_IN19 | J2-46 | AD590_EXC18 | J2-71 | AGND | J2-96 | GP_ANALOG_CH19 |
| J2-22 | AD590_IN20 | J2-47 | AD590_EXC19 | J2-72 | AGND | J2-97 | GP_ANALOG_CH20 |
| J2-23 | AD590_IN21 | J2-48 | AD590_EXC20 | J2-73 | ASUNSEN_IN1 | J2-98 | AGND |
| J2-24 | AD590_IN22 | J2-49 | AD590_EXC21 | J2-74 | ASUNSEN_RTN1 | J2-99 | AGND |
| J2-25 | AGND | J2-50 | AD590_EXC22 | J2-75 | ASUNSEN_IN2 | J2-100 | DGND |

- A-5.  PACI J3 Pin Assignments

| Pin Number | Assignment | Pin Number | Assignment | Pin Number | Assignment | Pin Number | Assignment |
| --- | --- | --- | --- | --- | --- | --- | --- |
| J3-1 | DGND | J3-26 | LCMD_BUS6 | J3-51 | (USER) | J3-76 | (USER) |
| J3-2 | LBUS_DAT0 | J3-27 | LCMD_BUS7 | J3-52 | (USER) | J3-77 | (USER) |
| J3-3 | LBUS_DAT1 | J3-28 | WR_PACI | J3-53 | (USER) | J3-78 | (USER) |
| J3-4 | LBUS_DAT2 | J3-29 | OE_PACI3 | J3-54 | (USER) | J3-79 | KEY FILLED |
| J3-5 | LBUS_DAT3 | J3-30 | OE_PACI4 | J3-55 | (USER) | J3-80 | AGND |
| J3-6 | LBUS_DAT4 | J3-31 | DONE_PACI3 | J3-56 | (USER) | J3-81 | PRT_IN1 |
| J3-7 | LBUS_DAT5 | J3-32 | DONE_PACI4 | J3-57 | (USER) | J3-82 | PRT_IN2 |
| PRT_IN1 | LBUS_DAT6 | J3-33 | SRAM_CS | J3-58 | (USER) | J3-83 | PRT_IN3 |
| J3-9 | LBUS_DAT7 | J3-34 | SRAM_WR | J3-59 | (USER) | J3-84 | PRT_IN4 |
| J3-10 | DGND | J3-35 | SRAM_OE | J3-60 | (USER) | J3-85 | PRT_IN5 |
| J3-11 | LBUS_DAT8 | J3-36 | DGND | J3-61 | (USER) | J3-86 | PRT_IN6 |
| J3-12 | LBUS_DAT9 | J3-37 | (USER) | J3-62 | (USER) | J3-87 | PRT_IN7 |
| J3-13 | LBUS_DAT10 | J3-38 | (USER) | J3-63 | (USER) | J3-88 | PRT_IN8 |
| J3-14 | LBUS_DAT11 | J3-39 | (USER) | J3-64 | (USER) | J3-89 | AGND |
| J3-15 | LBUS_DAT12 | J3-40 | (USER) | J3-65 | (USER) | J3-90 | AGND |
| J3-16 | LBUS_DAT13 | J3-41 | (USER) | J3-66 | (USER) | J3-91 | PRT_EXC1 |
| J3-17 | LBUS_DAT14 | J3-42 | (USER) | J3-67 | (USER) | J3-92 | PRT_EXC2 |
| J3-18 | LBUS_DAT15 | J3-43 | (USER) | J3-68 | (USER) | J3-93 | PRT_EXC3 |
| J3-19 | DGND | J3-44 | (USER) | J3-69 | (USER) | J3-94 | PRT_EXC4 |
| J3-20 | LCMD_BUS0 | J3-45 | (USER) | J3-70 | (USER) | J3-95 | PRT_EXC5 |
| J3-21 | LCMD_BUS1 | J3-46 | (USER) | J3-71 | (USER) | J3-96 | PRT_EXC6 |
| J3-22 | LCMD_BUS2 | J3-47 | (USER) | J3-72 | (USER) | J3-97 | PRT_EXC7 |
| J3-23 | LCMD_BUS3 | J3-48 | (USER) | J3-73 | (USER) | J3-98 | PRT_EXC8 |
| J3-24 | LCMD_BUS4 | J3-49 | (USER) | J3-74 | (USER) | J3-99 | AGND |
| J3-25 | LCMD_BUS5 | J3-50 | (USER) | J3-75 | (USER) | J3-100 | AGND |

# Text boxes

IDPU

PACI

CMDTX

49.9

49.9

CMDRX

TLMTX

49.9

49.9

TLMRX