|  | SPECTRUM ASTRO, INC. HIGH ENERGY SOLAR SPECTROSCOPIC IMAGER (HESSI) PRODUCT FUNCTIONAL SPECIFICATION (PFS) FOR THE AUXILIARY DRIVE BOARD (ADB) CONTRACT NO. PPB005884 |  |
| --- | --- | --- |
| SPECTRUM ASTRO PROPRIETARY DOCUMENT |
| THIS DOCUMENT CONTAINS SPECTRUM ASTRO PROPRIETARY INFORMATION. RECIPIENT, BY ACCEPTING THIS DOCUMENT, AGREES THAT NEITHER THE DOCUMENT NOR ANY INFORMATION CONTAINED WITHIN IT SHALL BE REPRODUCED OR TRANSFERRED TO OTHER DOCUMENTS NOR USED OR DISCLOSED TO OTHERS FOR MANUFACTURING OR ANY OTHER PURPOSES EXCEPT AS SPECIFICALLY AUTHORIZED IN WRITING BY SPECTRUM ASTRO. |
| PREPARED BY: |
| SPECTRUM ASTRO, INC. |
| 1440 N. Fiesta Boulevard |
| Gilbert, Arizona 85233 |
| CAGE Code 0T9D1 |
| INITIAL RELEASE DATE |
| 8 APRIL 1999 |
| 1110-EW-W13827 | REV A |
| 11 AUGUST 1999 |

1110-ew-w13827A

|  | SPECTRUM ASTRO, INC. HIGH ENERGY SOLAR SPECTROSCOPIC IMAGER (HESSI) PRODUCT FUNCTIONAL SPECIFICATION (PFS) FOR THE AUXILIARY DRIVE BOARD (ADB) CONTRACT NO. PPB005884 |  |
| --- | --- | --- |

| REVIEWED BY: |  |  |
| --- | --- | --- |
|  | CONFIGURATION/DATA CONTROL, dave maiden | DATE |
| APPROVED BY: |  |  |
|  | engineering, John Michalek | DATE |
| APPROVED BY: |  |  |
|  | QUALITY ASSURANCE, jeff squires | DATE |
| APPROVED BY: |  |  |
|  | engineering, eli kawam | DATE |
| APPROVED BY: |  |  |
|  | systems engineer, john jordan | DATE |
| APPROVED BY: |  |  |
|  | PROGRAM MANAGER, jeff preble | DATE |

| REVISION SUMMARY |  |  |  |
| --- | --- | --- | --- |
| REV | RELEASE DATE | BRIEF DESCRIPTION/REASON FOR CHANGE | EFFECTIVE PAGES |
| - | 8 April 1999 | Initial release. | All |
| a | 11 August 1999 | Changes throughout. Complete Rewrite | All |

TABLE OF CONTENTS

PAGE

1.  INTRODUCTION	1

1.1 Purpose	1

1.2 Scope	1

2.  APPLICABLE DOCUMENTS	1

2.1 Spectrum Astro, Inc. Documents	1

3.  REQUIREMENTS	1

3.1 Functional Requirements	1

3.2 General	2

3.2.1 Grounding and +28V supply	2

3.3 Detailed Requirements	3

3.3.1 FPGA Reset	3

3.3.1.1 VME Sysreset	3

3.3.1.2 Commandable Reset	3

3.3.1.3 Power Interrupt Reset	4

3.3.2 Separation Detection	4

3.3.3 Torque Rod Drivers	4

3.3.3.1 Torque Rod Command Timeout	4

3.3.4 Inertia Adjustment Device Drivers	4

3.3.5 Solar Array Release Mechanisms	6

3.3.5.1 Commandable Sequence Initiation	6

3.3.6 Current Monitors	6

3.3.7 Solar Array Release Status	7

4.  VME Interface	7

4.1 Data Interfacing Requirements	7

4.2 HCD Map	7

4.3 VME Address Map	7

4.4 VME Interface Requirements	8

TABLE OF CONTENTS (CONTINUED)

PAGE

4.4.1 VME Slave	8

4.4.2 VME Access Time	8

4.4.3 VME Address	8

4.4.4 VME Address Modifiers	9

4.4.5 VME Data Transfers	9

4.4.6 VME Isolation	9

4.4.7 VME System Reset	9

4.4.8 Triple Modular Redundancy	9

4.5 FPGA Register Assignments	9

4.5.1 Solar Array Release	9

4.5.2 Torque Rod Drive	11

4.5.3 IAD Motor Drive	12

4.5.4 ADB Status 1 Register	14

4.5.5 ADB Soft Reset	15

5.  Electrical Interfaces	16

5.1 Connector Pinouts	16

5.2 Physical Characteristics	21

6.  Power	21

6.1 Operating Voltage	21

6.1.2 Survival Voltage	21

6.1.3 Power Interrupt	21

6.1.4 Thermal Characteristics	21

6.2 Bonding	21

7.  Environmental Conditions	21

7.1 Temperature	21

7.1.1 Operating	21

7.1.2 Non Operating	22

TABLE OF CONTENTS (CONTINUED)

PAGE

7.1.3 Storage	22

7.1.4 Pressure Decay/Venting	22

7.1.5 Random Vibration	22

7.1.6 Acceleration	22

7.1.7 Pyrotechnic Shock	22

LIST OF FIGURES

Figure	3-1.  ADB Function Diagram	2

Figure	3-2.  Solar Array Release Driver Configuration	6

LIST OF TABLES

Table	3-1.  ADB Interface Requirements	3

Table	3-2.  Stepping Sequence	4

Table	3-3.  Separation Sequence	5

Table	4-1.  HCD Map	7

Table	4-2.  VME Address Map	7

Table	5-1.  Electrical Connector Types and Pinouts	16

Table	6-1.  Bus Voltage Acceptable Limits	21

LIST OF ACRONYMS

| ADB | Auxiliary Drive Board |
| --- | --- |
| CIB | Communications Interface Board |
| CPU | Central Processing Unit |
| C&DH | Command & Data Handling |
| CVS | Component Verification Specification |
| ESB | Essential Bus |
| fpga | Field Programmable Gate Array |
| hcd | Hardware Command Decode |
| HESSI | High Energy Solar Spectroscopic Imager |
| IAD | Inertia Adjustment Device |
| PACI | Payload and Attitude Control Interface |
| PCB | Power Control Board |
| Pri | Primary |
| RLS | Release |
| SA | Solar Array |
| Sec | Secondary |
| SPG | Single Point Ground |
| TRD | Torque Rod Drivers |
| vme | Versa Module Eurocard |

# 1.  INTRODUCTION

## 1.1 Purpose

The purpose of this document is to describe all of the technical requirements for the Auxiliary Drive Board (ADB) for the HESSI Program, as a tool to guide the design and development process.

## 1.2 Scope

This document captures all requirements, with the exception of environmental and quality assurance, which are covered by HESSI program technical manuals.  This document specifies the minimum performance required of the ADB.  Included are functional requirements, electrical interfaces, and mechanical interfaces.  The document also provides the necessary information, including references to other documents, required to mechanically and electrically interface to this ADB board.

# 2.  APPLICABLE DOCUMENTS

## 2.1 Spectrum Astro, Inc. Documents

Document	Description

a.	1110-EW-Y09781	HESSI Component Verification Specification (CVS)

b.	CID-209810	Spectrum Astro, Inc. Drawing, Component Interface Definition, ADB

c.	1110-EW-E11465	PACI Specification

d.	1110-EW-E11466	CIB Specification

e.	1110-EW-E11304	PCB Specification

f.	1110-et-e13829	Auxiliary Drive Board (ADB) Acceptance Test Procedure

# 3.  REQUIREMENTS

## 3.1 Functional Requirements

The primary function of the Auxiliary Drive Board (ADB) is to provide the signal and power interface to the Solar Array Release mechanisms, the Inertia Adjustment Device (IAD) stepper motors, and the Torque Rod Drivers (TRD) on the HESSI spacecraft.  The ADB shall receive power from the Power Control Board (PCB) to drive the 3 functions described above.

Other major functions of the ADB include space vehicle separation detection and startup, data interface to the avionics via VME bus interface, and telemetry instrumentation.

Refer to Figure 3-1 for an overall function diagram of the ADB.

- 3-1.  ADB Function Diagram

## 3.2 General

### 3.2.1 Grounding and +28V supply

The Single Point Ground (SPG) for the HESSI spacecraft is located on the PCB.  The +28V supply and 28V returns shall be supplied from the PCB to the ADB on five separate feeds.  The separate feeds are for the Array Release Drivers, Torque Rod X & Zp, Torque Rod Y & Zr, IAD X Drivers and IAD Y Drivers.

| 3-1. ADB Interface Requirements |
| --- |
| Output Name | Upper Array Releases | Lower Array Releases | TRD X & Zp | TRD Y & Zr | IAD “X” | IAD “Y” |
| Feed Channel | ESB +28 | ESB +28 | TR_XZp Pwr | TR_YZr Pwr | IAD_X Pwr | IAD_Y Pwr |
| Loads Supplied | Array Release Switch Matrix | Array Release Switch Matrix | Torque Rod Drivers “X” & “Z primary” | Torque Rod Drivers “Y” & “Z redundant” | IAD Stepper Motor X | IAD Stepper Motor Y |
| Switching Command Source Command Signal Type Command Decoding | State VME/HCDs/ Separation Bilevel Reference Table 4-1 and Table 4-2 | State VME/HCDs/ Separation Bilevel Reference Table 4-1 and Table 4-2 | State VME 12 Bit data Reference Table 4-2 | State VME 12 Bit data Reference Table 4-2 | State VME 12 bit data Reference Table 4-2 | State VME 12 bit data Reference Table 4-2 |
| Load Characteristics Maximum Current Load Inrush Peak Transient Constant I/P/R Input L/C Back EMF/BlockingRequired | 9.1 A (4 Loads) 2.27A ea. N/A Resistive N/A No | 9.1 A (4 Loads) 2.27A ea. N/A Resistive N/A No | 0.25 A N/A TRD Bus Voltage +0.7V Current 2.5H Yes | 0.25 A N/A TRD Bus Voltage +0.7V Current 2.5H Yes | 0.300 A N/A IAD Bus Voltage +0.7V Power < 0.5H Yes | 0.300 A N/A IAD Bus Voltage +0.7V Power < 0.5H Yes |
| Status Feedback | Yes | Yes | Yes | Yes | Yes | Yes |
| Current Sense Input Range Accuracy Transfer Function | None | None | Yes -250mA to 250mA ±5% Vo=ITRD *20 | Yes -250mA to 250mA ±5% Vo=ITRD *20 | None | None |

## 3.3 Detailed Requirements

### 3.3.1 FPGA Reset

### 3.3.1.1 VME Sysreset

The ADB shall reset its VME logic in response to the VME system reset signal being asserted low.

### 3.3.1.2 Commandable Reset

By executing a VME cycle to the SOFTRST register (Reference Table 4-2) all the FPGA logic is reset except the IAD’s current position.

### 3.3.1.3 Power Interrupt Reset

The ADB shall perform an FPGA reset if the ESB converter +5V output drops to 0V for more than 10mS, and returns to +5V +/- 0.25V.

### 3.3.2 Separation Detection

Three separation lines shall be biased to +5V through pull-up resistors, sensed, and voted by the ADB to determine launch vehicle separation.  Launch separation is determined by a low to a high transition on two of three separation signals. Once the ADB has determined valid separation has occurred, the solar array release mechanisms will be activated according to the timed release schedule given in Table 3.3.  Upon determination of separation, the ADB shall apply a +5V signal to Pin P2-C32.

### 3.3.3 Torque Rod Drivers

The ADB shall drive the X, Y, and Z torque rods.  The Z torque rod shall be provided redundant drive circuits such that either, if commanded, can drive one of two coils contained in the Z torque rod.  Each torque rod drive output shall be a commandable constant current source.  The full scale drive output shall range from -490 mA to +490 mA.  The command shall be a 12 bit code representing the full-scale range.

### 3.3.3.1 Torque Rod Command Timeout

It is expected that the torque rod 12 bit command will be updated on a 125 ms regular basis.  Should 1.5 ± 0.65 seconds expire prior to receipt of a new command, the ADB shall drive the outputs to 0 A.

### 3.3.4 Inertia Adjustment Device Drivers

The HESSI spacecraft shall contain two IAD's. Each IAD shall be driven by one 2-phase stepper motor.  The ADB shall drive each stepper motor separately.  The two motors shall not be driven simultaneously. The ADB shall supply up to 300 mA of 28 Volt power to each coil of each stepper motor.  The stepping sequence is shown in Table 3-2.  The motor drivers shall be capable of supplying 0 to 100 step changes per second.  Each command to the IAD’s via the VME Backplane shall command no greater than 1023 steps.

Motor drive command shall execute immediately upon receipt.  Motor position knowledge is not required; each drive sequence may begin at any position in Table 3-2.  The motor command shall be decoded in accordance with Section 4.5.3.

| 3-2. Stepping Sequence |
| --- |
| + Z Wingtip Travel | - Z Wingtip Travel | STEP | COIL DRIVE POLARITY |
| ( | ( |  | Phase A | Phase B |
|  |  | 1 | + | + |
|  |  | 2 | + | ( |
|  |  | 3 | ( | ( |
|  |  | 4 | ( | + |
|  |  | 1 | + | + |
| Counter Clock Wise | Clock Wise |  |  |  |

| 3-3. Separation Sequence |
| --- |
| Sep + | hh:mm:ss | HCD | Command Function | State |  |
| 0 | 0:00:00 | N/A | ADB Senses LV Separation |  |  |
| 30 | 0:00:30 | HCD08 | Primary Enable | Enable | 30 second delay from sep |
| 31 | 0:00:31 | HCD04 | ( X Upper Release | Release | (X Upper Primary On |
| 76 | 0:01:16 | HCD04 | ( X Upper Release | Standby | (X Upper Primary Off |
| 77 | 0:01:16 | HCD08 | Primary Enable | Disable | Disable Primary Power |
| 78 | 0:01:18 | HCD09 | Redundant Enable | Enable | Enable Redundant Power |
| 79 | 0:01:19 | HCD04 | ( X Upper Release | Release | ( X Upper Redundant On |
| 124 | 0:02:04 | HCD04 | ( X Upper Release | Standby | ( X Upper Redundant Off |
| 125 | 0:02:05 | HCD09 | Redundant Enable | Disable | Disable Redundant Power |
| 126 | 0:02:06 | HCD08 | Primary Enable | Enable | Enable Primary Power |
| 127 | 0:02:07 | HCD06 | ( Y Upper Release | Release | ( Y Upper Primary On |
| 172 | 0:02:52 | HCD06 | ( Y Upper Release | Standby | ( Y Upper Primary Off |
| 173 | 0:02:53 | HCD08 | Primary Enable | Disable | Disable Primary Power |
| 174 | 0:02:54 | HCD09 | Redundant Enable | Enable | Enable Redundant Power |
| 175 | 0:02:55 | HCD06 | ( Y Upper Release | Release | ( Y Upper Redundant On |
| 220 | 0:03:40 | HCD06 | ( Y Upper Release | Standby | ( Y Upper Redundant Off |
| 221 | 0:03:41 | HCD09 | Redundant Enable | Disable | Disable Redundant Power |
| 222 | 0:03:42 | HCD08 | Primary Enable | Enable | Enable Primary Power |
| 223 | 0:03:43 | HCD05 | ( X Lower Release | Release | ( X Lower Primary On |
| 268 | 0:04:28 | HCD05 | ( X Lower Release | Standby | ( X Lower Primary Off |
| 269 | 0:04:29 | HCD08 | Primary Enable | Disable | Disable Primary Power |
| 270 | 0:04:30 | HCD09 | Redundant Enable | Enable | Enable Redundant Power |
| 271 | 0:04:31 | HCD05 | ( X Lower Release | Release | ( X Lower Redundant On |
| 316 | 0:05:16 | HCD05 | ( X Lower Release | Standby | ( X Lower Redundant Off |
| 317 | 0:05:17 | HCD09 | Redundant Enable | Disable | Disable Redundant Power |
| 318 | 0:05:18 | HCD08 | Primary Enable | Enable | Enable Primary Power |
| 319 | 0:05:19 | HCD07 | ( Y Lower Release | Release | ( Y Lower Primary On |
| 364 | 0:06:04 | HCD07 | ( Y Lower Release | Standby | ( Y Lower Primary Off |
| 365 | 0:06:05 | HCD08 | Primary Enable | Disable | Disable Primary Power |
| 366 | 0:06:06 | HCD09 | Redundant Enable | Enable | Enable Redundant Power |
| 367 | 0:06:07 | HCD07 | ( Y Lower Release | Release | ( Y Lower Redundant On |
| 412 | 0:06:52 | HCD07 | ( Y Lower Release | Standby | ( Y Lower Redundant Off |
| 413 | 0:06:53 | HCD09 | Redundant Enable | Disable | Disable Redundant Power |
| 512 | 0:08:32 | N/A | N/A | N/A | Sequence Counter Stops |

### 3.3.5 Solar Array Release Mechanisms

The ADB shall control operation of sixteen (16) solar array release mechanisms.  Each of these mechanisms will appear as a 16  load.

The solar array release mechanisms shall be configured as depicted in Figure 3-2.

- 3-2.  Solar Array Release Driver Configuration

### 3.3.5.1 Commandable Sequence Initiation

Upon receipt of three sequential HCD20 commands within 15 minutes, the ADB FPGA shall initiate the separation detection sequence found in Table 3-3.  Each HCD20 command must be a minimum of 1ms in duration for both the high and low levels.  The ADB shall issue a separation detection acknowledgement after receipt of the HCD20 commands as described above, by applying a +5V signal to P2 - C32.

### 3.3.6 Current Monitors

The ADB shall incorporate current sensing circuitry for each torque rod.  The output of these current sensors shall be discrete analog voltage signals scaled –10V to 10V. The current sensor full scale range shall be -0.5A to +0.5A.  The transfer functions shall be Vout = Itorque x 20.

### 3.3.7 Solar Array Release Status

The ADB shall provide a 0 to +5V signal indicating that each high side and low side switch has closed and is delivering power to each solar array release.  Each status shall be accessible via VME command.

# 4.  VME Interface

## 4.1 Data Interfacing Requirements

The commands and statuses of the switched buses shall be transmitted via the VME data bus on the P1 connector, and other dedicated lines on the backplane, accessed via P2.  When the ADB receives a command from the VME bus, the FPGA shall provide VME readback of the information received.

## 4.2 HCD Map

The HCD commands that are to be used by the ADB are listed in Table 4-1.  Their number assignments and logic states are also indicated.  HCD commands are level states and are communicated from the CIB via dedicated lines on the P2 connector of the VME backplane.

- 4-1.  HCD Map

| Backplane HCD Commands |  |  |  |  |
| --- | --- | --- | --- | --- |
| No. | Component | Function | Low | High |
| 4 | ADB | X Upper Release | Standby | Release |
| 5 | ADB | X Lower Release | Standby | Release |
| 6 | ADB | Y Upper Release | Standby | Release |
| 7 | ADB | Y Lower Release | Standby | Release |
| 8 | ADB | Primary Power | Disable | Enable |
| 9 | ADB | Redundant Power | Disable | Enable |
| 20 | ADB | Sequenced Release | Disable | Start |

## 4.3 VME Address Map

Commands to the ADB for board control that are VME accessible each have a VME address.  Table 4-2 indicates the address for each of these.

- 4-2.  VME Address Map

| Acronym | Address (+base) | Register Description |
| --- | --- | --- |
| SAPDIS | 0 | PRIMARY SOLAR ARRAY RELEASE DISABLE |
| SASDIS | 2 | SECONDARY SOLAR ARRAY RELEASE DISABLE |
| SAXUDIS | 4 | X-AXIS UPPER SOLAR ARRAY RELEASE DISABLE |
| SAYUDIS | 6 | Y-AXIS UPPER SOLAR ARRAY RELEASE DISABLE |
| SAXLDIS | 8 | X-AXIS LOWER SOLAR ARRAY RELEASE DISABLE |

Table 4-2.  VME Address Map (Continued)

| SAYLDIS | A | Y-AXIS LOWER SOLAR ARRAY RELEASE DISABLE |
| --- | --- | --- |
| ADBSP1 | C | ADB SPARE REGISTER 1 |
| ADBSP2 | E | ADB SPARE REGISTER 2 |
| SAPEN | 10 | PRIMARY SOLAR ARRAY RELEASE ENABLE |
| SASEN | 12 | SECONDARY SOLAR ARRAY RELEASE ENABLE |
| SAXUEN | 14 | X-AXIS UPPER SOLAR ARRAY RELEASE ENABLE |
| SAYUEN | 16 | Y-AXIS UPPER SOLAR ARRAY RELEASE ENABLE |
| SAXLEN | 18 | X-AXIS LOWER SOLAR ARRAY RELEASE ENABLE |
| SAYLEN | 1A | Y-AXIS LOWER SOLAR ARRAY RELEASE ENABLE |
| ADBSP3 | 1C | ADB SPARE REGISTER 3 |
| ADBSP4 | 1E | ADB SPARE REGISTER 4 |
| TQX | 20 | X-TORQUE ROD DRIVER CURRENT |
| TQY | 22 | Y-TORQUE ROD DRIVER CURRENT |
| TQZP | 24 | Z-TORQUE ROD PRIMARY DRIVER CURRENT |
| TQZS | 26 | Z-TORQUE ROD SECONDARY DRIVER CURRENT |
| ADBSP5 | 28 | ADB SPARE REGISTER 5 |
| ADBSP6 | 2A | ADB SPARE REGISTER 6 |
| ADBSP7 | 2C | ADB SPARE REGISTER 7 |
| ADBSP8 | 2E | ADB SPARE REGISTER 8 |
| STEPCNT | 30 | STEPPER MOTOR STEP COUNT |
| STEPCNTL | 32 | STEPPER MOTOR CONTROL |
| ADBSP9 | 34 | ADB SPARE REGISTER 9 |
| ADBSP10 | 36 | ADB SPARE REGISTER 10 |
| SASTAT | 38 | SOLAR ARRAY RELEASE STATUS |
| ADBSP11 | 3A | ADB SPARE REGISTER 11 |
| ADBSP12 | 3C | ADB SPARE REGISTER 12 |
| SOFTRST | 3E | SOFTWARE RESET |

## 4.4 VME Interface Requirements

### 4.4.1 VME Slave

The ADB shall act as an A24/D16 slave on the VME bus.

### 4.4.2 VME Access Time

The ADB shall have an access time of < 800ns (worst case) for sustained data transfers on the VME bus, except the torque rods which shall be < 1 usec.

### 4.4.3 VME Address

The most significant byte (A23 to A16) of the ADB VME board address shall be jumper selectable.

### 4.4.4 VME Address Modifiers

The ADB shall support the following set of address modifiers: 0x39, 0x3A, 0x3D, and 0x3E.

### 4.4.5 VME Data Transfers

The ADB shall support D16 transfers only.

### 4.4.6 VME Isolation

The ADB shall be fully isolated from the VME bus such that when the VME bus master is powered off, the ADB shall not source more than 500 mA back into the bus.  The ADB shall monitor the CPU+5V power input on the VME backplane and shall use this signal to enable/disable its VME buffers.

### 4.4.7 VME System Reset

The ADB shall reset its VME logic in response to the VME system reset signal being asserted low (0).

### 4.4.8 Triple Modular Redundancy

The ADB FPGA shall be designed using triple modular redundant logic, where appropriate.

## 4.5 FPGA Register Assignments

The following information details the VME bit assignments for commands and statuses to and from the ADB FPGA.

### 4.5.1 Solar Array Release

The following is the base address and most significant bit to least significant bit configuration used for VME control of the primary and secondary switches.

| SAPDIS | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x00 | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will disable the primary power for the solar array releases.  A read of this register will report the following:

Bit 15. OVERRIDE

This bit will indicate that three correct pulses (>1mS high and >1mS low) on HCD20 in less than 15 minutes and the automated array release sequence has started.  This bit will clear at the completion of this sequence.

Bit 14. FSEP3

This bit is the filtered separation #3 input.  The filter requires this input be low for 1.5 +/- 0.6 seconds to read low.  It is this filtered signal which gets “voted” with FSEP1 and FSEP2 to start the automated array release sequence.  A high indicates separation. A low indicates stage two is still mated.

Bit 13. FSEP2

This bit is the filtered separation #2 input.  The filter requires this input be low for 1.5 +/- 0.6 seconds to read low.  It is this filtered signal which gets “voted” with FSEP1 and FSEP3 to start the automated array release sequence.  A high indicates separation. A low indicates stage two is still mated.

Bit 12. FSEP1

This bit is the filtered separation #1 input.  The filter requires this input be low for 1.5 +/- 0.6 seconds to read low.  It is this filtered signal which gets “voted” with FSEP2 and FSEP3 to start the automated array release sequence.  A high indicates separation. A low indicates stage two is still mated.

Bit 11. SEP3

This bit is the raw separation #3 input. A low indicates separation. A high indicates stage two is still mated.

Bit 10. SEP2

This bit is the raw separation #2 input. A low indicates separation. A high indicates stage two is still mated.

Bit 9. SEP1

This bit is the raw separation #1 input. A low indicates separation. A high indicates stage two is still mated.

Bits 8-0. SEP_COUNTER

These bits indicate the current automated array release counter.  Each count is one 1.0 +/- 0.6 seconds.  This counter will remain at zero until separation or the HCD20 override occurs.

| SASDIS | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x02 | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will disable the Secondary power for the solar array releases.  The read of this register will read the same contents as the SAPDIS register.

| SAXUDIS | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x04 | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will disable the X-upper solar array releases.  The read of this register will read the same contents as the SAPDIS register.

| SAYUDIS | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x06 | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will disable the Y-upper solar array releases.  The read of this register will read the same contents as the SAPDIS register.

| SAXLDIS | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x08 | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any access to this register will disable the X-lower solar array releases. The read of this register will read the same contents as the SAPDIS register.

| SAYLDIS | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x0A | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will disable the Y-lower solar array releases. The read of this register will read the same contents as the SAXDIS register.

| SAPEN | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x10 | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will enable the Primary power for the solar array releases. The read of this register will read the same contents as the SAPDIS register.

| SASEN | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x12 | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will enable the Secondary power for the solar array releases. The read of this register will read the same contents as the SAPDIS register.

| SAXUEN | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x14 | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will enable the X-upper solar array releases. The read of this register will read the same contents as the SAPDIS register.

| SAYUEN | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x16 | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will enable the Y-upper solar array releases.  The read of this register will read the same contents as the SAPDIS register.

| SAXLEN | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x18 | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will enable the X-lower solar array releases. The read of this register will read the same contents as the SAPDIS register.

| SAYLEN | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 – 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x1A | OVERRIDE | FSEP3 | FSEP2 | FSEP1 | SEP3 | SEP2 | SEP1 | SEP_COUNTER |
| Reset |  |  |  |  |  |  |  | 0 |

Any write to this register will enable the Y-lower solar array releases. The read of this register will read the same contents as the SAPDIS register.

### 4.5.2 Torque Rod Drive

The following is the base address and most significant bit to least significant bit configuration used for VME control of the Torque Rod Drivers.

| TQX | 15 (MSB) – 12 | 11 - 0 (LSB) |
| --- | --- | --- |
| base + 0x20 | N/A | CURRENT |
| Reset | 0 | 0 |

Bits 15 - 12. N/A

These bits are not implemented.

Bits 11 - 0. CURRENT

These bits determine the X-axis torque rod driver current. Each count corresponds to 244(A. If 1.5 +/- 0.5 seconds has elapsed since the last write to the TQZR register, this register will be reset to output zero current.  This value, along with the other 3 torque values (TQY, TQZP and TQZR) will not be written to the torque rod until the TQZR register is written.  After the TQZR register is written, no other VME access to the ADB is allowed for 250uS minimum.  Otherwise the access is ignored and a VME BERR* is generated.

| TQY | 15 (MSB) – 12 | 11 - 0 (LSB) |
| --- | --- | --- |
| base + 0x22 | N/A | CURRENT |
| Reset | 0 | 0 |

Bits 15 - 12. N/A

These bits are not implemented.

Bits 11 - 0. CURRENT

These bits determine the Y-axis torque rod driver current. Each count corresponds to 244µA. If 1.5 +/- 0.5 seconds has elapsed since the last write to the TQZR register, this register will be reset to output zero current.  This value, along with the other 3 torque values (TQX, TQZP and TQZR) will not be written to the torque rod until the TQZR register is written.  After the TQZR register is written, no other VME access to the ADB is allowed for 250uS minimum.  Otherwise the access is ignored and a VME BERR* is generated.

| TQZP | 15 (MSB) – 12 | 11 - 0 (LSB) |
| --- | --- | --- |
| base + 0x24 | N/A | CURRENT |
| Reset | 0 | 0 |

Bits 15 - 12. N/A

These bits are not implemented.

Bits 11 - 0. CURRENT

These bits determine the Z-axis primary torque rod driver current. Each count corresponds to 244µA. If 1.5 +/- 0.5 seconds has elapsed since the last write to the TQZR register, this register will be reset to output zero current.  This value, along with the other 3 torque values (TQX, TQY and TQZR) will not be written to the torque rod until the TQZS register is written.  After the TQZR register is written, no other VME access to the ADB is allowed for 250uS minimum.  Otherwise the access is ignored and a VME BERR* is generated.

| TQZR | 15 (MSB) – 12 | 11 - 0 (LSB) |
| --- | --- | --- |
| base + 0x26 | N/A | CURRENT |
| Reset | 0 | 0 |

Bits 15 - 12. N/A

These bits are not implemented.

Bits 11 - 0. CURRENT

These bits determine the Z-axis secondary torque rod driver current. Each count corresponds to 244µA. If 1.5 +/- 0.5 seconds has elapsed since the last write to this register the output will be reset to zero current.  This value, along with the other 3 torque values (TQX, TQY and TQZP) will be written when this register is written.  After this register is written, no other VME access to the ADB is allowed for 250uS minimum.  Otherwise the access is ignored and a VME BERR* is generated.

### 4.5.3 IAD Motor Drive

The following is the base address and most significant bit to least significant bit configuration used for VME control of the IAD Motor Drivers.

| STEPCNT | 15(MSB) - 12 | 11-10 | 9 – 0 (LSB) |
| --- | --- | --- | --- |
| base + 0x30 | N/A | PULSE_COUNT | STEP_COUNT |
| Reset |  |  | 0 |

The STEPCNTL register must be configured prior to writing to this register because the IAD stepper motor will start moving after this register has been written.

Bits 15 - 12. N/A

These bits will always read zero.

Bits 11 - 10. PULSE_COUNT

These bits report the number of HCD20 pulses detected.  These pulses are used to start the automated array release sequencing.

Bits 9 - 0. STEP_COUNT

When this register is written it will start one of the two Inertia Adjustment Devices.  The count will decrement every 10mS.  The selection of which IAD and the direction is made in the STEPCNTL register.

| STEPCNTL | 15 (MSB) | 14 | 13 | 12 | 11 | 10 | 9 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x32 | SAYLOW | SAXLOW | SAYUP | SAXUP | SASEC | SAPRI | IADYPHB | IADYPHA |
| Reset | 0 |  |  |  |  |  |  |  |

| 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| IADXPHB | IADXPHA | IN2 | IN1 | OUT2 | OUT1 | IADSEL | UPCNT |
|  |  |  |  |  |  | 0 | 0 |

Bit 15. SAYLOW

This bit is the Solar Array Release Y-axis lower command monitor.  When this bit is set it indicates the current command is to energize the release mechanism.  When clear it indicates the command is to not energize the release mechanism.  This bit does not indicate there is current going through the release mechanism.  Reference the SASTAT register.

Bit 14. SAXLOW

This bit is the Solar Array Release X-axis lower command monitor.  When this bit is set it indicates the current command is to energize the release mechanism.  When clear it indicates the command is to not energize the release mechanism.  This bit does not indicate there is current going through the release mechanism.  Reference the SASTAT register.

Bit 13. SAYUP

This bit is the Solar Array Release Y-axis upper command monitor.  When this bit is set it indicates the current command is to energize the release mechanism.  When clear it indicates the command is to not energize the release mechanism.  This bit does not indicate there is current going through the release mechanism.  Reference the SASTAT register.

Bit 12. SAXUP

This bit is the Solar Array Release X-axis upper command monitor.  When this bit is set it indicates the current command is to energize the release mechanism.  When clear it indicates the command is to not energize the release mechanism.  This bit does not indicate there is current going through the release mechanism.  Reference the SASTAT register.

Bit 11. SASEC

This bit is the Solar Array Release Secondary power enable command monitor.  When this bit is set it indicates the current command is to enable the secondary power.  When clear it indicates the command is to disable secondary power.  This bit does not indicate there is current going through the release mechanism.  Reference the SASTAT register.

Bit 10. SAPRI

This bit is the Solar Array Release Primary power enable command monitor.  When this bit is set it indicates the current command is to enable the primary power.  When clear it indicates the command is disable the primary power.  This bit does not indicate there is current going through the release mechanism.  Reference the SASTAT register.

Bit 9. IADYPHB

This bit is the current command for the IADY Phase B.

Bit 8. IADYPHA

This bit is the current command for the IADY Phase A.

Bit 7. IADYPHB

This bit is the current command for the IADX Phase B.

Bit 6. IADYPHB

This bit is the current command for the IADX Phase A.

Bit 5. IN2

This bit is a spare FPGA input (CQ172 Pin 91).  This bit is enabled by writing a “1” to the OUT1 bit.  If the OUT1 is a “0”, then this bit will always read “0”.

Bit 5. IN1

This bit is a spare FPGA input (CQ172 Pin 90).  This bit is enabled by writing a “1” to the OUT1 bit.  If the OUT1 is a “0”, then this bit will always read “0”.

Bit 5. OUT2

This bit is a spare FPGA output (CQ172 Pin 87).

Bit 5. OUT1

This bit is a spare FPGA output (CQ172 Pin 88).  This bit is also the enable for IN1 and IN2.  These inputs are enabled when OUT1 is “1” and disabled when OUT1 is “0”.

Bit 1. IADSEL

This bit determines whether the Inertia Adjustment Device (IAD) #1 or #2 will be driven when the STEPCNT register is written.  When clear the IAD1 is selected.  When set the IAD2 is selected.

Bit 0. UPCNT

This bit determines whether the Inertia Adjustment Device (IAD) will increase or decrease by the amount written to the STEPCNT register.  When clear the motor will rotate counter clockwise (+Z Wingtip Travel).  When set the motor will rotate clockwise (-Z Wingtip Travel).

### 4.5.4 ADB Status 1 Register

This register is a “read only” register.  It gives the status of all the array release mechanisms.  When the bit is set, that particular bus is OFF.  When the bit is cleared, that particular bus is ON.

| SASTAT | 15 (MSB) – 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 (LSB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| base + 0x38 | N/A | YLSEC | XLSEC | YUSEC | XUSEC | YLPRI | XLPRI | YUPRI | XUPRI |
| Reset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

Bits 15 - 8. N/A

These bits are not implemented.

Bit 7. YLSEC

This bit shows the status of the Y-axis lower secondary array release.  When this bit is set the release circuit is OFF. When this bit is set the release circuit is ON.

Bit 6. XLSEC

This bit shows the status of the X-axis lower secondary array release. When this bit is set the release circuit is OFF. When this bit is set the release circuit is ON.

Bit 5. YUSEC

This bit shows the status of the Y-axis upper secondary array release. When this bit is set the release circuit is OFF. When this bit is set the release circuit is ON.

Bit 4. XUSEC

This bit shows the status of the X-axis upper secondary array release. When this bit is set the release circuit is OFF. When this bit is set the release circuit is ON.

Bit 3. YLPRI

This bit shows the status of the Y-axis lower primary array release. When this bit is set the release circuit is OFF. When this bit is set the release circuit is ON.

Bit 2. XLPRI

This bit shows the status of the X-axis lower primary array release. When this bit is set the release circuit is OFF. When this bit is set the release circuit is ON.

Bit 1. YUPRI

This bit shows the status of the Y-axis upper primary array release. When this bit is set the release circuit is OFF. When this bit is set the release circuit is ON.

Bit 0. XUPRI

This bit shows the status of the X-axis upper primary array release. When this bit is set the release circuit is OFF. When this bit is set the release circuit is ON.

### 4.5.5 ADB Soft Reset

The following is the base address and most significant bit to least significant bit configuration used for VME control of the ADB FPGA local reset.

| SOFTRST | 15 (MSB) – 0 (LSB) |
| --- | --- |
| base + 0x0E | N/A |
| Reset | 0 |

Any access to this register will issue a local reset to the ADB FPGA logic. This will reset everything except the current IAD step.

# 5.  Electrical Interfaces

## 5.1 Connector Pinouts

Electrical connector types and pinouts shall be as defined in Table 5-1.

- 5-1.  Electrical Connector Types and Pinouts

| ADB Front Panel Connections |
| --- |
| J1 (50 Pin Female) |  |  |  |
| Pin # | Signal Name | Pin # | Signal Name |
| 1 | -X_PRI_UP | 26 | Sep Sense 2 |
| 2 | +X_SEC_LO | 27 | PACI_SENSE_2 |
| 3 | +Y_PRI_UP | 28 | SEC_EN |
| 4 | +X_SEC_UP | 29 | SEC_EN |
| 5 | +Y_PRI_LO | 30 | PRI_EN |
| 6 | +10V Front Panel | 31 | PRI_EN |
| 7 | +5V Front Panel | 32 | Spare |
| 8 | Sep_Rtn1 | 33 | NEB1 |
| 9 | Sep_Sense1 | 34 | -X_PRI_LO |
| 10 | +2.5V Front Panel | 35 | +X_PRI_LO |
| 11 | SEC_EN | 36 | -Y_SEC_UP |
| 12 | SEC_EN | 37 | +Y_SEC_UP |
| 13 | SEC_EN | 38 | +Y_SEC_LO |
| 14 | PRI_EN | 39 | -Y_SEC_LO |
| 15 | PRI_EN | 40 | NEB1 |
| 16 | PRI_EN | 41 | Sep Rtn 3 |
| 17 | Spare | 42 | Sep Sense 3 |
| 18 | +X_PRI_UP | 43 | PACI_SENSE_3 |
| 19 | -X_SEC_LO | 44 | SEC_EN |
| 20 | -Y_PRI_UP | 45 | SEC_EN |
| 21 | -X_RED_UP | 46 | SEC_EN |
| 22 | -Y_PRI_LO | 47 | PRI_EN |
| 23 | PACI_SENSE_1 | 48 | PRI_EN |
| 24 | NEB1 | 49 | PRI_EN |
| 25 | Sep Rtn 2 | 50 | Spare |

| Table 5-1. Electrical Connector Types and Pinouts (Continued) |
| --- |
| J2 (37 Pin Female) |  |  |  |
| Pin # | Signal Name | Pin # | Signal Name |
| 1 | TRX_START | 20 | TRX_START |
| 2 | TRX_FINISH | 21 | TRX_FINISH |
| 3 | TRY_START | 22 | TRY_START |
| 4 | TRY_FINISH | 23 | TRY_FINISH |
| 5 | TRZP_START | 24 | Spare |
| 6 | TRZP_FINISH | 25 | Spare |
| 7 | TRZR_START | 26 | Spare |
| 8 | TRZR__FINISH | 27 | Spare |
| 9 | Chassis GND | 28 | Chassis GND |
| 10 | IADXA_FINISH | 29 | Spare |
| 11 | IADXA_START | 30 | Spare |
| 12 | IADXB_FINISH | 31 | Spare |
| 13 | IADXB_START | 32 | Spare |
| 14 | Chassis GND | 33 | Chassis GND |
| 15 | IADYA_FINISH | 34 | Spare |
| 16 | IADYA_START | 35 | Spare |
| 17 | IADYB_FINISH | 36 | Spare |
| 18 | IADYB_START | 37 | Spare |
| 19 | Chassis GND |  |  |

Table 5-1.  Electrical Connector Types and Pinouts (Continued)

| J3 (37 Pin Male) |  |  |  |
| --- | --- | --- | --- |
| Pin # | Signal Name | Pin # | Signal Name |
| 1 | SPG | 20 | SPG |
| 2 | SPG | 21 | NEB1 |
| 3 | SPG | 22 | HCD_FP2 |
| 4 | IADY_BUS | 23 | ESB+28V |
| 5 | ESB+28V | 24 | ESB+28V |
| 6 | ESB+28V | 25 | NEB1 |
| 7 | NEB1 | 26 | IADY_BUS |
| 8 | IADX_BUS | 27 | IADX_BUS |
| 9 | Spare | 28 | NEB1 |
| 10 | NEB1 | 29 | NEB1 |
| 11 | +15V_RTN-CPU | 30 | -15V_RTN-CPU |
| 12 | TRDXZP_BUS | 31 | NEB1 |
| 13 | Spare | 32 | HCD_FP3 |
| 14 | TRDXZP_BUS | 33 | NEB1 |
| 15 | +15V_CPU | 34 | +15V_CPU |
| 16 | TRDYZR_BUS | 35 | AGND |
| 17 | -15V_CPU | 36 | -15V_CPU |
| 18 | TRDYZR_BUS | 37 | Torque Rod ZR Current |
| 19 | HCD_FP1 |  |  |

| Table 5-1. Electrical Connector Types and Pinouts (Continued) |
| --- |
| P1 – VME Connector Assignments |
| A1 | D0 | B1 | NC | C1 | D8 |
| A2 | D1 | B2 | NC | C2 | D9 |
| A3 | D2 | B3 | NC | C3 | D10 |
| A4 | D3 | B4 | NC | C4 | D11 |
| A5 | D4 | B5 | NC | C5 | D12 |
| A6 | D5 | B6 | NC | C6 | D13 |
| A7 | D6 | B7 | NC | C7 | D14 |
| A8 | D7 | B8 | NC | C8 | D15 |
| A9 | GND | B9 | NC | C9 | GND |
| A10 | NC | B10 | NC | C10 | NC |
| A11 | GND | B11 | NC | C11 | BERR* |
| A12 | DS1* | B12 | NC | C12 | SYSRESET* |
| A13 | DS0* | B13 | NC | C13 | LWORD* |
| A14 | WRITE* | B14 | NC | C14 | AM5 |
| A15 | GND | B15 | NC | C15 | A23 |
| A16 | DTACK* | B16 | AM0 | C16 | A22 |
| A17 | GND | B17 | AM1 | C17 | A21 |
| A18 | AS* | B18 | AM2 | C18 | A20 |
| A19 | GND | B19 | AM3 | C19 | A19 |
| A20 | IACK* | B20 | GND | C20 | A18 |
| A21 | A22 | B21 | NC | C21 | A17 |
| A22 | A21 | B22 | NC | C22 | A16 |
| A23 | AM4 | B23 | GND | C23 | A15 |
| A24 | A7 | B24 | NC | C24 | A14 |
| A25 | A6 | B25 | NC | C25 | A13 |
| A26 | A5 | B26 | NC | C26 | A12 |
| A27 | A4 | B27 | NC | C27 | A11 |
| A28 | A3 | B28 | NC | C28 | A10 |
| A29 | A2 | B29 | NC | C29 | A9 |
| A30 | A1 | B30 | NC | C30 | A8 |
| A31 | -15VDC | B31 | NC | C31 | +15VDC |
| A32 | VCC | B32 | VCC | C32 | VCC |

| Table 5-1. Electrical Connector Types and Pinouts (Continued) |
| --- |
| P2 – VME Connector Assignments |
| A1 | AGND | B1 | VCC | C1 | AGND |
| A2 | NC | B2 | GND | C2 | NC |
| A3 | NC | B3 | NC | C3 | NC |
| A4 | NC | B4 | NC | C4 | NC |
| A5 | NC | B5 | NC | C5 | NC |
| A6 | NC | B6 | NC | C6 | NC |
| A7 | NC | B7 | NC | C7 | NC |
| A8 | NC | B8 | NC | C8 | Torque Rod X Current |
| A9 | NC | B9 | NC | C9 | Torque Rod Y Current |
| A10 | NC | B10 | NC | C10 | Torque Rod Zp Current |
| A11 | NC | B11 | NC | C11 | NC |
| A12 | AGND | B12 | GND | C12 | AGND |
| A13 | NC | B13 | VCC | C13 | CPU_+5V |
| A14 | NC | B14 | NC | C14 | NC |
| A15 | NC | B15 | NC | C15 | NC |
| A16 | HCD04 | B16 | NC | C16 | NC |
| A17 | HCD05 | B17 | NC | C17 | NC |
| A18 | HCD06 | B18 | NC | C18 | NC |
| A19 | HCD07 | B19 | NC | C19 | NC |
| A20 | HCD08 | B20 | NC | C20 | NC |
| A21 | HCD09 | B21 | NC | C21 | HCD20 |
| A22 | NC | B22 | GND | C22 | NC |
| A23 | NC | B23 | NC | C23 | NC |
| A24 | NC | B24 | NC | C24 | NC |
| A25 | 1 HZ | B25 | NC | C25 | NC |
| A26 | GND | B26 | NC | C26 | GND |
| A27 | NC | B27 | NC | C27 | NC |
| A28 | NC | B28 | NC | C28 | GND |
| A29 | NC | B29 | NC | C29 | NC |
| A30 | NC | B30 | NC | C30 | NC |
| A31 | NC | B31 | GND | C31 | NC |
| A32 | NC | B32 | VCC | C32 | Separation Monitor |

## 5.2 Physical Characteristics

Envelope and mass, shall be as shown on Spectrum Astro Inc. Drawing CID-209810, Component Definition, ADB.

# 6.  Power

## 6.1 Operating Voltage

The ADB shall operate nominally with the voltage inputs given in Table 6-1:

- 6-1.  Bus Voltage Acceptable Limits

| Voltage Bus | Min | Max | Predicted Nominal Current Draw | Maximum Allowed Current Draw (Excluding Outputs) |
| --- | --- | --- | --- | --- |
| 28V | 24.0V | 34.0V | 0.234A | 0.3 A |
| +5V | 4.75V | 5.25V | 0.050A | 0.1A |
| +15V | 13.8V | 16.2V | 0.16A | 0.18A |
| -15V | -16.2V | -13.8V | 0.16A | 0.18A |
| +15V VME | 13.8V | 16.2V | 0.025 | 0.05 |
| -15V VME | -16.2V | -13.8V | 0.025 | 0.05 |

### 6.1.2 Survival Voltage

The ADB shall survive voltage inputs of 16V - 40V on the 28V input, with no degradation in performance.

### 6.1.3 Power Interrupt

The ADB board shall be able to operate with power interruptions less than 10 msec in duration.  Should the +5V or ± 15V supplies drop out of specification for less than 10 msec, ADB operation, including switch states, shall be unaltered.

### 6.1.4 Thermal Characteristics

The ADB shall not dissipate more than 15 W.

## 6.2 Bonding

Mechanical mounting interfaces shall be electrically isolated from all ADB board signals by a resistance of at least 1 M(.

# 7.  Environmental Conditions

## 7.1 Temperature

### 7.1.1 Operating

The ADB Board shall be cooled by conduction through the wedge lock clamps at the short edges of the ADB board.  The temperature of the HESSI VME rack at the wedge lock interface will be –24 °C to +61°C.

### 7.1.2 Non Operating

The ADB board shall be designed to withstand a non-operating temperature range from -34(C to + 71(C.

### 7.1.3 Storage

The ADB board shall be designed to withstand a storage temperature range from -34(C to + 71(C.

### 7.1.4 Pressure Decay/Venting

Not applicable.

### 7.1.5 Random Vibration

The ADB board is designed to withstand the qualification random vibration levels as described in Section 7.6 and listed in Figure 7-3 and Table 7-2 of the Component Verification Specification.

### 7.1.6 Acceleration

The ADB board is designed to withstand acceleration levels described in Section 7.2 of the Component Verification Specification.

### 7.1.7 Pyrotechnic Shock

The ADB board is designed to withstand the pyrotechnic shock levels given in Section 7.8, Table 7-4, and Figure 7-5 of the Component Verification Specification.