PmtrasMajorEventLog.doc

Sep 28, 2003

# PMTRAS MAJOR EVENTS LOG

PURPOSE:

To informally document significant RHESSI events relevant to PMTRAS roll solution.

Routine t/m and solution gaps are not included.

2002

Feb 05    10:58			Launch

Feb 08  ~07:30			PMTRAS turned on. (~9 rpm)

Feb 08, 11			Spinning up to 14 rpm

Feb 26  ~18:33			Integration time changed from 4 ms to 2 ms. (~15 rpm)

Feb 27				Spinning up to 15 rpm

May 02  ~01:30 to ~06:20	Spinning up to 15 rpm

May 02    09:36 to 11:22		CPU reset – PMTRAS off.

June 08				Offpointing tests

June 11				Partial solar eclipse – no effect expected on roll data.

June 13	,14			Offpointing tests

June 17 ~11:26			Crab offpointing begins

June 24 ~17:10			Sun reacquired after Crab operations.

July 7				Spinning up to 15 rpm

July 23				X4.8 flare – analysis supported by orbit-interpolated roll solution

Aug 15	~17:25			CPU reset turns PMTRAS off.

Aug 16   			PMTRAS turned on again.

Sept 14, 15			Spinning up to 15 rpm

Nov 02				Spinning up to 15 rpm

Dec 30				Spinning up to 15 rpm

2003

Feb 14    02:01 to 03:37		Diagnostic test sets integration time to 4 ms.

Feb 20				Spinning up to 15 rpm

April 10				Spinning up to 15 rpm

May 08 ~1100			Offpointing tests begin.

May 23  04:45			More offpointing tests begin

June 14				Crab offpointing begins

June 16				Sun reacquired after Crab operations

June 24				Spinning up to 15 rpm

Aug  19				Spinning up to 15 rpm