## Slide 1: Understanding the Origin of Solar Flares
Joseph M. Davila (GSFC)

## Slide 2: Can We Confirm Observationally Some Basic Flare Assumptions?
Flares originate from energy stored in the corona
Reconnection in the corona releases this stored energy
Accelerated electron beams which travel to denser regions where energetic emission is observed.

## Slide 3: Two New Enabling Discoveries
High Resolution white light corona imaging
  Contrary to previous conventional wisdom, recent eclipse images show that fine-scale (1 arcsec) structures are present and visible
  These structures are tracers of magnetic field lines
New diagnostic capability developed
  Davila and Reginald have developed and demonstrated at a series of recent eclipses a new temperature and velocity diagnostic capability applicable to ONSET-type white light coronagraphs

## Slide 4
2010

## Slide 5
2006

## Slide 6
2008

## Slide 7: Coronagraph-Eclipse Comparison
Eclipse 7-22-2009
COR1 7-22-2009

## Slide 8: Diagnostic Capability
Currently white light coronagraph images provide electron density
Density
Temperature
Velocity
The next generation of coronagraphs will use spectral information, to also determine

## Slide 9: How Does it Work?
High temperature coronal electron distribution “smooths” photospheric spectrum
The degree of smoothing is proportional to the electron temperature
Doppler shift of the entire spectrum is proportional to the flow speed
Coronal Model Spectrum
Photospheric Spectrum

## Slide 10: Temperature Measurement
The ratio of intensity two 50 A wide bands is temperature sensitive
Velocity sensitive ratio is available also
Coronal Model Spectrum

## Slide 11: Thomson Scattering Physics
Wavelength conserved in the frame of the moving electron
Doppler shift of source is observed in scattered radiation
Even if motion is transverse
Integration over Maxwellian velocity distribution, and line of sight sums all red and blue shift contributions
Spectral shift of approximately 4 A per 100 km/s
Technique demonstrated by observations during total solar eclipse

## Slide 12: Temperature Results from China Eclipse (2008)

## Slide 13
Radial Cut

## Slide 14: Results
Mg X 1.1 MK
N V 180 000 K
S II 25 000 K
H I Ly a 20 000 K)
C I < 10 000 K)
1.2
1.4
1
2
3
Temp (MK)
1.0
r/Rsun
SUMER Limb Scans
Filter Ratio Temperature

## Slide 15: West Limb Temperature (2006 Eclipse)

## Slide 16: Reconnection Jets

## Slide 17: Observing Reconnection
Line of Sight 1
Line of Sight 2
Sun
Wavelength
Flux Ratio
Few percent difference

## Slide 18: Reconnection Jets